3GPP TSG-SA3 LI Meeting#22														Tdoc S3LI0680

Montreal, Canada, 28 – 30 June 2006

LIT-TD02

Draft ETSI TS 1XX XXX V0.0.7 (2006-05)

Technical Specification

Telecoms & Internet converged Services & Protocols for Advanced Networks (TISPAN);

NGN Lawful Interception;

Lawful Interception functional entities, information flow and reference points

Reference

DTS/TISPAN-07013-Tech

Keywords

IP, Lawful Interception, Security, Telephony, VoIP

ETSI

650 Route des Lucioles

F-06921 Sophia Antipolis Cedex - FRANCE

Tel.: +33 4 92 94 42 00   Fax: +33 4 93 65 47 16

Siret N° 348 623 562 00017 - NAF 742 C

Association à but non lucratif enregistrée à la

Sous-Préfecture de Grasse (06) N° 7803/88

Important notice

Individual copies of the present document can be downloaded from:
http://www.etsi.org

The present document may be made available in more than one electronic version or in print. In any case of existing or perceived difference in contents between such versions, the reference version is the Portable Document Format (PDF). In case of dispute, the reference shall be the printing on ETSI printers of the PDF version kept on a specific network drive within ETSI Secretariat.

Users of the present document should be aware that the document may be subject to revision or change of status. Information on the current status of this and other ETSI documents is available at http://portal.etsi.org/tb/status/status.asp

If you find errors in the present document, send your comment to:
editor@etsi.org

Copyright Notification

No part may be reproduced except as authorized by written permission.
The copyright and the foregoing restriction extend to reproduction in all media.

© European Telecommunications Standards Institute yyyy.

All rights reserved.

DECTTM, PLUGTESTSTM and UMTSTM are Trade Marks of ETSI registered for the benefit of its Members.
TIPHONTM and the TIPHON logo are Trade Marks currently being registered by ETSI for the benefit of its Members. 3GPPTM is a Trade Mark of ETSI registered for the benefit of its Members and of the 3GPP Organizational Partners.

Contents

Intellectual Property Rights	4

Foreword	4

1	Scope	5

2	References	5

3	Definitions, symbols and abbreviations	6

3.1	Definitions	6

3.2	Abbreviations	6

4	Interception in the NGN	7

4.1	LI architecture model	7

4.2	Intercepted material	9

4.3	LI reference model	9

5	Interception of PSTN/ISDN Emulation System (PES)	10

5.1	Architecture for interception of PES	10

6	Interception of IMS	11

7	Identification of target of interception	12

7.1	ISDN/PSTN services	12

7.1.1	Emulation sub-system (PES)	12

7.1.2	Simulation sub-system (PSS)	12

7.2	IMS services	12

8	Security considerations	12

Annex A (normative): Endorsement statement for 3GPP TS 33.107	13

Annex B (normative):  Endorsement statement for 3GPP TS 33.108	14

Annex C (normative): Endorsement statement for TS 102 232	16

Annex D (normative): Endorsement statement for ES 201 671	17

Annex E (informative): Overview of handover interface	19

E.1	Document structure for LI NGN area	19

E.2	Selection of Handover interface	20

Annex F (informative): Bibliography	21

F.1	ETSI Specifications	21

F.2	3GPP specifications	21

F.3	ITU-T specifications	22

F.4	IETF specifications	22

F.5	ISO specifications	22

F.6	ANSI specifications	22

History	23

# Intellectual Property Rights

IPRs essential or potentially essential to the present document may have been declared to ETSI. The information pertaining to these essential IPRs, if any, is publicly available for ETSI members and non-members, and can be found in ETSI SR 000 314: "Intellectual Property Rights (IPRs); Essential, or potentially Essential, IPRs notified to ETSI in respect of ETSI standards", which is available from the ETSI Secretariat. Latest updates are available on the ETSI Web server (http://webapp.etsi.org/IPR/home.asp).

Pursuant to the ETSI IPR Policy, no investigation, including IPR searches, has been carried out by ETSI. No guarantee can be given as to the existence of other IPRs not referenced in ETSI SR 000 314 (or the updates on the ETSI Web server) which are, or may be, or may become, essential to the present document.

# Foreword

This Technical Specification (TS) has been produced by ETSI Technical Committee Telecoms & Internet converged Services & Protocols for Advanced Networks (TISPAN).

# Scope

The present document specifies the stage 1 and stage 2 model for Lawful Interception (LI) of TISPAN NGN services as specified by TR 180 001 [5] and covering the following services explicitly:

- PSTN/ISDN emulation services (non IMS) ; and,

- IMS based services.

A guide to the application of the handover specifications is given in informative annexes.

NOTE:	Handover aspects are not specified in this document but are described in TS 101 671 [2] and TS 102 232 [4].

# References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

- References are either specific (identified by date of publication and/or edition number or version number) or non-specific.

- For a specific reference, subsequent revisions do not apply.

- For a non-specific reference, the latest version applies.

Referenced documents which are not found to be publicly available in the expected location might be found at http://docbox.etsi.org/Reference.

[1]	ETSI ES 282 001: "Telecommunications and Internet converged Services and Protocols for Advanced Networking (TISPAN); NGN Functional Architecture Release 1"

[2]	ETSI TS 101 671: "Telecommunications security; Lawful Interception (LI); Handover Interface for the lawful interception of telecommunications traffic".

NOTE:	Periodically TS 101 671 is published as ES 201 671. A reference to the latest version of the TS as above reflects the latest stable content from ETSI TC LI.

[3]	ETSI TS 101 331: "Telecommunications security;Lawful Interception (LI);Requirements of Law Enforcement Agencies"

[4]	ETSI TS 102 232: "Telecommunications security; Lawful Interception (LI); Handover specification for IP delivery"

[5]	ETSI TR 180 001: "Telecommunications and Internet converged Services and Protocols for Advanced Networking (TISPAN); NGN Release 1; Release definition ".

[6]	ETSI TR 184 002: "Telecommunications and Internet Converged Services and Protocols for Advanced Networking (TISPAN); Identifiers (IDs) for NGN"

[7]	3GPP TS 33.107: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; 3G Security; Lawful interception architecture and functions".

[8]	3GPP TS 33.108: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; 3G security; Handover interface for Lawful Interception"

[9]	ETSI TR 102 058: "Telecommunications security; Lawful Interception (LI); Lawful Interception Architecture for IP Networks within a Communication Service Provider's domain"

[10]	ETSI ES 282 002: "Telecommunications and Internet converged Services and Protocols for Advanced Networking (TISPAN); PSTN/ISDN Emulation Sub-system (PES); Functional architecture"

[11]	ETSI ES 283 002: "Telecommunications and Internet converged Services and Protocols for Advanced Networking (TISPAN); PSTN/ISDN Emulation Sub-system (PES); NGN Release 1 H.248 Profile for controlling Access and Residential Gateways"

# Definitions, symbols and abbreviations

## Definitions

For the purposes of the present document, the terms and definitions given in TS 101 671 [2] and the following apply:

content of communication: information exchanged between two or more users of a telecommunications service, excluding intercept related information. This includes information which may, as part of some telecommunications service, be stored by one user for subsequent retrieval by another.

handover interface: physical and logical interface across which the interception measures are requested from Communications Service Provider (CSP), and the results of interception are delivered from a CSP to a law enforcement monitoring facility.

interception: action (based on the law), performed by a CSP, of making available certain information and providing that information to a law enforcement monitoring facility.

interception interface: physical and logical locations within the CSP telecommunications facilities where access to the content of communication and intercept related information is provided. The interception interface is not necessarily a single, fixed point.

intercept related information: collection of information or data associated with telecommunication services involving the target identity, specifically communication associated information or data (e.g. unsuccessful communication attempts), service associated information or data and location information.

internal network interface: network's internal interface between the Internal Intercepting Function and a mediation device.

law enforcement agency: organization authorized by a lawful authorization based on a national law to request interception measures and to receive the results of telecommunications interceptions.

law enforcement monitoring facility: law enforcement facility designated as the transmission destination for the results of interception relating to a particular interception subject.

mediation device: equipment, which realizes the mediation function.

mediation function: mechanism which passes information between a network operator, an access provider or service provider and a handover interface, and information between the internal network interface and the handover interface.

target identity: technical identity (e.g. the interception's subject directory number), which uniquely identifies a target of interception. One target may have one or several target identities.

## Abbreviations

For the purposes of the present document, the following abbreviations apply:

AF	Application Function

AGW	Access Gateway

CC	Content of Communication

CCCI	Content of Communication Control Interface

CCTF	Content of Communication Trigger Function

CCTI	Content of Communication Trigger Interface

CSP	Communications Service Provider

DF	Delivery Function

FE	Functional Entity

HI	Handover Interface

HI1	Handover Interface Port 1 (for Administrative Information)

HI2	Handover Interface Port 2 (for Intercept Related Information)

HI3	Handover Interface Port 3 (for Content of Communication)

ICI	Interception Configuration Information

IIF	Internal Interception Function

IMS	IP Multimedia Core Network Subsystem

INI	Internal network interface

IRI	Intercept Related Information

LEA	Law Enforcement Agency

LEMF	Law Enforcement Monitoring Facility

LI	Lawful Interception

MF	Mediation Function

MGC	Media Gateway Controller

MGW	Media Gateway

NGN	Next Generation Network

NGN-R1	NGN Release 1

PES	PSTN/ISDN Emulation Subsystem

PoI	Point of Interception

PSTN	Public Switched Telephone Network

PES	PSTN/ISDN Emulation Subsystem

PSS	PSTN/ISDN Simulation Subsystem

RGW	Residential Gateway

RTP	Real Time Protocol

SRTP	Secure Real Time Protocol

SGW	Signalling Gateway

TGW	Trunking Gateway

ToII	Target of Interception Identity

ToI	Target of Interception

UML	Unified Modelling Language

URI	Universal Resource Identifier

URL	Universal Resource Locator

# Interception in the NGN

The requirement for provision of lawful interception for all Communication Service Providers (CSP) is described in ETSI TS 101 331 [3] and the present document gives the stage 1 and stage 2 definition for provision of an interception capability in TISPAN NGN R1.

## 3	LI architecture model

The generic architecture of Interception is shown in figure 1. A Point of Interception (PoI), collocated with an NGN functional entity (the specific NGN FE varies with the service being intercepted), delivers intercepted material to a mediation function. The Mediation Function (MF) realizes (provides) an internal network interception interface that is provided between the PoI and the MF. The target is a specialist NGN user that receives service from the NGN FE.

NOTE 1:	The mediation function acts to mediate between the nationally specified handover interface and the internal interception interface.

NOTE 2:	A service offered to the NGN user may invoke many NGN-FEs.

NOTE 3:	There are a number of terms used across ETSI to refer to the various functions outlined in the previous paragraph. The MF is also known as a Delivery Function (DF) in 3GPP documents, the Internal Network Interception interfaces are also referred to in 3GPP as X interfaces.

Figure 1: Interception architecture as class interaction diagram

The data element "InterceptMaterial" is more fully described in figure 2.

NOTE:	The Intercept material class has two specialised forms that extend the intercept material class: content (visible at INI3); and, signalling (visible at INI2).

Figure 2: Class diagram of Intercepted Material

## 3	Intercepted material

The intercepted material illustrated in figure 2 contains the following information elements:

| Name | Shortname | Description |
| --- | --- | --- |
| Interception identity | InterceptId | Identifies the interception order and thus may identify the LEMF that the MF has to forward the intercepted data to |
| Target identity | TargetId | Uniquely identifies the target within the NGN |
| Direction | Direction | Identifies if the intercepted material originates from the target, or is intended for receipt by the target |
| Content type | ContentType | Serves to identify the media type (e.g. RTP, SRTP) |
| Media content | MediaContent | Container for the original media packet (copied in full) (see note) |
| Signalling type | SignallingType | Serves to identify the signalling protocol (e.g. SIP, DSS1) |
| Signalling content | SignallingContent | Container for the original signalling packet (copied in full) (see note) |
| NOTE: At stage 3 the impact of mutable fields and the detail handling of system inserted data to intercepted packets needs to be considered such that the final delivered intercepted material is an accurate record of the activity of the target. |

## 3	LI reference model

The present document adopts the generic reference model for the interception domain from TR 102 058 [9], its internal intercept functions, IRI-IIF, CCTF, and CC-IIF, and the internal interfaces INI1, INI2, INI3, CCTI and CCCI as shown in figure 3.

NOTE:	Interfaces INI1, INI1a, INI1b, INI1c, CCTF, CCTI and CCCI are not defined in the present document but are shown in the figure for completeness

Figure 3: Reference Model for Lawful Interception from [9]

The reference model depicts the following functions and interfaces:

Intercept Related Information Internal Intercept Function (IRI-IIF) generates signalling intercept material.

Content of Communication Internal Intercept Function (CC-IIF) generates content intercept material.

Content of Communication Trigger Function (CCTF) controls the CC-IIF.

Internal interface INI1 carries provisioning information from the Lawful Interception Administration Function (AF) to the Internal Intercept Functions (IIF).

Internal interface INI2 carries Intercept Related Information (IRI) from the IRI-IIF to the MF.

Internal interface INI3 carries Content of Communication (CC) information from the CC-IIF to the MF.

Content of Communication Trigger Interface (CCTI) carries trigger information from the IRI-IIF to the CCTF.

Content of Communication Control Interface (CCCI) carries controls information from the CCTF to the CC-IIF.

A complete explanation of the functions and interface is found in clause 4 of TR 102 058 [9].

# 3	Interception of PSTN/ISDN Emulation System (PES)

NOTE:	This clause refers only to a "softswitch" implementation of PES. If IMS is used to implement the PES service then clause 6 of the present document applies.

## 3	Architecture for interception of PES

The model for PES is shown in figure 4 as a UML model.

NOTE 1:	The classes shown as <<asset>> in the figure are NGN-FEs as defined by figure 1.

NOTE 2:	Specific protocol instances for the SGW(MGW and MGC(MGW are not shown although H.248 is recommended by ES 283 002 [11].

Figure 4: PES architecture as class diagram

The point of interception (as defined in clause 4) for capture of signalling interception material shall be the SGW (which may be collocated with the MGC in a deployed stage 3 implementation).

The point of interception (as defined in clause 4) for capture of content interception material shall be the MGW. The RGW should not be used as the PoI as the confidentiality of the interception measures cannot be assured if the PoI is not within the trusted and secured (including physical security) domain of the CSP.

# Interception of IMS

The stage 2 definition for interception of IMS found in 3GPP TS 33.107 [7] shall apply for TISPAN NGN R1. Annex B specifies the parts of 3GPP TS 33.107 that apply.

NOTE 1:	When IMS is providing a PES service the interception service identified above and defined in 3GPP TS 33.107 [7] still applies.

For interception of Content of Communication (CC) attached to IMS services 3GPP TS 33.107 [7] shall apply for TISPAN NGN R1. Annex B specifies the parts of 3GPP TS 33.107 that apply.

NOTE 2:	The allocation of interception capabilities in each of the T-MGF (Trunking Media Gateway Function); A-MGF (Access Media Gateway Function) (for IMS PSTN/ISDN emulation); BGF (Border Gateway Function); and MRFC (Multimedia Resource Function Controller) need to be described in 3GPP TS 33.107 .

NOTE 3:	Detail specification of interception of IMS where GSN packet data services do not apply has to be addressed in an update of 3GPP TS 33.107. An illustration of a solution is provided in annex .. of the present document.

# Identification of target of interception

## ISDN/PSTN services

### Emulation sub-system (PES)

In the PSTN/ISDN emulation sub-system the target shall be identified in the service domain by a globally unique E.164 identity.

NOTE:	The PES offers seamless ISDN/PSTN service to existing core network customers who will remain identified by their E.164 identity.

### Simulation sub-system (PSS)

In the PSTN/ISDN simulation sub-system the target shall be identified in the service domain by a globally unique E.164 identity that may be mapped to a system unique SIP-identity.

## IMS services

IMS service users shall be identified by either a SIP-url or a tel-url [].

# Security considerations

The guidelines for security identified in TS 101 331 [3] apply. The provision and actions of the interception measure should be confidential and not discoverable, or alterable, by unauthorised parties.

Annex A (normative):
Endorsement statement for 3GPP TS 33.107

For the stage 2 definition of the interception of IMS and generic IP subsystem parts of 3GPP TS 33.107 apply normatively in the context of TISPAN NGN. This annex summarises those parts of 3GPP TS 33.107 that apply in the context of TISPAN NGN LI.

NOTE:	Where no specific endorsement statement is given the text in the endorsed document is considered to have only background relevance and not to form part of the normative specification for NGN-R1 interception.

| Clause | Applicability in TISPAN NGN R1 |
| --- | --- |
| 1 |  |
| 2 |  |
| 3 |  |
| 4 | Fig. 1d applies |
| 5 |  |
| 6 | Does not apply |
| 7 |  |
| 7A | Applies in full |
| 7A.1 | Applies in full |
| 7A.2 | Applies in full |
| 7A.3 | Applies in full |
| 7A.4 | Applies in full |
| 7A.5 | Does not apply (service defined only for cellular network) |
| 8 |  |
| 9 |  |
| Annex A | Does not apply |
| Annex B |  |
| Annex C |  |
| Annex D | Does not apply |
| Annex G | Does not apply (informative annex showing history of CRs applied to the document) |
| NOTE: Annexes E and F do not exist in 3GPP TS 33.107 |

Annex B (normative): 
Endorsement statement for 3GPP TS 33.108

For stage 3 definition of the interception of IMS and generic IP subsystem parts of 3GPP TS 33.108 apply normatively in the context of TISPAN NGN. This annex summarises those parts of 3GPP TS 33.108 that apply in the context of TISPAN NGN LI.

NOTE:	Where no specific endorsement statement is given the text in the endorsed document is considered to have only background relevance and not to form part of the normative specification for NGN-R1 interception.

| Clause | Applicability in TISPAN NGN R1 |
| --- | --- |
| 1 |  |
| 2 |  |
| 3 |  |
| 4 |  |
| 4.1 |  |
| 4.2 |  |
| 4.3 |  |
| 4.4 |  |
| 4.4.1 | Applies in full |
| 4.4.2 |  |
| 4.5 | Applies in full |
| 4.5.1 | Applies in full |
| 4.5.2 | Applies in full |
| 4.5.3 | Applies in full |
| 5 | Does not apply |
| 6 |  |
| 7 |  |
| 7.1 |  |
| 7.1.1 |  |
| 7.1.2 |  |
| 7.1.3 | Correlation to the relevant CC is necessary |
| 7.2 |  |
| 7.3 |  |
| 7.4 |  |
| 7.5 | Yes / for correlation ASN.1 parameter correlation had to be used |
| 7.5.1 | Yes / for correlation ASN.1 parameter correlation had to be used |
| 7.6 |  |
| Annex A |  |
| Annex B |  |
| B.1 |  |
| B.2 |  |
| B.3 | Applies in full |
| B.3a | Does not apply |
| B.4 |  |
| B.5 |  |
| B.6 | Does not apply |
| Annex C |  |
| Annex D |  |
| Annex E |  |
| Annex F |  |
| Annex G |  |
| Annex H | Applies in full |
| Annex J | Does not apply |
| Annex K | Does not apply (informative annex showing history of CRs applied to the document) |
| NOTE: Whereas the scope of the present document is interception in the NGN domain the scope of 3GPP TS 33.108 is handover for the PLMN, the data emenating from the PLMN is described and covers a range of capabilities more specific than those of the NGN (although the NGN is a superset of the capabilities that form the PLMN). |

Annex C (normative):
Endorsement statement for TS 102 232

Annex D (normative):
Endorsement statement for ES 201 671

| Clause | Title | Applicability in TISPAN NGN R1 |
| --- | --- | --- |
| 1 | Scope |  |
| 2 | References |  |
| 3 | Definitions and abbreviations |  |
| 3.1 | Definitions |  |
| 3.2 | Abbreviations |  |
| 4 | General requirements |  |
| 4.1 | Basic principles for the Handover Interface | Applies in full |
| 4.2 | Legal requirements | Applies in full |
| 4.3 | Functional requirements | Applies in full |
| 5 | Overview of Handover Interface | Applies in full |
| 5.1 | Handover Interface port 1 (HI1) | No: national implementation |
| 5.1.1 | Manual interface | No: national implementation |
| 5.1.2 | Electronic interface | No: national implementation |
| 5.2 | Handover Interface port 2 (HI2) | Applies in full |
| 5.3 | Handover Interface port 3 (HI3) | Applies in full |
| 6 | Specific identifiers for LI | Applies in full |
| 6.1 | Lawful Interception IDentifier (LIID) | Applies in full |
| 6.2 | Communication IDentifier (CID) | Applies in full |
| 6.2.1 | Network IDentifier (NID) | Applies in full |
| 6.2.2 | Communication Identity Number (CIN) - optional | Applies in full |
| 7 | HI1: Interface port for administrative information |  |
| 7.1 | Information for the activation of lawful interception | Applies in full |
| 7.2 | LI notifications towards the LEMF | No: national implementation |
| 8 | HI2: Interface port for Intercept Related Information |  |
| 8.1 | Data transmission protocols |  |
| 8.1.1 | Application for IRI (HI2 information) |  |
| 8.2 | Types of IRI records |  |
| 9 | HI3: Interface port for Content of Communication |  |
| 10 | Performance and quality |  |
| 10.1 | Timing |  |
| 10.2 | Quality |  |
| 11 | Security aspects | Advisable |
| 11.1 | Security properties | Advisable |
| 11.2 | Security mechanisms | Advisable |
| 12 | Quantitative aspects | national matter |
| Annex A (normative): | Circuit switched network handover | Applies in full |
| Annex B (normative): | Packet switched network handover | Applies in full |
| Annex C (normative): | HI2 Delivery mechanisms and procedures |  |
| C.1 | ROSE |  |
| C.2 | FTP |  |
| Annex D (normative): | Structure of data at the Handover Interface (ASN.1) |  |
| Annex E (informative): | Use of subaddress and calling party number to carry correlation information | No |
| Annex F (informative): | GPRS HI3 Interface |  |
| Annex G (informative): | LEMF requirements - handling of unrecognized fields and parameters |  |
| Annex H (informative): | IP Multimedia Subsystem (IMS) handover |  |
| Annex I (informative): | Latest ASN.1 module versions | No |
| Annex J (informative): | Bibliography |  |
| Annex K (informative): | Change Request history | No |

Annex E (informative):
Overview of handover interface

# E.1	Document structure for LI NGN area

The relationships between LI documents are shown in figure E.1 (UML is used for this illustration).

Figure E.1: Document architecture for NGN LI domain

The realisation of the document relationships and the implied endorsements are shown in figure E.2 for the LI domain.

Figure E.2: NGN LI document relationships

# E.2	Selection of Handover interface

Hondover of intercepted material should be made by reference to one or more of the following specifications:

TS 101 671 [2]: Handover Interface for the lawful interception of telecommunications traffic

TS 33.108 [8]: Handover interface for Lawful Interception

TS 102 232 [4]: Handover specification for IP delivery

NOTE:	National specifications may be used instead of any of the ETSI specifications cited above.

Annex F (informative):
Bibliography

# F.1	ETSI Specifications

[A]	ETSI EN 300 356 (all parts): "Integrated Services Digital Network (ISDN); Signalling System No.7; ISDN User Part (ISUP) version 3 for the international interface".

[B]	ETSI EN 300 403-1 (V1.3.2): "Integrated Services Digital Network (ISDN); Digital Subscriber Signalling System No. one (DSS1) protocol; Signalling network layer for circuit-mode basic call control; Part 1: Protocol specification [ITU-T Recommendation Q.931 (1993), modified]".

[C]	ETSI ES 201 158: "Telecommunications security; Lawful Interception (LI); Requirements for network functions".

[D]	ETSI ETR 330: "Security Techniques Advisory Group (STAG); A guide to legislative and regulatory environment".

[E]	ETSI TR 101 331: "Telecommunications security; Lawful Interception (LI); requirements of Law Enforcement Agencies".

[F]	ETSI TS 101 671: "Handover Interface for the lawful interception of telecommunications traffic".

[G]	ETSI TS 102 232: Telecommunications security; Lawful Interception (LI); Handover specification for IP delivery

# F.2	3GPP specifications

[H]	3GPP TS 29.002: "3rd Generation Partnership Project; Technical Specification Group Core Network; Mobile Application Part (MAP) specification".

[I]	3GPP TS 23.003: "3rd Generation Partnership Project; Technical Specification Group Core Network; Numbering, addressing, and identification".

[J]	3GPP TS 23.107: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; Quality of Service QoS concepts and architecture".

[K]		3GPP TS 23.228: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; IP Multimedia Subsystem (IMS); Stage 2"

[L]	3GPP TS 24.008: "3GPP Technical Specification Group Core Network; Mobile radio interface Layer 3 specification, Core network protocol; Stage 3".

[M]	3GPP TS 29.060: "3rd Generation Partnership Project; Technical Specification Group Core Network; General Packet Radio Service (GPRS); GPRS Tunnelling Protocol (GTP) across the Gn and Gp interface".

[N]	3GPP TS 32.215: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; Telecommunication Management; Charging Management; Charging data description for the Packet Switched (PS) domain)".

[O]	3GPP TS 33.106: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; 3G Security; Lawful Interception Requirements".

[P]	3GPP TS 23.032: "3rd Generation Partnership Project; Technical Specification Group Core Network; Universal Geographical Area Description (GAD)".

[Q]	3GPP TR 21.905: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; Vocabulary for 3GPP Specifications".

# F.3	ITU-T specifications

[R]	ITU-T Recommendation Q.763: "Signalling System No. 7 - ISDN User Part formats and codes".

[S]	ITU-T Recommendation Q.931: "ISDN user-network interface layer 3 specification for basic call control".

[T]	ITU-T Recommendation X.680: "Abstract Syntax Notation One (ASN.1): Specification of Basic Notation".

[U]	ITU-T Recommendation X.681: "Abstract Syntax Notation One (ASN.1): Information Object Specification".

[V]	ITU-T Recommendation X.681: "Abstract Syntax Notation One (ASN.1): Constraint Specification".

[W]	ITU-T Recommendation X.681: "Abstract Syntax Notation One (ASN.1): Parameterization of ASN.1 Specifications".

[X]	ITU-T Recommendation X.690: "ASN.1 encoding rules: Specification of Basic Encoding Rules (BER), Canonical Encoding Rules (CER) and Distinguished Encoding Rules (DER)".

[Y]	ITU-T Recommendation X.880: "Information technology - Remote Operations: Concepts, model and notation".

[Z]	ITU-T Recommendation X.882: "Information technology - Remote Operations: OSI realizations - Remote Operations Service Element (ROSE) protocol specification".

# F.4	IETF specifications

[AA]	IETF STD 0005 (RFC 0791): "Internet Protocol".

[AB]	IETF STD 0007 (RFC 0793): "Transmission Control Protocol".

[AC]	IETF STD 0009 (RFC 0959): "File Transfer Protocol (FTP)".

[AD]	IETF RFC 1006: "ISO Transport Service on top of the TCP".

[AE]	IETF RFC 2126: "ISO Transport Service on top of TCP (ITOT)".

[AF]	IETF RFC 2806: "URLs for Telephone Calls".

[AG]	IETF RFC 3261: "SIP: Session Initiation Protocol".

# F.5	ISO specifications

[AH]	ISO 3166-1: "Codes for the representation of names of countries and their subdivisions - Part 1: Country codes".

# F.6	ANSI specifications

[AI]	ANSI/J-STD-025-A: "Lawfully Authorized Electronic Surveillance".

# History

| Document history |
| --- |
| V0.0.0 | April 2005 | Draft for initial review |
| V0.0.1 | May 2005 | Very minor tidy up resulting from April 21st 2005 meeting of WG7 in Oslo |
| V0.0.1 | May 2005 | Input draft to TISPAN06, 9-13 May 2005 |
| V0.0.2 | September 2005 | Input to Sorrento meeting (October 3rd 2005) |
| V0.0.3 | Nov. 2005 | Input to TISPAN #09 |
| V0,04 | January 2006 | Input to TISPAN#10 and to rapporteur’s meeting |
| V0.0.5 | March 2006 | Input to TISPAN#10bis |
| V0.0.6 | April 2006 | Input to rapporteur’s meeting (Limassol, May 8th) |
| V0.0.7 | May 2006 | Output from rapporteur’s meeting (Limassol, May 8th) |
| V0.0.8 | May 2006 | Input to TISPAN#10ter meeting (Sophia Antipolis, June 12th-16th, 2006) |
| V0.0.9 | June 2006 | Output of TISPAN#10ter meeting (Sophia Antipolis, June 12th-16th, 2006) |

# Text boxes

IRI Internal Intercept

Function

(IRI-IIF)

CC Trigger Function

(CCTF)

Administration Function (AF)

INI1c

INI1b

Law

Enforcement

Monitoring

Facility

(LEMF)

LEA

Administration

Function

CC Internal Intercept

Function

(CC-IIF)

CCTI

CSP DOMAIN

LEA DOMAIN

CCCI

INI1a

HI

INI3

INI2

HI3

HI2

Mediation

Function

(MF)

HI1