3GPP TSG SA WG3 LI Meeting #25  	SA3LI0y_0yyry

25-27 April 2007

Riga, Latvia

| CR-Form-v9.3 |
| --- |
| CHANGE REQUEST |
| ( | 33.107 | CR | CRNum | ( rev | - | ( Current version: | 7.5.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Add a method to realize IMS interception |
| --- | --- |
| Source to WG: ( | SA3-LI(ZTE Corporation) |
| Source to TSG: ( |  |
| Work item code: ( | SEC-LI |  | Date: ( | April, 2007 |
| Category: ( | B |  | Release: ( | 7 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) |
| Reason for change: ( | IRI Interception at a CSCF and CC Interception at a GSN are defined in the TS 33.107. However, CSCF and GSN locate in the control layer and transport layer seperately, it will be a complicated thing to set the target at every GSN statically in order to get the CC. Combined way of IRI Interception and CC interception should be defined in IMS interception. Here supplys a realization method based on the dynamic activation of the CC filter in GGSN. |
| Summary of change: ( | Addition of new section for the realization of IMS interception |
| Consequences if ( not approved: | No complete solution for IMS interception |
| Clauses affected: ( | Annex C (add annex C.7) |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

********** Modification ************

# C.7 IMS interception based on dynamic activation

## C.7.1 Configuration

In this configuration shown in Figure 1, the initial provision is set on the CSCF for the IRI, however this activation and invocation does not produce the content of communications. When the interception in CSCF is triggered, a dynamic activation through INI1b interface on the certain GGSN should be executed without time delay for the content of communications.

Figure 1 IMS interception configuration

## C.7.2 Operation flows

Figure 2 Operation flow

The following describes the sequence of the operation shown in Figure 2:

- The LEA delivers a court order to the network administrator who operates the LI Administration Function.

- The ADMF sends an INI1a LI_Activation_Request to provision the CSCF with the SIP_URI or TEL_URI target identifier.

- When the target has a communication activity, the interception in CSCF will be triggered. The bearer information including the GGSN address and the correlation number which contains the GGSN ID and GSN charging-ID could be achieved by CSCF through PDF. The GSN charging-ID is assigned for each PDP context activation on GGSN.

- The SIP messages related to the target  and the bearer information are sent to the MF from CSCF through INI2.

- In the MF, the INI2 message is forwarded to the LEMF in the standard HI2 format.

- In the MF, the Target Endpoint IP address and UDP port is got from the SDP of SIP message.

- The Target Endpoint IP address and UDP port and the Correlation Number identifying the PDP context will be taken as the CC filter. The MF sends an INI1c LI_DynamicActivation_Inform to ADMF to activate the interception on the certain GGSN dynamically with the CC filter.

- ADMF sends an INI1b LI_Activation_Request to the GGSN with the target CC filter and a dynamic_activation_number which identifys this dynamic activation. This step should be done on a automatic method so as to avoid the time delay.

- GGSN starts a CC filter process.

- The RTP packets meet the target CC filter are intercepted and sent to the MF throuth INI3 by the GGSN.

- INI3 is correlated with the INI2. CIN and sequence number is assigned when the interface is based on TS 102 232. The HI3 message is forwarded to the LEMF.

- The communication session is released.

- When GGSN detects the PDP Context is deactivated, CC filter is stopped automatically.

********** End of Modifications ************

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.