3GPP TSG SA WG3 LI Meeting #25  	SA3LI0y_0yyry

25-27 April 2007

Riga, Latvia

| CR-Form-v9.3 |
| --- |
| CHANGE REQUEST |
| ( | 33.107 | CR | CRNum | ( rev | - | ( Current version: | 7.5.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | IMS lawful interception solution based on media re-routing |
| --- | --- |
| Source to WG: ( | SA3-LI(ZTE Corporation) |
| Source to TSG: ( |  |
| Work item code: ( | SEC-LI |  | Date: ( | April, 2007 |
| Category: ( | B |  | Release: ( | 7 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) |
| Reason for change: ( | In IMS architecture, the control layer is totally separated with the transport layer. The communication content can’t be got directly from the communication control device. The output of CC is depended on a separate activation on the GSN device. Further more, there are much more kinds of devices than before. We can see that many a deploy scenarios are defined in ETSI TR 102528 Annex B. It defines the realization scenarios successfully. However, it will be a difficult thing for all of these devices referred in that clause supply the LI interface and functions. Because maybe they are developed by different vendors and these so many interfaces are not easy to negotiate, and it will be a very huge workload for all of these devices to support these functions. In the IMS domain, all of the communication will be controlled by P-CSCF/S-CSCF through SIP message. It supplys the possiblility that the LI function is realized only in P-CSCF/S-CSCF and the LIG device and all the IMS communication could be intercepted at the same time. In this document, an method is supplied to realize the interception of IMS based on rerouting and media duplication processor. This method could be a supplementary as the national option to the current solution. |
| Summary of change: ( | Addition of IMS lawful interception solution based on media re-routing |
| Consequences if ( not approved: | No complete solution for IMS interception |
| Clauses affected: ( | 7(Add clause 7B) |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

********** Modification ************

# 7B	Interception of IMS based on media re-routing

## 7B.1 realization configuration

The configuration of this realization is shown in Figure 7B-1.  This  implementation could be taken as the national option.

The interception is triggered in the P-CSCF/S-CSCF when the communication of the target starts and the SIP message reaches the P-CSCF/S-CSCF. Firstly, P-CSCF/S-CSCF needs apply the media tunnel traverse the LIG and the new ports will be supplied by the LIG which will be looked on as the agent ports of the calling party and the called party. The CSCF replace the calling party port in SDP part of the INVITE message with the calling party agent port which locates in the LIG.The the INVITE message is forwarded by the CSCF through the normal routing. When the 200OK reaches the CSCF from the called party, the called party port in SDP part is replaced with the called party agent port which locates in the LIG. Then the 200OK is forwarded to the next station.

So, the communication media streams will be re-routed to the LIG and traverse the LIG to the destination party, while the CC could be duplicated simultaneously by the media duplication process(MDP) in LIG, and sent to the LEMF for interception through HI3.

Figure 7B-1Interception configuration based on the media re-routing

********** End of Modifications ************

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.