ETSI TR 102 503 PROPOSED V1.3.1 (2007-10)

Technical Report

Lawful Interception (LI);

ASN.1 Object Identifiers in Lawful Interception Specifications

Reference

RTR/LI-00038

Keywords

ASN.1, object identifier

ETSI

650 Route des Lucioles

F-06921 Sophia Antipolis Cedex - FRANCE

Tel.: +33 4 92 94 42 00   Fax: +33 4 93 65 47 16

Siret N° 348 623 562 00017 - NAF 742 C

Association à but non lucratif enregistrée à la

Sous-Préfecture de Grasse (06) N° 7803/88

Important notice

Individual copies of the present document can be downloaded from:
http://www.etsi.org

The present document may be made available in more than one electronic version or in print. In any case of existing or perceived difference in contents between such versions, the reference version is the Portable Document Format (PDF). In case of dispute, the reference shall be the printing on ETSI printers of the PDF version kept on a specific network drive within ETSI Secretariat.

Users of the present document should be aware that the document may be subject to revision or change of status. Information on the current status of this and other ETSI documents is available at http://portal.etsi.org/tb/status/status.asp

If you find errors in the present document, please send your comment to one of the following services:
http://portal.etsi.org/chaircor/ETSI_support.asp

Copyright Notification

No part may be reproduced except as authorized by written permission.
The copyright and the foregoing restriction extend to reproduction in all media.

© European Telecommunications Standards Institute 2007.

All rights reserved.

DECTTM, PLUGTESTSTM and UMTSTM are Trade Marks of ETSI registered for the benefit of its Members.
TIPHONTM and the TIPHON logo are Trade Marks currently being registered by ETSI for the benefit of its Members. 3GPPTM is a Trade Mark of ETSI registered for the benefit of its Members and of the 3GPP Organizational Partners.

Contents

Intellectual Property Rights	4

Foreword	4

1	Scope	5

2	References	5

3	Definitions and abbreviations	5

3.1	Definitions	5

3.2	Abbreviations	6

4	Structure of the ETSI domain	6

4.1	Tree structure	6

4.2	Description of the ETSI domain	6

Annex A:	Change Request history	12

History	13

# Intellectual Property Rights

IPRs essential or potentially essential to the present document may have been declared to ETSI. The information pertaining to these essential IPRs, if any, is publicly available for ETSI members and non-members, and can be found in ETSI SR 000 314: "Intellectual Property Rights (IPRs); Essential, or potentially Essential, IPRs notified to ETSI in respect of ETSI standards", which is available from the ETSI Secretariat. Latest updates are available on the ETSI Web server (http://webapp.etsi.org/IPR/home.asp).

Pursuant to the ETSI IPR Policy, no investigation, including IPR searches, has been carried out by ETSI. No guarantee can be given as to the existence of other IPRs not referenced in ETSI SR 000 314 (or the updates on the ETSI Web server) which are, or may be, or may become, essential to the present document.

# Foreword

This Technical Report (TR) has been produced by ETSI Technical Committee Lawful Interception (LI).

# 1	Scope

The present document gives an overview over the relevant Object IDentifiers (OID) used in Lawful Interception specifications of ETSI and other specifications from ITU-T and ISO.

# 2	References

For the purposes of this Technical Report (TR), the following references apply:

[1]	ETSI EG 200 351: "ETSI object identifier tree; Rules and registration procedures".

[2]	ETSI ES 201 671: "Telecommunications security; Lawful Interception (LI); Handover Interface for the lawful interception of telecommunications traffic".

[3]	ETSI TS 101 671: "Lawful Interception (LI); Handover Interface for the lawful interception of telecommunications traffic".

NOTE:	Periodically TS 101 671 is published as ES 201 671. A reference to the latest version of the TS as above reflects the latest stable content from ETSI/TC LI.

[4]	ETSI TS 133 108: "Universal Mobile Telecommunications System (UMTS); 3G security; Handover interface for Lawful Interception (LI) (3GPP TS 33.108)".

[5]	ETSI TS 102 232: "Lawful Interception (LI); Handover specification for IP delivery".

[6]	ETSI TS 102 233: "Lawful Interception (LI); Service specific details for E-mail services"

[7]	ETSI TS 102 234: "Lawful Interception (LI); Service-specific details for internet access services".

[8]	ETSI TS 102 815: "Lawful Interception (LI); Service-specific details for Layer 2 Lawful Interception".

[9]	ITU-T Recommendation X.880: "Information technology - Remote Operations: Concepts, model and notation".

[10]	ETSI TS 101 909-20-1: "Digital Broadband Cable Access to the Public Telecommunications Network; IP Multimedia Time Critical Services; Part 20: Lawful Interception; 
Sub-part 1: CMS based Voice Telephony Services".

[11]	ETSI TS 101 909-20-2: "Digital Broadband Cable Access to the Public Telecommunications Network; IP Multimedia Time Critical Services; Part 20: Lawful Interception; 
Sub-part 2: Streamed multimedia services".

[12]	ETSI EN 301 040: "Terrestrial Trunked Radio (TETRA); Security; Lawful Interception (LI) interface".

[13]	ETSI TS 102 232-1: "Lawful Interception (LI); Handover Interface and Service-Specific Details (SSD) for IP delivery; Part 1: Handover specification for IP delivery".

[14]	ETSI TS 102 233-2: "Lawful Interception (LI); Handover Interface and Service-Specific Details (SSD) for IP delivery; Part 2: Service specific details for E-mail services".

[15]	ETSI TS 102 232-3: "Lawful Interception (LI); Handover Interface and Service-Specific Details (SSD) for IP delivery; Part 3: Service-specific details for internet access services",

[16]	ETSI TS 102 232-4 "Lawful Interception (LI); Handover Interface and Service-Specific Details (SSD) for IP delivery; Part 4: Service-specific details for Layer 2 services".

[17]	ETSI 102 232-5: "Lawful Interception (LI); Handover Interface and Service-Specific Details (SSD) for IP delivery; Part 5: Service-specific details for IP Multimedia Services”.

[18]	ETSI 102 232-6: "Lawful Interception (LI); Handover Interface and Service-Specific Details (SSD) for IP delivery; Part 6: Service-specific details for PSTN/ISDN services”.

# 3	Definitions and abbreviations

## 3.1	Definitions

For the purposes of the present document, the following terms and definitions apply:

common domain: set of objects, which are part of the definition of a protocol or a set of related protocols

information object: well-defined piece of information, definition, or specification, which requires a name in order to, identify its use in an instance of communication

Object identifier (OID): value (distinguishable from all other such values), which is associated with an information object

NOTE: 	An object identifier consists of a sequence of integers. Each integer represents a node in the object identifier tree. So, each successive integer can be thought of as a selection of an end of a branch of the tree. The branch is traversed to get to the next level in the tree.

## 3.2	Abbreviations

For the purposes of the present document, the following abbreviations apply:

ASN.1	Abstract Syntax Notation One

LI	Lawful Interception

OID	Object IDentifier

ROSE	Remote Operation Service Element

# 4	Structure of the ETSI domain

## 4.1	Tree structure

Figure 1 contains the structure for the ETSI domain with the included Lawful Intercept domain and ASN.1 modules from other Lawful Interception (LI) specifications.

ETSI/TC LI shall act as the formal registration authority for the Lawful Intercept domain, except for the "threeGPP(4)" subdomain which is administrated by 3GPP/SA3-LI, ETSI/TC AT-D is responsible for the "ts101909(1909)" subdomain and ETSI/EP TETRA is responsible for the "en301040(1040)" subdomain.

## 4.2	Description of the ETSI domain

Tables 1 to 3 contain the OIDs of the ETSI domain. The entries in the last column in the tables point to the specification where the modules can be found.

For information, in addition to those OIDs defined within ETSI/TC LI, table 4 contains the OIDs for the ROSE operations. Because of the imports, the ASN.1 modules of ROSE must be included when syntax checking or compiling the LI specific ASN.1 modules.

Figure 1: Tree structure of ETSI domain

NOTE: 	There are other standards which contain ASN.1 modules for interception (see http://portal.etsi.org/li/status.asp).

Table 1: OIDs of the ETSI domain

| Object IDentifier | Specification |
| --- | --- |
| itu-t (0) | identified-organizations(4) | etsi(0) | securityDomain(2) |  | TR 102 503 V1.1.1 |
|  |  |  |  | fraud(1) |  | ES 201 671 [2], V1.1.1 clause A.4 |
|  |  |  |  | lawfulIntercept(2) |  | ES 201 671 [2], V1.1.1 clause A.4 |
|  |  |  |  |  | hi1(0) | notification Operations (1) | version1(1) version2(2) version3(3) version4(4) version5(5) | ES 201 671 [2], V1.1.1 clause A.4 ES 201 671 [2], V2.1.1 clause D.4 TS 101 671 [3], V2.9.1 clause D.4 TS 101 671 [3], V2.11.1 clause D.4 TS 101 671 [3], V2.12.1 clause D.4 |
|  |  |  |  |  | hi2(1) | version1(1) version2(2) version3(3) version4(4) version5(5) version6(6) version7(7) version8(8) version9(9) version10(10) | ES 201 671 [2], V1.1.1 clause A.5 ES 201 671 [2], V2.1.1 clause D.5 TS 101 671 [3], V2.5.1 clause D.5 TS 101 671 [3], V2.7.1 clause D.5 TS 101 671 [3], V2.9.1 clause D.5 TS 101 671 [3], V2.10.1 clause D.5 TS 101 671 [3], V2.11.1 clause D.5 TS 101 671 [3], V2.12.1 clause D.5 TS 101 671 [3], V2.13.1 clause D.5 TS 101 671 [3], V2.14.1 clause D.5 |
|  |  |  |  |  | hi3(2) | circuitLI(1) | version1(1) version2(2) version3(3) | ES 201 671 [2], V1.1.1 clause A.6 ES 201 671 [2], V2.1.1 clause D.6 TS 101 671 [3], V.2.12.1 clause D.6 |
|  |  |  |  |  |  | tETRALI(2) | version1(1) | ES 201 671 [2], V1.1.1 clause A.7 For Further Study |
|  |  |  |  |  |  | gPRSLI(3) | version1(1) version2(2) version3(3) | ES 201 671 [2], V1.1.1 clause A.8 TS 101 671 [3], V2.10.1 clause D.9 TS 101 671 [3], V2.12.1 clause D.9 |
|  |  |  |  |  |  | cclinkLI(4) | version1(1) version2(2) version3(3) version4(4) | ES 201 671 [2], V1.1.1 clause A.9 ES 201 671 [2], V2.1.1 clause D.8 TS 101 671 [3], V2.7.1 clause D.8 TS 101 671 [3], V.2.12.1 clause D.8 |
|  |  |  |  |  |  | gSMLI(5) | ES 201 671 [2], V2.1.1 clause D.2 For Further Study |

| Object IDentifier | Specification |
| --- | --- |
| itu-t (0) | identified-organizations(4) | etsi(0) | securityDomain(2) | lawfulIntercept(2) | him(3) | version1(1) version2(2) version3(3) | ES 201 671 [2], V1.1.1 clause A.3 ES 201 671 [2], V2.1.1 clause D.3 TS 101 671 [3], V2.12.1 clause D.3 |
|  |  |  |  |  | threeGPP(4) | hi2(1) | version-1(1) version-2(2) | 3GPP TS 33.108 [4], V5.0.0 clause B.3 3GPP TS 33.108 [4], V6.0.0 clause B.3 |
|  |  |  |  |  |  |  | r5(5) | version-3(3) version-4(4) | 3GPP TS 33.108 [4], V5.7.0 clause B.3 3GPP TS 33.108 [4], V5.8.0 clause B.3 |
|  |  |  |  |  |  |  | r6(6) | version-3(3) version-4(4) version-5(5) version-6(6) | 3GPP TS 33.108 [4], V6.5.0 clause B.3 3GPP TS 33.108 [4], V6.6.0 clause B.3 3GPP TS 33.108 [4], V6.7.0 clause B.3 3GPP TS 33.108 [4], V6.8.0 clause B.3 |
|  |  |  |  |  |  |  | r7(7) | version-1(1) version-2(2) version-3(3) | 3GPP TS 33.108 [4], V7.2.0 clause B.3 3GPP TS 33.108 [4], V7.3.0 clause B.3 3GPP TS 33.108 [4], V7.8.0 clause B.3 |
|  |  |  |  |  |  |  | r8(8) | version-1(1) | 3GPP TS 33.108 [4], V8.0.0 clause B.3 |
|  |  |  |  |  |  | hi3(2) | version-1(1) | 3GPP TS 33.108 [4], V5.0.0 clause B.4 |
|  |  |  |  |  |  |  | r5(5) | version-2(2) | 3GPP TS 33.108 [4], V5.9.0 clause B.4 |
|  |  |  |  |  |  |  | r6(6) | version-1(1) version-2(2) version-3(3) | 3GPP TS 33.108 [4], V6.5.0 clause B.4 3GPP TS 33.108 [4], V6.7.0 clause B.4 3GPP TS 33.108 [4], V6.8.0 clause B.4 |
|  |  |  |  |  |  |  | r7(7) | version-0(0) | 3GPP TS 33.108 [4], V7.3.0 clause B.4 |
|  |  |  |  |  |  | hi2CS(3) | version-1(1) version-2(2) | 3GPP TS 33.108 [4], V6.1.0 clause B.3a 3GPP TS 33.108 [4], V6.6.0 clause B.3a |
|  |  |  |  |  |  |  | r6(6) | version-3(3) | 3GPP TS 33.108 [4], V6.8.0 clause B.3a |
|  |  |  |  |  |  |  | r7(7) | version-0(0) version-1(1) | 3GPP TS 33.108 [4], V7.3.0 clause B.4 3GPP TS 33.108 [4], V7.8.0 clause B.3 |
|  |  |  |  |  |  | hi3CS(4) | version1(1) | 3GPP TS 33.108 [4], V6.5.0 clause B.6 |
|  |  |  |  |  |  |  | r6(6) | version2(2) | 3GPP TS 33.108 [4], V6.8.0 clause B.6 |
|  |  |  |  |  |  |  | r7(7) | version0(0) | 3GPP TS 33.108 [4], V7.3.0 clause B.4 |
|  |  |  |  |  |  | him(5) | version1(1) | 3GPP TS 33.108 [4], V6.5.0 clause B.5 |
|  |  |  |  |  |  |  | version2(2) | 3GPP TS 33.108 [4], V7.1.0 clause B.5 |
|  |  |  |  |  |  | hi2wlan(6) | r7(7) | version-1(1) | 3GPP TS 33.108 [4], V7.8.0 clause B.3 |
|  |  |  |  |  |  |  | r8(8) | version-1(1) | 3GPP TS 33.108 [4], V8.0.0 clause B.3 |

| Object IDentifier | Specification |
| --- | --- |
| itu-t (0) | identified-organizations(4) | etsi(0) | securityDomain(2) | lawfulIntercept(2) | li-ps(5) | hi1(0) | TS 102 232 [5], V1.1.1 clause A.1 For Further Study |
|  |  |  |  |  |  | genHeader(1) | version1(1) version2(2) version3(3) version4(4) version5(5) version6(6) version7(7) | TS 102 232 [5], V1.1.1 clause A.2 TS 102 232 [5], V1.2.1 clause A.2 TS 102 232 [5], V1.3.1 clause A.2 TS 102 232 [5], V1.4.1 clause A.2 TS 102 232 [5], V1.5.1 clause A.2 TS 102 232-1 [13], V2.1.1 clause A.2 TS 102 232-1 [13], V2.2.1 clause A.2 |
|  |  |  |  |  |  | email(2) | version1(1) | iRI(1) cC(2) | TS 102 233 [6], V.1.1.1 annex D TS 102 233 [6], V.1.1.1 annex D |
|  |  |  |  |  |  |  | version2(2) | iRI(1) | TS 102 233 [6], V.1.2.1 annex D |
|  |  |  |  |  |  |  | version3(3) | iRI(1) | TS 102 233 [6], V.1.3.1 annex D TS 102 232-2 [14], V2.1.1 annex D |
|  |  |  |  |  |  | iPAccess(3) | version1(1) | iRI(1) cC(2) iRIOnly(3) | TS 102 234 [7], V1.1.1 clause 8 TS 102 234 [7], V1.1.1 clause 8 TS 102 234 [7], V1.1.1 clause 8 |
|  |  |  |  |  |  |  | version2(2) | iRI(1) cC(2) iRIOnly(3) | TS 102 234 [7], V.1.3.1 clause 8 TS 102 234 [7], V.1.3.1 clause 8 TS 102 234 [7], V.1.3.1 clause 8 |
|  |  |  |  |  |  |  | version3(3) | iRI(1) cC(2) iRIOnly(3) | TS 102 234 [7], V.1.4.1 clause 8 TS 102 234 [7], V.1.4.1 clause 8 TS 102 234 [7], V.1.4.1 clause 8 |
|  |  |  |  |  |  |  | version4(4) | iRI(1) cC(2) iRIOnly(3) | TS 102 234 [7], V.1.6.1 clause 8 TS 102 234 [7], V.1.6.1 clause 8 TS 102 234 [7], V.1.6.1 clause 8 |
|  |  |  |  |  |  |  | version5(5) | iRI(1) cC(2) iRIOnly(3) | TS 102 232-3 [15], V2.1.1 clause 8 TS 102 232-3 [15], V2.1.1 clause 8 TS 102 232-3 [15], V2.1.1 clause 8 |
|  |  |  |  |  |  | l2Access(4) | version1(1) | iRI(1) cC(2) iRIOnly(3) | TS 102 815 [8], V1.1.1 clause 8.2 TS 102 815 [8], V1.1.1 clause 8.2 TS 102 815 [8], V1.1.1 clause 8.2 |
|  |  |  |  |  |  |  | version2(2) | iRI(1) cC(2) iRIOnly(3) | TS 102 815 [8], V1.2.1 clause 8.2 TS 102 815 [8], V1.2.1 clause 8.2 TS 102 815 [8], V1.2.1 clause 8.2 |
|  |  |  |  |  |  |  | version3(3) | iRI(1) cC(2) iRIOnly(3) | TS 102 815 [8], V1.3.1 clause 8.2 TS 102 815 [8], V1.3.1 clause 8.2 TS 102 815 [8], V1.3.1 clause 8.2 |
|  |  |  |  |  |  |  | version4(4) | iRI(1) cC(2) iRIOnly(3) | TS 102 232-4 [16], V2.1.1 clause 8.1 TS 102 232-4 [16], V2.1.1 clause 8.1 TS 102 232-4 [16], V2.1.1 clause 8.1 |

| Object IDentifier | Specification |
| --- | --- |
| itu-t (0) | identified-organizations(4) | etsi(0) | securityDomain(2) | lawfulIntercept(2) | li-ps(5) | iPMultimedia(5) | version1(1) | iRI(1) cC(2) | TS 102 232-5 [17], V2.1.1 clause 7 |
|  |  |  |  |  |  | pstnIsdn(6) | version1(1) | iRI(1) cC(2) | TS 102 232-6 [18], V2.1.1 annex A.2 |
|  |  |  |  |  |  |  | version2(2) | iRI(1) cC(2) | TS 102 232-6 [18], V2.2.1 annex A.2 |

Table 2: OIDs of the ETSI/TC AT-D domain

| Object Identifier | Specification |
| --- | --- |
| itu-t (0) | identified-organizations(4) | etsi(0) | ts101909 (1909) | part20 (20) | subpart1 (1) | interceptVersion (0) |  | TS 101 909-20-1 [10], V1.1.2 annex A |
|  |  |  |  |  | subpart2 (2) | interceptVersion (0) |  | TS 101 909-20-2 [11], V1.1.2 annex A |

Table 3: OIDs of the ETSI/EP TETRA domain

| Object Identifier | Specification |
| --- | --- |
| itu-t (0) | identified-organizations(4) | etsi(0) | en301040 (1040) | interceptVersion (0) | EN 301 040 [12], V2.0.0 annex E |

Table 4: Object IDentifier of ROSE

| Object Identifier | Specification |
| --- | --- |
| joint-iso-itu-t(2) | remote-operations(4) | informationObjects(5) | version1(0) | ITU-T Recommendation X.880 [9], annex A |

Annex A:
Change Request history

| Status of the present document ASN.1 Object Identifiers in Lawful Intercept Specifications |
| --- |
| Date | Version | Remarks |
| October 2005 | 1.1.1 | First publication of the TR after approval by ETSI/TC LI#10 (4-6 October 2005, Sorrento); Version 1.1.1 prepared by Ralf Schmalbach (BNetzA) (rapporteur TR). |
| May 2006 | 1.2.1 | Included Change Request: TR102503CR001 (cat F) on Correction of mistakes performed during ETSI publication process of v1.1.1. This CR was approved by TC LI#11 (31 January – 2 February 2006, Saint Martin); Update of versions numbers of ASN.1 muldules in modified specifications during TC LI#12 (9-11 May 2006, Limassol). Version 1.2.1 prepared by Ralf Schmalbach (BNetzA) (rapporteur TR). |
| October 2007 | 1.3.1 | Included Change Request: TR102503CR002 (cat F) on Update of versions numbers of ASN.1 muldules in modified specifications This CR was approved by TC LI#16 (2-4 October 2007, Berlin). Version 1.3.1 prepared by Ralf Schmalbach (BNetzA) (rapporteur TR). |

# History

| Document history |
| --- |
| V1.1.1 | January 2006 | Publication |
| V1.2.1 | August 2006 | Publication |
| V1.3.1 |  |  |