3GPP SA 3 LI #30									Tdoc 052

26. – 28. Aug. 2008 Sophia Antipolis / FR

Title:	Checking history info header instead of dynamic triggering

Intention: 	Information / Decision

Source / Contact: mailto:bernhard.spalt@siemens.com

# Introduction:

Dynamic triggering was handled at the last meetings with missing details why at all and how to handle these cases within domain boarders and country boarders.

This document should show a concept for an LI solution for CF scenarios, which had not been handled until now. This is manly focussed on IRI, but might also be applicable for CC, but these cases might be out of scope of 3GPP …

This document goes also to SA3 LI & TISPAN WG7 joint meeting  as Tdoc 03

# Concept:

Based on the definitions out of RFC 4244 An Extension of the SIP for Request History Information, this info had to be check to allow interception of forwarded / redirected calls.

The History-Info field is an optional parameter and could be used to include ‘historic’ information which might be relevant for LI.

This would be necessary in the CSCF and in this case our definitions had to be extended to also include to requirement also the History Information field had to verified according the target list.

As this is an optional filed not necessary for interception including this field wouldn’t be a hint to LI.

# Way forward

Find an SA3 LI internal agreement, if this concept is appropriate.

- Adapt a CR(s) according this for IRI / CSCF

- Is this also applicable for CC?

  - Within which nodes? MRFP / SBC

    - Is this still part of 3GPP?

    - Only applicable for TISPAN?