3GPP TSG-SA WG3-LI Meeting #37 	(DocNumber SA3LI10_039r5

# New York, USA, 4th-6th May 2010

| CR-Form-v9.6 |
| --- |
| CHANGE REQUEST |
| ( | 33.106 | CR | CRNum | ( rev | - | ( Current version: | 9.0.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Encryption Requirements |
| --- | --- |
| Source to WG: ( | SA3-LI |
| Source to TSG: ( | SA3 |
| Work item code: ( | LI-10 |  | Date: ( | 05/05/2010 |
| Category: ( | C |  | Release: ( | Rel-10 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) |
| Reason for change: ( | The current version of 33.106 does not fully describe LI requirements concerned with the use of network applied encryption, especially in relation service layer encryption capabilities. |
| Summary of change: ( | The CR adds a new section 5.X with detailed requirements for LI relating to the use of operator applied encryption. |
| Consequences if ( not approved: | 33.106 will continue to not clearly define LI requirements relating to network applied encryption. |
| Clauses affected: ( | 5.X (New) |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

*** FIRST MODIFICATION ***

5.X LI Requirements for Encrypted Services

Section 5.1.2 provides a general description of requirements relating to network applied encryption. In addition to the general requirments, the following additonal LI requirements shall apply to network provided and/or network administered end to end or end to middle encryption, where this encryption prevents en-clair capture of communications required to be intercepted.

- When an encryption service is provided by the PLMN, lawful interception shall take place as for a non encrypted communications.

a.   In addition encrypted communications shall be decrypted, or the decryption keys and any required associated information (e.g.  roll over counters) shall be provided to the LEMF.b.  For the specific case where a key server based solution is used, it is a national option for the operator to make keys and any associated information (e.g.  roll over counters) directly available to the LEMF for the decryption of communications.

- Interception shall be performed in such a manner as to avoid detectability by the Target or others. In particular:

a.	There shall be no significant difference in latency during call setup or during communications compared to a non intercepted communications.

b.	Interception of a Target shall not prevent the use of key exchange applications which provide a user key confirmation mechanism.

NOTE: Key confirmation mechanisms such as an authentication string to be exchanged verbally are commonly used to provide additional assurance of authentication.

c.	Should interception fail during a call (or during call setup), the call shall be unaffected.

- Where the PLMN operator provides decryption of the communication, it is the operator’s choice where in the network this decryption is performed. However, following decryption, all IRI and CC shall be provided to the LEMF using handover mechanisms as per a non encrypted communication.

- An encryption solution shall not prohibit commencement of Interception and decryption of an existing communication.

- If key material and any associated information are available, it shall be possible to retrospectively decrypt encrypted communications.

NOTE: Unless national regulations require otherwise the operator is not required to retain key material or any communications  after the end of a communication.

For requirements in this section and section 5.1.2, the PLMN Operator is not obligated to comply with the requirements for any encryption which a Target may use which is outside the control of the PLMN Operator (e.g. 3rd party end to end VOIP software).

In addition the requirements do not apply where encryption is provided by the network between any network nodes or UEs where this encryption does not affect the ability of the core network to perform interception (eg hop by hop IMS signalling security or End to Access Edge radio bearer encryption).

*** END OF MODIFICATIONS ***

# Comments

Document numbers are allocated by the Working Group Secretary.   Use the format of document number specified by the 3GPP Working Procedures.

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.