## Slide 1: Multiparty Video in 3GPP
Annex to MMCMH S4 WID Permanent Document

## Slide 2: Current Architecture General
Call-in (INVITE), call-out (INVITE with list), and transfer (REFER) can be supported (TS 24.147 and TS 24.229)
Centralized conference with MRFP as conference focus
MRFP includes “isFocus” tag in SIP signaling (TS 24.147), so UE can know it is in a conference
Use of explicit floor control via BFCP is optional (TS 24.147)

## Slide 3: Current Architecture Video
Assumption: Without floor control, active speaker is shown to others in conference
Conference media handling is largely unspecified; MRFP is RTP “mixer” (RFC 3550)
Assumption: MRFP decodes, mixes, and re-encodes (transcodes) all media, but may alternatively switch incoming video to outgoing
Assumption: Without floor control, previous active speaker is shown to current active speaker
Active speaker
Previous active speaker

## Slide 4: Desirable Use Case 1 “Continuous Presence”
Assumption: In principle individual mixes to everyone, such that no one sees itself
Main feature: receivers can see more participants than just active speaker
Assumption: MRFP decodes, mixes, and re-encodes (transcodes) video Con: Requires large amount of MRFP processing and increases delay
Assumption: Participant layout controlled by local policy in MRFP
Active speaker
Previous active speaker

## Slide 5: Desirable Use Case 1 How Transcoding Free?
Assumption: When needed, send both large and small resolutions uplink; “simulcast”
Main feature: By handling multiple video streams, MRFP can often just switch video, gaining performance and delay
Con: Slightly higher UE complexity, and also slightly higher video bandwidth and/or slightly lower video quality, but still rather similar to transcoding case
Assumption: Participant layout composed locally and freely in receiver from multiple downlink video streams; “multistream”
Active speaker
Previous active speaker
(All video streams are not shown)

## Slide 6: Desirable Use Case 1 How Transcoding Free?
Active speaker
Previous active speaker
(All video streams are not shown)
SDP:
m=video … pt1 pt2 a=simulcast … pt1 pt2
…
SDP:
m=video … (active speaker)
m=video … (thumbnail 1)
m=video … (thumbnail 2)
…
Multiple m-lines in SDP per default mean that corresponding media are sent simultaneously, not as alternatives, e.g. audio and video
Simulcast is multiple representations, “payload types”, of a “single media”
SDP receiver shall per default ignore (disable) any m-lines with media it does not understand or does not wish to receive or send

## Slide 7: Desirable Use Case 2 Screen Sharing
Assumption: MRFP knows video is “content” and uses floor control (e.g. BFCP) for it
Main feature: Send screen content (e.g. presentation) instead of camera image
Note: MRFP cannot use active speaker criteria to choose which video to distribute to receivers
Assumption: Presenter wants to see reaction from “audience”, and can see presented document “locally”
Active speaker
Previous active speaker

## Slide 8: Desirable Use Case 2 How Screen Sharing?
Active speaker
Previous active speaker
SDP:
m=video … a=content:main (optional)
m=video … a=content:slides
m=application … (BFCP, optional)
…
Assumption: Screen share as additional video, identified as “content:slides” (RFC 4796)
Assumption: MRFP uses BFCP floor control for screen share (TS 24.147)
Assumption: MRFP switches screen share video, but may alternatively transcode it
Note: This way, screen share and continuous presence can even be combined, subject to UE capability, screen estate and bandwidth availability

## Slide 9: Desirable Use Case 3 “Bandwidth Negotiation”
Assumption: Severe network restrictions
Assumption: Not multistream capable
Assumption: Application limit > network restriction
Assumption: Application limit < network restriction
Active speaker
Previous active speaker

## Slide 10: Desirable Use Case 3 ”Bandwidth Negotiation” 1
Active speaker
Previous active speaker
(All video streams are not shown)
SDP answer:
m=video … p1 p2 b=AS:580 a=sendrecv a=simulcast recv p1 p2
m=video … b=AS:80 a=sendonly
m=video … b=AS:80 a=sendonly
SDP offer:
m=video … (active speaker) b=AS:500 a=sendrecv a=simulcast send p1 p2 p3
m=video … (thumbnail 1) b=AS:80 a=recvonly
m=video … (thumbnail 2) b=AS:80 a=recvonly
Can send 3 simulcast versions
Only interested in 2 of 3 simulcast versions
Each m-line has its own bandwidth
Assumption: Application limit < network restriction
Receive bandwidth includes both simulcast versions; one main and one thumbnail
All thumbnails are accepted

## Slide 11: Desirable Use Case 3 ”Bandwidth Negotiation” 2
Active speaker
Previous active speaker
(All video streams are not shown)
SDP answer:
m=video … b=AS:500 a=sendrecv
SDP offer:
m=video … b=AS:500 a=sendrecv
Will not send any separate thumbnails; either sends only active speaker, or MRFP has to make a composed image and transcode
Assumption: Not multistream capable
Can neither send simulcast nor receive separate thumbnails
Will not receive any thumbnail simulcast; either will not send thumbnail to others, or MRFP has to re-size and transcode

## Slide 12: Desirable Use Case 3 ”Bandwidth Negotiation” 3
Active speaker
Previous active speaker
(All video streams are not shown)
SDP answer:
m=video … p1 p2 b=AS:300 a=sendrecv a=simulcast recv p1 p2
m=video … b=AS:60 a=sendonly
m=video 0 …
SDP offer:
m=video … (active speaker) b=AS:500 a=sendrecv a=simulcast send p1 p2 p3
m=video … (thumbnail 1) b=AS:80 a=recvonly
m=video … (thumbnail 2) b=AS:80 a=recvonly
UE offer knows no restriction
Only interested in 2 of 3 simulcast versions
Limited thumbnail bandwidth; MRFP either has to align SDP to all participants, or transcode this thumbnail
Receive bandwidth is limited, jointly for both simulcast versions; not generally possible in SDP to specify bandwidth per version (see QOSE2EMTSI)
Thumbnails can be individually rejected
Assumption: Application limit > network restriction

## Slide 13: Desirable Use Case 3 ”Bandwidth Negotiation” 4
Assumption: Severe network restrictions
Active speaker
Previous active speaker
(All video streams are not shown)
SDP answer:
m=video … p1 p2 b=AS:300 a=sendrecv a=simulcast recv p1 p2 a=rtcp-fb:* ccm tmmbr
m=video … b=AS:60 a=sendonly a=rtcp-fb:* ccm tmmbr
SDP offer:
m=video … (active speaker) b=AS:350 a=sendrecv a=simulcast send p1 p2 a=rtcp-fb:* ccm tmmbr
m=video … (thumbnail 1) b=AS:60 a=recvonly a=rtcp-fb:* ccm tmmbr
UE offer knows of restrictions
Decides to offer fewer simulcast versions
All video RTP streams can be individually rate controlled, dynamically in the session, without any SDP re-negotiation
Receive bandwidth is limited further, jointly for both simulcast versions
Decides to offer fewer thumbnails

## Slide 14: Desirable Use Case 3 ”Bandwidth Negotiation” 5
Active speaker
Previous active speaker
(All video streams are not shown)
SDP answer:
m=video … b=AS:500 a=sendrecv
m=video 0 …
m=video 0 …
SDP offer:
m=video … (active speaker) b=AS:500 a=sendrecv a=simulcast send p1 p2 p3
m=video … (thumbnail 1) b=AS:80 a=recvonly
m=video … (thumbnail 2) b=AS:80 a=recvonly
UE offer knows no restriction
Simulcast is not understood, removed in answer and will therefore not be used
Additional video m-lines with thumbnails are not understood and will be disabled
Result: regular, single-stream video (or audio-only) session
Assumption: Point-to-point multistream offer to non-multistream UE

## Slide 15: Desirable Use Case 3 ”Bandwidth Negotiation” 6
Active speaker
Previous active speaker
(All video streams are not shown)
SDP answer:
m=video … b=AS:500 a=sendrecv
m=video 0 …
m=video 0 …
SDP offer:
m=video … (active speaker) b=AS:500 a=sendrecv a=simulcast send p1 p2 p3
m=video … (thumbnail 1) b=AS:80 a=recvonly
m=video … (thumbnail 2) b=AS:80 a=recvonly
UE offer knows no restriction
Simulcast is understood, but offer does not contain “isFocus” SIP tag, and simulcast is therefore removed in answer since it is not useful point-to-point
Additional video m-lines with thumbnails are understood, but offer does not contain “isFocus” SIP tag, and thumbnails are therefore disabled in answer since it is not useful point-to-point
Result: regular, single-stream video (or audio-only) session
Assumption: Point-to-point multistream offer to multistream UE

## Slide 16: SDP Details Identify Video Lines
SDP:
m=video … (active speaker) a=content:main
m=video … (screen share) a=content:slides
m=video … (thumbnail 1)
m=video … (thumbnail 2)
m=video … (thumbnail 3)
m=video … (thumbnail 4)
…
Optional RFC 4796 attribute for main video; suggest requiring main video is always first video m-line (already in HDVC, GSMA IR.39)
Suggest this RFC 4796 attribute mandatory to identify screen share video (is in IR.39); no restriction on where in SDP it occurs
Number of thumbnails to offer can be left up to offering UE; only the number both endpoints support and have network resources for will be accepted, the rest will be disabled in SDP answer
Suggest recommending that video m-lines that cannot be supported due to limited UE or network resources are disabled bottom-up in SDP, with the exception of m-lines that have specific meaning, e.g. content:slides.

## Slide 17: Discussion
Are the described use cases desirable?
Should we address also other desirable use cases?
Are the described solution principles acceptable?

## Slide 18: 3GPP IMS Conferencing Specifications
TS 24.147 Conferencing Using IM CN; Stage 3
  Subset of IETF RFC 4353
TS 24.605 CONF Using IM CN
  Makes extensive reference to TS 24.147
TS 22.228 Service Requirements for IM CN; Stage 1
TS 23.218 IM Session Handling; IM Call Model; Stage 2
TS 24.228 Signaling Flows for IM Call Control Based on SIP and SDP; Stage 3
TS 24.229 IM Call Control Protocol Based on SIP and SDP; Stage 3
TR 22.948 IMS Convergent Multimedia Conferencing
TR 29.847 SIP Conferencing Models, Flows and Protocols