3GPP TSG SA WG4 Meeting #109-e	       Tdoc S4-200906

Electronic meeting, May 20 – June 3, 2020

Title:	DRAFT LS on Media Feature Tag for IMS Data Channel

Response to:	-

Release:	Release 16

Source:	SA WG4

To:	CT WG1, CT WG3

Cc:	SA WG2

Contact Person:

#### Name:	Bo Burman

Tel. Number:	+46-10-714-1311

E-mail Address:	bo (dot) burman (at) ericsson (dot) com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:	S4-200905 CR 26.114-0499 Adding Media Feature Tag for IMS Data Channel

1. Background:

SA4 would like to inform CT1 and CT3 that SA4 discovered that it is ambiguous what streaming media feature tag to use for the recently introduced IMS data channel media in MTSI. Since this media uses the “application” media type, using only that information from RFC 3840 as a media feature tag would be too unspecific. This drawback is already recognized and mitigated by IETF RFC 5688, introducing an “app-subtype” media feature tag that can take individual application media format values. SA4 notes that IETF RFC 5688 is already referenced and used by TS 24.229. SA4 also notes that TS 24.229 specifies use of media feature tags in a media-agnostic fashion, not detailing or mandating what individual media feature tag values to use beyond the above-mentioned references.

Due to this ambiguity in the IMS data channel media feature tag value and media-agnostic handling of media feature tags in TS 24.229, SA4 has chosen to amend the IMS data channel media handling specification in TS 26.114 to specify what media feature tag value to use for IMS data channel media (see attached CR 26.114).

2. Actions:

To 3GPP CT WG1 and CT WG3:

ACTION:	SA4 asks CT1 and CT3 to consider the above and inform SA4:

- Whether the media feature tag value specified in TS 26.114 for IMS data channel media is sufficient.

- Whether any CT1 and CT3 specifications need to be updated.

3. Date of Next TSG-WG4 Meetings:

TSG SA WG4 Meeting 110-e		24-28 August 2020	Electronic meeting

TSG SA WG4 Meeting 111-e		9-13 November 2020	Electronic meeting