## Slide 1: Update to STL MNRU for Super-Wideband Signals
Contact:
Venkatesh Krishnan (vkrishna@qualcomm.com)
Imre Varga
(ivarga@qualcomm.com)

## Slide 2: Problems with existing MNRUs for SWB
ITU-T P.810 does not include recommendations for SWB,
Modulated noise has a flat spectrum, while speech has a spectrum with positive tilt. Therefore, the signal is buried deep in noise at the higher end of the spectrum,
Perceptually, x dB MNRU for SWB sounds significantly degraded compared to x dB MNRU for WB

## Slide 3: Spectrogram of 10 dB MNRU for a SWB input generated using STL mnrudemo tool

## Slide 4: Proposed update to MNRU for SWB inputs
0-14000 Hz Noise Source
DC Removal
Attenuator or Amplifier
Low pass filter
Filter 0-14000 Hz
X
+
Attenuator or Amplifier
Adjustment for Low pass filter group delay
Legend
Existing
Module
New
Module

## Slide 5: Low Pass Filter Design Goal
Perceptual quality of x dB MNRU for Super wideband approximately equal to that of the x dB MNRU for wideband
Approximately flat (unity gain) in the 0-8 KHz band,
Attenuate only the super high band,
Smooth transition from pass band to stop band,
FIR, Linear phase.

## Slide 6: Low Pass Filter Characteristics – Magnitude Spectrum
Frequency in Hz
Magnitude in dB

## Slide 7: Low Pass Filter Characteristics – Impulse Response

## Slide 8: Spectrogram Comparison without and with LPF

## Slide 9: Spectrum Comparison without and with LPF
Note: Purple plot represents the spectrum without the LPF and the yellow plot represents the spectrum with the LPF

## Slide 10: Some example files
Description | File
Wideband MNRU 10 dB | 
Old P.810 Superwideband MNRU 10 dB | 
Improved Superwideband MNRU Proposal with LPF, 10 dB | 

## Slide 11: Software Details
Source code changes included in mnru_updated.zip
Changes included with in the flag SWB_SOFTEN defined in mnru.h
Compiled on a 32 bit Linux machine
Command line to turn on the Low pass filter is –swb
Example use for turning on low pass filter
  mnrudemo –Q [x dB] –swb <input file> <output file>