## Slide 1: Network Simulator for testing the performance of the EVS coder’s robustness to packet loss and delay jitter
Qualcomm Incorporated

## Slide 2: From Frames to RTP packets
EVS Packet
(G.192 format)
RTP Sequence Number
RTP Time Stamp (in number of samples)
RTP Arrival Time Stamp (in milliseconds)
Length of the packet including this header (in bytes)
M (marker bit)
Information added by sender
Information added by receiver
Number of frames in the packet

## Slide 3: Information added at the Tx:
EVS Packet: Agreed upon by SA4 to be in the G.192 format,
Number of frames per packet ** :
  This is redundant and can be eliminated if the number of frames per packet can be derived from the packet size,
RTP Sequence Number:
  16 bit integer,
  Starts at random
  Incremented by 1 for every new packet (each packet may contain one or more speech frames depending on bundling)
RTP Time Stamp:
  32 bit integer,
  In # of samples
  Measures the time elapsed since start of the file / session, corresponding to the first sample of the oldest frame in the packet.
  Should start from a random starting point.
Frame Synchronization bit/ Marker bit:
  1 bit,
  Indicate the start of a talk spurt.
** see next slide

## Slide 4: Number of frames per packet field
The number of frames per packet may be part of the RTP payload header,
The EVS Design Constraint allows for non-negative integer multiples of 0.4 kbps for the payload header. This also includes the option of no payload header,
  If no payload header is provided, the onus is on the VoIP decoder to detect if frames have been bundled.
  For testing purposes, the network simulator can provide this information to the decoder.

## Slide 5: Information added at the Rx:
RTP arrival time stamp:
  Derived from the delay loss profile as follows:
  Where is the arrival time stamp in milliseconds, is the RTP time stamp as described in the previous slide,
  is the sampling frequency in KHz,
  is the delay value from the delay loss profile if it is not -1,
The packet is discarded if the value in the delay loss profile is -1
Length of the packet in bytes:
  Includes the header

## Slide 6: EVS over IP
EVS Encoder
G.192 Format Encoded Frames
Insert the following fields on the Tx Side:
RTP Seq Num
RTP Time Stamp
Marker bit
Insert the following fields on the Rx Side:
Arrival time stamp
Length of the packet
EVS VoIP Decoder
Tx
Rx
Transmission over PS network

## Slide 7: Handling silence period during DTX
The EVS encoder should generate a NoData frame between consecutive SID frames or between SID frames and active speech frames,
NoData frames are not sent to the VoIP decoder,
RTP sequence number:
  Shall be updated such that NoData frames are not assigned an incremental sequence number,
RTP time stamp:
  The time stamp shall be incremented to reflect the actual time elapsed between the packets
Packet with Active speech or SID frames
NoData
NoData
NoData
NoData
NoData
…
…
RTP sequence number
N
N+1
N+2
Elapsed Time at encoder
T0
T0+d
T0+2d
T0+3d
T0+k1 d
T0+k2 d
RTP Time Stamp
T0
T0+k1 d
T0+k2 d
Packet with Active speech or SID frames
Packet with Active speech or SID frames

## Slide 8: Handling Silence Period during DTX
The values in the delay loss profile corresponding to the NoData frames shall be skipped as illustrated in the example below (in this example, 2 frames per packet aggregation is assumed)
Packet Type | RTP Time Stamp | Delay Loss profile value (read from 26.114 profile) | Arrival Time Stamp
Contains Active Speech or SID | 1000 | 118 | 1118
Contains Active Speech or SID | 1040 | 100 | 1140
No Data | 1060 | 116 | Skip
No Data | 1080 | 100 | Skip
No Data | 1100 | 100 | Skip
No Data | 1120 | 116 | Skip
Contains Active Speech or SID | 1140 | 128 | 1268

## Slide 9: Frame Bundling
Network simulator to perform bundling of frames into packets.
To bundle m frames in the packet, the network simulator shall:
  Bundle atmost m active speech frames into one packet,
  NoData frames are not considered for bundling,
  A SID FIRST frame may be bundled with one or more active frames,
  A SID UPDATE frame shall not be bundled with other frames,
  The marker bit shall be set to 1 in the first packet containing active frames following NoData frames,

## Slide 10: Diagnostic Data from Network Simulator
The network simulator shall dump the following diagnostic data:
  A list of sequence numbers corresponding to the packets lost in the network,
  A list of data rate (kbps) that the encoder sends, one entry for every active and SID frame,

## Slide 11: Qualcomm’s Proposal for Network Simulator
G.192 Format Encoded Frames
Insert the following fields:
RTP Seq Num
RTP Time Stamp
Marker bit
Insert the following fields:
Arrival time stamp
Length of the packet
EVS VoIP Decoder
Network Simulator
EVS Encoder
Rearrange the packets in the order of increasing arrival time
Delay Loss Profile
Sampling frequency
Qualcomm can provide an updated pseudocode/ software to SA4 if the above network simulator functionality is agreed
Number of frames per packet
Diagnostic Data Dump out