## Slide 1
Clarification on NM confirmation upon clearing spectrum
RED Technologies
S5-164119
3GPP TSG|WG-5 Meeting #108
11-15 July 2016, Harbin(China)

## Slide 2
Background
As specified, in ETSI requirements (TS 103 154), the incumbent needs to be notified when spectrum is cleared by the operator. This enables the incumbent to know when he can start using the spectrum without being interfered:
eNB
Equipment from incumbent
2. The nework reconfigures cells
3. Confirmation from NM
1. The incumbent needs spectrum
4. The incumbent starts using spectrum
Example:

## Slide 3
End-to-end acknowledgement overview
Cell update (new cell / deleted cell / modified cells)
NM
LC
LR
Incumbent
Change in
spectrum need
Request Spectrum
LSRAI
Change in cell deployment
Constraints on cells
parameters
Reconfigure cells, if needed, to satisfy cells constraints
Constraints satisfied
LSRAI confirmation
Spectrum cleared
Start using
cleared spectrum
Note : those 2 events are asyncrhonous

## Slide 4
Proposal
Agree that the NM needs to confirm when the constraints on cells parameters provided by the LC are satisfied.