## Slide 1: SUMMARY OF ETSI TR 103 404: Autonomicity and Self-Management in the Backhaul and Core network parts of the 3GPP Architecture
ETSI NTECH AFI WG – Presentation to 3GPP SA5 (based on LS NTECHAFI(16)15_014)
June 30, 2016

## Slide 2: Outline
GANA (Generic Autonomic Networking Architecture) in a Nutshell
  as Reference Model for Autonomics, and the concept of autonomic functions
Introduction and Overview of ETSI TR 103 404:
  GANA Instantiation onto the 3GPP EPC core network, and backhaul
     Autonomicity and Self-Management in the Backhaul and Core (EPC) network parts of the 3GPP Architecture, and Interworking the instantiated GANA Autonomics for the Core Network with C-SON for RAN

## Slide 3: Reference Model of a holistic Generic Autonomic Network Architecture (GANA)
GANA
Level 1
GANA
Level 2
GANA
Level 3
GANA
Level 4

## Slide 4
ETSI GANA Reference Model: Value of Modularization of logically centralized Control Software (GANA Knowledge Plane)
Decision Elements (DEs) = Centralized and Distributed Control Software Logics (DEs) that operate in different time-scales but interworking harmoniously in realizing autonomic behaviors (self-configuration, self-optimization, …self-* of Managed Entities)
DE algorithms imply DE vendor differentiation.
DEs MAY be “loaded or replaced”  notion of “Software-Driven or Software-Empowered Networks” i.e. the broader picture than Software-Defined Networks
3-Levels of Hierarchical Control-Loops (GANA levels 2-4) demonstrate how Autonomics can be introduced in architectures without impact to stacks/resources layer
“Fast Control-Loops” in the Nodes/NEs, while “Slow but network-wide Control-Loops“ should operate in the outer centralized GANA Knowledge Plane (i.e. SDN – Controller & Net-Apps realm)
MBTS: Model-Based-Translation Service (mediation service between Knowledge Plane and NEs)
ONIX :Overlay Network for Information eXchange (publish/subscribe services for Info.)
Principles prescribed by FOCALE, IBM MAPE-K, and other Control-Loop models, can be applied to designing DE internal logic
Notes: 4
4

## Slide 5
AFI GANA Reference Model: Structure of the GANA Node

## Slide 6: What the ETSI TR 103 404 is about – Scope and approach
Scope: “Instantiation of the Generic Autonomic Network Architecture (GANA) model onto the 3GPP Core and Backhaul Network architectures”
Approach/Steps:
  Identification of working reference architecture – assumptions
  Instantiation of GANA reference model to 3GPP EPC architecture and basic functions
    Split the study between Self-configuration/commissioning, Self-optimization and Self-Healing phases
    Identification of the protocol-level entities (GANA Level 1) to be managed
    Identification of GANA DEs that are relevant to Self-x use cases
    Mapping to EPC nodes
  Autonomic behaviours across multiple segments to enable End-to-End (E2E) Self-Optimization
    Reference points and associated protocols
    Use cases
      Involved DEs
      Parameters or groups of parameters exchanged at the reference points

## Slide 7: What the ETSI TR 103 404 is about – Relation to SON
Studying the need for Autonomic Functions (called Decision Elements in GANA) in the 3GPP Core and Backhaul Networks, that enable “SON-like” features:
  Self-Configuration/Commissioning of network elements;
  Self-Optimization within network nodes and the overall core and backhaul network segments
  Self-healing of services and nodes / Self-Diagnosis and Self-Repair of network nodes
Clarification on how GANA (Autonomics) in the targeted segments complements SON for the RAN:
  SON functions were specifically defined and designed for automation and intelligence in managing RAN
  GANA’s Autonomic Functions is the broader concept (which includes SON and other Automation & Cognitive Functions for enabling Self-Management and Control of network resources in general)
  Autonomic Function = Decision-making software logic that drives a closed control-loop over managed parameters/resources
  The Hybrid SON model (D-SON & C-SON) is compliant with the GANA Model (hierarchical management & control functions that are based on combining distributed functions in the network nodes/elements with logically centralized functions that complement them )
  From E2E Self-Optimization Objective across domains (RAN, Backhaul and Core Network), there is a need to interwork SON with GANA Components instantiated in the Backhaul and Core Network

## Slide 8: Relationship between C-SON and GANA Knowledge Plane, and Knowledge Plane Southbound Interfaces Instantiations for 3GPP Core Network
C-SON
D-SON
GANA lower level DEs (distributed)
GANA Knowledge Plane
(Higher level DEs)

## Slide 9: What has the ETSI TR 103 404 achieved so far
Instantiation of the GANA Reference Model for Autonomic Networking, Cognition and Self-Management onto the 3GPP architecture defined in ETSI TS 123 401 and TS 123 402, by superimposing GANA Decision Elements (DEs) into node/device architectures and the overall network architecture,
  The DEs and their associated Control-Loops can be further designed to perform Autonomic Management & Control of the specific resources (Managed Entities) and (re)-configurable parameters in the target architecture, so as to achieve Self-* operations
Recommendations on the basic behaviours of the instantiated GANA Functional Blocks (FBs) in the above context
Taking into account 3GPP specifications on policy control (TS 123 203) and network management (TS 123 32x series)

## Slide 10: Working 3GPP reference architecture (1/2)
Non-Roaming: the simplest EPC architecture case (includes PCC architecture (PCRF, PCEF))
RANs (marked in grey) are considered only for their possible impact on the EPC KP, e.g., decisions made about Radio Access Technology (RAT) mobility or QoS control
Close collaboration of the EPC GANA entities with the centralized Self-Organizing Network (C-SON) and the RAN nodes
Similar for non-3GPP access
Include all the 3 planes involved in the operation of a CN: user plane, control plane, and management plane

## Slide 11: Working reference architecture (2/2)
Mobile backhaul network based on IP/MPLS enabled (P, PE) routers
No Convergence Architecture Scenario ("Current Scenario" in NGMN document “Requirement Specification (2008) NGMN Recommendation on SON and O&M Requirements”)

## Slide 12: Instantiation of GANA reference model to 3GPP EPC architecture and basic functions Example for the Self-optimization case (1/4)
Identification of protocol-level entities (GANA Level 1) & mechanisms to be managed
Related to:
  Mobility Management
  Network Management (O&M)
  Selection
  QoS related
  Energy savings
  Monitoring protocols, mechanisms and tools

## Slide 13: Instantiation of GANA reference model to 3GPP EPC architecture and basic functions Example for the Self-optimization case (2/4)
Identification of GANA DEs
Function level DEs
  Mobility-Management-DE [FUNC_LEVEL_MOM_DE] – Typical MEs associated to the DE are mobility management mechanisms and protocols.
  QoS-Management-DE [FUNC_LEVEL_QoS_M_DE] – Typical MEs associated to the DE are mechanisms and protocols associated with the QoS control and provisioning.
  Monitoring-DE [FUNC_LEVEL_MON _DE] – Typical MEs associated to the DE are mechanisms, protocols and tools for monitoring the status of the elements e.g. in terms of signalling/user load, CPU usage etc. as well as disseminating the monitoring data to entities (local or remote) that may need the data
Node level DEs
  AutoDiscoveryAndAutoConfiguration-DE [NODE_LEVEL_AC_DE] – Typical MEs are mechanisms for the selection of other nodes e.g. GWs, for OAM related mechanisms such as load balancing, or for saving energy at node level.
…

## Slide 14: Instantiation of GANA reference model to 3GPP EPC architecture and basic functions Example for the Self-optimization case (3/4)
… Identification of GANA DEs
Network level DEs
  Mobility-Management-DE [NET_LEVEL_MOM_DE] – Typical MEs are mobility management mechanisms and protocols managed at network level perspective (scope). *The algorithm at the network level should complement an algorithm introduced/implemented at the similar DE (MOM_DE) at GANA Function-Level (inside a GANA node).
  QoS-Management-DE [NET_LEVEL_QoS_M_DE] – Typical MEs are mechanisms and protocols associated with the QoS control and provisioning at the network level
  Monitoring-DE [NET_LEVEL_MON _DE] – Typical MEs are mechanisms, protocols and tools for monitoring the status of the network e.g. in terms of signalling/user load in all the interfaces. *The Network-Level Monitoring DE works in tandem with the Function-Level-DE in GANA nodes (in network elements (NEs)) to orchestrate/trigger and dynamically manage monitoring tools/sub-systems and mechanisms across the network, influencing the MEs to disseminate monitoring data to where it is needed. In a closed control-loop fashion they continue to monitor the monitoring MEs and adjusting them accordingly.

## Slide 15: Instantiation of GANA reference model to 3GPP EPC architecture and basic functions Example for the Self-optimization case (4/4)
DE-to-ME Mapping table for MME (control plane): Orchestration & Management of MEs/Parameters

## Slide 16: Instantiation of GANA reference model to 3GPP EPC architecture and basic functions. Example for the node level view of Self-configuration case in the MME

## Slide 17: Instantiation of GANA reference model to 3GPP EPC architecture and basic functions. Example for the node level view of Self-Healing case in the MME

## Slide 18: Example on Instantiation of GANA DEs and indicative autonomically managed parameters in the MME pooling management scenario (1/3)
The weight factors (combined with other complementary parameters) can be modified and enhanced by specific algorithms so that the following mechanisms can be supported:
  Load balancing
  Load re-balancing
  UE offloading
  Overload control
MME pooling is mainly based on a controllable parameter defined as “weight factor”

## Slide 19: Example on Instantiation of GANA DEs and indicative autonomically managed parameters in the MME pooling management scenario (2/3)

## Slide 20: Example on Instantiation of GANA DEs and indicative autonomically managed parameters in the MME pooling management scenario (3/3)
Vertical Coordination
Horizontal Coordination

## Slide 21: Autonomic behaviours across multiple segments enable End-to-End (E2E) Self-Optimization (1/2)

## Slide 22: Autonomic behaviours across multiple segments enable End-to-End (E2E) Self-Optimization (2/2)
DEs reside at network level in the KP (whole network operation) or at node and function level (local actions)
KP interfaces management plane (CN OSS i.e. NMS or EMS) and RAN C-SON (to retrieve RAN parameters and KPIs and communicate decisions) through the MBTS
Acquired knowledge is stored into the ONIX
Network level DEs use the information from the ONIX to run decision and data processing algorithms
Control loops may trigger commands, forwarded by the MBTS to the related entities in the GANA nodes

## Slide 23: Autonomic behaviours across multiple segments enable End-to-End (E2E) Self-Optimization (2/2)
Interactions use legacy protocols depending on the target:
Protocols that focus on the policy or rule exchange: COPS, BGP, DIAMETER
Protocols that focus on the configuration: SNMP, CMIP, Netconf, GTP-C, RestConf, Netflow, OpenFlow
Protocols that collect, aggregate, and move large amounts of streaming event data: Flume
Protocols that support application components to provide services to other components via a communications protocol, typically over a network: SOA
Protocols that support neighbour discovery and configuration: IPv6 Neighbour Discovery (ND); ANIMA (GRASP, RPL)

## Slide 24: Autonomic behaviours across multiple segments – “Load Control use case” (1/2)
Objective:
  To propose an assignment of the load control/balancing and gateway selection decisions taken by EPC NEs into GANA specified DEs,
  To drill into the details with respect to the involved reference points, as well as the policies to be injected, the load specific parameters to be delivered and the protocols to be used for delivering these parameters in order to support such load control decisions
Involved DEs:
  Network level (in the KP) and Function level (in the GANA nodes) i.e. Net/Func_Level_MON_DE (tune the monitoring behaviours and tools) and Net/Func_Level_MOM_DE (take decisions on the balancing and control of load in the NEs).
  ... (see TR)
Parameters or groups of parameters exchanged at the reference points
  Network level reference points e.g. Rfp Between RAN C-SON and MBTS: allows to retrieve RAN related information, parameters, streams of KPIs and/or decisions made at RAN level by C-SON algorithms.
  Node level reference points e.g. Rfp between the Func_Level_MON_DE and its corresponding MEs in the EPC node. The Func_Level_MON_DE uses the information it receives to run its own control loops. It communicates with the MEs it manages (monitoring mechanisms) to provide commands on how to measure the load, at which time, with what periodicity, with what granularity, for how long etc.
  … (See TR)

## Slide 25: Autonomic behaviours across multiple segments – “Load Control use case” (2/2)

## Slide 26: Summary of the Outcomes of TR 103 404 (1/2)
Introducing autonomics in these network segments complements the existing 3GPP management architecture with add-on automated and Autonomic Management & Control (AMC) features that target dynamic management and adaptation of resources in these core network and backhaul
It is possible to introduce autonomics (management and control intelligence) in the Core and the Backhaul without impacting the existing 3GPP reference points and architecture
Existing protocols and management mechanisms can be leveraged to execute the necessary interactions between the Core Network standardized nodes and functionalities and the overlay of atomic autonomic components (software) entities introduced by the GANA framework mapping

## Slide 27: Summary of the Outcomes of TR 103 404 (1/2)
The autonomic components may be launched in the network as intelligence-enhancing Management and Control software
There is no impact on the Data plane or the Control Plane
However the work identified the need for a reference point in the Management Plane to be placed between the C-SON and GANA Knowledge Plane for the Core network
  This would enable information (e.g. some KPIs) or decision sharing between the two entities so as to implement collaborative end-to-end self-optimization by C-SON and GANA Knowledge Plane for the Core network

## Slide 28: Summary of the Outcomes of TR 103 404 (1/3)
GANA levels 2-4 are the ones instantiated (i.e. we focus on the need to introduce control-loops at a GANA abstraction-level for autonomicity that is outside of individual protocols of the 3GPP protocol stacks)
Therefore, we consider that there are no protocol-level DEs (protocol-intrinsic control-loops) in 3GPP protocols/stacks, and no change to this is needed (only GANA levels 2-4 needed).
  In general, Protocol Level DEs (see GANA level-1) represent protocols, services (TCP/IP application-layer or OSI Application layer entities), and other fundamental mechanisms running in the target nodes/network considered as Managed Entities (MEs) and exhibiting control-loops. However, some MEs at protocol level in GANA may need no intrinsic control-loops

## Slide 29: Conclusion and Further Work
ETSI TR 103.404 aims at:
  introducing autonomics in the EPC 3GPP Core Network and the Backhaul (Based on the GANA framework)
  providing use case examples and recommendations for implementers to help them develop their algorithms and plan the testing of their products
  providing a guide on how to implement the instantiation of GANA Functional Blocks (FBs) and their reference points, to enable autonomicity in the target architecture
Further studies may cover:
  A wider set of possible use cases involving the EPC nodes
  Roaming model
  a thorough study of the synchronizations between C-SON and Core Network GANA Knowledge Plane (KP)
  extension towards virtualized 3GPP Core and backhaul network architectures in terms of autonomic functions, i.e. following principles for GANA integration with NFV and SDN in the context of 3GPP architectures
  We welcome any other ideas 3GPP SA5 or SA2 may recommend that ETSI performs further study

## Slide 30: Autonomic and Self-Managed Networks Phase 1 (3GPP)
Thank you!
STF 501
https://portal.etsi.org/STF/stfs/STFHomePages/STF501
Dissemination/Promotion of the Study to the industry: This Study has also been presented as a Poster at the EUCNC Conference:http://www.eucnc.eu/
Title of the Poster to be published in 2016:
Autonomic and Self-Managed 3GPP Core Networks

## Slide 31
Backup Slides:
Guidance to Vendors on implementing GANA DEs

## Slide 32: Guidance to implementing GANA DEs
Three Options ETSI NTECH AFI offers to GANA DEs Implementers:
  DEs in an NE as standalone processes
  or combined together as a single process
  or as executable behavioural models.
  Design and simulation phase considerations
  DE and their algorithms can be designed and simulated individually for each DE and its interactions with its MEs and with other DEs (particularly its upper DE),
Execution phase considerations
  The actual final DE implementations (for lower level DEs meant to be implemented and run in a NE (node) as run-time DE instances) can take the different Options listed above