## Slide 1: Enhancements to Offline Charging for IMS SA5 #109 – San Francisco, USA August 29-September 2, 2016
S5-165211

## Slide 2: Introduction
  SA5 specs allow for proprietary or implementation-specific information to be captured in Record Extension sections in CDRs, containing vendor-proprietary AVPsProvides a policy-driven operational management framework utilizing a metadata-driven repeating design pattern at each layer in the architecture
  Problem: Using Record Extensions to capture proprietary info needed for downstream consumption requires modifications to those downstream elements
    To support a new proprietary field in the CDRs, development is typically needed at the following points:
      CTF to provide the desired information in a new proprietary AVP
      CDF to support receiving and mapping the new proprietary AVP into a new CDR field
      Downstream systems to support the update to the CDR structure and recognize the new data being provided
    MNO incurs development cost each time a new proprietary field is added
  An extendible solution is needed that can be implemented in such a way as to reduce the time and cost associated with including additional non-standard information in the
S5-165211

## Slide 3: Proposal
  Service-Specific-Info is another method for capturing proprietary info in CDRs, but it is defined only for Application Servers
  Proposal #1: Define Service-Specific-Info to be available for all element types, not just application servers
  Proposal #2: Define a new set of AVPs and associated CDR fields with structure similar to Service-Specific-Info that can be available for all other network element types.
    This new set of AVPs and CDR fields could be called “Network-Specific-Info”
  Benefits: Proprietary information can be added to non-Application Server CDRs without requiring CDR structural changes (thus reducing the impact to consuming downstream systems) and impacting the CDF/CGF (CCF) development
    Note that downstream systems would still be impacted to recognize the new information, but the impact should be less since it does not also involve a CDR structural change
    Expanding the use of Service-Specific-Info for non-AS elements allows us to capture implementation specific information in the CDRs via standard AVPs and CDR fields, reducing the overall time and cost of development
S5-165211