## Slide 1: 3GPP SA5 update on SON, NFV and 5G
October 18-19, 2016
London, UK

## Slide 2: 3GPP

## Slide 3
Organizational Partners (SDOs)
  Regional standards organizations:
Market Representative Partners
  14 Market partners representing the broader industry:
Partnership
4G Americas, COAI (India), CTIA, GCF, GSA, GSMA, IPV6 Forum, | MDG (formerly CDG), NGMN Alliance, Small Cell Forum, TCCA, TD Industry Alliance, TD-Forum, UMTS Forum
ARIB (Japan), ATIS (USA), CCSA (China), | ETSI (Europe), TTA (Korea), TTC (Japan), TSDSI (India)

## Slide 4: The 3GPP Ecosystem
Developing internet protocol specs
ITU-R/T
Developing Mobile application specs
Referring to 3GPP specs
(contributed by individual members)
Partners of 3GPP
Referring to 3GPP specs for the local specs
Referring to specs
Cross reference
Developing Wireless LAN/MAN specs
Requirements
Input specs
Japan
EU
Korea
China
North America
Market
Partners
Developing Recommendations
Terminal Certification
Terminal certification based on 3GPP specs
Cross reference of specs
India

## Slide 5: 3GPP Structure
TSG RAN Radio Access Network
RAN WG1 Radio Layer 1 spec
RAN WG2 Radio Layer 2 spec Radio Layer 3 RR spec
RAN WG3 lub spec, lur spec, lu spec UTRAN O&M requirements
RAN WG4 Radio Performance Protocol aspects
RAN WG5 Mobile Terminal Conformance Testing
RAN WG6 GSM EDGE Radio Access Network
TSG SA Service & Systems Aspects
SA WG1 Services
SA WG2 Architecture
SA WG3 Security
SA WG4 Codec
SA WG5 Telecom Management
SA WG6 Mission-critical applications
TSG CT Core Network & Terminals
CT WG1 MM/CC/SM (lu)
CT WG3 Interworking with external networks
CT WG4 MAP/GTP/BCH/SS
CT WG6 Smart Card Application Aspects
Project Co-ordination Group (PCG)

## Slide 6
Chart: 
| 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016
R99 | 1408 | 4398 | 2266 | 1004 | 581 | 512 | 111 | 42 | 23 | 5 | 5 | 1 | 0 | 0 | 0 | 0
Rel-4 | 376 | 2828 | 1900 | 690 | 257 | 122 | 63 | 48 | 22 | 20 | 13 | 11 | 8 | 7 | 2
Rel-5 | 27 | 644 | 3274 | 2842 | 2162 | 1357 | 509 | 94 | 25 | 22 | 7 | 7 | 5 | 3 | 2
Rel-6 | 172 | 1088 | 2458 | 3721 | 2074 | 1078 | 212 | 74 | 19 | 17 | 10 | 4 | 4
Rel-7 | 1 | 20 | 663 | 2529 | 3132 | 1262 | 492 | 176 | 91 | 43 | 25 | 15
Rel-8 | 49 | 777 | 4609 | 7073 | 2347 | 706 | 347 | 184 | 91 | 46
Rel-9 | 49 | 2918 | 4991 | 3252 | 1366 | 376 | 165 | 70 | 11
Rel-10 | 47 | 1722 | 3800 | 3103 | 1636 | 584 | 267 | 12
Rel-11 | 32 | 1152 | 4178 | 3525 | 2186 | 622 | 24
Rel-12 | 6 | 102 | 2254 | 5181 | 4287 | 111
Rel-13 | 8 | 200 | 2648 | 1070
Rel-14 | 24 | 3110
~400 Companies from 39 Countries
50.000 delegate days per year
40.000 documents per year
1.200 specs per Release
New Release every ~18 months
3GPP Facts and Figures
R99
R4
R5
R6
R7
R8
R9
R10
R11
R12
R13
R14
Approved CRs per year per Release

## Slide 7: 3GPP Releases
Rel-12 frozen in September 2014
Rel-13 frozen in December 2015
Rel-14 stage 1 frozen in March 2016
Rel-14 stage 2 frozen in September 2016
Rel-14 stage 3 target date March 2017
Rel-15 stage 1 target date June 2017
Rel-15 stage 2 target date December 2017
Rel-15 stage 3 target date June 2018

## Slide 8: SA5

## Slide 9: 3GPP SA5 Telecom Management ToR
SA5 will specify the requirements, architecture and solutions for provisioning and management of the network (RAN, CN, IMS) and its services. The WG will define charging solutions in alignment with the related charging requirements developed by the relevant WGs, and will specify the architecture and protocols for charging of the network and its services.
The WG will ensure its work is also applicable to the management and charging of converged networks, and potentially applicable to fixed networks. The WG will coordinate with other 3GPP WGs and all relevant SDOs to achieve the specification work pertinent to the provisioning, charging and management of the network and its services.
http://www.3gpp.org/Specifications-groups/sa-plenary/56-sa5-telecom-management

## Slide 10: 3GPP SA5 Leadership
SA5
Thomas Tovinger (Ericsson) Chair since 08/2015 Jean-Michel Cornily (Orange) VC since 08/2013 Christian Toche (Huawei) VC since 08/2015
Charging Sub-Working Group (SWG)
Maryse Gardella (Alcatel-Lucent) Chair since 08/2013 Robert Törnkvist (Ericsson) VC since 05/2016 Chen Shan (Huawei) VC since 05/2016
OAM&P Sub-Working Group (SWG) Christian Toche (Huawei) Chair since 01/2016

## Slide 11: 3GPP SA5 Organization
Six face-to-face one-week plenary meetings per year
  Two Asia, two Europe, two North-America
  SWGs meet in parallel most of the time
  Average 350 documents per meeting
  Around 50 delegates attending meetings
  Conference calls between F2F meetings when needed
Work is based on company contributions
  Need at least four supporting companies for a Work Item or Study Item
  Use of consensus rule for decisions
  SA5 outputs are approved every quarter by TSG SA plenary
3GPP specifications are grouped into Releases
  SA5 maintains about 250 specifications
  32-series for FCAPS/Charging functionalities for Mobile Network
  28-series for Converged Management of Fixed & Mobile Networks and NFV
  Release 13 closure in December 2015
  Release 14 closure target in March 2017

## Slide 12: 3GPP Management Reference Model (TS 32.101)
1: Between the Network Elements (NEs) and the Element Manager (EM) of a single broadband wireless network
2: Between the Element Manager (EM) and the Network Manager (NM) of a single broadband wireless network
3: Between the Network Managers and the Enterprise Systems of a single broadband wireless network
4: Between the Network Managers (NMs) of a single broadband wireless network
4a: Between the Domain Managers (DMs) of a single broadband wireless network
5: Between Enterprise Systems & Network Managers of different broadband wireless networks
5a: Between the Domain Managers (DMs) of different broadband wireless networks
6: Between Network Elements (NEs)
7: Between the Network Management Layer Service (NMLS) and the Network Manager (NM).
3GPP Management Standards Focus

## Slide 13: 3GPP SA5 IRP Concept (TS 32.150)
Solution Set Definitions (CORBA, XML, SOAP)
Requirements / Use Cases
Information Service (UML)
Solution Set Definitions (other/future)
Relatively stable
over long
period of time
Change with
new/better
technologies
Change only with
respect to functional
addition and
corrections
Interface IRPs
  Notification IRP
  Alarm IRP
  Bulk CM IRP
  Kernel CM IRP
  Basic CM IRP
  PM IRP
  Etc
Network Resource Model (NRM) IRPs
  Generic NRM IRP
  UTRAN NRM IRP
  E-UTRAN NRM IRP
  IMS NRM IRP
  EPC NRM IRP
  Etc
Data Definition IRPs
  State Management IRP

## Slide 14: 3GPP Charging Architecture and Principles (TS 32.240)
OCF: Online Charging Function
ABMF: Account Balance Management Function
RF: Rating Function
CTF: Charging Trigger Function
CDF: Charging Data Function
CGF: Charging Gateway Function
3GPP Charging mechanisms are specified to allow collection of usage resources:
  in a real-time interaction, affecting the service rendered (Online Charging).
  processing the collected data prior to delivery to the BSS (Offline Charging)
Online Charging Offline Charging

## Slide 15: SON

## Slide 16: Release 8 SON SA5 Features (1/3)
SON Concepts and Requirements
  TS 32.500 “Self-Organizing Networks (SON); Concepts and requirements” describes high level use cases, business level requirements, specification level requirements and SON reference architecture
  SON reference architecture
    NM-Centralised SON: SON solution where SON algorithms are executed at the Network Management level
    EM-Centralised SON: SON solution where SON algorithms are executed at the Element Management level
    Distributed SON: SON solution where SON algorithms are executed at the Network Element level
    Hybrid SON: SON solution where SON algorithms are executed at two or more levels

## Slide 17: Release 8 SON SA5 Features (2/3)
Self-Configuration of eNodeB, including automated Software Management (TSs 32.50x)
  Self-configuration includes automated download of software and radio configuration data
  Dynamic configuration of X2 and S1 interfaces may also be done as part of the signalling included in the Transport Network Layer address discovery
Automatic Neighbour Relation (ANR) management (TSs 32.511, 32.76x)
  eNB requests to UE to report Intra-LTE/Inter-Frequency neighbours cells identification
  ANR function deals with automatic NR additions and removals
  The ANR function in eNB can be enabled or disabled by OAM
  If the operator chooses, the OAM system can add and configure Neighbour Cell Relations before the eNB goes into operation
  If the operator chooses, the OAM system can add and configure or remove Neighbour Cell Relations after the eNB goes into operation

## Slide 18: Release 8 SON SA5 Features (3/3)
Framework for PCI Selection (TS 28.658)
  Allows the eNB to select its own PCI based on UE reports and information received from neighbour eNBs
  OAM can configure a list of valid Physical Cell Identifiers (PCI) in the eNB in order to allow the eNB to choose an appropriate PCI for a cell from within this list to support distributed PCI assignment
  OAM can configure a valid PCI in the eNB to support centralized PCI assignment

## Slide 19: Release 9 SON SA5 Features
Automatic Radio Network Configuration Data Preparation (TSs 32.50x)
  When eNBs are inserted into an operational radio network, some network configuration parameters cannot be set before-hand because they have interdependencies with the configuration of operational Network Elements
  This functionality allows the generation and distribution of such interdependent parameters to provide fully automatic establishment of an eNB into a network
Self-optimization management (TSs 28.627-8-9)
  Definition of requirements, targets and control for the use case Hand Over Optimization (distributed architecture)
  Definition of requirements, targets and control for the use case Load Balancing Optimization (distributed architecture)
  Definition of requirements and control for the use case Inter-Cell Interference Coordination (distributed Architecture)
  Definition of Performance Measurements for Hand Over Optimization and Load Balancing Optimization

## Slide 20: Release 10 SON SA5 Features
Self-optimization management – continuation (TSs 28.627-8-9)
  Definition of requirements, targets and control for the use case RACH Optimization (distributed architecture)
  Definition of parameters for NM-Centralized architecture for the use case Capacity and Coverage Optimization
  SON range control and NMS-Centralized SON Management
  Performance Measurements for RACH Optimization and Capacity and Coverage Optimization
Self-healing management (TS 32.541)
  Introduction of use cases and high level requirements based on monitoring and analyses of relevant data like fault management, alarms, notifications, and self-test results

## Slide 21: Release 11 SON SA5 Features
UTRAN Self-Organizing Network management (TSs 32.511, 28.652, 28.655)
  Automatic Neighbour Relation (ANR), including Intra-UTRAN ANR, UTRAN IRAT ANR from UTRAN to GERAN, and UTRAN IRAT ANR from UTRAN to E-UTRAN
LTE Self-Organizing Networks (SON) coordination management (TSs 28.627-8-9)
  Coordination between Configuration Management and configuration parameters changes made by SON functions
  Coordination between different SON functions to detect, prevent or resolve conflicts or negative influences between SON functions to make SON functions comply with operator’s policy

## Slide 22: Release 12 SON SA5 Features
Study on Enhanced Network Management (NM) Centralized Coverage and Capacity Optimization (TR 32.836)
  Identify use cases for NM centralized CCO function.
  Identification of required (potentially new) UE and network based measurements for an NM centralized CCO function
  Identification of the required configuration attributes for an NM centralized CCO function
Multi-vendor Plug and Play eNB connection to the network (TSs 32.50x)
  Existing self-configuration function is mainly focused on radio network element parameters
  Extension to enable automatic set-up of a secure connection between eNB and its EMS

## Slide 23: Release 13 SON SA5 Features
Enhanced Network Management (NM) Centralized Coverage and Capacity Optimization (TSs 28.627, 28.628, 32.103, 32.422, 32.425, 32.442)
  Specify new performance measurements and MDT measurements to be reported over Itf-N to support the NM centralized CCO function
Study on OAM aspects of Distributed MLB SON function (TR 32.860)
  Study if D-SON Mobility Load Balancing (MLB) function can be improved in terms of operational efficiency
  Identify possible impacts on existing SA5 NRMs and measurement specifications

## Slide 24: NM Centralized CCO Functional Architecture (TR 32.836)

## Slide 25: Release 14 Study on OAM Aspects of SON for AAS-based Deployments (TR 32.865)
Use Cases of SON for AAS
  Cell Splitting
    (triggering, mgmt of new cell, Cov&Cap planning)
  Cell Merging
    (triggering, mgmt of new cell)
  Cell Shaping
    (triggering, scale of change)
Potential architecture options
  NM centralized SON for AAS (note1)
  EM centralized SON for AAS
  Distributed SON for AAS
OR
A
B
C
NM
DM
eNB
eNB
eNB
EM
DM
EM
A
B
B
C
C
C
B/C
C
C
Itf-N
Itf-N
Note 1: NM may not be efficient enough to react the fast change in conditions of the network
Active Antenna System (AAS) enables flexible software re-configuration of the BS and antenna system.
  Symbol:
  Algorithm of SON for AAS. This functionality is out of scope of this TR
  Management & Control of SON for AAS
  The letter in the functionality blocks represent functionality applied to architecture option A, B or C
B
B/C

## Slide 26: Release 14 Study on OAM Aspects of SON for AAS-based Deployments (Cont’d)
Potential Requirements*
  EM allows NM to
  switch on/off each SON for AAS function
  set split cell quantity
  pre-configure ECGI
  pre-allocate PCI range
  Pre-configure parameter range affecting the coverage
  Modify ECGI & PCI
  Pre-configure the alternative coverage configuration for cell shaping
  EM notify NM about information of new split/merged cell
Potential Solutions
  Activation and deactivation of SON for AAS
    (TS 28.628)
  Cell identities management for AAS
    (TS 28.658)
  Alternative coverage configurations for AAS
  Cell Splitting and Cell Merging relation management
    (TS 28.628)
NM
EM
eNB
eNB
Itf-N
M&C of SON for AAS
M&C of SON for AAS
Algorithm of SON for AAS#
<<InformationObjectClass>>
SONControl
…
aasSwitch
<<InformationObjectClass>>
EUtranGenericCell
…
pciList
cellLocalIdList
<<InformationObjectClass>>
EUtranCellSON
…
AlterCovConfig
ReplacedCells
3GPP TS 28.628: SON Policy NRM IRP; IS
3GPP TS 28.658: TM; CM; E-UTRAN network resources IRP: NRM
Note *: The requirements listed above are applicable to the EM centralized SON for AAS and distributed SON for AAS architecture.
Note #: Algorithm of SON for AAS is out of scope of this TR

## Slide 27: SON for 5G (1/3)
SON is considered to be essential for 5G to address the increasing network dimension and complexity and the more and more challenging demand for OPEX reduction
The addition of another Radio Access Technology (RAT) will trigger the need for automated tools to help Operators in operating multi-RAT networks
The Next Generation network will be based on NFV & SDN and this could imply some SON-MANO cooperation
The 5G network architecture is built to address verticals (connected automotive, IoT, smart city, etc.) and this could lead to per vertical SON features
The new concept of network slicing could lead to per network slice SON features. The Rel-14 SA5 5G Study Item on Slicing includes “Automation of management and orchestration of network slice instances and the related policy configurations”
SON in 5G may apply to the optimization of network, services, and business features

## Slide 28: SON for 5G (2/3)
The 5G network needs to be deployed, adapted and operated as much as possible in automated manner in order to efficiently support diverse 5G services
The volume and diversity of services in 5G make the network unmanageable without advanced automation, hence the need for SON
The diversity of technology as described in the NGMN 5G White Paper, and the need for seamless inter-working between these, make SON a must
NGMN has defined requirements for “Network Deployment, Operation and Management” (see NGMN 5G White Paper, Section 4.6) and there is a need for assessing if SON can bring a solution to any of these requirements

## Slide 29: SON for 5G (3/3)
SA5 has been one of the key organizations developing SON specifications for past and current generations of mobile networks
Addressing 5G SON is a natural evolution of the on-going studies in 3GPP SA5
SA5 has just started studying the Management and Orchestration of 5G, where SON is included
SA5 is therefore well positioned to maintain their leading role in the development of SON specifications for future generation networks

## Slide 30: NFV

## Slide 31: Network Management Framework 3GPP - NFV MANO
Interfaces in scope of SA5

## Slide 32: SA5 NFV Roadmap
SA#69 (Sep 2015)
SA#70
SA#71
SA#72
SA#64
SA#73
SA5 NFV Study
Concept, Architecture, Requirements
SA#68
Configuration Management
Fault Management
Rel-14
Lifecycle Management
Performance Management
Rel-13
SA#74
(Dec 2016)

## Slide 33
Ongoing work in ETSI ISG NFV EVE WG:
  EVE08 "Charging and Billing report“: “This informative Work Item will define use cases for usage metering of virtual resources and charging triggers in NFVIaaS model, NFVPaaS model, and VNFaaS model in the NFV environment. It will outline a high-level architecture evaluating: functional blocks expected to provide accounting information,functional block expected to trigger charging requests, and the information flows among functional blocks. The impacts on the current NFV architectural framework will be investigated with particular attention on the enhancements required to implement the aforementioned features, including new functional blocks, reference points and interfaces. The outcome of this study will include recommendations to modify existing specifications, start new normative work or both. The results of this WI could impact requirements in NFV interface design.”
  Targeting approval in December 2016, but slow progress on use cases description.
Once the corresponding NFV architecture framework will be specified, SA5 Charging will take this into account in their future work.
SA5 NFV - Charging aspects

## Slide 34: 5G

## Slide 35: 3GPP 5G Roadmap
  5G RAT features will be phased as it will be not possible to standardize all in time for Rel-15 completion and early deployments
Release 15 will aim at a first phase of expected 5G deployments in 2020
Release 16 will meet the ITU IMT-2020 submission requirements
  Key requirement: NR design should be forward compatible at its core so that features can be added in later releases in an optimal way

## Slide 36: Release 14 Study on Management and Orchestration Architecture of Next Generation Network and Service
Scope of the study (TR 28.800)
  Clarify the terminology and use cases
  Support of network operational features such as real-time, on demand, automation etc. as evolution from 4G management aspects
  Support of vertical applications (e.g. V2X)
  Support of the scenario in which the applications are hosted close to the access network
  Support of management and orchestration aspect of E2E user services
  Potential reuse of existing 3GPP management architecture and architectural framework defined by ETSI NFV ISG

## Slide 37: Release 14 Study on Management and Orchestration of Network Slicing
Scope of the study (TR 28.801)
  Define terminology, use cases and requirements for management and orchestration of network slicing
  Management of network function sharing in the context of network slicing
  Impacts to management when a slice instance is shared between multiple parties
  Isolation of management data between different parties within a slice instance if needed
  Automation of management and orchestration of network slice instances and the related policy configurations
  Management and orchestration mechanisms to support the isolation/separation of mobile network resources used by different network slice instances
  Study solution for management and orchestration of network slicing and how it affects the existing SA5 specifications

## Slide 38: Release 14 Study on Management Aspects of Next Generation Network Architecture and Features
Scope of the study (TR 28.802)
  Identify the use cases for management aspects of the next generation network in terms of network architecture and high level features such as mobility on demand and QoE/QoS
  Investigate the potential impact of the next generation network architecture and high level features to the functional blocks of 3GPP management system
  Figure out the location and role of management functionality to support next generation network architecture
  Study and develop the potential management related requirements for the next generation network in terms of network architecture and high level features
  Study the possible solutions to support the management requirements brought from the end to end next generation network architecture
  Study the possible solutions of management aspects to support the key features of the next generation network

## Slide 39: SA5 5G Roadmap
SA5 will take into account the outcome from other 3GPP WGs and other SDOs including 3GPP SA1, 3GPP SA2, RAN WGs, NGMN, ITU-T, ETSI ISG NFV
  SA5 will actively cooperate on OAM aspects with these groups when needed for the progress of 5G work
  SA5 Charging work will be conducted based on 3GPP SA2 Rel-14 study conclusions and 5G consolidated Architecture.
The ongoing Release 14 studies should be completed by March 2017
  The outcome of the studies is recorded in TRs 28.800, 28.801, 28.802
The normative work will target Release 15
  Start form March 2017
  Target closure date June 2018

## Slide 40: ANNEX

## Slide 41: Requirements & Architecture Specifications
TS 32.101 Principles and high level requirements
TS 32.102 Architecture
TS 32.103 Integration Reference Point (IRP) overview and usage guide
TS 32.111-1 3G Fault Management requirements
TS 32.140 SuM requirements
TS 32.141 SuM architecture
TS 32.300 Name convention for Managed Objects
TS 32.401 Performance Management concept and requirements
TS 32.500 SON concepts and requirements
TS 32.511 ANR management concepts and requirements
TS 32.541 SON self-healing concepts and requirements
TS 32.551 Energy Saving Management concepts and requirements
TS 32.600 Configuration Management concept and high-level requirements

## Slide 42
TS 32.150 Integration Reference Point (IRP) Concept and definitions
TS 32.151 IRP Information Service (IS) template (applicable to 32-series IRPs)
TS 32.152 IRP IS Unified Modelling Language (UML) repertoire (applicable to 32-series IRPs)
TS 32.153 IRP technology specific templates, rules and guidelines
TS 32.154 Backward and Forward Compatibility Concept and definitions
TS 32.155 Requirements template
TS 32.156 Fixed Mobile Convergence (FMC) Model repertoire (applicable for FMC)
TS 32.157 IRP Information Service (IS) template (applicable for FMC)
IRP Methodology Specifications

## Slide 43: Interface IRP & NRM IRP
Interface IRPs
Defining HOW information is shared (Operations & Notifications)
Network Manager (NM)
User Equipment
Core/IMS Network
Radio Access Network
DM/EM
Network Resource Model (NRM) IRPs
Defining WHAT can be managed (Object Models)
Itf-N
DM/EM

## Slide 44: IRP Development Principles
NRM IRP Flexibility and Extendibility
    Use of qualifiers “mandatory”, “optional”, “read/write” for attributes
    NRM extensions (e.g. sub-classing)
    Vendor specific NRM extensions
    VsDataContainer
Interface IRP Flexibility
    Use of qualifiers “mandatory”, “optional” for operation, notifications and parameters
    NRM/Technology-neutrality
    Not just for mobile networks

## Slide 45: Interface IRPs
Common IF IRPs
Notification IRP (32.30x)
Generic IRP (32.31x)
FM-related IF IRPs
Alarm IRP (32.111-x)
AAM IRP (32.12x)
Test Mgmt IRP (32.32x)
CM-related IF IRPs
Basic CM IRP (32.60x)
Bulk CM IRP (32.61x)
Kernel CM IRP (32.66x)
Supporting IF IRPs
Notification Log IRP (32.33x)
File Transfer IRP (32.34x)
Communication Surveillance IRP (32.35x)
Entry Point IRP (32.36x)
PM-related IF IRPs
PM IRP (32.41x)
PM collection (32.43x)
Trace Mgmt (32.42X, 32.44x)
Other IF IRPs
Partial Suspension (32.38x)
Delta synchronization (32.39x)
SON-related IF IRPs
Self-Configuration IRP (32.50x)
Software Management IRP (32.53x)

## Slide 46: Network Resource Model (NRM) IRPs
Common NRM IRP
Generic NRM IRP (28.621/2/3)
3GPP Access Network NRM IRPs
Generic RAN NRM IRP (28.661/2/3)
GERAN NRM IRP (28.654/5/6)
UTRAN NRM IRP (28.651/2/3)
E-UTRAN NRM IRP (28.657/8/9)
3GPP Core Network NRM IRPs
Core NRM IRP (28.701/2/3)
IMS NRM IRP (28.704/5/6)
EPC NRM IRP (28.707/8/9)
Supporting NRM IRPs
Inventory Management NRM IRP (28.631/2/3)
Transport Network NRM IRP (28.731/2/3)
Signalling Transport NW IF NRM IRP (28.734/5/6)
Services related NRM IRPs
SuM NRM IRP (28.751/2/3)
3GPP H(e)NS NRM IRPs
HNS NRM IRP (28.671/2/3)
HeNS NRM IRP (28.674/5/6)
FMC model
Umbrella Information Model (28.620)

## Slide 47
TS 28.500 Concept, architecture and requirements for mobile networks that include virtualized network functions
TS 28.510 Configuration Management (CM) for mobile networks that include virtualized network functions; Requirements
TS 28.511 Configuration Management (CM) for mobile networks that include virtualized network functions; Procedures
TS 28.512 Configuration Management (CM) for mobile networks that include virtualized network functions; Stage 2
TS 28.513 Configuration Management (CM) for mobile networks that include virtualized network functions; Stage 3
TS 28.515 Fault Management (FM) for mobile networks that include virtualized network functions; Requirements
TS 28.516 Fault Management (FM) for mobile networks that include virtualized network functions; Procedures
TS 28.517 Fault Management (FM) for mobile networks that include virtualized network functions; Stage 2
TS 28.518 Fault Management (FM) for mobile networks that include virtualized network functions; Stage 3
SA5 NFV Specifications (1/2)

## Slide 48
TS 28.520 Performance Management (PM) for mobile networks that include virtualized network functions; Requirements
TS 28.521 Performance Management (PM) for mobile networks that include virtualized network functions; Procedures
TS 28.522 Performance Management (PM) for mobile networks that include virtualized network functions; Stage 2
TS 28.523 Performance Management (PM) for mobile networks that include virtualized network functions; Stage 3
TS 28.525 Life Cycle Management (LCM) for mobile networks that include virtualized network functions; Requirements
TS 28.526 Life Cycle Management (LCM) for mobile networks that include virtualized network functions; Procedures
TS 28.527 Life Cycle Management (LCM) for mobile networks that include virtualized network functions; Stage 2
TS 28.528 Life Cycle Management (LCM) for mobile networks that include virtualized network functions; Stage 3
SA5 NFV Specifications (2/2)

## Slide 49
3GPP portal
https://portal.3gpp.org/
3GPP SA5 home page
http://www.3gpp.org/Specifications-groups/sa-plenary/56-sa5-telecom-management
3GPP SA5 specifications
  http://www.3gpp.org/ftp/Specs/html-info/TSG-WG--S5.htm
  http://www.3gpp.org/ftp/Specs/archive/32_series/
  http://www.3gpp.org/ftp/Specs/archive/28_series/
3GPP SA5 meeting documents
http://www.3gpp.org/ftp/tsg_sa/WG5_TM/
3GPP SA5 email lists
  http://list.etsi.org/3gpp_tsg_sa_wg5.html
  http://list.etsi.org/3gpp_tsg_sa_wg5_oam.html
  http://list.etsi.org/3gpp_tsg_sa_wg5_charging.html
Useful Links

## Slide 50
www.3gpp.org
contact@3gpp.org
Thank You!