3GPP TSG-SA5 Meeting #133-e	S5-205157

# Online, , 12th Oct 2020 - 21st Oct 2020

| CR-Form-v12.1 |
| --- |
| CHANGE REQUEST |
|  | 28.532 | CR | 0151 | rev | - | Current version: | 16.5.1 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME |  | Radio Access Network | X | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Rel-16 CR 28.532 Extend object creation method with id selection by the MnS producer (stage 2) |
| --- | --- |
| Source to WG: | Nokia, Nokia Shanghai Bell |
| Source to TSG: |  |
| Work item code: | TEI16 |  | Date: | 2020-10-02 |
| Category: | F |  | Release: | Rel-16 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) … Rel-15 (Release 15) Rel-16 (Release 16) Rel-17 (Release 17) Rel-18 (Release 18) |
| Reason for change: | When objects are created by a MnS consumer on a MnS producer, the DN of the new resource can be assigned by the MnS consumer or the MnS producer. Currently Rel-16 conatns only the option where the MnS consumer creates the DN. This is not acceptable as only solution in the SBMA where multiple MnS consumers can create objects on a MnS producer. For example, when two MnS consumers create performance metric production jobs on a MnS producer, the only way to avoid name clashes is to let the the MnS producer selects the DNs for the new objects. |
| Summary of change: | Object creation with DN selection by MnS producer is added. |
| Consequences if not approved: | When multiple MnS consumers create objects at the same time name clashes cannot be avoided. |
| Clauses affected: |  |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) | X |  | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |
| This CR's revision history: |  |

First modification

#### 11.1.1.1	createMOI operation with DN generation by the MnS consumer

##### 11.1.1.1.1	Description

This operation is invoked by  Generic Provisioning MnS consumer to request the  Generic Provisioning MnS producer to create a Managed Object instance in the MIB maintained by  Generic Provisioning MnS producer. This operation will create only one Managed Object instance. The DN of the instance to be created is generated by the MnS consumer and provided to the MnS producer in the creation request.

The Generic Provisioning MnS consumer supplies the values of all attributes that are supported, i.e. a) attributes whose Support Qualifier is M and b) attributes whose Support Qualifier is O. The special cases are:

1)	If the attribute has a default value specified. In such case, if the Generic Provisioning MnS consumer supplies a value, the supplied value is used; otherwise, the default value is used.

2)	If the attribute is specified as capable of carrying a null value or carrying no information. In such case, if the Generic Provisioning MnS consumer supplies a (non-null) value, the supplied value is used; otherwise, the null value is used.

3)	If the attribute does not have a default value specified and is specified as incapable of carrying null value and incapable of carrying no information, if there is a Generic Provisioning MnS producer defined default value, then that value will be used.

##### 11.1.1.1.2	Input parameters

| Parameter Name | S | Information Type / Legal Values | Comment |
| --- | --- | --- | --- |
| managedObjectClass | M | class | Class of the managed object to be created |
| managedObjectInstance | M | DN | Instance of the managed object to be created. |
| attributeListIn | M | LIST OF SEQUENCE< attribute name, attribute value> | This parameter may have a null value. When this parameter is supplied, it contains a list of name/value pairs specifying attribute identifiers and their values to be assigned to the new managed object. These values override the values for the corresponding attributes derived from the default value set specified in the definition of the managed object's class. |

##### 11.1.1.1.3	Output parameters

| Parameter name | S | Matching Information / Legal Values | Comment |
| --- | --- | --- | --- |
| attributeListOut | M | LIST OF SEQUENCE< attribute name, attribute value> | Name/value pairs containing the attributes of the new managed object and the value assigned to each. |
| status | M | ENUM (OperationSucceeded, OperationFailed) |  |

##### 11.1.1.1.4	Results

In case of success, the ManagedEntity instance has been createdwith the supplied DN. In case of failure, indication of the failure is provided in the output parameters.

#### 11.1.1.1a	createMOI operation with DN generation by the MnS producer

##### 11.1.1.1a.1	Description

This operation has the same semantics as the operation described in clause 11.1.1.1, except for that the DN of the newly created resource is assigned by the MnS producer and returned to the MnS consumer in the creation response.

##### 11.1.1.1a.2	Input parameters

| Parameter Name | S | Information Type / Legal Values | Comment |
| --- | --- | --- | --- |
| managedObjectClass | M | class | Class of the managed object to be created |
| parentManagedObjectInstance | M | DN | Parent instance of the managed object to be created. |
| attributeListIn | M | LIST OF SEQUENCE< attribute name, attribute value> | This parameter may have a null value. When this parameter is supplied, it contains a list of name/value pairs specifying attribute identifiers and their values to be assigned to the new managed object. These values override the values for the corresponding attributes derived from the default value set specified in the definition of the managed object's class. |

##### 11.1.1.1a.3	Output parameters

| Parameter name | S | Matching Information / Legal Values | Comment |
| --- | --- | --- | --- |
| managedObjectInstance | M | DN | Instance of the managed object created. |
| attributeListOut | M | LIST OF SEQUENCE< attribute name, attribute value> | Name/value pairs containing the attributes of the new managed object and the actual value assigned to each. |
| status | M | ENUM (OperationSucceeded, OperationFailed) |  |

##### 11.1.1.1.4	Results

In case of success, the ManagedEntity instance has been created and its DN assigned by the MnS producer. In case of failure, indication of the failure is provided in the output parameters.

End of modifications