3GPP TSG SA WG5 Meeting 134-e 	TDoc S5-206062rev1

electronic meeting, online, 16th - 25th November 2020

# Source:	Huawei

# Title:	pCR 28.811 Add cross-operator network slicing scenario

# Document for:	Approval

Agenda Item:	6.5.2

# 1	Decision/action requested

The group is asked to approve the proposal.

# 2	References

[1]	3GPP TR 28.811 v0.1.0: “Management and orchestration; Network Slice Management Enhancement”

# 3	Rationale

This contribution adds scenario related to multi-operator network slicing and identifies possible problems.

# 4	Detailed proposal

This contribution proposes to make the following changes in [1].

1st Change

# 5	Scenarios for Network Slicing Management Enhancements

## 5.1	Network Slice covering multiple networks

#### 5.1.1	Description

CSP wishes to provide a communication service in multiple countries or regions. The CSP has selected NOP-A as network slice provider. NOP-A does not have RAN coverage in all of the geographical areas that are required by the CSP.

NOP-A selects NOP-B to provide RAN coverage for one or more geographical areas, and agrees slice subnet requirements with NOP-B.

NOP-A orders the allocation of a network slice subnet by NOP-B. NOP-A may issue the request to NOP-B’s 3GPP management system, or NOP-B may issue the request to its own 3GPP management system.

#### 5.1.2	Identified problems

Figure 5.1.5-1 shows a part of the Managed Information Model in NOP-A’s Management System.

Figure 5.1.5-1: Managed Information Model in NOP-A’s Management System

This is a valid model according to 28.541 [2], but there is no way to represent the RAN NetworkSliceSubnet instance which is managed by NOP-B’s management system. This means that the NOP-A has no visibility of the external network slice subnet which is provided by NOP-B.

End of changes

# Text boxes

networkSliceSubnetRef

NetworkSlice:slice1

NetworkSliceSubnet:crossDomainSubnet1

ServiceProfile:xx

SliceProfile:xx

ManagedFunction:SMF1

NetworkSliceSubnet:cnDomainSubnet1

networkSliceSubnetRef

SliceProfile:xx

SliceProfile:xx

ManagedFunction:gNB1

NetworkSliceSubnet:ranDomainSubnet1