3GPP TSG SA WG5 Meeting 136-e		S5-212443

# electronic meeting, online, 1 - 9 March 2021								            Revision of S5-212208

# Source:	Huawei,China Mobile

# Title:	Add stage2 information model definition for intent

# Document for:	Approval

Agenda Item:	6.4.10

# 1	Decision/action requested

The group is asked to discuss and approval.

# 2	References

[1]	3GPP draft TS 28.312: “Management and orchestration; Intent driven management services for mobile networks v0.2.0”.

# 3	Rationale

This contribution proposes to add stage2 information model definition for intent.

# 4	Detailed proposal

It proposes to make the following changes to TS 28.312[1].

1st Change

# 6	Stage 2 definition for Intent Driven Management

Editor's note: this clause will specify the stage2 definition for Intent driven management which may include the management operations, management entities and management information

## 6.2	Information model definition for Intent (MnS component typeB)

### 6.2.1	Information model definition for Intent

### Editor’s Note: The following information model needs to be revisited based on the further discussion, and he alignment/coordination work with other SDO needs to be considered, which may impact the following information model.

#### 6.2.1.1	Class diagram

##### 6.2.1.1.1	Relationship

Figure 6.2.1.1.1-1 Relationship UML diagram for intent

Editor’s Note: Whether the intentExpectation is a <<dataType>> or a <<IOC>> is FFS.

##### 6.2.1.1.2	Inheritence

Figure 6.2.1.1.2-1 Inheritence UML diagram for generic intent

#### 6.2.1.2	Class definition

##### 6.2.1.2.1 	Intent <<IOC>>

###### 6.2.1.2.1.1	Definition

This IOC represents the properties of an Intent. This Intent framework also allows new intents, both standardized or as vendor specific, by specifying the concrete intentExpectation which includes requirements, goals and constraints given to a 3GPP system.

###### 6.2.1.2.1.2	Attributes

The Intent includes attributes inherited from TOP IOC (defined in TS 28.622) and the following attributes:

| Attribute Name | Support Qualifier | isReadable | isWritable | isInvariant | isNotifyable |
| --- | --- | --- | --- | --- | --- |
| adminstrativeState | M | T | T | F | T |
| intentExpectation | M | T | T | F | T |
| userLabel | M | T | T | F | T |
| intentFulfilStatus | M | T | F | F | T |

Editor’s Note: whther the attribute intentType is needed for the Intent IOC needs further discussion.

###### 6.2.1.2.1.3	Attribute constraints

None

#### 6.2.1.3	DataType definition

None

#### 6.2.1.4	Attribute definition

| Attribute Name | Documentation and Allowed Values | Properties |
| --- | --- | --- |
| adminstrativeState | It describes the administrative state of the intent, which can be configured by MnS consumer to trigger to active and de-active the intent allowedValues: “LOCKED”, “UNLOCKED” | type: ENUM multiplicity: 1 isOrdered: F isUnique: F defaultValue: None isNullable: False |
| userLabel | A user-friendly (and user assignable) name of the intent. allowedValues: Not Applicable | type: String multiplicity: 1 isOrdered: F isUnique: F defaultValue: None isNullable: False |
| intentExpectation | It indicates the the expectations including requirements, goals and constraints given to a 3GPP system. The intentExpectation includes the intentAreas which describes a list of coverage areas for the intent to be applied. Editor’s Note: the detailed intentExpectation is for further discussion | type: FFS multiplicity: 1 isOrdered: F isUnique: F defaultValue: None isNullable: False |
| intentFulfilStatus | It describes the status of the intent fulfilment result, which is configured by MnS producer and can be read by MnS consumer. allowedValues: "FULFILLED", “NOT_FULFILLED Editor’s Note: whether other allowed values should be supported is FFS, and the name for the attribute intentFulfilStatus is FFS. | type: ENUM multiplicity: 1 isOrdered: N/A isUnique: N/A defaultValue: None isNullable: False |

End of changes