3GPP TSG SA WG5 Meeting 143-e	S5-223512

# electronic meeting, online, 9– 17th  May 2022

| CR-Form-v12.0 |
| --- |
| CHANGE REQUEST |
|  | 28.405 | CR | 0011 | rev | - | Current version: | 17.1.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME |  | Radio Access Network | X | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Adding missing parameters and updating definition |
| --- | --- |
| Source to WG: | Ericsson |
| Source to TSG: | S5 |
| Work item code: | eQoE |  | Date: | 2021-04-22 |
| Category: | F |  | Release: | Rel-17 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) … Rel-15 (Release 15) Rel-16 (Release 16) Rel-17 (Release 17) Rel-18 (Release 18) |
| Reason for change: | Adding missing parameter definition and updating to clarify a parameter definition |
| Summary of change: | The parameter qoETarget was used but not defined in the TS, definition of parameter qoECollectionEntityadress updated, adding definition of Term Network session |
| Consequences if not approved: | Missing parameter defintion used in TS but not defined |
| Clauses affected: | 2, 3.1, 5.5, 5.x (new) |
|  | Y | N |  |  |
| Other specs |  | x | Other core specifications | TS/TR ... CR ... |
| affected: |  | x | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | x | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |
| This CR's revision history: |  |

First change

## 2 	References

[x]	3GPP TS 38.331: " NR; Radio Resource Control (RRC); Protocol specification".

Next change

## 3.1	Terms

For the purposes of the present document, the terms given in TR 21.905 [1] and the following apply. A term defined in the present document takes precedence over the definition of the same term, if any, in TR 21.905 [1].

Network session: Network session is used when a NF requests a UE to perform QoE Measurement Collection for specified end user service type, see clause 5.8.Next change

## 5.5	Container for Application layer Measurement Configuration (M)

The “Container for Application layer Measurement Configuration” parameter contains application layer measurements configuration over NGAP as specified in  see[6] or [7]. The corresponding parameter name in Radio Resource Control (RRC) Protocol specification [x], is measConfigAppLayerContainer. In the management interface the parameter contAppLayerMeasConfigRef provides a reference to a file, the contents of which are used to configure the container.

Next change

## 5.x 	QoE Target (CM)

## This parameter specifies the target object (individual UE) for the QMC in case of signalling based QMC. The qoETarget parameter shall be able to carry "IMSI” or "SUPI".

End change