## Slide 1: Enablers for Security Monitoring
Clifton Fernandes
Nokia, Shanghai Bell

## Slide 2: Background – SA3 studies need SA5 to bind the overall usecase
Rel 18
ZTS study (TR 33.894): Identified the requirement for continuous security monitoring:
  - Conclusion for Key Issue #1: Solution#1 illustrates how existing services can be used to collect the necessary data listed in the solution for security monitoring purposes in line with the principles of zero trust (Tenet 5). However, no consensus could be reached on the normative work.
  NOTE 1: How the OAM collects the inference data and what type of additional security related data (e.g. security logs or events) is collected is for further study.
Rel 19
ZTS study (S3-234417):
  WT1.1: Based on TR 33.894 KI#1 security requirement, conclusion, and Tenet 5 evaluation, for events which can lead to security threats, define the data to be exposed by the NF and define how those data can be securely exposed to the Operator’s security functions (e.g., SIEM) to enable the external security evaluation and monitoring.
    NOTE: The external security evaluation and monitoring is up to operator’s implementation and outside the 3GPP domain. The aspects to enable OAM based data collection is up to SA5 WG. The necessary adaptations specific to exposure services for providing data to the external security function needs SA2 collaboration.
CMCC study (S3-234773):
  Focusses on identifying new use cases under the SBMA architecture, e.g. NF intrusion detection analysis, security analysis and access control of internal traffic, security configuration baseline check, security configuration enrolment/update, etc.
  Aims at identifying potential security requirements and solutions for such new use cases

## Slide 3: Submitted text for Rel-19 topics in SA5 (meeting #151) - Justification
With the network management capabilities expanding immensely towards 5G Advanced and beyond, security needs to be enhanced. Today we have analytics function in the network like the MDAS and NWDAF. They have minimal placeholders for analytics for security. Considering the complexity of the 5G networks and beyond we need enhancements to automatically and continuously monitoring the security health of the network. Hence for such automated security monitoring, below are the security data management related topics which are the focus to begin with.
Potential scope includes:
(1) Security metrics: Generic security metrics are required to be collected and analysed to reflect the security health of the network as well as the network management system. For example, in the context of API security, we could collect counters and KPIs related to the number of API invocations which are out of order. Such metrics(counters and KPIs) if analysed further could possibly detect a security issue.
(2) Security alarms: Events leading to security breaches need regular monitoring and inform users in a management system. This can be accomplished with the help of security related alarms. For example the data type AlarmList as defined in TS28.622 has optional securityAlarmDetector attribute. But there is no events defined as to when this needs to be populated and triggered. This needs a study to identify the enhancement in the standards to determine if additional configurations may be needed and possible definitions of new alarms.
(3) Security logging: Network management systems need to collect security related log data and security events from the entire network in order to enrich and transfer the data to automated and intelligent security analysis systems for proactive security risk assessment and mitigation. The primary challenges regarding security logging and monitoring are the sheer volume of logs that are generated by information systems and applications and the lack of trained security staff to identify abnormal events using automated techniques. For automated and intelligent security analysis, enhancements may be required in security logging. Also, in order to facilitate security log analysis from multiple vendor components, standardization aspects of security logging need to be studied.
Potential collaboration groups and related topics: SA3.

## Slide 4: Submitted text for Rel-19 topics in SA5 (meeting #151) - Objective
This study item aims at investigating the mechanisms to enhance the collection and aggregation of data required for continuous security monitoring like security alarms, security logs and security metrics, from various network entities(possibly radio and core NFs, MnFs, UEs). The entities sending such relevant security data to the management systems considered but not limited to in this study include radio network functions and entities, core network functions, network management systems. This study considers 5G system architecture including and up to the features defined in Rel-18.
Accordingly, this study aims at identifying the standardization enhancements required for:
WoP#1 - collection, management and aggregation of security logs,
WoP#2 - collection, management and aggregation of security metrics,
WoP#3 - collection, management and corelation of security alarms,
The above data could be possibly collected from radio and core NFs, MnFs and UEs.
Note: The events which can lead to security risks/threats and the related data that needs to be exposed need to be primarily defined by SA3. There could be cases where OAM related security risks/threats may be defined by SA5.
Based on a risk based threat analysis, various aspects of security, including authentication, authorization, DDoS attacks, scanning, replay attacks and man-in-the-middle attacks will be considered while identifying these enhancements.
Clarification on the gaps and what is needed are in upcoming slides

## Slide 5: Security Metrics, Security events and Security logging
Security Monitoring and Assessment systems
KPIs
Security Events
Security Events
Security Log
e.g:SIEM
e.g:Fault Monitoring
e.g:SOAR
Security Alarms
Cross a threshold
KPIs
Managed Services or Network functions
counters
SA3 – What and where
SA5 – How to manage
Security scope of work
Analytics function
Analytics function
Analytics function
Perimeter security as in the past is not sufficient enough. We need to inculcate Zero trust architecture as is being driven in SA3
SA3 is driving this security topic and they dictate WHAT is to be done. SA5 decides HOW it is managed in such a way that the consumers of this data have the flexibility and possibility to injest this data with ease
SA5 adds value and focus’ on the FCAPS where security is also an important contribution for network wide security solutions
SA5 needs to study if the required infrastructure is sufficient to enable the security monitoring for the NFs including radio and Core, MnF and UEs(The data provided by UEs could also be used to correlate with other NFs data to help in correlation. Eg: for CAPIF interface, there could be indicators of API spoofing attacks also the UE).
The threats in the OAM system also need to be identified by SA5 in some cases where we are better experts
The outcome from SA5 should result in a standard that is interoperable for the security enablers

## Slide 6: Security Logging

## Slide 7: SA3 and SA5 potential split going forward
SA3
Background: Identify new security event logs for automated security log management and analysis
Scope of work:
  Addition of Rel-18 feature specific security event logs (ProSe, Ranging, NTN …)
  IT system related analysis is possible and exists, but wireless network specific security analytics can require additional standardization
  Types of logs and formats can be different and not yet considered for standardization
  In multi-vendor environment, especially for split-BTS kind of scenarios, standardized formats can help automated analysis
SA3: In Zero Trust Study : TR 33.894 : Key Issue 6.1 states: “As a result, the solutions addressing this key issue can identify various NF/AF relevant factors for data collection to enable security monitoring and continual trust evaluation.”
SA5
Background: Security event logs filtering, secure collection, management, retention, access control and transfer
Scope of work:
  Syslog is a possible industry standard, but should be enhanced for automated security log management and faster detection of security threats
  For example: Some key-value pairs standardized for security event logs, like: security event ID=XXX, security event source IP=YYY, etc…
  Ensure that such log collection and management does not impact system performance including management system

## Slide 8
What is really required from management point of view
  In general security logging requires who did what and when in the system.
    Sending security logs to a specific consumer in a secure manner(authorization)
    Filter only security logs out of all logs
    Ensure secure logs do not get tampered(combination of secure storage and transit)
    Special retention policy for security
What is NOT required from management point of view in this study
  Define the log format
  Define detailed events for security logging
What is already there
  In 32.332 there is a possibility to notify a subscriber and in addition write a general log record
  Industry specified standards of log format like syslog RFC 5432
  TR28.831 was also capturing some aspects of logging
What is concretely the gap to be studied?
    Security logging policy to filter/segregate/store security Logs and not all types logs
    Access to critical security logs
    Pre-processing of security logs
    Support from management system to transfer to an SIEM system
Examples
  Some event logs defined in SA3, but not yet enhanced for Rel-18 features
Further clarity in security logging

## Slide 9
Notifications and Logs
Entities common to 3GPP and ITU-T
Interfaces involved in Log management
  (1) Something happens in the system that needs to be send as notification, or the system needs to forward something as notification.
  (2) The notification MnS sends the notification to the (external) MnS consumer and
  (2) The notification MnS sends the notification to the event log.
  (3) The event log applies an Inputfilter and appends the notification as LogRecord to the log.
  Note: Management Function that receives the notification might differ from the tool that manages the logs !

## Slide 10
Notifications and Logs
Related entities as of ITU-T
Interfaces involved in Log management
  (1) Something happens in the system that shall be logged, but no need to be send as notification.
  (2) The event is send to the event log.
  (3) The event log applies an Inputfilter and appends the notification as LogRecord to the log.
  We don’t want to prescribe a format, only a container for proprietary log records.
  But nevertheless we need certain, few standardized fields to filter and select.

## Slide 11
Syslog RFC 5424 defines SDID formats and name-value pairs for syslog. However, for security logging, we can define new SDIDs. RFC 5424 clause 6.3.2 states: “Anyone can define additional SD-IDs using names in the format name@<private enterprise number>, e.g., "ourSDID@32473".”
For example:
secSDID@00001: For authentication failures
secSDID@00002: For authorization failures
secSDID@00003: For replay attack detection
secSDID@00004: For DDoS attack detection
etc.
In 3GPP, we can standardize such IDs and the relevant name-value pairs for each kind of attacks. This will allow usage of structured data syslog for continuous security monitoring and analytics. Further, for each SDID, the corresponding SD-PARAMs (clause 6.3.3 RFC 5424) can be standardized in 3GPP for wireless telecom network security usage.
For example:
secSDID@00001: For authentication failures
  SD-PARAM-value pairs for this kind of security event log can be: sourceIP=”1.2.3.4” sourcePort=”8080” username=”sysadmin” … etc.
secSDID@00003: For replay attack detection
  SD-PARAM-value pairs for this kind of security event log can be: sourceID=”UE-SUCI-XXXX” messageReplayID=”1234” messageSeqNum=”4321”… etc.
Example of potential log related IDs

## Slide 12: Security Alarms

## Slide 13
Notifications and subscriptions
Entities common to 3GPP and ITU-T
Notifications (e.g. Alarms) and subscriptions
(1) Something happens in the system that needs to be send as notification.
(2) The notification MnS sends the notification to the MnS consumer
Precondition: As part of the subscription the MnS consumer selected the candidate notifications by notificationTypes and notificationFilter.
Internally the MnS consumer might write the received notifications into a storage to evaluate them by whatever means.

## Slide 14: SA3 and SA5 potential split going forward
SA3
Background: Identify which events should trigger security alarms (faults)
  Example: Brute-force attacks detected, DDoS attacks detected, False-BTS detected
  Also, addition of Rel-18 feature specific alarms (ProSe, Ranging, NTN …)
Scope of work:
  Which security events map to potential detection of attacks
  For example, burst of authentication failures can indicate a brute-force attack, or, increase in system latency can indicate a DDoS attack, or, some symptoms identified specifically for FBS can indicate detection of a FBS
  May need to define new security events for SBA, and 5G specific features
SA5
Background: Infrastructure for security alarms exists. New alarms need to be defined.
Scope of work:
  How to capture the event on different management services? Different for different kinds of attacks
    Alarms for new counters or KPIs? Like number of packets received in a burst?
  How to raise alarm?

## Slide 15
What is really required from management point of view
  In general security alarms need to be available at the earliest as an indicator to the consumer
    Categorization of security alarms
    Correlation of security alarms
What is NOT required from management point of view in this study
  Define detailed events for security alarms
What is already there
  In 28.622 there is ONLY an attribute called secureAlarmDetector
  In 28.532, the different alarmTypes are present including security alarm
What is concretely the gap to be studied?
    Filtering of security alarms in specific
    Alarm reporting
    Retention policy of security alarms
Examples
  Raise an alarm when the number of failed authentications in last 5 minutes exceeded 100! This can indicate potential Distributed Brute-force attack.
Further clarity in security alarms

## Slide 16: Security Metrics

## Slide 17
What is really required from management point of view
  In general security counters and metrics for
    Security health of the network
What is NOT required from management point of view in this study
  Define detailed events for security counters and metrics
What is already there
  In 28.552 and 554 there are NO security related counters and KPIs
What is concretely the gap to be studied?
    Family of security counters and KPIs is not defined
    Security counters and KPIs for basic security health indicators for system security
Examples
  Security Management should define some counters and KPIs which can help measure the strength and weaknesses of system security
Further clarity in security metrics

## Slide 18: SA3 and SA5 potential split going forward
SA3
Background: SA3 should define which metrics (counters and KPIs) should be collected by security management
  For example, to measure the strengths and weaknesses of API security, some counters and KPIs can be collected
  Threat: Reverse engineering attack on APIs
  Possible counters: Number of times out-of-order APIs called
Scope of work: Definition of high-level requirements for security metrics
  Enablers for enhanced analytics-based security assessment in management plane
  Requirement: SBA should have mechanism to collect counters and KPIs which can help assess potential security weaknesses for exposed APIs
SA5
Reference / target: 28.552, 28.554
Background: Security metrics may need to be handled differently as compared to performance metrics in terms of higher security requirements for collection, access control, storage, transfer and usage
Scope of work: Collection, management and analytics of such counters and KPIs for different threats identified by SA3
  Analytics can be done by 3rd party
Outcome: Defined security counters and KPIs, defined methods to secure the collection, access control, storage, transfer and usage of these metrics

## Slide 19
Existing Performance Metrics in SA5 Standards
3GPP TS 28.552 (5G Performance Measurements)
  Counters related to 5G system Performance
  Performance measurements for gNB
  Performance measurements for AMF
  Performance measurements for SMF
  Performance measurements for UPF
  Performance measurements for PCF
  …
  NOTHING to measure how good/bad the system security is performing
    Example: Performance measurements for API Security
    Can be same or different spec
3GPP TS 28.554 (5G end-to-end KPIs)
  Accessibility KPI
  Integrity KPI
  Utilization KPI
  Retainability KPI
  Mobility KPI
  Energy Efficiency KPI
  …
  NOTHING yet for Security KPI
    Example: Average latencies observed during API access-response can be a KPI which can indicate a potential Man-in-the-middle for API accesses (including for CAPIF)

## Slide 20
Counter / KPI Name | Description | Attack | Threat
NUM_API_INVOCATIONS | Total number of API invocations in the periodic collection interval | All | -
OUT_OF_SEQUENCE_API | Number of times out-of-sequence API is invoked in the collection interval | Reverse Engineering | Retrieve account info, In 5G – retrieve network planning info (CM)
INCORRECT_API_CALLED | Number of times APIs called with invalid attributes in the collection interval | Reverse Engineering | Passive attack
UNAUTH_API_USER | Number of times an un-authorized user invoked an API | API Spoofing | Passive attack
TOKEN_REUSE_COUNT | Number of times a token (JWT/access/…) is reused | API Spoofing | Gain un-authorized access
USING_EXPIRED_TOKEN | Number of times expired token is attempted to be used | API Spoofing, Reverse Engineering | Presence of malicious applications
Examples of API Security Metrics

## Slide 21
Counter / KPI Name | Description | Attack | Threat
EXTERNAL_CONSUMER_API_ACCESS_COUNT | Number of times an external MnS consumer has invoked an API during periodic counter interval | All | -
EXTERNAL_CONSUMER_OUT_OF_SEQUENCE_API | Number of times an external MnS consumer has invoked out-of-sequence API | Reverse Engineering | Social engineering
UNAUTH_EXTERNAL_API_ACCESS | Number of times an unauthorized external API access is attempted | API Spoofing | Passive attack
SESSION_TOKEN_REUSE | Number of times session tokens are reused | Session Replay | Confidentiality
AVG_API_LATENCY | Models trained for normal average API latencies and sequence of APIs. Anomalies detected in this can indicate MitM attacks. | MitM | Confidentiality, Integrity
MEAN_SQUARE_API_LATENCY | Models trained for second order stats API latencies and sequence of APIs. Anomalies detected in this can indicate MitM attacks. | MitM | Confidentiality, Integrity
Examples of API Security Metrics