3GPP TSG-SA5 (Telecom Management)	(S5-070168

# Meeting SA5#51, 22 - 26 Jan 2007, Seville, SPAIN

| CR-Form-v9.3 |
| --- |
| CHANGE REQUEST |
| ( | 32.250 | CR | 0011 | ( rev | - | ( Current version: | 6.6.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | x |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Add MCC MNC in Location/change of location field |
| --- | --- |
| Source to WG: ( | Alcatel-Lucent (Xiaoping.F.She@alcatel-sbell.com.cn, veronique.belfort@alcatel-lucent.fr) |
| Source to TSG: ( | S5 |
| Work item code: ( | CH7 |  | Date: ( | 24/01/2007 |
| Category: ( | B |  | Release: ( | Rel-7 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) |
| Reason for change: ( | In case of national and international roaming, handovers between several operators is possible. Nevertheless in the current specification, location information is populated with the LAC or SAC; however, without the MCC+MNC. So in case of an inter-PLMN handover, the location/change of location fields from the anchor MSC only contain the LAC/SAI identity, without MCC+MNC resulting in an inability to distiguish the PLMN. |
| Summary of change: ( | Addition of the MCC+MNC values to the Location and Change of Location parameters in order to inform about the PLMN id. |
| Consequences if ( not approved: | Inability to apply differentiated charging depending on the HPLMN while roaming. |
| Clauses affected: ( | 5.1.3.6; 6.1.3.1; 6.1.3.2; 6.1.3.4; 6.1.3.9; 6.1.3.11; 6.1.3.13; 6.1.3.14; 6.1.3.19; 6.1.3.20; 6.1.3.23 |
|  | Y | N |  |  |
| Other specs ( |  | x | Other core specifications ( |  |
| affected: |  | x | Test specifications |  |
|  | x |  | O&M Specifications | 32.298 |
| Other comments: ( | Related R7 CR 32.298 in S5-070172 |

1st Modified Section

#### 5.1.3.6	Partial records

…

change of location (MCC+MNC+ LAC or Cell Id. or the Service Access Code, for UMTS) during a connection;

…

Next Modified Section

#### 6.1.3.1	Mobile originated call attempt

Table 6.1.3.1: MOC record

…

| Location | M | M | The identity of the cell or the SAC at the time of CDR creation, including the location area code and MCC+MNC. |
| --- | --- | --- | --- |
| Change of Location | OC | OC | A list of changes in Location Area Code / Service Area Code / Cell Id and MCC+MNC. Each time-stamped. |

…

Next Modified Section

#### 6.1.3.2	Mobile originated emergency call attempt

Table 6.1.3.2: MOC emergency record

…

| Location | M | M | The identity of the cell or the SAC at the time of CDR creation, including the location area code and MCC+MNC. |
| --- | --- | --- | --- |
| Change of Location | OC | OC | A list of changes in Location Area Code / Service Area Code / Cell Id and MCC+MNC. Each time-stamped. |

…

Next Modified Section

#### 6.1.3.4	Mobile terminated call attempt

Table 6.1.3.4: MTC record

…

| Location | C | C | The identity of the cell or the SAC occupied by the called party when the call was set up, including the location area code and MCC+MNC. |
| --- | --- | --- | --- |
| Change of Location | OC | OC | A list of changes in Location Area Code / Service Area Code / Cell Id and MCC+MNC. Each time-stamped. |

…

Next Modified Section

#### 6.1.3.9	Supplementary service actions

Table 6.1.3.9: SS-action record

…

| Location | OM | OM | The identity of the cell or the SAC, including the location area code and MCC+MNC, from which the request originated. |
| --- | --- | --- | --- |

…

Next Modified Section

#### 6.1.3.11	Location update (VLR)

Table 6.1.3.11: Location update (VLR) record

…

| Old location | C C | C C | Not present for registration: VMSC E.164 Number Location Area Code and MCC+MNC |
| --- | --- | --- | --- |
| New location | M M OM | M M OM | VMSC E.164 Number Location Area Code Cell Identification or Service Area Code and MCC+MNC |

…

Next Modified Section

#### 6.1.3.13	Short message service, mobile originated

Table 6.1.3.13: SMS-MO record

…

| Location | OM | OM | The Location Area Code and Cell Identity / Service Area Code and MCC+MNC from which the message originated. |
| --- | --- | --- | --- |

…

Next Modified Section

#### 6.1.3.14	Short message service, mobile terminated

Table 6.1.3.14: SMS-MT record

…

| Location | OM | OM | The Location Area Code and Cell Identity /Service Area Code and MCC+MNC to which the message was delivered. |
| --- | --- | --- | --- |

…

Next Modified Section

#### 6.1.3.19	IMEI observation ticket

Table 6.1.3.19:IMEI ticket

…

| Location | M | M | The location area code and cell identity of the cell and MCC+MNC from which the mobile equipment was used. |
| --- | --- | --- | --- |

…

Next Modified Section

#### 6.1.3.20	Mobile terminated location request (MT-LR)

Table 6.1.3.20: LCS-MT record

…

| Location | OM | - | The LAC and CI and MCC+MNC when the LR is received. |
| --- | --- | --- | --- |

…

Next Modified Section

#### 6.1.3.23	Mobile originated call attempt (CAMEL CPH adapted version)

Table 6.1.3.23: MOC record (CAMEL CPH adapted version)

…

| Location | M | M | The identity of the cell or the SAC and MCC+MNC at the time of CDR creation, including the location area code. |
| --- | --- | --- | --- |
| Change of Location | OC | OC | A list of changes in Location Area Code / Service Area Code / Cell Id and MCC+MNC. Each time-stamped. |

…

End of modifications

# Comments

Document numbers are allocated by the Working Group Secretary.   Use the format of document number specified by the 3GPP Working Procedures.

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2002.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.