3GPP TSG-SA5 (Telecom Management)	(S5-070174

# Meeting SA5#51, 22 - 26 Jan 2007, Seville, SPAIN

| CR-Form-v9.3 |
| --- |
| CHANGE REQUEST |
| ( | 32.733 | CR | 0001 | ( rev | - | ( Current version: | 7.0.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Add HssFunction to the CORBA SS |
| --- | --- |
| Source to WG: ( | Nokia, Ericsson (gyula.bodog@nokia.com) |
| Source to TSG: ( | S5 |
| Work item code: ( | OAM7-NIM |  | Date: ( | 26/01/2007 |
| Category: ( | F |  | Release: ( | Rel-7 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) |
| Reason for change: ( | HssFunction is missing from the IMS NRM |
| Summary of change: ( | HssFunction, Link_As_Hss, Link_Hss_Scscf and Link_Cscf_Hss is added to the NRM according to the IS specification |
| Consequences if ( not approved: | If HSS is not modelled there will be no possibility for managing the HSS in the 3GPP network. |
| Clauses affected: ( | Section 1, section 5 and Annex A |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  | x |  | O&M Specifications | 32.732, 32.735, 32.632, 32.633, 32.635 |
| Other comments: ( | Related R7 CR to 32.732 is in S5-070173, CR to 32.735 is in S5-070175, CR to 32.632 is in S5-070176, CR to 32.633 is in S5-070177 and CR to 32.635 is in S5-070178 |

1st Modified Section

# 1	Scope

The purpose of this IMS NRM IRP: CORBA Solution Set is to define the mapping of the IRP Information Service (see TS 32.732 [3]) to the protocol specific details necessary for implementation of this IRP in a CORBA/IDL environment.

This Solution Set specification is related to 3GPP TS 32.732 V7.1.X.

Next Modified Section

## 5.2	Information Object Class (IOC) mapping

### 5.2.1	IOC AsFunction

Mapping from NRM IOC AsFunction attributes to SS equivalent MOC AsFunction

| Attributes of IOC AsFunction in TS 32.732 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| asFunctionId | asFunctionId | string | Read-Only, M |

### 5.2.2	IOC BgcfFunction

Mapping from NRM IOC BgcfFunction attributes to SS equivalent MOC BgcfFunction

| Attributes of IOC BgcfFunction in TS 32.732 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| bgcfFunctionId | bgcfFunctionId | string | Read-Only, M |

### 5.2.3	IOC CscfFunction

Mapping from NRM IOC CscfFunction attributes to SS equivalent MOC CscfFunction

| Attributes of IOC CscfFunction in TS 32.732 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| cscfFunctionId | cscfFunctionId | string | Read-Only, M |
| userLabel | userLabel | string | Read-Write, M |

### 5.2.4	IOC IcscfFunction

Mapping from NRM IOC IcscfFunction attributes to SS equivalent MOC IcscfFunction

| Attributes of IOC IcscfFunction in TS 32.732 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| icscfFunctionId | icscfFunctionId | string | Read-Only, M |

### 5.2.5	IOC ImsMgwFunction

Mapping from NRM IOC ImsMgwFunction attributes to SS equivalent MOC ImsMgwFunction attributes

| Attributes of IOC ImsMgwFunction in TS 32.732 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| imsMgwFunctionId | imsMgwFunctionId | string | Read-Only, M |

### 5.2.6	IOC MgcfFunction

Mapping from NRM IOC MgcfFunction attributes to SS equivalent MOC MgcfFunction

| Attributes of IOC MgcfFunction in TS 32.732 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| mgcfFunctionId | mgcfFunctionId | string | Read-Only, M |

### 5.2.7	IOC MrfcFunction

Mapping from NRM IOC MrfcFunction attributes to SS equivalent MOC MrfcFunction

| Attributes of IOC MrfcFunction in TS 32.732 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| mrfcFunctionId | mrfcFunctionId | string | Read-Only, M |

### 5.2.8	IOC MrfpFunction

Mapping from NRM IOC MrfpFunction attributes to SS equivalent MOC MrfpFunction

| Attributes of IOC MrfpFunction in TS 32.732 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| mrfpFunctionId | mrfpFunctionId | string | Read-Only, M |

### 5.2.9	IOC PcscfFunction

Mapping from NRM IOC PcscfFunction attributes to SS equivalent MOC PcscfFunction

| Attributes of IOC PcscfFunction in TS 32.732 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| pcscfFunctionId | pcscfFunctionId | string | Read-Only, M |

### 5.2.10	IOC ScscfFunction

Mapping from NRM IOC ScscfFunction attributes to SS equivalent MOC ScscfFunction

| Attributes of IOC ScscfFunction in TS 32.732 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| scscfFunctionId | scscfFunctionId | string | Read-Only, M |

### 5.2.11	IOC SlfFunction

Mapping from NRM IOC SlfFunction attributes to SS equivalent MOC SlfFunction

| Attributes of IOC SlfFunction in TS 32.732 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| slfFunctionId | slfFunctionId | string | Read-Only, M |

### 5.2.12	IOC Link_As_Cscf

All attributes are inherited from Link. See mapping of attributes for Link IOC in 3GPP TS 32.623 [5].

### 5.2.13	IOC Link_As_Scscf

All attributes are inherited from Link. See mapping of attributes for Link IOC in 3GPP TS 32.623 [5].

### 5.2.14	IOC	Link_As_Slf

All attributes are inherited from Link. See mapping of attributes for Link IOC in 3GPP TS 32.623 [5].

### 5.2.15	IOC Link_Bgcf_Bgcf

All attributes are inherited from Link. See mapping of attributes for Link IOC in 3GPP TS 32.623 [5].

### 5.2.16	IOC Link_Bgcf_Cscf

All attributes are inherited from Link. See mapping of attributes for Link IOC in 3GPP TS 32.623 [5].

### 5.2.17	IOC Link_Bgcf_Mgcf

All attributes are inherited from Link. See mapping of attributes for Link IOC in 3GPP TS 32.623 [5].

### 5.2.18	IOC Link_Bgcf_Scscf

All attributes are inherited from Link. See mapping of attributes for Link IOC in 3GPP TS 32.623 [5].

### 5.2.19	IOC Link_Cscf_Cscf

All attributes are inherited from Link. See mapping of attributes for Link IOC in 3GPP TS 32.623 [5].

### 5.2.20	IOC Link_Cscf_Icscf

All attributes are inherited from Link. See mapping of attributes for Link IOC in 3GPP TS 32.623 [5].

### 5.2.21	IOC Link_Cscf_Mgcf

All attributes are inherited from Link. See mapping of attributes for Link IOC in 3GPP TS 32.623 [5].

### 5.2.22	IOC Link_Cscf_Mrfc

All attributes are inherited from Link. See mapping of attributes for Link IOC in 3GPP TS 32.623 [5].

### 5.2.23	IOC Link_Cscf_Pcscf

All attributes are inherited from Link. See mapping of attributes for Link IOC in 3GPP TS 32.623 [5].

### 5.2.24	IOC Link_Cscf_Scscf

All attributes are inherited from Link. See mapping of attributes for Link IOC in 3GPP TS 32.623 [5].

### 5.2.25	IOC Link_Cscf_Slf

All attributes are inherited from Link. See mapping of attributes for Link IOC in 3GPP TS 32.623 [5].

### 5.2.26	IOC Link_Icscf_Slf

All attributes are inherited from Link. See mapping of attributes for Link IOC in 3GPP TS 32.623 [5].

### 5.2.27	IOC Link_ImsMgw_Mgcf

All attributes are inherited from Link. See mapping of attributes for Link IOC in 3GPP TS 32.623 [5].

### 5.2.28	IOC Link_Mgcf_Scscf

All attributes are inherited from Link. See mapping of attributes for Link IOC in 3GPP TS 32.623 [5].

### 5.2.29	IOC Link_Mrfc_Mrfp

All attributes are inherited from Link. See mapping of attributes for Link IOC in 3GPP TS 32.623 [5].

### 5.2.30	IOC Link_Mrfc_Scscf

All attributes are inherited from Link. See mapping of attributes for Link IOC in 3GPP TS 32.623 [5].

### 5.2.31	IOC Link_Scscf_Scscf

All attributes are inherited from Link. See mapping of attributes for Link IOC in 3GPP TS 32.623 [5].

### 5.2.32	IOC Link_Scscf_Slf

All attributes are inherited from Link. See mapping of attributes for Link IOC in 3GPP TS 32.623 [5].

### 5.2.xx	IOC HssFunction

Mapping from NRM IOC HssFunction attributes to SS equivalent MOC HssFunction

| Attributes of IOC HssFunction in TS 32.732 [3] | SS Attributes | SS Type | Qualifier |
| --- | --- | --- | --- |
| hssFunctionId | hssFunctionId | string | Read-Only, M |

### 5.2.yy	IOC Link_Hss_Scscf

All attributes are inherited from Link. See mapping of attributes for Link IOC in 3GPP TS 32.623 [5].

### 5.2.zz	IOC Link_Cscf_Hss

All attributes are inherited from Link. See mapping of attributes for Link IOC in 3GPP TS 32.623 [5].

### 5.2.vv	IOC Link_As_Hss

All attributes are inherited from Link. See mapping of attributes for Link IOC in 3GPP TS 32.623 [5].

Next Modified Section

Annex A (normative):
CORBA IDL, NRM Definitions

# A.1	IDL specification (file name "IMSNRMDefs.idl")

// File: IMSNRMDefs.idl

#ifndef _IMSNRMDEFS_IDL_

#define _IMSNRMDEFS_IDL_

#include "GenericNetworkResourcesNRMDefs.idl"

#pragma prefix "3gppsa5.org"

/**

* This module defines constants for each MO class name and

* the attribute names for each defined MO class.

*/

module IMSNRMDefs

{

/**

*  Definitions for MO class AsFunction

*/

interface AsFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "AsFunction";

// Attribute Names

//

const string asFunctionId = "asFunctionId";

};

/**

*  Definitions for MO class BgcfFunction

*/

interface BgcfFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "BgcfFunction";

// Attribute Names

//

const string bgcfFunctionId = "bgcfFunctionId";

};

/**

*  Definitions for MO class CscfFunction

*/

interface CscfFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "CscfFunction";

// Attribute Names

//

const string cscfFunctionId = "cscfFunctionId";

};

/**

*  Definitions for MO class IcscfFunction

*/

interface IcscfFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "IcscfFunction";

// Attribute Names

//

const string icscfFunctionId = "icscfFunctionId";

};

/**

*  Definitions for MO class ImsMgwFunction

*/

interface ImsMgwFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "ImsMgwFunction";

// Attribute Names

//

const string imsMgwFunctionId = "imsMgwFunctionId";

};

/**

*  Definitions for MO class MgcfFunction

*/

interface MgcfFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "MgcfFunction";

// Attribute Names

//

const string mgcfFunctionId = "mgcfFunctionId";

};

/**

*  Definitions for MO class MrfcFunction

*/

interface MrfcFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "MrfcFunction";

// Attribute Names

//

const string mrfcFunctionId = "mrfcFunctionId";

};

/**

*  Definitions for MO class MrfpFunction

*/

interface MrfpFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "MrfpFunction";

// Attribute Names

//

const string mrfpFunctionId = "mrfpFunctionId";

};

/**

*  Definitions for MO class PcscfFunction

*/

interface PcscfFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "PcscfFunction";

// Attribute Names

//

const string pcscfFunctionId = "pcscfFunctionId";

};

/**

*  Definitions for MO class ScscfFunction

*/

interface ScscfFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "ScscfFunction";

// Attribute Names

//

const string scscfFunctionId = "scscfFunctionId";

};

/**

*  Definitions for MO class SlfFunction

*/

interface SlfFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "SlfFunction";

// Attribute Names

//

const string slfFunctionId = "slfFunctionId";

};

/**

*  Definitions for MO class Link_As_Cscf

*/

interface Link_As_Cscf: GenericNetworkResourcesNRMDefs::Link

{

const string CLASS = "Link_As_Cscf";

// All Attributes inherited from Link

};

/**

*  Definitions for MO class Link_As_Scscf

*/

interface Link_As_Scscf : GenericNetworkResourcesNRMDefs::Link

{

const string CLASS = "Link_As_Scscf";

// All Attributes inherited from Link

};

/**

*  Definitions for MO class Link_As_Slf

*/

interface Link_As_Slf : GenericNetworkResourcesNRMDefs::Link

{

const string CLASS = "Link_As_Slf";

// All Attributes inherited from Link

};

/**

*  Definitions for MO class Link_Bgcf_Bgcf

*/

interface Link_Bgcf_Bgcf : GenericNetworkResourcesNRMDefs::Link

{

const string CLASS = "Link_Bgcf_Bgcf";

// All Attributes inherited from Link

};

/**

*  Definitions for MO class Link_Bgcf_Cscf

*/

interface Link_Bgcf_Cscf: GenericNetworkResourcesNRMDefs::Link

{

const string CLASS = "Link_Bgcf_Cscf";

// All Attributes inherited from Link

};

/**

*  Definitions for MO class Link_Bgcf_Mgcf

*/

interface Link_Bgcf_Mgcf : GenericNetworkResourcesNRMDefs::Link

{

const string CLASS = "Link_Bgcf_Mgcf";

// All Attributes inherited from Link

};

/**

*  Definitions for MO class Link_Bgcf_Scscf

*/

interface Link_Bgcf_Scscf : GenericNetworkResourcesNRMDefs::Link

{

const string CLASS = "Link_Bgcf_Scscf";

// All Attributes inherited from Link

};

/**

*  Definitions for MO class Link_Cscf_Cscf

*/

interface Link_Cscf_Cscf: GenericNetworkResourcesNRMDefs::Link

{

const string CLASS = "Link_Cscf_Cscf";

// All Attributes inherited from Link

};

/**

*  Definitions for MO class Link_Cscf_Icscf

*/

interface Link_Cscf_Icscf: GenericNetworkResourcesNRMDefs::Link

{

const string CLASS = "Link_Cscf_Icscf";

// All Attributes inherited from Link

};

/**

*  Definitions for MO class Link_Cscf_Mgcf

*/

interface Link_Cscf_Mgcf: GenericNetworkResourcesNRMDefs::Link

{

const string CLASS = "Link_Cscf_Mgcf";

// All Attributes inherited from Link

};

/**

*  Definitions for MO class Link_Cscf_Mrfc

*/

interface Link_Cscf_Mrfc: GenericNetworkResourcesNRMDefs::Link

{

const string CLASS = "Link_Cscf_Mrfc";

// All Attributes inherited from Link

};

/**

*  Definitions for MO class Link_Cscf_Pcscf

*/

interface Link_Cscf_Pcscf: GenericNetworkResourcesNRMDefs::Link

{

const string CLASS = "Link_Cscf_Pcscf";

// All Attributes inherited from Link

};

/**

*  Definitions for MO class Link_Cscf_Scscf

*/

interface Link_Cscf_Scscf: GenericNetworkResourcesNRMDefs::Link

{

const string CLASS = "Link_Cscf_Scscf";

// All Attributes inherited from Link

};

/**

*  Definitions for MO class Link_Cscf_Slf

*/

interface Link_Cscf_Slf: GenericNetworkResourcesNRMDefs::Link

{

const string CLASS = "Link_Cscf_Slf";

// All Attributes inherited from Link

};

/**

*  Definitions for MO class Link_Icscf_Slf

*/

interface Link_Icscf_Slf : GenericNetworkResourcesNRMDefs::Link

{

const string CLASS = "Link_Icscf_Slf";

// All Attributes inherited from Link

};

/**

*  Definitions for MO class Link_ImsMgw_Mgcf

*/

interface Link_ImsMgw_Mgcf : GenericNetworkResourcesNRMDefs::Link

{

const string CLASS = "Link_ImsMgw_Mgcf";

// All Attributes inherited from Link

};

/**

*  Definitions for MO class Link_Mgcf_Scscf

*/

interface Link_Mgcf_Scscf : GenericNetworkResourcesNRMDefs::Link

{

const string CLASS = "Link_Mgcf_Scscf";

// All Attributes inherited from Link

};

/**

*  Definitions for MO class Link_Mrfc_Mrfp

*/

interface Link_Mrfc_Mrfp : GenericNetworkResourcesNRMDefs::Link

{

const string CLASS = "Link_Mrfc_Mrfp";

// All Attributes inherited from Link

};

/**

*  Definitions for MO class Link_Mrfc_Scscf

*/

interface Link_Mrfc_Scscf : GenericNetworkResourcesNRMDefs::Link

{

const string CLASS = "Link_Mrfc_Scscf";

// All Attributes inherited from Link

};

/**

*  Definitions for MO class Link_Scscf_Scscf

*/

interface Link_Scscf_Scscf : GenericNetworkResourcesNRMDefs::Link

{

const string CLASS = "Link_Scscf_Scscf";

// All Attributes inherited from Link

};

/**

*  Definitions for MO class Link_Scscf_Slf

*/

interface Link_Scscf_Slf : GenericNetworkResourcesNRMDefs::Link

{

const string CLASS = "Link_Scscf_Slf";

// All Attributes inherited from Link

};

/**

*  Definitions for MO class HssFunction

*/

interface HssFunction : GenericNetworkResourcesNRMDefs::ManagedFunction

{

const string CLASS = "HssFunction";

// Attribute Names

//

const string hssFunctionId = "hssFunctionId";

};

/**

*  Definitions for MO class Link_Hss_Scscf

*/

interface Link_Hss_Scscf : GenericNetworkResourcesNRMDefs::Link

{

const string CLASS = "Link_Hss_Scscf";

// All Attributes inherited from Link

};

/**

*  Definitions for MO class Link_Cscf_Hss

*/

interface Link_Cscf_Hss : GenericNetworkResourcesNRMDefs::Link

{

const string CLASS = "Link_Cscf_Hss";

// All Attributes inherited from Link

};

/**

*  Definitions for MO class Link_As_Hss

*/

interface Link_As_Hss : GenericNetworkResourcesNRMDefs::Link

{

const string CLASS = "Link_As_Hss";

// All Attributes inherited from Link

};

};

#endif // _IMSNRMDEFS_IDL_

Next Modified Section

End of modifications

Annex B (informative):
Change history

| Change history |
| --- |
| Date | TSG # | TSG Doc. | CR | R | Subject/Comment | Cat | Old | New |
| Sep 2006 | SA_33 | SP-060564 | -- | -- | Submitted to TSG SA #33 for Information | -- | -- | 1.0.0 |
| Dec 2006 | SA_34 | SP-060751 | -- | -- | Submitted to TSG SA #34 for Approval | -- | 2.0.0 | 7.0.0 |

# Comments

Document numbers are allocated by the Working Group Secretary.   Use the format of document number specified by the 3GPP Working Procedures.

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2002.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.