3GPP TSG-SA5 (Telecom Management) 	Tdoc (S5-070212

Meeting SA5#51, 22 - 26 Jan 2007, Seville, SPAIN

| CR-Form-v9.1 |
| --- |
| CHANGE REQUEST |
| ( | 32.151 | CR | 0006 | ( rev | - | ( Current version: | 7.1.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network | x | Core Network | x |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Suppress inherited items |
| --- | --- |
| Source to WG: ( | Ericsson (thomas.tovinger@ericsson.com ) |
| Source to TSG: ( | S5 |
| Work item code: ( | OAM7-NIM |  | Date: ( | 26/01/2007 |
| Category: ( | F |  | Release: ( | Rel-7 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) |
| Reason for change: ( | In today’s IRP IS specifications, it has become a “random habit” (a habit not consistently applied), although neither required by the methodology specifications nor the object-oriented technique used, to repeat inherited items in subclass IOC definitions. This causes redundancy, risk for errors and duplicated specification work. |
| Summary of change: ( | Add statements in this IS template to clarify that inherited items shall not be repeated. |
| Consequences if ( not approved: | Redundancy, risk for errors and duplicated specification work. |
| Clauses affected: ( | X.3, X.4, X.5. |
|  | Y | N |  |  |
| Other specs ( |  | x | Other core specifications ( |  |
| affected: |  | x | Test specifications |  |
|  |  | x | O&M Specifications |  |
| Other comments: ( |  |

1st Modified Section

## X.3	Information object class definitions

Each information object class is defined using the following structure.

Inherited items (attributes etc.) shall not be shown, as they are defined in the parent IOC(s) and thus valid for all subclasses.

Next Modified Section

## X.4	Information relationship definitions

Each information relationship is defined using the following structure.

Inherited relationships shall not be shown, as they are defined by the parent IOC(s) and thus valid for all subclasses.

Next Modified Section

## X.5	Information attribute definitions

Each information attribute is defined using the following structure.

Inherited attributes shall not be shown, as they are defined in the parent IOC(s) and thus valid for all subclasses.

End of modifications

Annex A (informative):
Change history

| Change history |
| --- |
| Date | TSG # | TSG Doc. | CR | Rev | Subject/Comment | Cat | Old | New |
| Sep 2006 | SA_33 | SP-060548 | 0004 | -- | Update of 32.151 to use a MCC supported font | F | 6.3.0 | 7.0.0 |
| Dec 2006 | SA_34 | SP-060724 | 0005 | -- | Correct the clause numbering instructions for Operations and Notifications | F | 7.0.0 | 7.1.0 |

# Comments

Document number

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least three digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "x WGn" where 
	x = "CT" for TSG CT, "RAN" for TSG RAN, "SA" for TSG SA, "GERAN" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "TSG x". 
Examples: "CT WG4", "RAN WG5", "GERAN WG3", "TSG SA".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, B & C CRs for release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See http://www.3gpp.org/ftp/information/work_plan/ .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2002.

Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory necessary to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.