3GPP TSG-SA5 (Telecom Management)	(S5-070170

# Meeting SA5#51, 22 - 26 Jan 2007, Seville, SPAIN

| CR-Form-v9.3 |
| --- |
| CHANGE REQUEST |
| ( | 32.251 | CR | 0044 | ( rev | - | ( Current version: | 7.2.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | x |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Add MCC and MNC in M-CDR |
| --- | --- |
| Source to WG: ( | Alcatel-Lucent (Xiaoping.F.She@alcatel-sbell.com.cn, veronique.belfort@alcatel-lucent.fr) |
| Source to TSG: ( | S5 |
| Work item code: ( | CH7 |  | Date: ( | 25/01/2007 |
| Category: ( | B |  | Release: ( | Rel-7 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) |
| Reason for change: ( | In case of national roaming or network sharing, handovers between several operators is possible. |
| Summary of change: ( | Addition of the MCC+MNC values to the Location and Change of Location parameters in order to inform about the PLMN id. |
| Consequences if ( not approved: | Inability to apply differentiated charging depending on the HPLMN while roaming. |
| Clauses affected: ( | 6.1.4 |
|  | Y | N |  |  |
| Other specs ( |  | x | Other core specifications ( |  |
| affected: |  | x | Test specifications |  |
|  | x |  | O&M Specifications | 32.298 |
| Other comments: ( | Related R7 CR 32.298 in S5-070172 |

1st Modified Section

### 6.1.4	Mobile Station mobility management data in SGSN (M-CDR)

If the collection of MS mobility management data is enabled then the SGSN shall start collecting the information specified in the following table each time the mobile is attached to the SGSN.

Table 6.1.4: SGSN Mobile Station mobility management data (M-CDR)

| Field | Category | Description |
| --- | --- | --- |
| Record Type | M | SGSN mobility management record. |
| Served IMSI | M | IMSI of the MS. |
| Served IMEI | OC | The IMEI of the ME, if available. |
| SGSN Address | OM | The IP address of the current SGSN. |
| MS Network Capability | OM | The mobile station network capability. |
| Routing Area Code | OM | Routing Area at the time of the Record Opening Time. |
| Local Area Code | OM | Location Area Code at the time of Record Opening Time. |
| Cell Identifier | OM | The Cell Identity for GSM or Service Area Code (SAC) for UMTS at the time of the Record Opening Time. |
| Cell PLMN Id | OM | The MCC and MNC of the Cell at the time of Record Opening Time. |
| Change of Location | OC | A list of changes in Routing Area Code including MCC and MNC, each with a time stamp. This field is not required if partial records are generated when the location changes. |
| Record Opening Time | M | Timestamp when MS is attached to this SGSN or record opening time on following partial record. |
| Duration | OM | Duration of this record. |
| SGSN Change | C | Present if this is first record after SGSN change. |
| Cause for Record Closing | M | The reason for the closure of the record in this SGSN. |
| Diagnostics | OM | A more detailed reason for the release of the connection. |
| Record Sequence Number | C | Partial record sequence number in this SGSN; only present in case of partial records. |
| Node ID | OM | Name of the recording entity. |
| Record Extensions | OC | A set of network operator/manufacturer specific extensions to the record. Conditioned upon the existence of an extension. |
| Local Record Sequence Number | OM | Consecutive record number created by this node. The number is allocated sequentially including all CDR types. |
| Served MSISDN | OM | The primary MSISDN of the subscriber. |
| Charging Characteristics | M | The Charging Characteristics used by the SGSN. |
| CAMEL Information | OC | Set of CAMEL information related to Attach/Detach session. For more information see Description of Record Fields. This field is present if CAMEL service is activated. |
| RAT Type | OC | This field indicates the Radio Access Technology (RAT) type, e.g. UTRAN or GERAN, currently used by the Mobile Station as defined in TS 29.060 [204]. |
| Charging Characteristics Selection Mode | OM | Holds information about how Charging Characteristics were selected. |

End of modifications

# Comments

Document numbers are allocated by the Working Group Secretary.   Use the format of document number specified by the 3GPP Working Procedures.

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2002.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.