3GPP TSG-SA5 (Telecom Management)	(S5-070192

# Meeting SA5#51, 22 - 26 Jan 2007, Seville, SPAIN

| CR-Form-v9.3 |
| --- |
| CHANGE REQUEST |
| ( | 32.260 | CR | 0046 | ( rev | - | ( Current version: | 7.1.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Corrections to BGCF state during PSTN and IMS intiated session establishment and releases |
| --- | --- |
| Source to WG: ( | Alcatel-Lucent (njmazzarella@alcatel-lucent.com) |
| Source to TSG: ( | S5 |
| Work item code: ( | CH7 |  | Date: ( | 26/01/2007 |
| Category: ( | F |  | Release: ( | Rel-7 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) |
| Reason for change: ( | IMS and PSTN Session release flows incorrectly show the BGCF as always in a stateful condition, when it should be stateless . TS 24.229 clause 5.6 states that the BGCF may not remain in the signalling path after the initial INVITE. |
| Summary of change: ( | Add corrections in both PSTN and IMS Session Initiations and Releases stating that the BGCF will not remain in the signalling path nor store interim and release information in its CDR. |
| Consequences if ( not approved: | The current flow and CDR/ACR information is incorrect, and can cause incorrect implementation for BGCF status during session releases. |
| Clauses affected: ( | 5.2.1.1, 5.2.2.1.7, 5.2.2.1.8, 5.2.2.1.9, 6.3.2 |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( | This case was verified through incoming CT1 LS to SA5 SWGB in S5-070065 (C1-062275) |

1st Modified Section

Table 5.2.1.1: Accounting Request messages triggered by SIP Methods or ISUP Messages
for all IMS nodes except for MRFC and AS

| Diameter message | Triggering SIP Method /ISUP message |
| --- | --- |
| ACR [Start] | SIP 200 OK acknowledging an initial SIP INVITE (see note 2) (not applicable for BGCF) |
|  | ISUP:ANM (applicable for the MGCF) |
| ACR [Interim] | SIP 200 OK acknowledging a SIP RE-INVITE or SIP UPDATE [e.g. change in media components] (see note 2) |
|  | Expiration of AVP [Acct-Interim-Interval] (see note 2) |
| ACR [Stop] | SIP BYE message (both normal and abnormal session termination cases) (see note 2) (not applicable for BGCF) |
|  | ISUP:REL (applicable for the MGCF) |
| ACR [Event] | SIP 200 OK acknowledging non-session related SIP messages, which are: |
|  | SIP NOTIFY (see note 1 and note 2) |
|  | SIP MESSAGE |
|  | SIP REGISTER (see note 1) |
|  | SIP SUBSCRIBE (see note 3) |
|  | SIP PUBLISH |
|  | SIP 200 OK acknowledging an initial SIP INVITE (only for BGCF) |
|  | SIP 202 Accepted acknowledging a SIP REFER or any other method |
|  | SIP Final Response 2xx (except SIP 200 OK) |
|  | SIP Final/Redirection Response 3xx |
|  | SIP Final Response (4xx, 5xx or 6xx), indicating an unsuccessful SIP session set-up |
|  | SIP Final Response (4xx, 5xx or 6xx), indicating an unsuccessful session-unrelated procedure |
|  | SIP CANCEL, indicating abortion of a SIP session set-up (see note 2) |
|  | I-CSCF completing a Cx Query that was issued in response to a SIP INVITE |
| NOTE 1: SIP REGISTER with its "Expires" header field or "Expires" parameter equal to 0 or local deregistration due to expiry means Deregistration (see 3GPP TS 24.229 [204]). NOTE 2: (only for I-CSCF): This trigger may only occur if I-CSCF is acting in THIG mode. NOTE 3: SIP SUBSCRIBE with the field "Expires" set to 0 means unsubscribe. |

##### 5.2.2.1.7	Session Establishment - IMS Initiated

The following figure shows the Diameter transactions that are required between BGCF, MGCF and CDF during session establishment initiated from the IMS side.

# Figure : Message Sequence Chart for Session Establishment (IMS Initiated)

1.	The session is originated from the IMS.

2.	A session towards PSTN is established.

3.	The destination party answers and an answer message are received.

4.	A final response message is sent to the session originator.

5.	Upon reception of the answer message, the MGCF sends an Accounting-Request with
Accounting-Record-Type indicating START_RECORD to record start of a user session and start of a media component in the MGCF CDR.

6.	The CDF acknowledges the reception of the data and opens a MGCF CDR.

7.	Upon reception of the 200 OK message, the BGCF sends an Accounting-Request with
Accounting-Record-Type indicating EVENT_RECORD to record start of a user session and start of a media component in the BGCF CDR.

8.	The CDF acknowledges the reception of the data and creates a BGCF CDR.

##### 5.2.2.1.8	Session Release - PSTN initiated

The following figure shows the Diameter transactions that are required between MGCF and CDF during a PSTN initiated session release.

# Figure : Message Sequence Chart for Session Release (PSTN initiated)

1.	The session release is initiated from PSTN.

2.	Session release continues within IMS.

3.	The reception of the release message is acknowledged.

4.	Upon reception of the release message, the MGCF sends an Accounting-Request with
Accounting-Record-Type indicating STOP_RECORD to record stop of a session in the MGCF CDR.

5.	The CDF acknowledges the reception of the data and closes the MGCF CDR.

Next Modified Section

##### 5.2.2.1.9	Session Release - IMS Initiated

The following figure shows the Diameter transactions that are required between MGCF and CDF during a IMS initiated session release.

# Figure : Message Sequence Chart for Session Release (IMS initiated)

1.	The session release is initiated from the IMS side.

2.	A release message is sent towards PSTN.

3.	The acknowledgement of the release message is received from PSTN.

4.	Upon reception of the BYE message the MGCF sends an Accounting Request with Accounting Record Type indicating STOP_RECORD to record stop of a session in the MGCF CDR.

5.	The CDF acknowledges the reception of the data and closes the MGCF CDR.

### 6.3.2	Detailed Message Format for offline charging

The following chapter specifies per Operation Type the charging data that are sent by each of the IMS network elements:

- S-CSCF

- P-CSCF

- CSCF

- MRFC

- MGCF

- BGCF

- AS

The Operation Types are listed in the following order: S (start)/I (interim)/S (stop)/E (event). Therefore, when all Operation Types are possible it is marked as SISE. If only some Operation Types are allowed for a node, only the appropriate letters are used (i.e. SIS or E) as indicated in the table heading. The omission of an Operation Type for a particular field is marked with "-" (i.e. SI-E). Also, when an entire field is not allowed in a node the entire cell is marked as "-".

Table 6.3.2.1 illustrates the basic structure of the supported fields in the Charging Data Request message for IMS offline charging.

Table 6.3.2.1 : Supported fields in Charging Data Request Message

| Field | Node Type | S-CSCF | P-CSCF | I-CSCF | MRFC | MGCF | BGCF | AS |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Supported Operation Types | S/I/S/E | S/I/S/E | E | S/I/S | S/I/S/E | E | S/I/S/E |
| Session Identifier | SISE | SISE | E | SIS | SISE | E | SISE |
| Originator Node | SISE | SISE | E | SIS | SISE | E | SISE |
| Originator Domain | SISE | SISE | E | SIS | SISE | E | SISE |
| Destination Domain | SISE | SISE | E | SIS | SISE | E | SISE |
| Operation Type | SISE | SISE | E | SIS | SISE | E | SISE |
| Operation Number | SISE | SISE | E | SIS | SISE | E | SISE |
| Operation Identifier | SISE | SISE | E | SIS | SISE | E | SISE |
| User Name | SISE | SISE | E | SIS | SISE | E | SISE |
| Operation Interval | SISE | SISE | E | SIS | SISE | E | SISE |
| Origination State | SISE | SISE | E | SIS | SISE | E | SISE |
| Origination Timestamp | SISE | SISE | E | SIS | SISE | E | SISE |
| Proxy Information | SISE | SISE | E | SIS | SISE | E | SISE |
| Route Information | SISE | SISE | E | SIS | SISE | E | SISE |
| Operation Token | SISE | SISE | E | SIS | SISE | E | SISE |
| Subscriber Identifier | SISE | SISE | - | SIS | - | - | SISE |
| Service Information with PS and IMS Information |
| Event Type | SISE | SISE | E | SIS | SISE | E | SISE |
| Role of Node | SISE | SISE | E | SIS | SISE | E | SISE |
| Node Functionality | SISE | SISE | E | SIS | SISE | E | SISE |
| User Session Id | SISE | SISE | E | SIS | SISE | E | SISE |
| Calling Party Address | SISE | SISE | E | SIS | SISE | E | SISE |
| Called Party Address | SISE | SISE | E | SIS | SISE | E | SISE |
| Requested Party Address | S--E | - | - | S-- | - | - | S--E |
| Called Asserted Identity | S--E | - | - | S-- | - | - | S--E |
| Associated URI | ---E | ---E | E | - | - | - | - |
| Time stamps (see note 3) | SISE | SISE | E | SIS | SISE | E | SISE |
| Application server Information (see note 1) | SISE | - | - | SIS | - | - | - |
| Inter Operator Identifiers (see note 1) | SISE | SISE | E | SIS | SISE | E | SISE |
| IMS Charging Identifier | SISE | SISE | E | SIS | SISE | E | SISE |
| SDP Session Description | SI-- | SI-- | - | SI-- | SI-- | - | SI-- |
| SDP Media Component | SI-- | SI-- |  | SI-- | SI-- | - | SI-- |
| GGSN Address | SI-- | SI-- |  | SI-- | SI-- | - | SI-- |
| Served Party (see note 1) | - | SISE | - | - | - | - | - |
| Authorized QoS (see note 1) | - | SI-- | - | - | - | - | - |
| Server Capabilities (see note 1) | - | - | E | - | - | - | - |
| Trunk Group ID (see note 1) | - | - | - | - | SISE | - | - |
| Bearer Service (see note 1) | - | - | - | - | SISE | - | - |
| Service Id (see note 1) | - | - | - | SIS | - | - | - |
| Service Specific Info (see note 1) | - | - | - | - | - | - | SISE |
| Message Bodies (see note 2) | SISE | SISE |  |  | SISE |  | SISE |
| Cause Code | --SE | --SE | E | --S | --SE | E | --SE |
| Access Network Information | SISE | SISE | E | SIS | SISE | E | SISE |
| NOTE 1: Only present if available in the CTF of the IMS node. NOTE 2: Present only if Messages Bodies is included in the SIP message that triggered the Charging Data Request. NOTE 3: Only present if ACR is triggered on a SIP message (e.g. SIP INVITE, SIP UPDATE). |

Table 6.3.2.2 illustrates the basic structure of the supported fields in the Charging Data Response message for IMS offline charging.

Table 6.3.2.2 : Supported fields in Charging Data Response Message

| Field | Node Type | S-CSCF | P-CSCF | I-CSCF | MRFC | MGCF | BGCF | AS |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Supported Operation Types | S/I/S/E | S/I/S/E | E | S/I/S | S/I/S/E | S/I/S/E | S/I/S/E |
| Session Identifier | SISE | SISE | E | SIS | SISE | SISE | SISE |
| Originator Node | SISE | SISE | E | SIS | SISE | SISE | SISE |
| Originator Domain | SISE | SISE | E | SIS | SISE | SISE | SISE |
| Destination Domain | SISE | SISE | E | SIS | SISE | SISE | SISE |
| Operation Type | SISE | SISE | E | SIS | SISE | SISE | SISE |
| Operation Number | SISE | SISE | E | SIS | SISE | SISE | SISE |
| Operation Identifier | SISE | SISE | E | SIS | SISE | SISE | SISE |
| User Name | SISE | SISE | E | SIS | SISE | SISE | SISE |
| Operation Interval | SISE | SISE | E | SIS | SISE | SISE | SISE |
| Origination State | SISE | SISE | E | SIS | SISE | SISE | SISE |
| Origination Timestamp | SISE | SISE | E | SIS | SISE | SISE | SISE |
| Proxy Information | SISE | SISE | E | SIS | SISE | SISE | SISE |
| Route Information | SISE | SISE | E | SIS | SISE | SISE | SISE |

End of modifications

# Comments

Document numbers are allocated by the Working Group Secretary.   Use the format of document number specified by the 3GPP Working Procedures.

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2002.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.

# Text boxes

Next Modified Section

Next Modified Section

Next Modified Section