3GPP TSG-SA5 (Telecom Management) 	Tdoc (S5-070249

Meeting SA5#51, 22 - 26 Jan 2007, Seville, ES

| CR-Form-v9.2 |
| --- |
| CHANGE REQUEST |
| ( | 32.298 | CR | 0066 | ( rev | - | ( Current version: | 7.1.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Correction on SDP Media Info - Align with 24.229 |
| --- | --- |
| Source to WG: ( | Siemens Networks, Nokia (gerald.goermer@siemens.com, benni.alexander@nokia.com) |
| Source to TSG: ( | S5 |
| Work item code: ( | CH |  | Date: ( | 26/01/2007 |
| Category: ( | A |  | Release: ( | Rel-7 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) |
| Reason for change: ( | According to TS 24.229 the S-CSCF shall remove the access-network-charging-info parameter from the P-Charging-Vector header prior to forwarding the message to MGCF and BGCF. Therefore the Access Correlation ID as the part of the access-network-charging-info is not available at MGCF and BGCF. The Acces Network address is already removed but the Access Correlation ID as the part of the SDP Media components is present in the description. |
| Summary of change: ( | The Access Correlation ID is not used in the SDP media component parameter for MGCF and BGCF ASN.1 definition. |
| Consequences if ( not approved: | Error in IMS Billing based on MGCF and BGCF CDRs. |
| Clauses affected: ( | 5.2.3 |
|  | Y | N |  |  |
| Other specs ( | x |  | Other core specifications ( |  |
| affected: | x |  | Test specifications |  |
|  |  | x | O&M Specifications | 32.260 |
| Other comments: ( | Rel-7 Mirror CR of S5-070248, Corresponding Rel-7 CR 32.260 in S5-070247 |

1st Modified Section

### 5.2.3	Subsystem level CDR definitions

This subclause contains the syntax definitions of the CDRs on the subsystem level. At present, only the IM subsystem is defined in 3GPP, thus this subclause comprises the CDR types specified for the IMS in TS 32.260 [20].

#### 5.2.3.1	IMS CDRs

…

SDP-Media-Component ::=  SEQUENCE

{

sDP-Media-Name        	[0] GraphicString OPTIONAL,

sDP-Media-Descriptions	[1] SDP-Media-Description OPTIONAL,

accessCorrelationID			AccessCorrelationID OPTIONAL, 		-- not used in MGCF and BGCF

-- [2] is used by gPRS-Charging-Id

-- [4] is used by accessNetworkChargingIdentifier

authorized-QoS        	[3] GraphicString OPTIONAL

}

…

End of modifications

Annex C (informative):
Change history

| Change history |
| --- |
| Date | TSG # | TSG Doc. | CR | Rev | Subject/Comment | Cat | Old | New |
| Dec 2006 | SA_34 | SP-060719 | 0046 | -- | Corrections of the ICID description - Align with 32.260 | F | 7.0.0 | 7.1.0 |
| Dec 2006 | SA_34 | SP-060719 | 0047 | -- | Add an identifier for the service initiating offline Diameter Accounting | B | 7.0.0 | 7.1.0 |
| Dec 2006 | SA_34 | SP-060719 | 0048 | -- | Add an identifier for the served user in offline Diameter Accounting | B | 7.0.0 | 7.1.0 |
| Dec 2006 | SA_34 | SP-060908 | 0049 | -- | Correction on MMS CDR record type definition | A | 7.0.0 | 7.1.0 |
| Dec 2006 | SA_34 | SP-060908 | 0050 | -- | Correction on MBMS Information ASN.1 syntax - Align with 23.246 | A | 7.0.0 | 7.1.0 |
| Dec 2006 | SA_34 | SP-060908 | 0051 | -- | Correction on Private User Id - Align with 32.260 | A | 7.0.0 | 7.1.0 |
| Dec 2006 | SA_34 | SP-060719 | 0052 | -- | Correction on Service Specific Data | F | 7.0.0 | 7.1.0 |
| Dec 2006 | SA_34 | SP-060714 | 0053 | -- | Introduce support of event based charging for PCC | B | 7.0.0 | 7.1.0 |
| Dec 2006 | SA_34 | SP-060908 | 0054 | 1 | Correction on IMS CDRs - Align with 32.260 | A | 7.0.0 | 7.1.0 |
| Dec 2006 | SA_34 | SP-060713 | 0055 | -- | Add Access Network Charging Identifier | C | 7.0.0 | 7.1.0 |

# Comments

Document number

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least three digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "x WGn" where 
	x = "CT" for TSG CT, "RAN" for TSG RAN, "SA" for TSG SA, "GERAN" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "TSG x". 
Examples: "CT WG4", "RAN WG5", "GERAN WG3", "TSG SA".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, B & C CRs for release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See http://www.3gpp.org/ftp/information/work_plan/ .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2002.

Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory necessary to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.