3GPP TSG-SA5 (Telecom Management)	S5-090514

Meeting SA5#62bis OAM, 14-16 January 2009, Sophia-Antipolis, France

# Source:	Ericsson, T-Mobile

# Title:	pCR to TS 32.425 v0.4.0

# Cell counters for Availability KPI

# Document for:	Approval

Agenda Item:	5.2 UID_390002 Performance measurements for E-UTRAN

1. Introduction

Objective: Propose measurements to support the Availability KPI in [1].

References:

[1] 3GPP TS 32.450 v1.0.0		Key Performance Indicators (KPI) for E-UTRAN: Definitions

[2] 3GPP TS 32.425 v0.4.0		Performance measurements E-UTRAN

[3] 3GPP S5-090513 			Availability Formula in KPI definition for E-UTRAN

2. pCR to TS 32.425 v0.4.0

First modified section

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

- References are either specific (identified by date of publication and/or edition number or version number) or non-specific.

- For a specific reference, subsequent revisions do not apply.

- For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TS 32.101: "Telecommunication management; Principles and high level requirements".

[2]	3GPP TS 32.102: "Telecommunication management; Architecture".

[3]	3GPP TS 32.600: "Telecommunication management; Configuration Management (CM); Concept and high-level requirements".

[5]	3GPP TS 32.401: "Telecommunication management; Performance Management (PM); Concept and requirements".

[6]	3GPP TS 32.404: "Performance Management (PM); Performance measurements - Definitions and template".

[7]	3GPP TS 32.762: "Evolved Universal Terrestrial Radio Access Network (E-UTRAN) Network Resource Model (NRM) Integration Reference Point (IRP): Information Service (IS)".

[8]	3GPP TS 36.331: "Evolved Universal Terrestrial Radio Access (E-UTRA); Radio Resource Control (RRC) protocol specification".

[9]	3GPP TS 36.413: "Evolved Universal Terrestrial Access Network (E-UTRAN); S1 Application Protocol (S1AP)".

[10]	3GPP TS 36.423: "Evolved Universal Terrestrial Radio Access Network (EUTRAN); X2 application protocol (X2AP)".

[11]	TS 36.314, “Evolved Universal Terrestrial Radio Access (E-UTRA);Layer 2 – Measurements (Release 8)”

[12]	3GPP TS 32.450 Telecommunication management; Key Performance Indicators (KPI) for E-UTRAN: Definitions (Release 8)

Next modified section

## 4.5	Radio resource utilization related measurements

### 4.5.x	Cell Unavailable Time

- This measurement provides the length of time the cell has been unavailable for each cause.

- DER (n=1)

- This measurement is obtained by accumulating the time periods when the cell is unavailable per cause. The possible cause could be “manual intervention” and “fault”. The sum of all supported per cause measurements shall equal the total time periods of cell unavailability. In case only a subset of per cause measurements is supported, a sum subcounter will be provided first.

- A single integer value presenting seconds

- The measurement name has the form RRU.CellUnavailableTime.cause.

where cause identifies the cause resuling cell unavailable.

- EutranCell

- Valid for packet switched traffic

- EPS

- This measurement is to support KPI “E-UTRAN Cell Availability” defined in [12].

End of modifications