3GPP TSG-SA5 (Telecom Management)	S5-090551

Meeting SA5#62 bis, 14-16 January 2009, Sophia Antipolis, France

# Source:	Qualcomm Europe

# Title:	Add Specification-level Requirements for Autoconfiguration (Configuration Management Section)

# Document for:	Discussion and Approval

Agenda Item:	6.1 UID_xxxxxx 3G Home NodeB OAM&P Interface Type 1 Management

# 1	Decision/action requested

The group is asked to discuss the configuration management related requirements for 3G HNB Management, and introduce the agreed part into the draft TS 32.XX1.

# 2	References

[1]	3GPP TR 32.821: "Study of Self-Organising Networks (SON) related OAM for Home NodeB (Release 8)"

# 3	Rationale

This contribution is to configuration management requirements to the TS32.xx1.

# 4	Detailed proposal

# Text Proposal for TS 32.xx1

1st Modified Section

## 6.5	Requirements

### 6.5.1	Configuration Management

REQ-HNBOAMP-CM-FUN-001 The HMS shall specify which parameters it needs to be notified of when the HNB changes their values through auto-configuration. The HNB shall notify the HMS of changes in the values of any such autoconfigured parameters.

REQ-HNBOAMP-CM-FUN-003 The HNB shall inform the HMS of its ability to auto-configure parameters or groups of parameters that are relevant to the HMS.

REQ-HNBOAMP-CM-FUN-004 HMS shall be able to specify a value, or a valid range of values, for any parameter that is auto-configurable by the HNB.

End of 1st modifications