3GPP WG SA5-62bis

Minutes for agenda item 5.2 “Performance Measurements for E-UTRAN”

14 January 2009

Tdoc S5-090510 : Handover measurements for E-UTRAN - use cases : Nokia Siemens Networks

Some details had been added to the use cases as an action from a previous meeting.

Motorola suggested adding incoming handover success rate.

On a wide-area it is enough to get outgoing rate otherwise get double-counting.

To analyse localised problems, proposal allows incoming to be enabled (level 2 and 3).

If company can present use cases that indicate need for incoming then these can be considered.

Motorola Suggested removing word “outgoing” as it will be implicit.

Consensus was that “outgoing” needed.

No use case was presented for inter-system case.  It was agreed that this will be provided in a later meeting.

Tdoc S5-090509 : Handover measurements for E-UTRAN : Nokia Siemens Networks

It was agreed to remove editor’s note from sections 4.2.1.1, 4.2.1.2 and 4.2.1.3.

Lucent noted that in 4.2.1.3, IRATHO.Unsucc.Cause may not always be available for inter-RAT.  Proposal was to take these causes from appropriate RAN specification.  This is for FFS along with trigger points.  NSN will add pointer to the specification for inter-RAT.

Marie (Nortel) asked why have failure causes been removed?  This was because it was agreed in Miami meeting to do so.

Ericsson noted that there is a typo in 4.1.3.1 Handover measurements on per cell basis only.  AttOutIntereNBTarget is a typo as would not include intra-eNB.

It was enquired why gap-assisted was included in 4.1.4.3?  It was a requirement from some operators.  NSN agreed to add reference to measurement specs.  NSN also to add reference for DRX.

NSN will put clean-up CR into next meeting.

Changes to this document will be reflected in updates to document 605.

S5-090514 : Cell counters for Availability KPI : Ericsson, T-Mobile

New Tdoc S5-090514 becomes S5-090606.

No objections were received.  Contribution accepted.

S5-090516 : EPS Bearer counters for Accessibility KPI : Ericsson

Motorola asked whether there was a need to split between initial and additional.  This had already been agreed at a previous meeting.

S5-090516 was agreed with no objections

S5-090517 : S1Sig counters for Accessibility KPI : Ericsson

Motorola stated that they did not see the need for this measurement as it is normally 100% successful.  Use cases for KPIs were requested.

This is used in KPIs in submission S5-090515.  Need to discuss the KPI first; if S5-090515 is agreed then S5-090515 is agreed.

Contribution was agreed subject to agreeing the KPIs in S5-090515 (this was subsequently agreed – see below).

S5-090520 : EPS Bearer counters for Retainability KPI : Ericsson

NSN asked why 100ms was used and should it be configurable?  Reason was that E2E RTT for TCP is a little less than 100ms.  Need to provide TCP reference to back up choice of 100ms, then will have new Tdoc number S5-090520.

Agreed in principle subject to new Tdoc being changed acceptably.

S5-090554 : Revision of cause values for counters using S1-protocol procedures : Huawei Technologies

The origin of the causes and the whereabouts of the use cases were requested?  Causes were revealed to come from the RAN spec 36.413.  Author’s belief was that the chosen causes are useful for network management.  Motorola argued that the counters don’t add value, just complexity.  Motorola stated that by restricting the set of counters included in OAM, we are not cooperating with RAN colleagues that designed a set of counters that they deemed useful for RAN diagnostics.  Until we get agreement from all operators on what the subset should be then it is not practical to move forward with a common set of causes.  An LS to RAN would be needed to achieve this.

General agreement with the approach was achieved but no agreement on the chosen causes.  Huawei will make contribution to the next meeting suggesting the groupings.

S5-090556 : Revison of use case for cell bit-rate : Huawei Technologies

Agreed with no objection.

S5-090555 : Revison of cell bit-rate : Huawei Technologies

Motorola questioned why measurements could not be done at PDCP level.

This had already been addressed by a RAN2 response to a previous LS

Some other changes were discussed.  Consensus was to agree submission subject to an update to the document.  This will be prepared for the next meeting.

S5-090557 : Cleanup to active UE counter : Huawei Technologies

Agreed with no objections.

S5-090558 : Cleanup to DL packet delay counter : Huawei Technologies

Agreed with no objections.