3GPP TSG-SA5 (Telecom Management)	S5-101554

Meeting SA5#71, 10-14 May 2010, Montreal, Canada

| CR-Form-v9.6 |
| --- |
| CHANGE REQUEST |
| ( | 32.502 | CR | 0006 | ( rev | - | ( Current version: | 9.1.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network | X | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Correction of UML for ARCF Handling |
| --- | --- |
| Source to WG: ( | Nokia Siemens Networks |
| Source to TSG: ( | SA5 |
| Work item code: ( | OAM9 |  | Date: ( | 14/05/2010 |
| Category: ( | F |  | Release: ( | Rel-9 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) |
| Reason for change: ( | The current UML diagram does not cover one of the options to transport ARCF data, i.e. Bulk CM. |
| Summary of change: ( | Add missing UML diagram, adapt existing UML diagrams, add definitions of new object classes. |
| Consequences if ( not approved: | Bulk CM IRP cannot be used for transport of ARCF data. |
| Clauses affected: ( | 3.2., 5.2, 5.3.5, 5.3.6, 5.3.7, new clauses 5.3.8-13 |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

1st Modified Section

## 3.2	Abbreviations

For the purposes of the present document, the abbreviations given in TR 21.905 [4], TS 32.501 [6] and the following apply. An abbreviation defined in the present document takes precedence over the definition of the same abbreviation, if any, in TR 21.905 [4] and TS 32.501 [6].

DNS	Domain Name System

ARCF	Automatic Radio Configuration Function

Next Modified Section

## 5.2	Class diagram

### 5.2.1	Attributes and relationships

The following UML diagram identifies IOCs providing Self Configuration.

Figure 5.2.1-1: Self Configuration IRP Containment/Naming and Association diagram

The following UML diagrams identify the IOCs required for capturing the ARCF data and their relations to IOCs defined in some NRM IRP specifications.

!!!!!!

Figure 5.2.1-2: Definition of abstract IOCs for ARCF

Figure 5.2.1-3: Definition of ARCF IOCs for usage of for operation resumeScProcessWithArcfData and usage of FT IRP

Figure 5.2.1-4: Definition of ARCF IOCs for usage of Bulk CM IRP

## 5.2.2	Inheritance

The diagram reflects the definitions in the text of the following clauses. In case of conflict text takes precedence.

The following UML diagram describes the inheritance of the objects required for ARCF.

Next Modified Section

### 5.3.5	GenericENBLevelArcfData

#### 5.3.5.1	Definition

This IOC represents the eNB level data defined only for the ARCF Handling.

#### 5.3.5.2	Attributes

| Attribute name | Support Qualifier | Read Qualifier | Write Qualifier |
| --- | --- | --- | --- |
| identifierInArcfContext | M | - | - |

#### 5.3.5.3	Notifications

None.

Next Modified Section

### 5.3.6	GenericEUtranCellLevelArcfData

#### 5.3.6.1	Definition

This IOC represents the E-Utran Cell level data defined only for the ARCF Handling.

#### 5.3.6.2	Attributes

| Attribute name | Support Qualifier | Read Qualifier | Write Qualifier |
| --- | --- | --- | --- |
| identifierInArcfContext | M | - | - |
| cellIdentity | M | - | - |
| pci | M | - | - |
| pciList | CM | - | - |
| qRxLevMin | M | - | - |
| threshXHigh | M | - | - |
| threshXLow | M | - | - |
| maxTxPower | M | - | - |
| tac | CM | - | - |
| qOffSetCell | M | - | - |
| nrt | CM | - | - |

For the conditions relevant to the attributes with CM qualifier see §5.5.1.

#### 5.3.6.3	Notifications

None.

Next Modified Section

### 5.3.7	GenericAntennaLevelArcfData

#### 5.3.7.1	Definition

This IOC represents the Antenna level data defined only for the ARCF Handling.

#### 5.3.7.2	Attributes

| Attribute name | Support Qualifier | Read Qualifier | Write Qualifier |
| --- | --- | --- | --- |
| identifierInArcfContext | M | - | - |
| antennaAzimuth | M | - | - |
| antennaTilt | M | - | - |

#### 5.3.7.3	Notifications

None.

New Section

### 5.3.8	ENBLevelArcfData

### This IOC inherits from IOC GenericENBLevelArcfData. All proporties remain unchanged.

### This IOC is for usage in case the option to transport ARCF via resumeScProcessWithArcfData or via FT IRP is chosen.

### 5.3.9	ENBLevelArcfData2

This IOC inherits from IOC GenericENBLevelArcfData. All proporties remain unchanged.

This IOC is for usage in case the option to transport ARCF data via Bulk CM IRP is chosen.

### 5.3.10	EUtranCellLevelArcfData

This IOC inherits from IOC GeneraicellLevelArcfData. All proporties remain unchanged.

This IOC is for usage in case the option to transport ARCF via resumeScProcessWithArcfData or via FT IRP is chosen.

### 5.3.11	EUtranCellLevelArcfData2

This IOC inherits from IOC GenericCellLevelArcfData. All proporties remain unchanged.

This IOC is for usage in case the option to transport ARCF data via Bulk CM IRP is chosen.

### 5.3.12	AntennaLevelArcfData

This IOC inherits from IOC GenericAntennaLevelArcfData. All proporties remain unchanged.

This IOC is for usage in case the option to transport ARCF via resumeScProcessWithArcfData or via FT IRP is chosen.

### 5.3.13	AntennaLevelArcfData2

This IOC inherits from IOC GenericAntennaLevelArcfData. All proporties remain unchanged.

### This IOC is for usage in case the option to transport ARCF data via Bulk CM IRP is chosen.

End of Modified Sections

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.