3GPP TSG-SA5 (Telecom Management)	S5-101443

Meeting SA5#71, 10 – 14 May 2010, Montreal, CANADA

| CR-Form-v9.6 |
| --- |
| CHANGE REQUEST |
| ( | 32.503 | CR | 0001 | ( rev | - | ( Current version: | 9.0.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network | X | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Alignment of CORBA SS with TS 32.502 for ARCF |
| --- | --- |
| Source to WG: ( | Nokia Siemens Networks |
| Source to TSG: ( | SA5 |
| Work item code: ( | OAM9 |  | Date: ( | 14/05/2010 |
| Category: ( | B |  | Release: ( | Rel-9 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) |
| Reason for change: ( | ARCF allows more efficient OAM. |
| Summary of change: ( | Implementing changes in CR to 32.502 in the CORBA solution set. |
| Consequences if ( not approved: | Unnecessary complex management. Self-configuration not complete. ARCF not possible via CORBA interface |
| Clauses affected: ( | 5.1, 5.2, 5.3, new section 5.4, Annex A.1, Annex A.2, Annex A.3, new Annex A.4 |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

1st Modifications

## 5.1	Operation and Notification mapping

Software Management IRP: IS 3GPP TS (see 3GPP TS 32.502 [7]) defines semantics of operations and notifications visible across the Itf-N.  Table 5.1.1 indicates mapping of these operations and notifications to their equivalents defined in this SS.

Table 5.1.1: Mapping from IS Notification/Operation to SS equivalents

| IS Operation/ notification Self-Configuration IRP: IS 3GPP TS 32.502[7] | SS Method | Qualifier |
| --- | --- | --- |
| listScManagementCapabilities | listScManagementCapabilities | M |
| listScManagementProfiles | listScManagementProfiles | M |
| createScManagementProfile | createScManagementProfile | M |
| deleteScManagementProfile | deleteScManagementProfile | M |
| listScProcesses | listScProcesses | M |
| resumeScProcess | resumeScProcess | M |
| resumeScProcessWithArcfData | resumeScProcessWithArcfData | M |
| swFallback | swFallback | M |
| terminateScManagementProcess | terminateScManagementProcess | M |
| changeScManagementProfile | changeScManagementProfile | O |
| notifyScManagementProfileCreation | notifyScManagementProfileCreation | M |
| notifyScManagementProfileDeletion | notifyScManagementProfileDeletion | M |
| notifyScManagementProcessCreation | notifyScManagementProcessCreation | M |
| notifyScManagementProcessStage | notifyScManagementProcessStage | M |
| notifyScManagementProcessDeletion | notifyScManagementProcessDeletion | M |
| notifyNewScManagementCapabilitiesAvailability | notifyNewScManagementCapabilitiesAvailability | O |
| notifyScManagementProfileChange | notifyScManagementProfileChange | O |

Next modifications

## 5.2	Operation parameter mapping

Reference 3GPP TS 32.302 [6] defines semantics of parameters carried in operations across the Itf-N.  The following set of tables indicate the mapping of these parameters, as per operation, to their equivalents defined in this SS.

Table 5.2-1: Mapping from IS listScManagementCapabilities parameters to SS equivalents

| IS Operation parameter | SS Method parameter | Qualifier |
| --- | --- | --- |
| result | Exceptions: SelfConfIRPConstDefs::ListScManagementCapabilities, GenericIRPManagementSystem::ParameterNotSupported, GenericIRPManagementSystem::InvalidParameter, GenericIRPManagementSystem::ValueNotSupported, GenericIRPManagementSystem::OperationNotSupported | M |

For all other parameters see TS 32.533 [11] mapping from IS listSwMCapabilities parameters to SS equivalents

Table 5.2-2: Mapping from IS listScManagementProfiles parameters to SS equivalents

| IS Operation parameter | SS Method parameter | Qualifier |
| --- | --- | --- |
| result | Exceptions: SelfConfIRPConstDefs::ListScManagementProfile, GenericIRPManagementSystem::ParameterNotSupported, GenericIRPManagementSystem::InvalidParameter, GenericIRPManagementSystem::ValueNotSupported, GenericIRPManagementSystem::OperationNotSupported | M |

For all other parameters see TS 32.533 [11] mapping from IS listSwMProfiles parameters to SS equivalents

Table 5.2-3: Mapping from IS createScManagementProfile parameters to SS equivalents

| IS Operation parameter | SS Method parameter | Qualifier |
| --- | --- | --- |
| result | Exceptions: SelfConfIRPConstDefs::CreateScManagementProfile, GenericIRPManagementSystem::ParameterNotSupported, GenericIRPManagementSystem::InvalidParameter, GenericIRPManagementSystem::ValueNotSupported, GenericIRPManagementSystem::OperationNotSupported | M |

For all other parameters see TS 32.533 [11] mapping from IS createSwMProfile parameters to SS equivalents

Table 5.2-4: Mapping from IS deleteScManagementProfile parameters to SS equivalents

| IS Operation parameter | SS Method parameter | Qualifier |
| --- | --- | --- |
| result | Exceptions: SelfConfIRPConstDefs::DeleteScManagementProfile, GenericIRPManagementSystem::ParameterNotSupported, GenericIRPManagementSystem::InvalidParameter, GenericIRPManagementSystem::ValueNotSupported, GenericIRPManagementSystem::OperationNotSupported | M |

For all other parameters see TS 32.533 [11] mapping from IS deleteSwMProfile parameters to SS equivalents

Table 5.2-5: Mapping from IS listScManagementProcesses parameters to SS equivalents

| IS Operation parameter | SS Method parameter | Qualifier |
| --- | --- | --- |
| result | Exceptions: SelfConfIRPConstDefs::ListScManagementProcesses, GenericIRPManagementSystem::ParameterNotSupported, GenericIRPManagementSystem::InvalidParameter, GenericIRPManagementSystem::ValueNotSupported, GenericIRPManagementSystem::OperationNotSupported | M |

For all other parameters see TS 32.533 [11] mapping from IS listSwMProcesses parameters to SS equivalents

Table 5.2-6: Mapping from IS resumeScManagementProcess parameters to SS equivalents

| IS Operation parameter | SS Method parameter | Qualifier |
| --- | --- | --- |
| result | Exceptions: SelfConfIRPConstDefs::ResumeScManagementProcess, GenericIRPManagementSystem::ParameterNotSupported, GenericIRPManagementSystem::InvalidParameter, GenericIRPManagementSystem::ValueNotSupported, GenericIRPManagementSystem::OperationNotSupported | M |

For all other parameters see TS 32.533 [11] mapping from IS resumeSwMProcess parameters to SS equivalents

Table 5.2-7: Mapping from IS swFallback parameters to SS equivalents

| IS Operation parameter | SS Method parameter | Qualifier |
| --- | --- | --- |
| result | Exceptions: SelfConfIRPConstDefs::SwFallback, GenericIRPManagementSystem::ParameterNotSupported, GenericIRPManagementSystem::InvalidParameter, GenericIRPManagementSystem::ValueNotSupported, GenericIRPManagementSystem::OperationNotSupported | M |

For all other parameters see TS 32.533 [11] mapping from IS swFallback parameters to SS equivalents

Table 5.2-8: Mapping from IS terminateScManagementProcess parameters to SS equivalents

| IS Operation parameter | SS Method parameter | Qualifier |
| --- | --- | --- |
| result | Exceptions: SelfConfIRPConstDefs::TerminateScManagementProcess, GenericIRPManagementSystem::ParameterNotSupported, GenericIRPManagementSystem::InvalidParameter, GenericIRPManagementSystem::ValueNotSupported, GenericIRPManagementSystem::OperationNotSupported | M |

For all other parameters see TS 32.533 [11] mapping from IS terminateSwMProcess parameters to SS equivalents

Table 5.2-9: Mapping from IS changeScManagementProfile parameters to SS equivalents

| IS Operation parameter | SS Method parameter | Qualifier |
| --- | --- | --- |
| result | Exceptions: SelfConfIRPConstDefs::CreateScManagementProfile, GenericIRPManagementSystem::ParameterNotSupported, GenericIRPManagementSystem::InvalidParameter, GenericIRPManagementSystem::ValueNotSupported, GenericIRPManagementSystem::OperationNotSupported | M |

For all other parameters see TS 32.533 [11] mapping from IS changeSwMProfile parameters to SS equivalents

Table 5.2-10: Mapping from IS resumeScProcessWithArcfData parameters to SS equivalents

| IS Operation parameter | SS Method parameter | Qualifier |
| --- | --- | --- |
| valuesOfNeededRadioParameter | SelfConfIRPConstDefs::ValuesOfNeededRadioParameterOrNull | M |
| fileLocation | SelfConfIRPConstDefs::FileLocationOrNull | M |
| validationError | SelfConfIRPConstDefs::ValidationErrorInfoOrNull | CM |
| result | SelfConfIRPConstDefs::ResumeScProcessWithArcfDataResult SelfConfIRPConstDefs::ResumeScManagementProcessWithArcfData, GenericIRPManagementSystem::ParameterNotSupported, GenericIRPManagementSystem::InvalidParameter, GenericIRPManagementSystem::ValueNotSupported, GenericIRPManagementSystem::OperationNotSupported | M |

For all other parameters see TS 32.533 [11] mapping from IS resumeSwMProcess parameters to SS equivalents

Next modifications

## 5.3	Notification parameter mapping

Reference 3GPP TS 32.502 [7] defines semantics of parameters carried in notifications. The following tables indicate the mapping of these parameters to their SS equivalents."

The following tables indicate the mapping of these parameters to their OMG CORBA Structured Event (defined in OMG Notification Service [8]) equivalents. The composition of OMG Structured Event, as defined in the OMG Notification Service [8], is:

Header

Fixed Header

domain_name

type_name

event_name

Variable Header

Body

filterable_body_fields

remaining_body

The following tables list all OMG Structured Event attributes in the second column. The first column identifies the Software Management IRP: IS [7] defined notification parameters.

Table 5.3.1: Mapping for notifyScManagementProfileCreation

See TS 32.533 [11] mapping from IS notifySwMProfileCreation

Table 5.3.2: Mapping for notifyScManagementProfileDeletion

See TS 32.533 [11] mapping from IS notifySwMProfileDeletion

Table 5.3.3: Mapping for notifyScProcessCreation

See TS 32.533 [11] mapping from IS notifySwMProcessCreation

Table 5.3.4: Mapping for notifyScProcessStage

See TS 32.533 [11] mapping from IS notifySwMProcessStage and in addition:

| IS Parameters | <SS> Parameters | Qualifier | Comment |
| --- | --- | --- | --- |
| listOfNeededRadioParameters | SelfConfIRPConstDefs::ListOfNeededRadioParameters | O |  |
| inputForRadioParameterDetermination | SelfConfIRPConstDefs::InputForRadioParameterDetermination | O |  |

Table 5.3.5: Mapping for notifyScProcessDeletion

See TS 32.533 [11] mapping from IS notifySwMProcessDeletion

Table 5.3.6: Mapping for notifyNewScManagementCapabilityAvailability

| IS Parameters | <SS> Parameters | Qualifier | Comment |
| --- | --- | --- | --- |
| id | SwMIRPConstDefs::Id | M |  |
| nEInformation | SwMIRPConstDefs::NEInformation | M |  |
| stepsAndOfferedStopPointList | SwMIRPConstDefs::StepsAndOfferedStopPointList | M |  |
| offeredFinalAdministrativeStateInformation | SwMIRPConstDefs:: OfferedFinalAdministrativeStateInformation | M |  |
| swVersionToBeInstalledOfferList | SwMIRPConstDefs:: SwVersionToBeInstalledOfferListConditional | C |  |

Table 5.3.7: Mapping for notifyScManagementProfileChange

See TS 32.533 [11] mapping from IS notifySwMProfileChange

Next modifications (new section)

## 5.4	Information Object Class (IOC) mapping

### 5.4.1	IOC ENBLevelArcfData

| Attribute of IOC ENBFunction in 3GPP TS 32.762 [2] | SS Attribute | SS Type | Support Qualifier | Read Qualifier | Write Qualifier |
| --- | --- | --- | --- | --- | --- |
| identifierInArcfContext | identifierInArcfContext | string | M | - | - |

### 5.4.1	IOC EUtranCellLevelArcfData

| Attribute of IOC ENBFunction in 3GPP TS 32.762 [2] | SS Attribute | SS Type | Support Qualifier | Read Qualifier | Write Qualifier |
| --- | --- | --- | --- | --- | --- |
| identifierInArcfContext | identifierInArcfContext | string | M | - | - |
| cellIdentity | cellIdentity | GenericNetworkResourcesIRPSystem:: AttributeTypes::MOReferenceSet | M | - | M |
| pci | pci | GenericNetworkResourcesIRPSystem:: AttributeTypes::MOReferenceSet | M | - | M |
| pciList | pciList | GenericNetworkResourcesIRPSystem:: AttributeTypes::MOReferenceSet | CM | - | M |
| qRxLevMin | qRxLevMin | SelfConfIRPConstDefs::QRxLevMin | M | - | - |
| threshXHigh | threshXHigh | SelfConfIRPConstDefs::ThreshXHigh | M | - | - |
| threshXLow | threshXLow | SelfConfIRPConstDefs::ThreshXLow | M | - | - |
| maxTxPower | maxTxPower | GenericNetworkResourcesIRPSystem:: AttributeTypes::MaximumTransmissionPower | M | - | - |
| tac | tac | GenericNetworkResourcesIRPSystem:: AttributeTypes::Tac | CM | - | - |
| qOffSetCell | qOffSetCell | SelfConfIRPConstDefs::QOffSetCell | M | - | - |
| nrt | nrt | SelfConfIRPConstDefs::Nrt | CM | - | - |

### 5.4.1	IOC AntennaLevelArcfData

| Attribute of IOC ENBFunction in 3GPP TS 32.762 [2] | SS Attribute | SS Type | Support Qualifier | Read Qualifier | Write Qualifier |
| --- | --- | --- | --- | --- | --- |
| identifierInArcfContext | identifierInArcfContext | string | M | - | - |
| antennaAzimuth | antennaAzimuth | SelfConfIRPConstDefs::AntennaAzimuth | M | - | - |
| antennaTilt | antennaTilt | SelfConfIRPConstDefs::AntennaTilt | M | - | - |

Next modifications

# A.1	IDL specification (file name "SelfConfIRPConstDefs.idl")

// File: SelfConfIRPConstDefs.idl

#ifndef _SELF_CONF_IRP_CONST_DEFS_IDL_

#define _SELF_CONF_IRP_CONST_DEFS_IDL_

#include <KernelCmConstDefs.idl>

#include <NotificationIRPConstDefs.idl>

#include <SwMIRPConstDefs.idl>

#include <ManagedGenericIRPConstDefs.idl>

#include "GenericNetworkResourcesNRMDefs.idl"

#include "EUtranNetworkResourcesNRMDefs.idl"

// This statement must appear after all include statements

#pragma prefix "3gppsa5.org"

/* ## Module: SelfConfIRPConstDefs */

module SelfConfIRPConstDefs

{

/*******************************************************************/

/* definition of types used in operations for Self-Configuration : */

/*******************************************************************/

enum ResumeScProcessWithArcfDataResult { SUCCESS, FAILURE, VALIDATION_ERROR };

struct ValueOfNeededRadioParameter

{

string radioParameterName;

any radioParameterValue;

};

typedef sequence<ValueOfNeededRadioParameter> ValuesOfNeededRadioParameter;

/* ValuesOfNeededRadioParameterOrNull is a type which can contain information or not.

If the discriminator is true the information is present.

Otherwise the value is null.

*/

union ValuesOfNeededRadioParameterOrNull switch (boolean)

{

case TRUE: ValuesOfNeededRadioParameter value;

};

/* FileLocationOrNull is a type which can contain information or not.

If the discriminator is true the information is present.

Otherwise the value is null.

*/

union FileLocationOrNull switch (boolean)

{

case TRUE: SwmIRPConstDefs::FileLocation value;

};

enum ValidationErrorReason

{

ParameterNotSupported,

InvalidParameter,

ValueNotSupported,

MissingParameterValue,

ConflictingParamterValue,

SemanticsError,

OtherError

};

struct ParameterValidationError

{

string radioParameterName;

ValidationErrorReason validationErrorReason  ;

};

typedef sequence<ParameterValidationError> ValidationErrorInfo;

/* ValidationErrorOrNull is a type which can contain information or not.

If the discriminator is true the information is present.

Otherwise the value is null.

*/

union ValidationErrorOrNull switch (boolean)

{

case TRUE: ValidationError value;

};

typedef IdentifierInArcfContext;

typedef long CellIdentity;

typedef short Pci;

typedef EUtranNetworkResourcesNRMDefs::PciListType PciListType

enum Q-offset { dB-24, dB-22, dB-20, dB-18, dB-16, dB-14, dB-12, dB-10, dB-8, dB-6, dB-5, dB-4, dB-3, dB-2, dB-1, dB0, dB1, dB2, dB3, dB4, dB5, dB6, dB8, dB10, dB12, dB14, dB16, dB18, dB20, dB22, dB24 };

typedef short Q-RxLevMin;

typedef short ReselectionThreshold;

typedef short ThreshX-High;

typedef short ThreshX-Low;

typedef short MaxTxPower;

typedef short Tac;

typedef short AntennaAzimuth;

typedef short AntennaTilt;

struct NrtEntry

{

long tci;

boolean isRemoveAllowed;

boolean isHOAllowed;

};

typedef sequence<NrtEntry> Nrt;

/* all other types used in  operations are imported from 32.533 */

/******************************************************************/

/* definition of types in notifications for self-configuration :  */

/******************************************************************/

enum TriggerForDeletion { IRP_AGENT_TERMINATION, IRP_MANAGER_TERMINATION, SELF_CONFIGURATION_SUCCESFULLY_CONCLUDED };

typedef string NeededRadioParameter;

typedef sequence<NeededRadioParameter> ListOfNeededRadioParameters;

/* ListOfNeededRadioParameters is a type representing an optional parameter.

If the discriminator is true, then the value is present.

Otherwise the value is absent.

*/

union ListOfNeededRadioParameters switch (boolean)

{

case TRUE: ListOfNeededRadioParameters value;

};

typedef string SingleInputForRadioParameterDetermination;

typedef sequence<SingleInputForRadioParameterDetermination> InputForRadioParameterDetermination;

/* InputForRadioParameterDetermination is a type of a parameter which can be present or not.

If the discriminator is true the value is present.

Otherwise the value is null.

*/

union InputForRadioParameterDetermination switch (boolean)

{

case TRUE: InputForRadioParameterDetermination value;

};

interface AttributeNameValue

{

const string ID = "ID";

const string NE_INFORMATION = "NE_INFORMATION";

const string STEPS_AND_OFFERED_STOP_POINT_LIST = "STEPS_AND_OFFERED_STOP_POINT_LIST";

const string OFFERED_FINAL_ADMINISTRATIVE_STATE_INFORMATION = "OFFERED_FINAL_ADMINISTRATIVE_STATE_INFORMATION";

const string SW_VERSION_TO_BE_INSTALLED_OFFER_LIST = "SW_VERSION_TO_BE_INSTALLED_OFFER_LIST";

const string LIST_OF_NEEDED_RADIO_PARAMETERS = "LIST_OF_NEEDED_RADIO_PARAMETERS";

const string INPUT_FOR_RADIO_PARAMETER_DETERMINATION = "INPUT_FOR_RADIO_PARAMETER_DETERMINATION";

const string CELL_IDENTITY= "CELL_IDENTITY";

const string PCI= "PCI";

const string PCI_LIST= "PCI_LIST";

const string Q-RX_LEV_MIN= "Q-RX_LEV_MIN";

const string THRESHX-HIGH= "THRESHX-HIGH";

const string THRESHX-LOW= "THRESHX-LOW";

const string MAX_TX_POWER= "MAX_TX_POWER";

const string TAC= "TAC";

const string Q-OFFSET_CELL= "Q-OFFSET_CELL";

const string NRT= "NRT";

const string ANTENNA_AZIMUTH= "ANTENNA_AZIMUTH";

const string ANTENNA_TILT= "ANTENNA_TILT";

};

};

#endif // _SELF_CONF_IRP_CONST_DEFS_IDL_

Next modifications

# A.2	IDL specification (file name "SelfConfIRPSystem.idl")

//File: SelfConfIRPSystem.idl

#ifndef _SELF_CONF_IRP_SYSTEM_IDL_

#define _SELF_CONF_IRP_SYSTEM_IDL_

#include <SelfConfIRPConstDefs.idl>

#include <SwMIRPConstDefs.idl>

#include <GenericIRPManagementSystem.idl>

// This statement must appear after all include statements

#pragma prefix "3gppsa5.org"

/* ## Module: SelfConfIRPSystem */

module SelfConfIRPSystem

{

/*

If the system fails to complete an operation, then it can provide a reason

to qualify the exception. The semantics carried in this reason are outside

the scope of the present document.

*/

exception ListScManagementCapabilities { string reason; };

exception ListScManagementProfiles { string reason; };

exception CreateScManagementProfile { string reason; };

exception DeleteScManagementProfile { string reason; };

exception ListScProcesses { string reason; };

exception ResumeScProcess { string reason; };

exception ResumeScProcessWithArcfData { string reason; };

exception SwFallback { string reason; };

exception TerminateScProcess { string reason; };

exception ChangeScManagementProfile { string reason; };

interface SelfConfIRPOperations_1

{

/* for the purpose of this operation see 3GPP TS 32.502 */

SwMIRPConstDefs::Result listScManagementCapabilities

(

in SwMIRPConstDefs::NEInformationOpt nEInformation,

out SwMIRPConstDefs::CapabilitiesList capabilitiesList

)

raises

(

ListScManagementCapabilities,

GenericIRPManagementSystem::ParameterNotSupported,

GenericIRPManagementSystem::InvalidParameter,

GenericIRPManagementSystem::ValueNotSupported,

GenericIRPManagementSystem::OperationNotSupported

);

/* for the purpose of this operation see 3GPP TS 32.502 */

SwMIRPConstDefs::Result listScProfiles

(

in SwMIRPConstDefs::NEInformationOpt nEInformation,

out SwMIRPConstDefs::ProfileList profileList

)

raises

(

ListScProfiles,

GenericIRPManagementSystem::ParameterNotSupported,

GenericIRPManagementSystem::InvalidParameter,

GenericIRPManagementSystem::ValueNotSupported,

GenericIRPManagementSystem::OperationNotSupported

);

/* for the purpose of this operation see 3GPP TS 32.502 */

SwMIRPConstDefs::Result createScManagementProfile

(

in SwMIRPConstDefs::IdOpt id,

in SwMIRPConstDefs::NEInformation nEInformation,

in SwMIRPConstDefs::SwVersionToBeInstalledOpt swVersionToBeInstalled,

in SwMIRPConstDefs::StepsAndSelectedStopPointList stepsAndSelectedStopPointList,

in SwMIRPConstDefs::SelectedFinalAdministrativeState selectedFinalAdministrativeState

)

raises

(

CreateScManagementProfile,

GenericIRPManagementSystem::ParameterNotSupported,

GenericIRPManagementSystem::InvalidParameter,

GenericIRPManagementSystem::ValueNotSupported,

GenericIRPManagementSystem::OperationNotSupported

);

/* for the purpose of this operation see 3GPP TS 32.502 */

SwMIRPConstDefs::Result deleteScManagementProfile

(

in SwMIRPConstDefs::Id id

)

raises

(

DeleteScManagementProfile,

GenericIRPManagementSystem::ParameterNotSupported,

GenericIRPManagementSystem::InvalidParameter,

GenericIRPManagementSystem::ValueNotSupported,

GenericIRPManagementSystem::OperationNotSupported

);

/* for the purpose of this operation see 3GPP TS 32.502 */

SwMIRPConstDefs::Result listScProcesses

(

in SwMIRPConstDefs::NEIdentificationOpt nEIdentification,

out SwMIRPConstDefs::ProcessList processList

)

raises

(

ListScProcesses,

GenericIRPManagementSystem::ParameterNotSupported,

GenericIRPManagementSystem::InvalidParameter,

GenericIRPManagementSystem::ValueNotSupported,

GenericIRPManagementSystem::OperationNotSupported

);

/* for the purpose of this operation see 3GPP TS 32.502 */

SwMIRPConstDefs::Result resumeScProcess

(

in SwMIRPConstDefs::Id id

)

raises

(

ResumeScProcess,

GenericIRPManagementSystem::ParameterNotSupported,

GenericIRPManagementSystem::InvalidParameter,

GenericIRPManagementSystem::ValueNotSupported,

GenericIRPManagementSystem::OperationNotSupported

);

/* for the purpose of this operation see 3GPP TS 32.502 */

SelfConfIRPConstDefs::ResumeScProcessWithArcfDataResult resumeScProcessWithArcfData

(

in SwMIRPConstDefs::Id id,

in SelfConfIRPConstDefs::ListOfNeededRadioParameters listOfNeededRadioParameters,

in SelfConfIRPConstDefs::InputForRadioParameterDetermination inputForRadioParameterDetermination,

out SelfConfIRPConstDefs::ValidationErrorInfoOrNull validationError

)

raises

(

ResumeScProcessWithArcfData,

GenericIRPManagementSystem::ParameterNotSupported,

GenericIRPManagementSystem::InvalidParameter,

GenericIRPManagementSystem::ValueNotSupported,

GenericIRPManagementSystem::OperationNotSupported

);

/* for the purpose of this operation see 3GPP TS 32.502 */

SwMIRPConstDefs::Result swFallback

(

in SwMIRPConstDefs::Filter filter,

out SwMIRPConstDefs::NEList nEList

)

raises

(

SwFallback,

GenericIRPManagementSystem::ParameterNotSupported,

GenericIRPManagementSystem::InvalidParameter,

GenericIRPManagementSystem::ValueNotSupported,

GenericIRPManagementSystem::OperationNotSupported

);

/* for the purpose of this operation see 3GPP TS 32.502 */

SwMIRPConstDefs::Result terminateScProcess

(

in SwMIRPConstDefs::Id id

)

raises

(

TerminateScProcess,

GenericIRPManagementSystem::ParameterNotSupported,

GenericIRPManagementSystem::InvalidParameter,

GenericIRPManagementSystem::ValueNotSupported,

GenericIRPManagementSystem::OperationNotSupported

);

};

interface SelfConfIRPOperations_2

{

/* for the purpose of this operation see 3GPP TS 32.502 */

SwMIRPConstDefs::Result changeScManagementProfile

(

in SwMIRPConstDefs::Id id,

in SwMIRPConstDefs::NEInformation nEInformation,

in SwMConfIRPConstDefs::SwVersionToBeInstalledOpt swVersionToBeInstalled,

in SwMConfIRPConstDefs::StepsAndSelectedStopPointList stepsAndSelectedStopPointList,

in SwMIRPConstDefs::SelectedFinalAdministrativeState selectedFinalAdministrativeState

)

raises

(

ChangeScManagementProfile,

GenericIRPManagementSystem::ParameterNotSupported,

GenericIRPManagementSystem::InvalidParameter,

GenericIRPManagementSystem::ValueNotSupported,

GenericIRPManagementSystem::OperationNotSupported

);

};

};

#endif // _SELF_CONF_IRP_SYSTEM_IDL_

Next modifications

# A.3	IDL specification (file name "SelfConfIRPNotifications.idl")

//File: SelfConfIRPNotifications.idl

#ifndef _SELF_CONF_IRP_NOTIFICATIONS_IDL_

#define _SELF_CONF_IRP_NOTIFICATIONS_IDL_

#include <SelfConfIRPConstDefs.idl>

#include <SwMIRPConstDefs.idl>

#include <NotificationIRPNotifications.idl>

#include <SwMIRPNotifications.idl>

// This statement must appear after all include statements

#pragma prefix "3gppsa5.org"

/* ## Module: SelfConfIRPNotifications

This contains the specification of notifications of Software Management.

==========================================================================

*/

module SelfConfIRPNotifications

{

/* Constant definitions for the notifyScManagementProfileCreation notification */

interface NotifyScManagementProfileCreation: SwMIRPNotifications::NotifySwMProfileCreation

{

const string EVENT_TYPE = "notifyScManagementProfileCreation";

};

/* Constant definitions for the notifyScManagementProfileDeletion notification */

interface NotifyScManagementProfileDeletion: SwMIRPNotifications::NotifySwMProfileDeletion

{

const string EVENT_TYPE = "notifyScManagementProfileDeletion";

};

/* Constant definitions for the notifyScProcessCreation notification */

interface NotifyScProcessCreation: SwMIRPNotifications::NotifySwMProcessCreation

{

const string EVENT_TYPE = "notifyScProcessCreation";

};

/* Constant definitions for the notifyScProcessStage notification */

interface NotifyScProcessStage: SwMIRPNotifications::NotifySwMProcessStage

{

const string EVENT_TYPE = "notifyScProcessStage";

/**

* This constant defines the name of the listOfNeededRadioParameters property,

* which is transported in the remaining_body.

* The data type for the value of this property is

* SelfConfIRPConstDefs::ListOfNeededRadioParameters.

*/

const string ID =

SelfConfIRPConstDefs::AttributeNameValue::LIST_OF_NEEDED_RADIO_PARAMETERS;

/**

* This constant defines the name of the inputForRadioParameterDetermination property,

* which is transported in the remaining_body.

* The data type for the value of this property is

* SelfConfIRPConstDefs::InputForRadioParameterDetermination.

*/

const string ID =

SelfConfIRPConstDefs::AttributeNameValue::INPUT_FOR_RADIO_PARAMETER_DETERMINATION;

};

/* Constant definitions for the notifyScProcessDeletion notification */

interface NotifyScProcessDeletion: SwMIRPNotifications::NotifyScProcessDeletion

{

const string EVENT_TYPE = "notifyScProcessDeletion";

};

/* Constant definitions for the notifyNewScManagementCapabilityAvailability notification */

interface NotifyNewScManagementCapabiliyAvailability: NotificationIRPNotifications::Notify

{

const string EVENT_TYPE = "notifyNewScManagementCapabilityAvailability";

/**

* This constant defines the name of the id property,

* which is transported in the filterable_body_fields.

* The data type for the value of this property is

* SwMIRPConstDefs::Id.

*/

const string ID =

SelfConfIRPConstDefs::AttributeNameValue::ID;

/**

* This constant defines the name of the nEInformation property,

* which is transported in the filterable_body_fields.

* The data type for the value of this property is

* SwMIRPConstDefs::NEInformation.

*/

const string ID =

SelfConfIRPConstDefs::AttributeNameValue::NE_INFORMATION;

/**

* This constant defines the name of the stepsAndOfferedStopPointList property,

* which is transported in the remaining_body.

* The data type for the value of this property is

* SwMIRPConstDefs::StepsAndOfferedStopPointList.

*/

const string ID =

SelfConfIRPConstDefs::AttributeNameValue::STEPS_AND_OFFERED_STOP_POINT_LIST;

/**

* This constant defines the name of the offeredFinalAdministrativeStateInformation property,

* which is transported in the remaining_body.

* The data type for the value of this property is

* SwMIRPConstDefs::OfferedFinalAdministrativeStateInformation.

*/

const string ID =

SelfConfIRPConstDefs::AttributeNameValue::OFFERED_FINAL_ADMINISTRATIVE_STATE_INFORMATION;

/**

* This constant defines the name of the swVersionToBeInstalledOfferList property,

* which is transported in the remaining_body.

* The data type for the value of this property is

* SwMIRPConstDefs::SwVersionToBeInstalledOfferListOpt.

*/

const string ID =

SelfConfIRPConstDefs::AttributeNameValue::SW_VERSION_TO_BE_INSTALLED_OFFER_LIST;

};

/* Constant definitions for the notifyScManagementProfileChange notification */

interface NotifyScManagementProfileChange: SwMIRPNotifications::NotifySwMProfileChange

{

const string EVENT_TYPE = "notifyScManagementProfileChange";

};

};

#endif // _SELF_CONF_IRP_NOTIFICATIONS_IDL_

Next modifications (new Annex)

Annex D (normative):
CORBA IDL, NRM definitions

//File:ArcfNRMDefs.idl

#ifndef _ArcfNRMDEFS_IDL_

#define _ArcfNRMDEFS_IDL_

#include "GenericNetworkResourcesNRMDefs.idl"

#include "EUtranNetworkResourcesNRMDefs.idl"

#pragma prefix "3gppsa5.org"

/**

* This module defines constants for each MO class name and

* the attribute names for each defined MO class.

*/

module ArcfNRMDefs

{

/*

* Definitions for MO class ENBLevelArcfData

*/

interface ENBLevelArcfData: GenericNetworkResourcesNRMDefs::Top

{

const string id = "id";

const string CLASS = "ENBLevelArcfData";

// Attribute Names

//

const string identifierInArcfContext= "identifierInArcfContext";

};

/*

* Definitions for MO class EUtranCellLevelArcfData

*/

interface EUtranCellLevelArcfData: GenericNetworkResourcesNRMDefs::Top

{

const string CLASS = "EUtranCellLevelArcfData";

// Attribute Names

//

const string id = "id";

const string identifierInArcfContext= "identifierInArcfContext";

const string cellIdentity = "cellIdentity";

const string pci = "pci";

const string pciList = "pciList";

const string qRxLevMin = "qRxLevMin";

const string threshXHigh = "threshXHigh";

const string threshXLow = "threshXLow";

const string maxTxPower = "maxTxPower";

const string qOffSetCell = "qOffSetCell";

const string tac = "tac";

const string nrt = "nrt";

};

/*

* Definitions for MO class AntennaLevelArcfData

*/

interface AntennaLevelArcfData: GenericNetworkResourcesNRMDefs::Top

{

const string CLASS = "AntennaLevelArcfData";

// Attribute Names

//

const string id = "id";

const string identifierInArcfContext= "identifierInArcfContext";

const string antennaAzimuth = "antennaAzimuth";

const string antennaTilt = "antennaTilt";

};

};

#endif // _EUTRANNETWORKRESOURCESNRMDEFS_IDL_

End of modifications

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.