3GPP TSG-SA5 (Telecom Management)	S5-101446

Meeting SA5#71, 10– 14 May 2010, Montreal, Canada	revision of S5-101198

| CR-Form-v9.6 |
| --- |
| CHANGE REQUEST |
| ( | 32.507 | CR | 0094 | ( rev | - | ( Current version: | 9.0.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network | X | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Alignment of SOAP SS with TS 32.507 for ARCF |
| --- | --- |
| Source to WG: ( | Nokia Siemens Networks |
| Source to TSG: ( | SA5 |
| Work item code: ( | OAM9 |  | Date: ( | 14/05/2010 |
| Category: ( | B |  | Release: ( | Rel-9 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) |
| Reason for change: ( | WSDL definitions do net yet support definitions for ARCF. |
| Summary of change: ( | WSDL definitions for ARCF added. |
| Consequences if ( not approved: | No SOAP support for ARCF |
| Clauses affected: ( | 4.1, 5.1, 5.2.7 5.2.8 5.2.9, Annex A |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

1st Modifications

## 4.1 General

Figure 4.1:  Self-Configuration of Network Elements IRP SOAP Solution Set WSDL structure

Next modifications

## Operation and notification mapping

Table 5.1: Mapping from IS Operation to SS Equivalents

| IS Operation in 3GPP TS 32.502 [4] | SS: Operation for WSDL port type and WSDL binding | SS: Port of SCIRPService | Qualifier |
| --- | --- | --- | --- |
| listScManagementCapabilities | listScManagementCapabilities (note 1) | SCIRPOperation1 | M |
| listScManagementProfiles | listScManagementProfiles (note 1) | SCIRPOperation1 | M |
| createScManagementProfile | createScManagementProfile (note1) | SCIRPOperation1 | M |
| deleteScManagementProfile | deleteScManagementProfile (note1) | SCIRPOperation1 | M |
| listScProcesses | listScProcesses (note1) | SCIRPOperation1 | M |
| resumeScProcess | resumeScProcess (note1) | SCIRPOperation1 | M |
| resumeScProcessWithArcfData | resumeScProcessWithArcfData(note1) | SCIRPOperation1 | M |
| terminateScProcess | terminateScProcess (note1) | SCIRPOperation1 | M |
| changeScManagementProfile | changeScManagementProfile (note1) | SCIRPOperation1 | O |
| notifyScManagementProfileCreation | notify (note 2) | NotificationIRPNtfPort | M |
| notifyScManagementProfileDeletion | notify (note 2) | NotificationIRPNtfPort | M |
| notifyScProcessCreation | notify (note 2) | NotificationIRPNtfPort | M |
| notifyScProcessStage | notify (note 2) | NotificationIRPNtfPort | M |
| notifyScProcessDeletion | notify (note 2) | NotificationIRPNtfPort | M |
| notifyNewScManagementCapabilityAvailability | notify (note 2) | NotificationIRPNtfPort | M |
| notifyScManagementProfileChange | notify (note 2) | NotificationIRPNtfPort | O |
| getIRPVersion (note 3) | See TS 32.317 [8] | GenericIRPPort | M |
| getOperationProfile (note 3) | See TS 32.317 [8] | GenericIRPPort | O |
| getNotificationProfile (note 3) | See TS 32.317 [8] | GenericIRPPort | O |
| NOTE 1: The operation is under the port type SCIRPSystem:SCIRPPortType and under the binding SCIRPSystem:SCIRPBinding. |
| NOTE 2: The IS equivalent maps to an XML definition specified in 3GPP TS 32.505 [5], and this being an input parameter to the operation notify under the port type ntfIRPNtfSystem:NotificationIRPNtf and under the binding ntfIRPNtfSystem:NotificationIRPNtf of 3GPP TS 32.307 [10]. This binding is linked to a port of the SCIRPService as indicated in the table above.. |
| NOTE 3: The IS operation is inherited from the ManagedGenericIRP IOC specified in 3GPP TS 32.312 [7]. This inheritance is by the SelfConfigurationIRP IOC of 3GPP TS 32.502 [4] inheriting from the ManagedGenericIRP IOC. The corresponding binding is linked to a port of the SCIRPService as indicated in the table above. |

Next modifications

## Operation resumeScProcessWithArcfData

## Input parameters

Table 5.2.7.1: Mapping from IS resumeScProcessWithArcfData input parameters to SS equivalents

| IS Operation parameter | SS WSDL type sub-element used in corresponding input message under corresponding port type operation as indicated in Table 5.1 | Qualifier |
| --- | --- | --- |
| valuesOfNeededRadioParameter | valuesOfNeededRadioParameter | M |
| fileLocation | fileLocation | M |

## Output parameters

Table 5.2.7.2: Mapping from IS resumeScProcessWithArcfData output parameters to SS equivalents

| IS Operation parameter | SS WSDL type sub-element used in corresponding input message under corresponding port type operation as indicated in Table 5.1 | Qualifier |
| --- | --- | --- |
| validationErrorInfo | validationErrorInfo | CM |

## Operation terminateScProcess

## Input parameters

Table 5.2.8.1: Mapping from IS terminateScProcess input parameters to SS equivalents

| IS Operation parameter | SS WSDL type sub-element used in corresponding input message under corresponding port type operation as indicated in Table 5.1 | Qualifier |
| --- | --- | --- |
| id | id | M |

## Output parameters

Table 5.2.8.2: Mapping from IS terminateScProcess output parameters to SS equivalents

| IS Operation parameter | SS WSDL type sub-element used in corresponding input message under corresponding port type operation as indicated in Table 5.1 | Qualifier |
| --- | --- | --- |
| result | result | M |

## Operation changeScManagementProfile

## Input parameters

Table 5.2.9.1: Mapping from IS changeScManagementProfile input parameters to SS equivalents

| IS Operation parameter | SS WSDL type sub-element used in corresponding input message under corresponding port type operation as indicated in Table 5.1 | Qualifier |
| --- | --- | --- |
| id | id | M |
| nEInformation | nEInformation | M |
| swVersionToBeInstalled | swVersionToBeInstalled | M |
| stepsAndSelectedStopPointList | stepsAndSelectedStopPointList | M |
| selectedFinalAdministrativeState | selectedFinalAdministrativeState | M |

## Output parameters

Table 5.2.9.1: Mapping from IS changeScManagementProfile input parameters to SS equivalents

| IS Operation parameter | SS WSDL type sub-element used in corresponding input message under corresponding port type operation as indicated in Table 5.1 | Qualifier |
| --- | --- | --- |
| result | result | M |
| versionNumber | versionNumber | M |
| conflictingProfileId | conflictingProfileId | C *) |

Next modifications

Annex A (normative):
WSDL specifications

<?xml version="1.0" encoding="UTF-8"?>

<!--

3GPP TS 32.507 Self Configuration IRP SOAP Solution Set

-->

<definitions xmlns="http://schemas.xmlsoap.org/wsdl/" xmlns:soap="http://schemas.xmlsoap.org/wsdl/soap/" xmlns:ScIRPSystem="http://www.3gpp.org/ftp/Specs/archive/32_series/32.507#ScIRPSystem" xmlns:ScIRPData="http://www.3gpp.org/ftp/Specs/archive/32_series/32.507#ScIRPData" xmlns:xsci="http://www.3gpp.org/ftp/specs/archive/32_series/32.505#scIRPIOCs" xmlns:xn="http://www.3gpp.org/ftp/specs/archive/32_series/32.625#genericNrm" xmlns:genericIRPSystem="http://www.3gpp.org/ftp/Specs/archive/32_series/32.317/schema/32317-810/GenericIRPSystem" xmlns:ntfIRPNtfSystem="http://www.3gpp.org/ftp/Specs/archive/32_series/32.307/schema/32307-810/notification/NotificationIRPNtfSystem" xmlns:ns="http://www.w3.org/2001/XMLSchema" xmlns:ns1="http://schemas.xmlsoap.org/soap/encoding/" targetNamespace="http://www.3gpp.org/ftp/Specs/archive/32_series/32.507#ScIRPSystem">

<import namespace="http://www.3gpp.org/ftp/Specs/archive/32_series/32.307/schema/32307-810/notification/NotificationIRPNtfSystem" location="http://www.3gpp.org/ftp/Specs/archive/32_series/32.307/schema/32307-810-wsdl.zip"/>

<import namespace="http://www.3gpp.org/ftp/Specs/archive/32_series/32.317/schema/32317-810/GenericIRPSystem" location="http://www.3gpp.org/ftp/Specs/archive/32_series/32.317/schema/32317-810-wsdl.zip"/>

<types>

<schema xmlns="http://www.w3.org/2001/XMLSchema" targetNamespace="http://www.3gpp.org/ftp/Specs/archive/32_series/32.507#ScIRPData">

<import namespace="http://www.3gpp.org/ftp/specs/archive/32_series/32.505#scIRPIOCs"/>

<import namespace="http://www.3gpp.org/ftp/specs/archive/32_series/32.625#genericNrm"/>

<!-- The following types are defined for the SC IRP operations -->

<simpleType name="NEInformation">

<restriction base="string"/>

</simpleType>

<simpleType name="Id">

<restriction base="xn:dn"/>

</simpleType>

<simpleType name="radioParameterName">

<restriction base="string"/>

</simpleType>

<simpleType name="radioParameterValue">

<restriction/>

</simpleType>

<simpleType name="FileLocation">

<restriction base="string"/>

</simpleType>

<complexType name="capability">

<sequence>

<element name="Id" type="ScIRPData:Id"/>

<element name="NEInformation" type="ScIRPData:NEInformation"/>

<element name="StepsAndOfferedStopPointList" type="xsci:StepsAndOfferedStopPointList"/>

<element name="OfferedFinalAdministrativeStateInformation" type="xsci:OfferedFinalAdministrativeStateInformation"/>

</sequence>

</complexType>

<complexType name="capabilitiesList">

<sequence>

<element name="capability" type="ScIRPData:capability" maxOccurs="unbounded"/>

</sequence>

</complexType>

<complexType name="ScProfile">

<sequence>

<element name="Id" type="ScIRPData:Id"/>

<element name="VersionNumber" type="xsci:VersionNumber"/>

<element name="NEInformation" type="ScIRPData:NEInformation"/>

<element name="StepsAndSelectedStopPointList" type="xsci:StepsAndSelectedStopPointList"/>

<element name="FinalAdministrativeStateValue" type="xsci:FinalAdministrativeStateValue"/>

<element name="swVersionToBeInstalled" type=" xsci:VersionNumber" minOccurs="0"/>

</sequence>

</complexType>

<complexType name="ScProfileList">

<sequence>

<element name="ScProfile" type=" ScIRPData:ScProfile" maxOccurs="unbounded"/>

</sequence>

</complexType>

<complexType name="ScProcess">

<sequence>

<element name="Id" type="ScIRPData:Id"/>

<element name="NEInformation" type="ScIRPData:NEInformation"/>

<element name="ProfileId" type="xsci:ProfileId"/>

<element name="StepInfoList" type="xsci:StepInfoList"/>

</sequence>

</complexType>

<complexType name="ScProcessList">

<sequence>

<element name="ScProcess" type="ScIRPData:ScProcess" maxOccurs="unbounded"/>

</sequence>

</complexType>

<complexType name="startStepName">

<sequence>

<element name="startStepName" type="string"/>

</sequence>

</complexType>

<complexType name="listOfNeededRadioParameters">

<sequence>

<element name="radioParameterName" type="ScIRPData:radioParameterName"/>

<element name="radioParameterValue" type="ScIRPData:radioParameterValue"/>

</sequence>

</complexType>

<complexType name="valuesOfNeededRadioParameter">

<sequence>

<element name="listOfNeededRadioParameters" type="ScIRPData:listOfNeededRadioParameters"/>

</sequence>

</complexType>

<!--listScManagementCapabilities Request-->

<element name="listScManagementCapabilitiesRequest">

<complexType>

<sequence>

<element name="nEInformation" type="ScIRPData:NEInformation"/>

</sequence>

</complexType>

</element>

<!--listScManagementCapabilities Response -->

<element name="listScManagementCapabilitiesResponse">

<complexType>

<sequence>

<element name="capabilitiesList" type="ScIRPData:capabilitiesList"/>

<element name="Result">

<simpleType>

<restriction base="string">

<enumeration value="success"/>

<enumeration value="failure"/>

<enumeration value="stepNameNotMatch"/>

<enumeration value="nEInformationIntersection"/>

</restriction>

</simpleType>

</element>

</sequence>

</complexType>

</element>

<!--listScManagementCapabilities Fault -->

<element name="listScManagementCapabilitiesFault">

<simpleType>

<restriction base="string">

<enumeration value="operationfailed"/>

</restriction>

</simpleType>

</element>

<!--listScManagementProfiles  Request -->

<element name="listScManagementProfilesRequest">

<complexType>

<sequence>

<element name="nEInformation" type="ScIRPData:NEInformation"/>

</sequence>

</complexType>

</element>

<!--listScManagementProfiles  Response -->

<element name="listScManagementProfilesResponse">

<complexType>

<sequence>

<element name="ScProfileList" type="ScIRPData:ScProfileList"/>

<element name="Result">

<simpleType>

<restriction base="string">

<enumeration value="success"/>

<enumeration value="failure"/>

<enumeration value="stepNameNotMatch"/>

<enumeration value="nEInformationIntersection"/>

</restriction>

</simpleType>

</element>

</sequence>

</complexType>

</element>

<!--createScManagementProfile Request -->

<element name="createScManagementProfileRequest">

<complexType>

<sequence>

<element name="id" type="ScIRPData:Id" minOccurs="0"/>

<element name="nEInformation" type="ScIRPData:NEInformation"/>

<element name="swVersionToBeInstalled" type="xsci:VersionNumber"/>

<element name="stepsAndSelectedStopPointList" type="xsci:StepsAndSelectedStopPointList"/>

<element name="selectedFinalAdministrativeState" type="xsci:FinalAdministrativeStateValue"/>

</sequence>

</complexType>

</element>

<!--createScManagementProfile Response -->

<element name="createScManagementProfileResponse">

<complexType>

<sequence>

<element name="id" type="ScIRPData:Id" minOccurs="0"/>

<element name="Result">

<simpleType>

<restriction base="string">

<enumeration value="Success"/>

<enumeration value="Failure"/>

<enumeration value="nEInformationIntersection"/>

<enumeration value="notAllowedBecauseOfOngoingSwmActivity"/>

</restriction>

</simpleType>

</element>

</sequence>

</complexType>

</element>

<!--deleteScManagementProfile Request -->

<element name="deleteScManagementProfileRequest">

<complexType>

<sequence>

<element name="id" type="ScIRPData:Id"/>

</sequence>

</complexType>

</element>

<!--deleteScManagementProfile Response -->

<element name="deleteScManagementProfileResponse">

<complexType>

<sequence>

<element name="Result">

<simpleType>

<restriction base="string">

<enumeration value="success"/>

<enumeration value="failure"/>

<enumeration value="stepNameNotMatch"/>

<enumeration value="nEInformationIntersection"/>

</restriction>

</simpleType>

</element>

</sequence>

</complexType>

</element>

<!--listScProcesses Request -->

<element name="listScProcessesRequest">

<complexType>

<sequence>

<element name="nEIdentification" type="ScIRPData:NEInformation" minOccurs="0"/>

</sequence>

</complexType>

</element>

<!--listScProcesses Response -->

<element name="listScProcessesResponse">

<complexType>

<sequence>

<element name="ScProcessList" type="ScIRPData:ScProcessList"/>

<element name="Result">

<simpleType>

<restriction base="string">

<enumeration value="success"/>

<enumeration value="failure"/>

<enumeration value="stepNameNotMatch"/>

<enumeration value="nEInformationIntersection"/>

</restriction>

</simpleType>

</element>

</sequence>

</complexType>

</element>

<!--resumeScProcess Request -->

<element name="resumeScProcessRequest">

<complexType>

<sequence>

<element name="id" type="ScIRPData:Id"/>

<element name="startStepName" type="ScIRPData:startStepName"/>

</sequence>

</complexType>

</element>

<!--resumeScProcess Response -->

<element name="resumeScProcessResponse">

<complexType>

<sequence>

<element name="Result">

<simpleType>

<restriction base="string">

<enumeration value="success"/>

<enumeration value="failure"/>

<enumeration value="stepNameNotMatch"/>

<enumeration value="nEInformationIntersection"/>

</restriction>

</simpleType>

</element>

</sequence>

</complexType>

</element>

<!--resumeScProcessWithArcfData Request -->

<element name="resumeScProcessWithArcfDataRequest">

<complexType>

<sequence>

<element name="valuesOfNeededRadioParameter" type="ScIRPData:valuesOfNeededRadioParameter"/>

<element name="fileLocation" type="ScIRPData:FileLocation"/>

</sequence>

</complexType>

</element>

<!--resumeScProcessWithArcfData Response -->

<element name="resumeScProcessWithArcfDataResponse">

<complexType>

<sequence>

<element name="validationErrorInfo">

<simpleType>

<restriction base="string">

<enumeration value="ParameterNotSupported"/>

<enumeration value="InvalidParameter"/>

<enumeration value="ValueNotSupported"/>

<enumeration value="MissingParameterValue"/>

<enumeration value="ConflictingParamterValue"/>

<enumeration value="SemanticsError"/>

<enumeration value="OtherError "/>

</restriction>

</simpleType>

</element>

</sequence>

</complexType>

</element>

<!--terminateScProcess Request -->

<element name="terminateScProcessRequest">

<complexType>

<sequence>

<element name="id" type="ScIRPData:Id"/>

</sequence>

</complexType>

</element>

<!--terminateScProcess Response -->

<element name="terminateScProcessResponse">

<complexType>

<sequence>

<element name="Result">

<simpleType>

<restriction base="string">

<enumeration value="success"/>

<enumeration value="failure"/>

<enumeration value="stepNameNotMatch"/>

<enumeration value="nEInformationIntersection"/>

</restriction>

</simpleType>

</element>

</sequence>

</complexType>

</element>

<!--ChangeScManagementProfile Request -->

<element name="ChangeScManagementProfileRequest">

<complexType>

<sequence>

<element name="id" type="ScIRPData:Id"/>

<element name="nEInformation" type="ScIRPData:NEInformation"/>

<element name="swVersionToBeInstalled" type="xsci:VersionNumber"/>

<element name="stepsAndSelectedStopPointList" type="xsci:StepsAndSelectedStopPointList"/>

<element name="selectedFinalAdministrativeState" type="xsci:FinalAdministrativeStateValue"/>

</sequence>

</complexType>

</element>

<!--ChangeScManagementProfile Response -->

<element name="ChangeScManagementProfileResponse">

<complexType>

<sequence>

<element name="Result">

<simpleType>

<restriction base="string">

<enumeration value="Success"/>

<enumeration value="Failure"/>

<enumeration value="nEInformationIntersection"/>

<enumeration value="notAllowedBecauseOfOngoingSwmActivity"/>

</restriction>

</simpleType>

</element>

<element name="versionNumber" type="xsci:VersionNumber"/>

<element name="conflictingProfileId" minOccurs="0">

<simpleType>

<restriction base="string">

<enumeration value="swMprofileId"/>

<enumeration value="swMprofileAId"/>

<enumeration value="swMprofileBId"/>

<enumeration value="empty"/>

</restriction>

</simpleType>

</element>

</sequence>

</complexType>

</element>

</schema>

</types>

<message name="listScManagementCapabilitiesRequest">

<part name="parameter" element="ScIRPData:listScManagementCapabilitiesRequest"/>

</message>

<message name="listScManagementCapabilitiesResponse">

<part name="parameter" element="ScIRPData:listScManagementCapabilitiesResponse"/>

</message>

<message name="listScManagementCapabilitiesFault">

<part name="parameter" element="ScIRPData:listScManagementCapabilitiesFault"/>

</message>

<message name="listScManagementProfilesRequest">

<part name="parameter" element="ScIRPData:listScManagementProfilesRequest"/>

</message>

<message name="listScManagementProfilesResponse">

<part name="parameter" element="ScIRPData:listScManagementProfilesResponse"/>

</message>

<message name="createScManagementProfileRequest">

<part name="parameter" element="ScIRPData:createScManagementProfileRequest"/>

</message>

<message name="createScManagementProfileResponse">

<part name="parameter" element="ScIRPData:createScManagementProfileResponse"/>

</message>

<message name="deleteScManagementProfileRequest">

<part name="parameter" element="ScIRPData:deleteScManagementProfileRequest"/>

</message>

<message name="deleteScManagementProfileResponse">

<part name="parameter" element="ScIRPData:deleteScManagementProfileResponse"/>

</message>

<message name="listScProcessesRequest">

<part name="parameter" element="ScIRPData:listScProcessesRequest"/>

</message>

<message name="listScProcessesResponse">

<part name="parameter" element="ScIRPData:listScProcessesResponse"/>

</message>

<message name="resumeScProcessRequest">

<part name="parameter" element="ScIRPData:resumeScProcessRequest"/>

</message>

<message name="resumeScProcessResponse">

<part name="parameter" element="ScIRPData:resumeScProcessResponse"/>

</message>

<message name="resumeScProcessWithArcfDataRequest">

<part name="parameter" element="ScIRPData:resumeScProcessWithArcfDataRequest"/>

</message>

<message name="resumeScProcessWithArcfDataResponse">

<part name="parameter" element="ScIRPData:resumeScProcessWithArcfDataResponse"/>

</message>

<message name="terminateScProcessRequest">

<part name="parameter" element="ScIRPData:terminateScProcessRequest"/>

</message>

<message name="terminateScProcessResponse">

<part name="parameter" element="ScIRPData:terminateScProcessResponse"/>

</message>

<message name="ChangeScManagementProfileRequest">

<part name="parameter" element="ScIRPData:ChangeScManagementProfileRequest"/>

</message>

<message name="ChangeScManagementProfileResponse">

<part name="parameter" element="ScIRPData:ChangeScManagementProfileResponse"/>

</message>

<portType name="ScIRPOperation1">

<operation name="listScManagementCapabilities">

<input message="ScIRPSystem:listScManagementCapabilitiesRequest"/>

<output message="ScIRPSystem:listScManagementCapabilitiesResponse"/>

<fault name="listScManagementCapabilitiesFault" message="ScIRPSystem:listScManagementCapabilitiesFault"/>

</operation>

<operation name="listScManagementProfiles">

<input message="ScIRPSystem:listScManagementProfilesRequest"/>

<output message="ScIRPSystem:listScManagementProfilesResponse"/>

</operation>

<operation name="createScManagementProfile">

<input message="ScIRPSystem:createScManagementProfileRequest"/>

<output message="ScIRPSystem:createScManagementProfileResponse"/>

</operation>

<operation name="deleteScManagementProfile">

<input message="ScIRPSystem:deleteScManagementProfileRequest"/>

<output message="ScIRPSystem:deleteScManagementProfileResponse"/>

</operation>

<operation name="listScProcesses">

<input message="ScIRPSystem:listScProcessesRequest"/>

<output message="ScIRPSystem:listScProcessesResponse"/>

</operation>

<operation name="resumeScProcess">

<input message="ScIRPSystem:resumeScProcessRequest"/>

<output message="ScIRPSystem:resumeScProcessResponse"/>

</operation>

<operation name="resumeScProcessWithArcfData">

<input message="ScIRPSystem:resumeScProcessWithArcfDataRequest"/>

<output message="ScIRPSystem:resumeScProcessWithArcfDataResponse"/>

</operation>

<operation name="terminateScProcess">

<input message="ScIRPSystem:terminateScProcessRequest"/>

<output message="ScIRPSystem:terminateScProcessResponse"/>

</operation>

</portType>

<portType name="ScIRPOperation2">

<operation name="ChangeScManagementProfile">

<input message="ScIRPSystem:ChangeScManagementProfileRequest"/>

<output message="ScIRPSystem:ChangeScManagementProfileResponse"/>

</operation>

</portType>

<binding name="ScIRPOperation1" type="ScIRPSystem:ScIRPOperation1">

<soap:binding style="document" transport="http://schemas.xmlsoap.org/soap/http"/>

<operation name="listScManagementCapabilities">

<soap:operation soapAction="http://www.3gpp.org/ftp/Specs/archive/32_series/32.507#listScManagementCapabilities" style="document"/>

<input>

<soap:body use="literal"/>

</input>

<output>

<soap:body use="literal"/>

</output>

<fault name="listScManagementCapabilitiesFault"/>

</operation>

<operation name="listScManagementProfiles">

<soap:operation soapAction="http://www.3gpp.org/ftp/Specs/archive/32_series/32.507#listScManagementProfiles" style="document"/>

<input>

<soap:body use="literal"/>

</input>

<output>

<soap:body use="literal"/>

</output>

</operation>

<operation name="createScManagementProfile">

<soap:operation soapAction="http://www.3gpp.org/ftp/Specs/archive/32_series/32.507#createScManagementProfile" style="document"/>

<input>

<soap:body use="literal"/>

</input>

<output>

<soap:body use="literal"/>

</output>

</operation>

<operation name="deleteScManagementProfile">

<soap:operation soapAction="http://www.3gpp.org/ftp/Specs/archive/32_series/32.507#deleteScManagementProfile" style="document"/>

<input>

<soap:body use="literal"/>

</input>

<output>

<soap:body use="literal"/>

</output>

</operation>

<operation name="listScProcesses">

<soap:operation soapAction="http://www.3gpp.org/ftp/Specs/archive/32_series/32.507#listScProcesses" style="document"/>

<input>

<soap:body use="literal"/>

</input>

<output>

<soap:body use="literal"/>

</output>

</operation>

<operation name="resumeScProcess">

<soap:operation soapAction="http://www.3gpp.org/ftp/Specs/archive/32_series/32.507#resumeScProcess" style="document"/>

<input>

<soap:body use="literal"/>

</input>

<output>

<soap:body use="literal"/>

</output>

</operation>

<operation name="resumeScProcessWithArcfData">

<soap:operation soapAction="http://www.3gpp.org/ftp/Specs/archive/32_series/32.507#resumeScProcessWithArcfData" style="document"/>

<input>

<soap:body use="literal"/>

</input>

<output>

<soap:body use="literal"/>

</output>

</operation>

<operation name="terminateScProcess">

<soap:operation soapAction="http://www.3gpp.org/ftp/Specs/archive/32_series/32.507#terminateScProcess" style="document"/>

<input>

<soap:body use="literal"/>

</input>

<output>

<soap:body use="literal"/>

</output>

</operation>

</binding>

<binding name="ScIRPOperation2" type="ScIRPSystem:ScIRPOperation2">

<soap:binding style="document" transport="http://schemas.xmlsoap.org/soap/http"/>

<operation name="ChangeScManagementProfile">

<soap:operation soapAction="http://www.3gpp.org/ftp/Specs/archive/32_series/32.507#ChangeScManagementProfile" style="document"/>

<input>

<soap:body use="literal"/>

</input>

<output>

<soap:body use="literal"/>

</output>

</operation>

</binding>

<service name="ScIRPService">

<port name="ScIRPOperation1" binding="ScIRPSystem:ScIRPOperation1">

<soap:address location="http://www.3gpp.org/ftp/Specs/archive/32_series/32.507#ScIRP"/>

</port>

<port name="GenericIRPPort" binding="genericIRPSystem:GenericIRPBinding">

<soap:address location="http://www.3gpp.org/ftp/Specs/archive/32_series/32.317#GenericIRP"/>

</port>

<port name="NotificationIRPNtfPort" binding="ntfIRPNtfSystem:NotificationIRPNtf">

<soap:address location="http://www.3gpp.org/ftp/Specs/archive/32_series/32.307#NotificationIRPNtf"/>

</port>

<port name="ScIRPOperation2" binding="ScIRPSystem:ScIRPOperation2">

<soap:address location="http://www.3gpp.org/ftp/Specs/archive/32_series/32.507#ScIRP"/>

</port>

</service>

</definitions>

End of modifications

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.