3GPP TSG-SA5 (Telecom Management)	S5-101452

Meeting SA5#71, 10 May - 14 May 2010, Montreal, Canada	revision of S5-101377

| CR-Form-v9.6 |
| --- |
| CHANGE REQUEST |
| ( | 32.175 | CR | 0011 | ( rev | - | ( Current version: | 9.1.1 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Aligning with the IS – Modifications to Packet Access Service Parameters and Modeling |
| --- | --- |
| Source to WG: ( | Alcatel-Lucent, Nokia Siemens Networks |
| Source to TSG: ( | SA5 |
| Work item code: ( | OAM9-SuM |  | Date: ( | 03/05/2010 |
| Category: ( | C |  | Release: ( | Rel-9 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) |
| Reason for change: ( | Main Changes: - align with the IS changes for packet access service parameters and modeling |
| Summary of change: ( | Include new IOCs: EPSService, EPSSubscribedService, EPSServiceProfile, IWANParameters, PSCommonParameters, OptHandover3GPP2Parameters, Non3GPPAccessParameters Correcting PSService and PSSubscribedService and PSServiceProfile to new names of GPRSService, GPRSSubscribedService, and GPRSServiceProfile and aligning parameters with most recent TS 23.008. Removed PS Common and IWAN parameters from newly renamed GPRSServiceProfile. |
| Consequences if ( not approved: | Not aligned with the IS.. |
| Clauses affected: ( | Annex A |
|  | Y | N |  |  |
| Other specs ( |  | x | Other core specifications ( |  |
| affected: |  | x | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

1st Modified Section

Annex A (normative):
Subscription Management NRM-specific XML schema (file name "sumNrm.xsd")

The following XML schema sumNrm.xsd is the NRM-specific schema for the Subscription Management Network Resources IRP NRM defined in 3GPP TS 32.172 [5]:

<?xml version="1.0" encoding="UTF-8"?>

<!--
  3GPP TS 32.175 SuM Network Resources IRP
  SuM NRM-specific XML schema
  sumNrm.xsd
-->

<schema
  targetNamespace=
"http://www.3gpp.org/ftp/specs/archive/32_series/32.175#sumNrm"
  elementFormDefault="qualified"
  xmlns="http://www.w3.org/2001/XMLSchema"
  xmlns:sn=
"http://www.3gpp.org/ftp/specs/archive/32_series/32.175#sumNrm"
  xmlns:xn=
"http://www.3gpp.org/ftp/specs/archive/32_series/32.625#genericNrm"
>

  <import
    namespace=
"http://www.3gpp.org/ftp/specs/archive/32_series/32.625#genericNrm"
  />

  <!-- SuM Network Resources IRP NRM class associated XML elements -->

  <element
    name="ServiceProviderFunction"
    substitutionGroup="xn:SubNetworkOptionallyContainedNrmClass"
  >
    <complexType>
      <complexContent>
        <extension base="xn:NrmClass">
          <sequence>
            <element name="attributes" minOccurs="0">
              <complexType>
                <all>
                  <element name="userLabel" minOccurs="0"/>

<element name="theService" type="xn:dnList"/>
                </all>
              </complexType>
            </element>
          </sequence>
        </extension>
      </complexContent>
    </complexType>
  </element>

  <element
    name="SubscriptionFunction"
    substitutionGroup="xn: SubNetworkOptionallyContainedNrmClass"
  >
    <complexType>
      <complexContent>
        <extension base="xn:NrmClass">
          <sequence>
            <element name="attributes" minOccurs="0">
              <complexType>
                <all>
                  <element name="userLabel" minOccurs="0"/>

<element name="theUser" type="xn:dnList"/>

<element name="theSubscriberProfile" type="xn:dnList"/>    
                </all>
              </complexType>
            </element>
          </sequence>
        </extension>
      </complexContent>
    </complexType>
  </element>

  <element name="SuMSubscriberProfile" substitutionGroup="xn: SubNetworkOptionallyContainedNrmClass">
    <complexType>
      <complexContent>
        <extension base="xn:NrmClass">
          <sequence>
            <element name="attributes" minOccurs="0">
              <complexType>
                <all>
                  <element name="suMSubscriberProfileInfo" minOccurs="0"/>
                  <element name="theUser" type="xn:dnList" />
				  <element name="theSubscribedService" type="xn:dnList"/>

</all>
              </complexType>
            </element>
          </sequence>
        </extension>
      </complexContent>
    </complexType>
  </element>

<element name="MobileUserData" substitutionGroup="xn: SubNetworkOptionallyContainedNrmClass">
    <complexType>
      <complexContent>
        <extension base="xn:NrmClass">
          <sequence>
            <element name="attributes" minOccurs="0">
              <complexType>
                <all>
                  <element name="theServiceProfile" type="xn:dnList"/>
                  <element name="iMSI" type="string" minOccurs="0"/>
                  <element name="mSISDN" type="string" minOccurs="0"/>
                  <element name="multinumberingMSISDNs" type="sn:multinumberingMSISDNList" minOccurs="0" />
                  <element name="iMEISV" type="string" minOccurs="0"/>
                </all>
              </complexType>
            </element>
          </sequence>
        </extension>
      </complexContent>
    </complexType>
  </element>

<element name="SuMUser" substitutionGroup="xn:SubNetworkOptionallyContainedNrmClass">
    <complexType>
      <complexContent>
        <extension base="xn:NrmClass">
          <sequence>
            <element name="attributes" minOccurs="0">
              <complexType>
                <all>
                  <element name="theMobileUserData" type="xn:dnList" />
                  <element name="theSubscriber" type="xn:dnList" />
                  <element name="theCredentials" type="xn:dnList"/>
                  <element name="theServiceProfile" type="xn:dnList"/>
                  <element name="theIdentity" type="xn:dnList" minOccurs="0"/>
                </all>
              </complexType>
            </element>
          </sequence>
        </extension>
      </complexContent>
    </complexType>
  </element>

<element name="SuMCredentials" substitutionGroup="xn:SubNetworkOptionallyContainedNrmClass">
    <complexType>
      <complexContent>
        <extension base="xn:NrmClass">
          <sequence>
            <element name="attributes" minOccurs="0">
              <complexType>
                <all>
                  <element name="thePublicId" type="xn:dnList" />
                  <element name="theServiceProfile" type="xn:dnList" />
                  <element name="iMSPrivateUserIdentity" type="string" minOccurs="0"/>
                </all>
              </complexType>
            </element>
          </sequence>
        </extension>
      </complexContent>
    </complexType>
  </element>


  <element name="SuMService" type="xn:NrmClass" abstract="true" substitutionGroup="xn:SubNetworkOptionallyContainedNrmClass"/>

  <element
    name="CSService" substitutionGroup="sn:SuMService">
    <complexType>
      <complexContent>
        <extension base="xn:NrmClass">
          <sequence>
            <element name="attributes" minOccurs="0">
              <complexType>
                <all>
                  <element name="theContract" minOccurs="0"/>
                  <element name="networkAccessMode" minOccurs="0"/>
                  <element name="basicMSISDNIndicator" minOccurs="0"/>
                  <element name="mSISDNAlertIndicator" minOccurs="0"/>
                  <element name="subscriptionRestriction" minOccurs="0"/>
                  <element name="rSZIlists" minOccurs="0"/>
                  <element name="lSAIdentity" minOccurs="0"/>
                  <element name="lSAPriority" minOccurs="0"/>
                  <element name="lSAPreferentialAccessIndicator" minOccurs="0"/>
                  <element name="lSAActiveModeSupportIndicator" minOccurs="0"/>
                  <element name="lSAOnlyAccessIndicator" minOccurs="0"/>
                  <element name="lSAActiveModeIndicator" minOccurs="0"/>
                  <element name="vPLMNIdentifier" minOccurs="0"/>
                  <element name="accessRestrictionData" minOccurs="0"/>
                  <element name="privacyExceptionList" minOccurs="0"/>
                  <element name="gMLCNumbers" minOccurs="0"/>
                  <element name="mOLRList" minOccurs="0"/>
                  <element name="serviceTypes" minOccurs="0"/>
                  <element name="mobileStationCategory" minOccurs="0"/>
                  <element name="lMUIdentifier" minOccurs="0"/>
                  <element name="subscriberStatus" minOccurs="0"/>
                  <element name="gsmSCFaddresslistForODB" minOccurs="0"/>
                  <element name="provisionOfBearerService" minOccurs="0"/>
                  <element name="provisionOfTeleservice" minOccurs="0"/>
                  <element name="bCAllocation" minOccurs="0"/>
                  <element name="barringOfOutgoingCalls" minOccurs="0"/>
                  <element name="barringOfIncomingCalls" minOccurs="0"/>
                  <element name="barringOfRoaming" minOccurs="0"/>
                  <element name="barringOfPremiumRateCalls" minOccurs="0"/>
                  <element 
                    name="barringOfSupplementaryServiceManagement"
                    minOccurs="0"
                  />
                  <element
                    name="barringOfRegistrationOfCallForwarding"
                    minOccurs="0"
                  />
                  <element
                    name="barringOfInvocationOfCallTransfer"
                    minOccurs="0"
                  />
                  <element
                    name="operatorDeterminedBarringPLMNspecificData"
                    minOccurs="0"
                  />
                  <element name="vGCSGroupMembershipList" minOccurs="0"/>
                  <element name="vBSGroupMembershipList" minOccurs="0"/>
                  <element
                    name="broadcastCallInitiationAllowedList"
                    minOccurs="0"
                  />
                  <element
                    name="originatingCAMELSubscriptionInformationOCSI"
                    minOccurs="0"
                  />
                  <element
                    name="terminatingCAMELSubscriptionInformationTCSI"
                    minOccurs="0"
                  />
                  <element
                    name="vMSCTerminatingCAMELSubscriptionInformationVTCSI"
                    minOccurs="0"
                  />
                  <element
                    name="locationInformationSubscriberStateInformation"
                    minOccurs="0"
                  />
                  <element
                    name="uSSDCAMELSubscriptionInformationUCSI"
                    minOccurs="0"
                  />
                  <element name="sSInvocationNotificationSSCSI" minOccurs="0"/>
                  <element
                    name="translationInformationFlagTIFCSI"
                    minOccurs="0"
                  />
                  <element
                    name="dialledServiceCAMELSubscriptionInformationDCSI"
                    minOccurs="0"
                  />
                  <element
                    name="uSSDGeneralCAMELServiceInformationUGCSI"
                    minOccurs="0"
                  />
                  <element
                  name="shortMessageServiceCAMELSubscriptionInformationMOSMSCSI"
                    minOccurs="0"
                  />
                  <element
                  name="shortMessageServiceCAMELSubscriptionInformationMTSMSCSI"
                    minOccurs="0"
                  />
                  <element
                    name="mTSMSCSIVLRNegotiatedCAMELCapabilityHandling"
                    minOccurs="0"
                  />
                  <element name="gsmSCFaddressforCSI" minOccurs="0"/>
                  <element name="iSTAlertTimer" minOccurs="0"/>
                  <element name="cSAllocationRetentionpriority" minOccurs="0"/>
                  <element name="iCSIndicator" minOccurs=”0”/>
                  <element name="sS-Code" minOccurs="0"/>
                  <element name="provisioningState" minOccurs="0"/>
                  <element name="activationState" minOccurs="0"/>
                  <element name="registrationState" minOccurs="0"/>
                  <element name="overrideCategory" minOccurs="0"/>
                  <element name="cLIRestrictionOption" minOccurs="0"/>
                  <element name="forwarded-toNumber" minOccurs="0"/>
                  <element name="forwarded-toSubaddress" minOccurs="0"/>
                  <element name="noReplyConditionTimer" minOccurs="0"/>
                  <element name="maximumEntitledPriority" minOccurs="0"/>
                  <element name="defaultPriority" minOccurs="0"/>
                  <element name="nbrUser" minOccurs="0"/>
                  <element name="nbrSB" minOccurs="0"/>
				  <element name="theCSSupplServiceForCS" type="xn:dnList"/>

</all>
              </complexType>
            </element>
          </sequence>
        </extension>
      </complexContent>
    </complexType>
  </element>
  <element name="SuMCSSupplService"

substitutionGroup="xn:SubNetworkOptionallyContainedNrmClass">
    <complexType>
      <complexContent>
        <extension base="xn:NrmClass">
          <sequence>
            <element name="attributes" minOccurs="0">
              <complexType>
                <all>
                  <element name="sS-Code" minOccurs="0"/>
                  <element name="provisioningState" minOccurs="0"/>
                  <element name="activationState" minOccurs="0"/>
                  <element name="registrationState" minOccurs="0"/>
                  <element name="overrideCategory" minOccurs="0"/>
                  <element name="cLIRestrictionOption" minOccurs="0"/>
                  <element name="forwarded-toNumber" minOccurs="0"/>
                  <element name="forwarded-toSubaddress" minOccurs="0"/>
                  <element name="noReplyConditionTimer" minOccurs="0"/>
                  <element name="maximumEntitledPriority" minOccurs="0"/>
                  <element name="defaultPriority" minOccurs="0"/>
                  <element name="nbrUser" minOccurs="0"/>
                  <element name="nbrSB" minOccurs="0"/>
                </all>
              </complexType>
            </element>
          </sequence>
        </extension>
      </complexContent>
    </complexType>
  </element>


  <element
    name="GPRSService"
    substitutionGroup="sn:SuMService">
    <complexType>
      <complexContent>
        <extension base="xn:NrmClass">
          <sequence>
            <element name="attributes" minOccurs="0">
              <complexType>
                <all>
                  <element name="theContract" minOccurs="0"/>
                  <element name="networkAccessMode" minOccurs="0"/>
                  <element name="basicMSISDNIndicator" minOccurs="0"/>
                  <element name="mSISDNAlertIndicator" minOccurs="0"/>
                  <element name="subscriptionRestriction" minOccurs="0"/>
                  <element name="rSZIlists" minOccurs="0"/>
                  <element name="lSAIdentity" minOccurs="0"/>
                  <element name="lSAPriority" minOccurs="0"/>
                  <element name="lSAPreferentialAccessIndicator" minOccurs="0"/>
                  <element name="lSAActiveModeSupportIndicator" minOccurs="0"/>
                  <element name="lSAOnlyAccessIndicator" minOccurs="0"/>
                  <element name="lSAActiveModeIndicator" minOccurs="0"/>
                  <element name="vPLMNIdentifier" minOccurs="0"/>
                  <element name="accessRestrictionData" minOccurs="0"/>
                  <element name="privacyExceptionList" minOccurs="0"/>
                  <element name="gMLCNumbers" minOccurs="0"/>
                  <element name="mOLRList" minOccurs="0"/>
                  <element name="serviceTypes" minOccurs="0"/>
                  <element name="gGSNNumber" minOccurs="0"/>
                  <element name="provisionofTeleservice" minOccurs="0"/>
                  <element name="subscriberStatus" minOccurs="0"/>

<element name="transferofSMoption" minOccurs="0"/>
                  <element
                    name="barringofPacketOrientedServices"
                    minOccurs="0"
                  />
                  <element name="pDPType" minOccurs="0"/>
                  <element name="pDPAddress" minOccurs="0"/>
                  <element name="accessPointName" minOccurs="0"/>
                  <element name="vPLMNAddressAllowed" minOccurs="0"/>
                  <element name="qualityofServiceSubscribed" minOccurs="0"/>
                  <element
                    name="pDPContextChargingCharacteristics"
                    minOccurs="0"
                  />
                  <element
                    name="gPRSCAMELSubscriptionInformationGPRSCSI"
                    minOccurs="0"
                  />
                  <element
                name="mOShortMessageServiceCAMELSubscriptionInformationMOSMSCSI"
                    minOccurs="0"
                  />
                  <element
                name="mTShortMessageServiceCAMELSubscriptionInformationMTSMSCSI"
                    minOccurs="0"
                  />
                  <element
                    name="mOSMSCSISGSNNegotiatedCAMELCapabilityHandling"
                    minOccurs="0"
                  />
                  <element
                    name="mTSMSCSISGSNNegotiatedCAMELCapabilityHandling"
                    minOccurs="0"
                  />
                  <element
                    name="mobilityManagementforGPRSeventnotificationMGCSI"
                    minOccurs="0"
                  />
                  <element
                    name="mGCSINegotiatedCAMELCapabilityHandling"
                    minOccurs="0"
                  />
                  <element name="gsmSCFaddressforCSI" minOccurs="0"/>
                  <element
                    name="subscribedChargingCharacteristics"
                    minOccurs="0"
                  />
                  <element name="closedSubscriberGroupInformation" minOccurs="0"/>

<element name="gSMSCFaddresslistForODB" minOccurs="0"/>

<element name="barringOfOutgoingCalls" minOccurs="0"/>

<element name="barringOfRoaming" minOccurs="0"/>

<element name="operatorDeterminedBarringPLMNspecificData" minOccurs="0"/>

<element name="sTNSR" minOccurs="0"/>

<element name="iCSIndicator" minOccurs="0"/>

<element name="w-APN" minOccurs="0"/>
                  <element
                    name="listofauthorizedvisitednetworkidentifiers"
                    minOccurs="0"
                  />
                  <element name="wLANUERemoteIPaddress" minOccurs="0"/>
                  <element name="staticWLANUERemoteIPAddressList" minOccurs="0"/>

<element name="wLANAccess" minOccurs="0"/>
                  <element name="wLANTunnelling" minOccurs="0"/>
                  <element name="wLANDirectIPAccess" minOccurs="0"/>
                  <element name="wAPNAuthorised" minOccurs="0"/>
                  <element name="w-APNBarringTypeList" minOccurs="0"/>
                  <element name="w-APNChargingDataList" minOccurs="0"/>
                  <element name="wLANUERemoteIPAddress" minOccurs="0"/>
                  <element name="accessDependenceFlag" minOccurs="0"/>
                  <element name="i-WLANAccessType" minOccurs="0"/>
                  <element name="chargingData" minOccurs="0"/>
                  <element name="chargingCharacteristics" minOccurs="0"/>
                  <element name="primaryOCSChargingFunctionName" minOccurs="0"/>
                  <element
                    name="secondaryOCSChargingFunctionName"
                    minOccurs="0"
                  />
                  <element
                    name="primaryChargingCollectionFunctionName"
                    minOccurs="0"
                  />
                  <element
                    name="secondaryChargingCollectionFunctionName"
                    minOccurs="0"
                  />
                  <element name="w-APNIdentifierList" minOccurs="0"/>
                  <element name="maxNumberAccessesList" minOccurs="0"/>
                  <element name="maxSubscribedBandwidth" minOccurs="0"/>

<element name=”subscribed3GPPWLANQoSProfile” minOccurs=”0”/>
				  <element name="theGPRSSupplServiceForGPRS" type="xn:dnList"/>

</all>
              </complexType>
            </element>
          </sequence>
        </extension>
      </complexContent>
    </complexType>
  </element>

  <element name="SuMGPRSSupplService" substitutionGroup="xn:SubNetworkOptionallyContainedNrmClass">
    <complexType>
      <complexContent>
        <extension base="xn:NrmClass">
          <sequence>
            <element name="attributes" minOccurs="0">
              <complexType>
                <all>
                  <element name="sS-Code" minOccurs="0"/>
                  <element name="provisioningState" minOccurs="0"/>
                  <element name="activationState" minOccurs="0"/>
                </all>
              </complexType>
            </element>
          </sequence>
        </extension>
      </complexContent>
    </complexType>
  </element>

<element name="EPSService" substitutionGroup="sn:SuMService">
    <complexType>
      <complexContent>
        <extension base="xn:NrmClass">
          <sequence>
            <element name="attributes" minOccurs="0">
              <complexType>
                <all>
                  <element name="theContract" minOccurs="0"/>
                  <element name="accessPointName" minOccurs="0"/>
                  <element name="accessRestrictionData" minOccurs="0"/>
                  <element name="aPNAMBR" minOccurs="0"/> 
                  <element name="barringofPacketOrientedServices" minOccurs="0"/>
                  <element name="contextIdentifier" minOccurs="0"/>
                  <element name="operatorDeterminedBarringPLMNspecificData" minOccurs="0"/>
                  <element name="pDNAddress" minOccurs="0"/>
                  <element name="rSZILists" minOccurs="0"/>
                  <element name="sTNSR" minOccurs="0"/>
                  <element name="subscribedChargingCharacteristics" minOccurs="0"/>
                  <element name="subscriberStatus" minOccurs="0"/>
                  <element name="networkAccessMode" minOccurs="0"/>
                  <element name="barringOfOutgoingCalls" minOccurs="0"/>
                  <element name="barringOfRoaming" minOccurs="0"/>
                  <element name="privacyExceptionList" minOccurs="0"/>
                  <element name="gMLCNumbers" minOccurs="0"/>
                  <element name="mOLRList" minOccurs="0"/>
                  <element name="serviceTypes" minOccurs="0"/>
                  <element name="iCSIndicator" minOccurs="0"/>

<element name="aPNOIReplacement" minOccurs="0"/>
                  <element name="subscribedUEAMBR" minOccurs="0"/>
                  <element name="aPNConfigurationProfile" minOccurs="0"/>
                  <element name="rFSP" minOccurs="0"/>
                  <element name="vPLMNAddressAllowed-EPS" minOccurs="0"/>
                  <element name="pDNGWIdentity" minOccurs="0"/>
                  <element name="ePSPDNConnectedChargingCharacteristics" minOccurs="0"/>
                  <element name="pDNGWAllocationType" minOccurs="0"/>
                  <element name="aPNLevelAPNOIReplacement" minOccurs="0"/>
                  <element name="closedSubscriberUserGroupInformation" minOccurs="0"/>
                  <element name="listofAuthorizedvisitednetowrkidentifiers" minOccurs="0"/>
                  <element name="staticWLANUERemoteIPAddressList" minOccurs="0"/>
                  <element name="w-APONBarringTypeList" minOccurs="0"/>
                  <element name="w-APNChargingDataList" minOccurs="0"/>
                  <element name="wLANUERemoteIPAddress" minOccurs="0"/>
                  <element name="accessDependenceFlag" minOccurs="0"/>
                  <element name="chargingCharacteristics" minOccurs="0"/>
                  <element name="primaryOCSChargingFunctionName" minOccurs="0"/>

<element name="secondaryOCSChargingFunctionName" minOccurs="0"/>

<element name="primaryChargingCollectionFunctionName" minOccurs="0"/>

<element name="secondaryChargingCollectionFunctionName" minOccurs="0"/>
                  <element name="w-APNIdentifierList" minOccurs="0"/>
                  <element name="maxNumberAccessesList" minOccurs="0"/>
                  <element name="maxSubscribedBandwidth" minOccurs="0"/>
                  <element name="subscribed3GPPWLANQoSProfile" minOccurs="0"/>
                  <element name="permanentUserIdentity" minOccurs="0"/>
                  <element name="mIPSubscriberProfile" minOccurs="0"/>
                  <element name="accessRestrictionData" minOccurs="0"/>

</all>
              </complexType>
            </element>
          </sequence>
        </extension>
      </complexContent>
    </complexType>
  </element>

  <element
    name="IMSService"
    substitutionGroup="sn:SuMService">
    <complexType>
      <complexContent>
        <extension base="xn:NrmClass">
          <sequence>
            <element name="attributes" minOccurs="0">
              <complexType>
                <all>
                  <element name="theContract" minOccurs="0"/>
                  <element
                    name="listofauthorizedvisitednetworkidentifiers"
                    minOccurs="0"
                  />
                  <element name="registrationStatus" minOccurs="0"/>
                  <element name="sCSCFName" minOccurs="0"/>
                  <element name="diameterClientAddressofSCSCF" minOccurs="0"/>
                  <element name="theServerCapabilities" type="xn:dn" minOccurs="0"/>
                  <element
                    name="subscribedMediaProfileIdentifier"
                    minOccurs="0"
                  />
                  <element name="initialFilterCriteriaList" minOccurs="0">
    <complexType>

<sequence>

<element name="initialFilterCriteria" minOccurs="1" maxOccurs="unbounded"/>

</sequence>

</complexType>

</element>
                  <element name="applicationServerInformation" minOccurs="0"/>
                  <element name="serviceIndicationList" minOccurs="0">

<complexType>

<sequence>

<element name="serviceIndication" minOccurs="1" maxOccurs="unbounded"/>

</sequence>

</complexType>

</element>

                  <element
                    name="primaryEventChargingFunctionName"
                    minOccurs="0"
                  />
                  <element
                    name="secondaryEventChargingFunctionName"
                    minOccurs="0"
                  />
                  <element
                    name="primaryChargingCollectionFunctionName"
                    minOccurs="0"
                  />
                  <element
                    name="secondaryChargingCollectionFunctionName"
                    minOccurs="0"
                  />
                  <element name="gsmSCFaddressforIMCSI" minOccurs="0"/>
                  <element name="oIMCSI" minOccurs="0"/>
                  <element name="vTIMCSI" minOccurs="0"/>
                  <element name="dIMCS" minOccurs="0"/>
                  <element name="gAAServiceType" minOccurs="0"/>
                  <element name="gAAServiceIdentifier" minOccurs="0"/>
                  <element name="gBAUserSecuritySettings" minOccurs="0"/>
                  <element name="userSecuritySetting" minOccurs="0"/>
                  <element name="userPublicIdentity" minOccurs="0"/>
                  <element name="gAAAuthorizationflag" minOccurs="0"/>
                  <element name="keyLifetime" minOccurs="0"/>
                  <element name="uICCSecurityType" minOccurs="0"/>
                  <element name="nAFGroupIdentity" minOccurs="0"/>
                </all>
              </complexType>
            </element>
          </sequence>
        </extension>
      </complexContent>
    </complexType>
  </element>

  <element name="SuMSubscribedService"

substitutionGroup="xn:SubNetworkOptionallyContainedNrmClass" type="xn:NrmClass"

abstract="true"/>

  <element
    name="CSSubscribedService"
    substitutionGroup="sn:SuMSubscribedService">
    <complexType>
      <complexContent>
        <extension base="xn:NrmClass">
          <sequence>
            <element name="attributes" minOccurs="0">
              <complexType>
                <all>
                  <element name="theService" minOccurs="0"/>
                  <element name="theOffer" minOccurs="0"/>
                  <element name="networkAccessMode" minOccurs="0"/>
                  <element name="basicMSISDNIndicator" minOccurs="0"/>
                  <element name="mSISDNAlertIndicator" minOccurs="0"/>
                  <element name="subscriptionRestriction" minOccurs="0"/>
                  <element name="rSZIlists" minOccurs="0"/>
                  <element name="lSAIdentity" minOccurs="0"/>
                  <element name="lSAPriority" minOccurs="0"/>
                  <element name="lSAPreferentialAccessIndicator" minOccurs="0"/>
                  <element name="lSAActiveModeSupportIndicator" minOccurs="0"/>
                  <element name="lSAOnlyAccessIndicator" minOccurs="0"/>
                  <element name="lSAActiveModeIndicator" minOccurs="0"/>
                  <element name="vPLMNIdentifier" minOccurs="0"/>
                  <element name="accessRestrictionData" minOccurs="0"/>
                  <element name="privacyExceptionList" minOccurs="0"/>
                  <element name="gMLCNumbers" minOccurs="0"/>
                  <element name="mOLRList" minOccurs="0"/>
                  <element name="serviceTypes" minOccurs="0"/>
                  <element name="mobileStationCategory" minOccurs="0"/>
                  <element name="lMUIdentifier" minOccurs="0"/>
                  <element name="subscriberStatus" minOccurs="0"/>
                  <element name="gsmSCFaddresslistForODB" minOccurs="0"/>
                  <element name="provisionOfBearerService" minOccurs="0"/>
                  <element name="provisionOfTeleservice" minOccurs="0"/>
                  <element name="bCAllocation" minOccurs="0"/>
                  <element name="barringOfOutgoingCalls" minOccurs="0"/>
                  <element name="barringOfIncomingCalls" minOccurs="0"/>
                  <element name="barringOfRoaming" minOccurs="0"/>
                  <element name="barringOfPremiumRateCalls" minOccurs="0"/>
                  <element
                    name="barringOfSupplementaryServiceManagement"
                    minOccurs="0"
                  />
                  <element
                    name="barringOfRegistrationOfCallForwarding"
                    minOccurs="0"
                  />
                  <element
                    name="barringOfInvocationOfCallTransfer"
                    minOccurs="0"
                  />
                  <element
                    name="operatorDeterminedBarringPLMNspecificData"
                    minOccurs="0"
                  />
                  <element name="vGCSGroupMembershipList" minOccurs="0"/>
                  <element name="vBSGroupMembershipList" minOccurs="0"/>
                  <element
                    name="broadcastCallInitiationAllowedList"
                    minOccurs="0"
                  />
                  <element
                    name="originatingCAMELSubscriptionInformationOCSI"
                    minOccurs="0"
                  />
                  <element
                    name="terminatingCAMELSubscriptionInformationTCSI"
                    minOccurs="0"
                  />
                  <element
                    name="vMSCTerminatingCAMELSubscriptionInformationVTCSI"
                    minOccurs="0"
                  />
                  <element
                    name="locationInformationSubscriberStateInformation"
                    minOccurs="0"
                  />
                  <element
                    name="uSSDCAMELSubscriptionInformationUCSI"
                    minOccurs="0"
                  />
                  <element name="sSInvocationNotificationSSCSI" minOccurs="0"/>
                  <element
                    name="translationInformationFlagTIFCSI"
                    minOccurs="0"
                  />
                  <element
                    name="dialledServiceCAMELSubscriptionInformationDCSI"
                    minOccurs="0"
                  />
                  <element
                    name="uSSDGeneralCAMELServiceInformationUGCSI"
                    minOccurs="0"
                  />
                  <element
                  name="shortMessageServiceCAMELSubscriptionInformationMOSMSCSI"
                    minOccurs="0"
                  />
                  <element
                  name="shortMessageServiceCAMELSubscriptionInformationMTSMSCSI"
                    minOccurs="0"
                  />
                  <element
                    name="mTSMSCSIVLRNegotiatedCAMELCapabilityHandling"
                    minOccurs="0"
                  />
                  <element name="gsmSCFaddressforCSI" minOccurs="0"/>
                  <element name="iSTAlertTimer" minOccurs="0"/>
                  <element name="cSAllocationRetentionpriority" minOccurs="0"/>
                  <element name="iCSIndicator" minOccurs=”0”/>
                  <element name="sS-Code" minOccurs="0"/>
                  <element name="provisioningState" minOccurs="0"/>
                  <element name="activationState" minOccurs="0"/>
                  <element name="registrationState" minOccurs="0"/>
                  <element name="overrideCategory" minOccurs="0"/>
                  <element name="cLIRestrictionOption" minOccurs="0"/>
                  <element name="forwarded-toNumber" minOccurs="0"/>
                  <element name="forwarded-toSubaddress" minOccurs="0"/>
                  <element name="noReplyConditionTimer" minOccurs="0"/>
                  <element name="maximumEntitledPriority" minOccurs="0"/>
                  <element name="defaultPriority" minOccurs="0"/>
                  <element name="nbrUser" minOccurs="0"/>
                  <element name="nbrSB" minOccurs="0"/>
				  <element name="theCSSupplServiceForCSSS" type="xn:dnList"/>
                </all>
              </complexType>
            </element>
          </sequence>
        </extension>
      </complexContent>
    </complexType>
  </element>

  <element
    name="GPRSSubscribedService" substitutionGroup="sn:SuMSubscribedService">
    <complexType>
      <complexContent>
        <extension base="xn:NrmClass">
          <sequence>
            <element name="attributes" minOccurs="0">
              <complexType>
                <all>
                  <element name="theService" minOccurs="0"/>
                  <element name="theOffer" minOccurs="0"/>
                  <element name="networkAccessMode" minOccurs="0"/>
                  <element name="basicMSISDNIndicator" minOccurs="0"/>
                  <element name="mSISDNAlertIndicator" minOccurs="0"/>
                  <element name="subscriptionRestriction" minOccurs="0"/>
                  <element name="rSZIlists" minOccurs="0"/>
                  <element name="lSAIdentity" minOccurs="0"/>
                  <element name="lSAPriority" minOccurs="0"/>
                  <element name="lSAPreferentialAccessIndicator" minOccurs="0"/>
                  <element name="lSAActiveModeSupportIndicator" minOccurs="0"/>
                  <element name="lSAOnlyAccessIndicator" minOccurs="0"/>
                  <element name="lSAActiveModeIndicator" minOccurs="0"/>
                  <element name="vPLMNIdentifier" minOccurs="0"/>
                  <element name="accessRestrictionData" minOccurs="0"/>
                  <element name="privacyExceptionList" minOccurs="0"/>
                  <element name="gMLCNumbers" minOccurs="0"/>
                  <element name="mOLRList" minOccurs="0"/>
                  <element name="serviceTypes" minOccurs="0"/>
                  <element name="gGSNNumber" minOccurs="0"/>
                  <element name="provisionofTeleservice" minOccurs="0"/>

<element name="subscriberStatus" minOccurs="0"/>
                  <element name="transferofSMoption" minOccurs="0"/>
                  <element name="barringofPacketOrientedServices" minOccurs="0"/>
                  <element name="pDPType" minOccurs="0"/>
                  <element name="pDPAddress" minOccurs="0"/>
                  <element name="accessPointName" minOccurs="0"/>
                  <element name="vPLMNAddressAllowed" minOccurs="0"/>
                  <element name="qualityofServiceSubscribed" minOccurs="0"/>
                  <element name="pDPContextChargingCharacteristics" minOccurs="0"/>
                  <element name="gPRSCAMELSubscriptionInformationGPRSCSI" minOccurs="0"/>
                  <element name="mOShortMessageServiceCAMELSubscriptionInformationMOSMSCSI" minOccurs="0"/>
                  <element name="mTShortMessageServiceCAMELSubscriptionInformationMTSMSCSI” minOccurs="0"/>
                  <element name="mOSMSCSISGSNNegotiatedCAMELCapabilityHandling" minOccurs="0"/>
                  <element name="mTSMSCSISGSNNegotiatedCAMELCapabilityHandling" minOccurs="0"/>
                  <element name="mobilityManagementforGPRSeventnotificationMGCSI" minOccurs="0"/>
                  <element name="mGCSINegotiatedCAMELCapabilityHandling" minOccurs="0"/>
                  <element name="gsmSCFaddressforCSI" minOccurs="0"/>

<element name="closedSubscriberGroupInformation" minOccurs="0"/>

<element name="gSMSCFaddresslistForODB" minOccurs="0"/>

<element name="barringOfOutgoingCalls" minOccurs="0"/>

<element name="barringOfRoaming" minOccurs="0"/>

<element name="operatorDeterminedBarringPLMNspecificData" minOccurs="0"/>

<element name="sTNSR" minOccurs="0"/>

<element name="iCSIndicator" minOccurs="0"/>

<element name="subscribedChargingCharacteristics" minOccurs="0"/>
                  <element name="w-APN" minOccurs="0"/>
                  <element name="listofauthorizedvisitednetworkidentifiers" minOccurs="0"/>
                  <element name="wLANUERemoteIPaddress" minOccurs="0"/>

<element name="staticWLANUERemoteIPAddressList" minOccurs="0"/>
                  <element name="wLANAccess" minOccurs="0"/>
                  <element name="wLANTunnelling" minOccurs="0"/>
                  <element name="wLANDirectIPAccess" minOccurs="0"/>
                  <element name="wAPNAuthorised" minOccurs="0"/>
                  <element name="w-APNBarringTypeList" minOccurs="0"/>
                  <element name="w-APNChargingDataList" minOccurs="0"/>
                  <element name="wLANUERemoteIPAddress" minOccurs="0"/>
                  <element name="accessDependenceFlag" minOccurs="0"/>
                  <element name="i-WLANAccessType" minOccurs="0"/>
                  <element name="chargingData" minOccurs="0"/>
                  <element name="chargingCharacteristics" minOccurs="0"/>
                  <element name="primaryOCSChargingFunctionName" minOccurs="0"/>
                  <element name="secondaryOCSChargingFunctionName" minOccurs="0"/>
                  <element name="primaryChargingCollectionFunctionName" minOccurs="0"/>
                  <element name="secondaryChargingCollectionFunctionName" minOccurs="0"/>
                  <element name="w-APNIdentifierList" minOccurs="0"/>
                  <element name="maxNumberAccessesList" minOccurs="0"/>
                  <element name="maxSubscribedBandwidth" minOccurs="0"/>

<element name=”subscribed3GPPWLANQoSProfile” minOccurs=”0”/>
<element name="sS-Code" minOccurs="0"/>
                  <element name="provisioningState" minOccurs="0"/>
                  <element name="activationState" minOccurs="0"/>
				  <element name="theGPRSSupplServiceForGPRSSS" type="xn:dnList"/>
                </all>
              </complexType>
            </element>
          </sequence>
        </extension>
      </complexContent>
    </complexType>
  </element>

<element name="EPSSubscribedService" substitutio nGroup="sn:SuMSubscribedService">
    <complexType>
      <complexContent>
        <extension base="xn:NrmClass">
          <sequence>
            <element name="attributes" minOccurs="0">
              <complexType>
                <all>
                  <element name="theService" minOccurs="0"/>
                  <element name="theOffer" minOccurs="0"/>
                  <element name="accessPointName" minOccurs="0"/>
                  <element name="accessRestrictionData" minOccurs="0"/>
                  <element name="aPNAMBR" minOccurs="0"/> 
                  <element name="barringofPacketOrientedServices" minOccurs="0"/>
                  <element name="contextIdentifier" minOccurs="0"/>
                  <element name="operatorDeterminedBarringPLMNspecificData" minOccurs="0"/>
                  <element name="pDNAddress" minOccurs="0"/>
                  <element name="rSZILists" minOccurs="0"/>
                  <element name="sTNSR" minOccurs="0"/>
                  <element name="subscribedChargingCharacteristics" minOccurs="0"/>
                  <element name="subscriberStatus" minOccurs="0"/>
                  <element name="networkAccessMode" minOccurs="0"/>
                  <element name="barringOfOutgoingCalls" minOccurs="0"/>
                  <element name="barringOfRoaming" minOccurs="0"/>
                  <element name="privacyExceptionList" minOccurs="0"/>
                  <element name="gMLCNumbers" minOccurs="0"/>
                  <element name="mOLRList" minOccurs="0"/>
                  <element name="serviceTypes" minOccurs="0"/>
                  <element name="iCSIndicator" minOccurs="0"/>

<element name="aPNOIReplacement" minOccurs="0"/>
                  <element name="subscribedUEAMBR" minOccurs="0"/>
                  <element name="aPNConfigurationProfile" minOccurs="0"/>
                  <element name="rFSP" minOccurs="0"/>
                  <element name="vPLMNAddressAllowed-EPS" minOccurs="0"/>
                  <element name="pDNGWIdentity" minOccurs="0"/>
                  <element name="ePSPDNConnectedChargingCharacteristics" minOccurs="0"/>
                  <element name="pDNGWAllocationType" minOccurs="0"/>
                  <element name="aPNLevelAPNOIReplacement" minOccurs="0"/>
                  <element name="closedSubscriberUserGroupInformation" minOccurs="0"/>
                  <element name="listofAuthorizedvisitednetowrkidentifiers" minOccurs="0"/>
                  <element name="staticWLANUERemoteIPAddressList" minOccurs="0"/>
                  <element name="w-APONBarringTypeList" minOccurs="0"/>
                  <element name="w-APNChargingDataList" minOccurs="0"/>
                  <element name="wLANUERemoteIPAddress" minOccurs="0"/>
                  <element name="accessDependenceFlag" minOccurs="0"/>
                  <element name="chargingCharacteristics" minOccurs="0"/>
                  <element name="primaryOCSChargingFunctionName" minOccurs="0"/>

<element name="secondaryOCSChargingFunctionName" minOccurs="0"/>

<element name="primaryChargingCollectionFunctionName" minOccurs="0"/>

<element name="secondaryChargingCollectionFunctionName" minOccurs="0"/>
                  <element name="w-APNIdentifierList" minOccurs="0"/>
                  <element name="maxNumberAccessesList" minOccurs="0"/>
                  <element name="maxSubscribedBandwidth" minOccurs="0"/>
                  <element name="subscribed3GPPWLANQoSProfile" minOccurs="0"/>
                  <element name="permanentUserIdentity" minOccurs="0"/>
                  <element name="mIPSubscriberProfile" minOccurs="0"/>
                  <element name="accessRestrictionData" minOccurs="0"/>

</all>
              </complexType>
            </element>
          </sequence>
        </extension>
      </complexContent>
    </complexType>
  </element>

<element name="IMSSubscribedService" substitutionGroup="sn:SuMSubscribedService">
    <complexType>
      <complexContent>
        <extension base="xn:NrmClass">
          <sequence>
            <element name="attributes" minOccurs="0">
              <complexType>
                <all>
                  <element name="theService" minOccurs="0"/>
                  <element name="theOffer" minOccurs="0"/>
                  <element
                    name="listofauthorizedvisitednetworkidentifiers"
                    minOccurs="0"
                  />
                  <element name="registrationStatus" minOccurs="0"/>
                  <element name="sCSCFName" minOccurs="0"/>
				  <element name="diameterClientAddressofSCSCF" minOccurs="0"/>
                  <element name="theServerCapabilities" type="xn:dn" minOccurs="0"/>
                  <element
                    name="subscribedMediaProfileIdentifier"
                    minOccurs="0"
                  />
                  <element name="initialFilterCriteriaList" minOccurs="0">
		     <complexType>

<sequence>

<element name="initialFilterCriteria" minOccurs="1" maxOccurs="unbounded"/>

</sequence>

</complexType>

</element>
                  <element name="applicationServerInformation" minOccurs="0"/>
                  <element name="serviceIndication" minOccurs="0">
		     <complexType>

<sequence>

<element name="serviceIndication" minOccurs="1" maxOccurs="unbounded"/>

</sequence>

</complexType>

</element>
                  <element
                    name="primaryEventChargingFunctionName"
                    minOccurs="0"
                  />
                  <element
                    name="secondaryEventChargingFunctionName"
                    minOccurs="0"
                  />
                  <element
                    name="primaryChargingCollectionFunctionName"
                    minOccurs="0"
                  />
                  <element
                    name="secondaryChargingCollectionFunctionName"
                    minOccurs="0"
                  />
                  <element name="gsmSCFaddressforIMCSI" minOccurs="0"/>
                  <element name="oIMCSI" minOccurs="0"/>
                  <element name="vTIMCSI" minOccurs="0"/>
                  <element name="dIMCS" minOccurs="0"/>
                  <element name="gAAServiceType" minOccurs="0"/>
                  <element name="gAAServiceIdentifier" minOccurs="0"/>
                  <element name="gBAUserSecuritySettings" minOccurs="0"/>
                  <element name="userSecuritySetting" minOccurs="0"/>
                  <element name="userPublicIdentity" minOccurs="0"/>
                  <element name="gAAAuthorizationflag" minOccurs="0"/>
                  <element name="keyLifetime" minOccurs="0"/>
                  <element name="uICCSecurityType" minOccurs="0"/>
                  <element name="nAFGroupIdentity" minOccurs="0"/>
                </all>
              </complexType>
            </element>
          </sequence>
        </extension>
      </complexContent>
    </complexType>
  </element>

  <element name="SuMServiceProfile" substitutionGroup="xn:SubNetworkOptionallyContainedNrmClass"

type="xn:NrmClass" abstract="true"/>

  <element
    name="CSServiceProfile"
    substitutionGroup="sn:SuMServiceProfile"
  >
    <complexType>
      <complexContent>
        <extension base="xn:NrmClass">
          <sequence>
            <element name="attributes" minOccurs="0">
              <complexType>
                <all>
                  <element name="theSpecification" minOccurs="0"/>
                  <element name="networkAccessMode" minOccurs="0"/>
                  <element name="basicMSISDNIndicator" minOccurs="0"/>
                  <element name="mSISDNAlertIndicator" minOccurs="0"/>
                  <element name="vLRNumber" minOccurs="0"/>
                  <element name="mSCNumber" minOccurs="0"/>
                  <element name="subscriptionRestriction" minOccurs="0"/>
                  <element name="rSZIlists" minOccurs="0"/>
                  <element name="mSCAreaRestrictedFlag" minOccurs="0"/>
                  <element name="oDBinducedBarringData" minOccurs="0"/>
                  <element
                    name="roamingRestrictionDueToUnsupportedFeature"
                    minOccurs="0"
                  />
                  <element name="lSAIdentity" minOccurs="0"/>
                  <element name="lSAPriority" minOccurs="0"/>
                  <element name="lSAPreferentialAccessIndicator" minOccurs="0"/>
                  <element name="lSAActiveModeSupportIndicator" minOccurs="0"/>
                  <element name="lSAOnlyAccessIndicator" minOccurs="0"/>
                  <element name="lSAActiveModeIndicator" minOccurs="0"/>
                  <element name="vPLMNIdentifier" minOccurs="0"/>
                  <element name="accessRestrictionData" minOccurs="0"/>
                  <element name="privacyExceptionList" minOccurs="0"/>
                  <element name="gMLCNumbers" minOccurs="0"/>
                  <element name="mOLRList" minOccurs="0"/>
                  <element name="serviceTypes" minOccurs="0"/>
                  <element name="ageIndicator" minOccurs="0"/>
                  <element name="lMSI" minOccurs="0"/>
                  <element name="mobileStationCategory" minOccurs="0"/>
                  <element name="lMUIdentifier" minOccurs="0"/>
                  <element name="mNRRMSC" minOccurs="0"/>
                  <element name="subscriberStatus" minOccurs="0"/>
                  <element name="notificationToCSEFlagForODB" minOccurs="0"/>
                  <element name="gsmSCFaddresslistForODB" minOccurs="0"/>
                  <element name="messagesWaitingData" minOccurs="0"/>
                  <element name="mobileStationNotReachableFlag" minOccurs="0"/>
                  <element name="memoryCapacityExceededFlag" minOccurs="0"/>
                  <element name="traceReference" minOccurs="0"/>
                  <element name="traceType" minOccurs="0"/>
                  <element name="operationsSystemsIdentity" minOccurs="0"/>
                  <element name="hLRTraceType" minOccurs="0"/>
                  <element name="mAPErrorOnTrace" minOccurs="0"/>
                  <element name="traceActivatedInVLR" minOccurs="0"/>
                  <element name="provisionOfBearerService" minOccurs="0"/>
                  <element name="provisionOfTeleservice" minOccurs="0"/>
                  <element name="bCAllocation" minOccurs="0"/>
                  <element name="checkSSIndicator" minOccurs="0"/>
                  <element name="mSPurgedForNonGPRSFlag" minOccurs="0"/>
                  <element name="barringOfOutgoingCalls" minOccurs="0"/>
                  <element name="barringOfIncomingCalls" minOccurs="0"/>
                  <element name="barringOfRoaming" minOccurs="0"/>
                  <element name="barringOfPremiumRateCalls" minOccurs="0"/>
                  <element
                    name="barringOfSupplementaryServiceManagement"
                    minOccurs="0"
                  />
                  <element
                    name="barringOfRegistrationOfCallForwarding"
                    minOccurs="0"
                  />
                  <element
                    name="barringOfInvocationOfCallTransfer"
                    minOccurs="0"
                  />
                  <element
                    name="operatorDeterminedBarringPLMNspecificData"
                    minOccurs="0"
                  />
                  <element name="vGCSGroupMembershipList" minOccurs="0"/>
                  <element name="vBSGroupMembershipList" minOccurs="0"/>
                  <element
                    name="broadcastCallInitiationAllowedList"
                    minOccurs="0"
                  />
                  <element
                    name="originatingCAMELSubscriptionInformationOCSI"
                    minOccurs="0"
                  />
                  <element
                    name="terminatingCAMELSubscriptionInformationTCSI"
                    minOccurs="0"
                  />
                  <element
                    name="vMSCTerminatingCAMELSubscriptionInformationVTCSI"
                    minOccurs="0"
                  />
                  <element
                    name="locationInformationSubscriberStateInformation"
                    minOccurs="0"
                  />
                  <element
                    name="uSSDCAMELSubscriptionInformationUCSI"
                    minOccurs="0"
                  />
                  <element name="sSInvocationNotificationSSCSI" minOccurs="0"/>
                  <element
                    name="translationInformationFlagTIFCSI"
                    minOccurs="0"
                  />
                  <element
                    name="dialledServiceCAMELSubscriptionInformationDCSI"
                    minOccurs="0"
                  />
                  <element
                    name="uSSDGeneralCAMELServiceInformationUGCSI"
                    minOccurs="0"
                  />
                  <element
                    name="oCSINegotiatedCAMELCapabilityHandling"
                    minOccurs="0"
                  />
                  <element
                    name="sSCSINegotiatedCAMELCapabilityHandling"
                    minOccurs="0"
                  />
                  <element
                    name="vTCSINegotiatedCAMELCapabilityHandling"
                    minOccurs="0"
                  />
                  <element
                  name="shortMessageServiceCAMELSubscriptionInformationMOSMSCSI"
                    minOccurs="0"
                  />
                  <element
                  name="shortMessageServiceCAMELSubscriptionInformationMTSMSCSI"
                    minOccurs="0"
                  />
                  <element
                    name="mOSMSCSIVLRNegotiatedCAMELCapabilityHandling"
                    minOccurs="0"
                  />
                  <element
                    name="mTSMSCSIVLRNegotiatedCAMELCapabilityHandling"
                    minOccurs="0"
                  />
                  <element
                    name="mCSINegotiatedCAMELCapabilityHandling"
                    minOccurs="0"
                  />
                  <element name="vLRSupportedCAMELPhases" minOccurs="0"/>
                  <element name="gsmSCFaddressforCSI" minOccurs="0"/>
                  <element name="vLROfferedCAMEL4CSIs" minOccurs="0"/>
                  <element name="iSTAlertTimer" minOccurs="0"/>
                  <element name="cSAllocationRetentionpriority" minOccurs="0"/>
                  <element name="traceReference2" minOccurs="0"/>
                  <element name="TraceDepth" minOccurs="0"/>
                  <element name="ListofNeTypestoTrace" minOccurs="0"/>
                  <element name="TriggeringEvents" minOccurs="0"/>
                  <element name="ListofInterfacestoTrace" minOccurs="0"/>
                  <element name="iCSIndicator" minOccurs=”0”/>
                  <element name="sS-Code" minOccurs="0"/>
                  <element name="provisioningState" minOccurs="0"/>
                  <element name="activationState" minOccurs="0"/>
                  <element name="registrationState" minOccurs="0"/>
                  <element name="overrideCategory" minOccurs="0"/>
                  <element name="cLIRestrictionOption" minOccurs="0"/>
                  <element name="forwarded-toNumber" minOccurs="0"/>
                  <element name="forwarded-toSubaddress" minOccurs="0"/>
                  <element name="noReplyConditionTimer" minOccurs="0"/>
                  <element name="maximumEntitledPriority" minOccurs="0"/>
                  <element name="defaultPriority" minOccurs="0"/>
                  <element name="nbrUser" minOccurs="0"/>
                  <element name="nbrSB" minOccurs="0"/>
				  <element name="theCSSupplServiceForCSSP" type="xn:dnList"/>

</all>
              </complexType>
            </element>
          </sequence>
        </extension>
      </complexContent>
    </complexType>
  </element>

  <element name="GPRSServiceProfile" substitutionGroup="sn:SuMServiceProfile">
    <complexType>
      <complexContent>
        <extension base="xn:NrmClass">
          <sequence>
            <element name="attributes" minOccurs="0">
              <complexType>
                <all>
                  <element name="theSpecification" minOccurs="0"/>
                  <element name="networkAccessMode" minOccurs="0"/>
                  <element name="basicMSISDNIndicator" minOccurs="0"/>
                  <element name="mSISDNAlertIndicator" minOccurs="0"/>
                  <element name="vLRNumber" minOccurs="0"/>
                  <element name="mSCNumber" minOccurs="0"/>
                  <element name="subscriptionRestriction" minOccurs="0"/>
                  <element name="rSZIlists" minOccurs="0"/>
                  <element name="mSCAreaRestrictedFlag" minOccurs="0"/>
                  <element name="oDBinducedBarringData" minOccurs="0"/>
                  <element
                    name="roamingRestrictionDueToUnsupportedFeature"
                    minOccurs="0"
                  />
                  <element name="lSAIdentity" minOccurs="0"/>
                  <element name="lSAPriority" minOccurs="0"/>
                  <element name="lSAPreferentialAccessIndicator" minOccurs="0"/>
                  <element name="lSAActiveModeSupportIndicator" minOccurs="0"/>
                  <element name="lSAOnlyAccessIndicator" minOccurs="0"/>
                  <element name="lSAActiveModeIndicator" minOccurs="0"/>
                  <element name="vPLMNIdentifier" minOccurs="0"/>
                  <element name="accessRestrictionData" minOccurs="0"/>
                  <element name="privacyExceptionList" minOccurs="0"/>
                  <element name="gMLCNumbers" minOccurs="0"/>
                  <element name="mOLRList" minOccurs="0"/>
                  <element name="serviceTypes" minOccurs="0"/>
                  <element name="ageIndicator" minOccurs="0"/>
                  <element name="sGSNNumber" minOccurs="0"/>
                  <element name="gGSNNumber" minOccurs="0"/>
                  <element name="sGSNarearestrictedflag" minOccurs="0"/>
                  <element
                    name="roamingRestrictedintheSGSNduetounsupportedfeature"
                    minOccurs="0"
                  />
                  <element name="mNRG" minOccurs="0"/>
                  <element name="traceActivatedinSGSN" minOccurs="0"/>
                  <element name="provisionofTeleservice" minOccurs="0"/>
                  <element name="transferofSMoption" minOccurs="0"/>
                  <element name="mSpurgedforGPRSflag" minOccurs="0"/>
                  <element
                    name="barringofPacketOrientedServices"
                    minOccurs="0"
                  />
                  <element name="pDPType" minOccurs="0"/>
                  <element name="pDPAddress" minOccurs="0"/>
                  <element name="accessPointName" minOccurs="0"/>
                  <element name="vPLMNAddressAllowed" minOccurs="0"/>
                  <element name="gGSNlist" minOccurs="0"/>
                  <element name="qualityofServiceSubscribed" minOccurs="0"/>
                  <element name="pDPContextIdentifier" minOccurs="0"/>
                  <element name="pDPContextChargingCharacteristics" minOccurs="0"/>
                  <element name="gPRSCAMELSubscriptionInformationGPRSCSI" minOccurs="0"/>
                  <element name="mOShortMessageServiceCAMELSubscriptionInformationMOSMSCSI" minOccurs="0"/>
                  <element name="mTShortMessageServiceCAMELSubscriptionInformationMTSMSCSI" minOccurs="0"/>
                  <element name="mOSMSCSISGSNNegotiatedCAMELCapabilityHandling" minOccurs="0"/>
                  <element name="mTSMSCSISGSNNegotiatedCAMELCapabilityHandling" minOccurs="0"/>
                  <element name="mobilityManagementforGPRSeventnotificationMGCSI" minOccurs="0"/>
                  <element name="mGCSINegotiatedCAMELCapabilityHandling" minOccurs="0"/>
                  <element name="gPRSCSINegotiatedCAMELCapabilityHandling" minOccurs="0"/>
                  <element name="sGSNSupportedCAMELPhases" minOccurs="0"/>
                  <element name="sGSNOfferedCAMEL4CSIs" minOccurs="0"/>
                  <element name="gsmSCFaddressforCSI" minOccurs="0"/>
                  <element
                    name="subscribedChargingCharacteristics"
                    minOccurs="0"
                  />
                  <element name="w-APN" minOccurs="0"/>
                  <element
                    name="listofauthorizedvisitednetworkidentifiers"
                    minOccurs="0"
                  />
                  <element name="wLANUERemoteIPaddress" minOccurs="0"/>
                  <element name="wLANAccess" minOccurs="0"/>
                  <element name="wLANTunnelling" minOccurs="0"/>
                  <element name="wLANDirectIPAccess" minOccurs="0"/>
                  <element name="wAPNAuthorised" minOccurs="0"/>
                  <element name="w-APNBarringType" minOccurs="0"/>
                  <element name="w-APNChargingData" minOccurs="0"/>
                  <element name="wLANUERemoteIPAddress" minOccurs="0"/>
                  <element name="accessIndependenceFlag" minOccurs="0"/>
                  <element name="i-WLANAccessType" minOccurs="0"/>
                  <element name="chargingData" minOccurs="0"/>
                  <element name="chargingCharacteristics" minOccurs="0"/>
                  <element name="primaryOCSChargingFunctionName" minOccurs="0"/>
                  <element
                    name="secondaryOCSChargingFunctionName"
                    minOccurs="0"
                  />
                  <element name="traceReference2" minOccurs="0"/>
                  <element name="TraceDepth" minOccurs="0"/>
                  <element name="ListofNeTypestoTrace" minOccurs="0"/>
                  <element name="TriggeringEvents" minOccurs="0"/>
                  <element name="ListofInterfacestoTrace" minOccurs="0"/>
                  <element
                    name="primaryChargingCollectionFunctionName"
                    minOccurs="0"
                  />
                  <element name="gSMSCFaddresslistForODB" minOccurs="0"/>
                  <element name="iPSMGWNumber" minOccurs="0"/>
                  <element name="mNRR-SGSN" minOccurs="0"/>
                  <element name="notificationToCSEFlagForODB" minOccurs="0"/>
				  <element name="thePSCommonPar" type="xn:dn"/>

</all>
              </complexType>
            </element>
          </sequence>
        </extension>
      </complexContent>
    </complexType>
  </element>

<element name="EPSServiceProfile" substitutionGroup="sn:SuMServiceProfile">
    <complexType>
      <complexContent>
        <extension base="xn:NrmClass">
          <sequence>
            <element name="attributes" minOccurs="0">
              <complexType>
                <all>
                  <element name="theSpecification" minOccurs="0"/>

<element name="aPNAMBR" minOccurs="0"/>
                  <element name="contextIdentifier" minOccurs="0"/>
                  <element name="pDNAddress" minOccurs="0"/>
                  <element name="aPNOIReplacement" minOccurs="0"/>
                  <element name="subscribedUEAMBR" minOccurs="0"/>
                  <element name="aPNConfigurationProfile" minOccurs="0"/>
                  <element name="rFSP" minOccurs="0"/>
                  <element name="pDNGWIdentity" minOccurs="0"/>
                  <element name="ePSPDNConnectionChargingCharacteristics" minOccurs="0"/>
                  <element name="pDNGWAllocationType" minOccurs="0"/>
                  <element name="aPNLevelAPNOIReplacement" minOccurs="0"/>
                  <element name="roamingRestrictionsDueToUnsupportedFeatureMME" minOccurs="0"/>
                  <element name="roamingRestrictionsDueToUnsupportedFeatureSGSN" minOccurs="0"/>
                  <element name="mSPurgedForEPSFlag" minOccurs="0"/>
                  <element name="uRRPMME" minOccurs="0"/>
                  <element name="mMEName" minOccurs="0"/>
                  <element name="sGSNName" minOccurs="0"/>
                  <element name="iWFNumber" minOccurs="0"/>
                  <element name="sGSNAreaRestrictedFlag" minOccurs="0"/>
                  <element name="permanentUserIdentity" minOccurs="0"/>

<element name="vPLMNAddressAllowed-EPS" minOccurs="0"/>

<element name="thePSCommonParameters" type="xn:dn"/>

<element name="theOptHandover3GPP2Parameters" type="xn:dn"/>

<element name="theNon3GPPAccessParameters" type="xn:dn"/>

</all>
              </complexType>
            </element>
          </sequence>
        </extension>
      </complexContent>
    </complexType>
  </element>

<element name="PSCommonParameters" substitutionGroup="xn: SubNetworkOptionallyContainedNrmClass">
    <complexType>
      <complexContent>
        <extension base="xn:NrmClass">
          <sequence>
            <element name="attributes" minOccurs="0">
              <complexType>
                <all>
                  <element name="theIWANParameters" type="xn:dnList"/>
                  <element name="rSZILists" minOccurs="0"/>
                  <element name="roamingRestrictedintheSGSNduetounsupportedfeature" minOccurs="0"/>
                  <element name="accessRestrictionData" minOccurs="0" />
                  <element name="subscriberStatus" minOccurs="0"/>

<element name="barringOfOutgoingCalls" minOccurs="0"/>

<element name="barringOfRoaming" minOccurs="0"/>

<element name="operatorDeterminedBarringPLMNspecificData" minOccurs="0"/>

<element name="barringofPacketOrientedServices" minOccurs="0"/>

<element name="traceReference2" minOccurs="0"/>

<element name="traceDepth" minOccurs="0"/>

<element name="listOfNETypestoTrace" minOccurs="0"/>

<element name="triggeringEvents" minOccurs="0"/>

<element name="listOfInterfacesToTrace" minOccurs="0"/>

<element name="traceActivatedinSGSN" minOccurs="0"/>

<element name="iPAddressOfTraceCollectionEntity" minOccurs="0"/>

<element name="accessPointName" minOccurs="0"/>

<element name="privacyExceptionList" minOccurs="0"/>

<element name="gMLCNumbers" minOccurs="0"/>

<element name="iCSIndicator" minOccurs="0"/>

<element name="mOLRList" minOccurs="0"/>

<element name="serviceTypes" minOccurs="0"/>

<element name="subscribedChargingCharacteristics" minOccurs="0"/>

<element name="sTNSR" minOccurs="0"/>

<element name="networkAccessMode" minOccurs="0"/>

<element name="closedSubscriberGroupInformation" minOccurs="0"/>

<element name="theIWANPar" type="xn:dn"/>

</all>
              </complexType>
            </element>
          </sequence>
        </extension>
      </complexContent>
    </complexType>
  </element>

<element name="IWANParameters" substitutionGroup="xn: SubNetworkOptionallyContainedNrmClass">
    <complexType>
      <complexContent>
        <extension base="xn:NrmClass">
          <sequence>
            <element name="attributes" minOccurs="0">
              <complexType>
                <all>
                  <element name="w-APN" minOccurs="0"/>
                  <element name="listofauthorizedvisitednetworkidentifiers" minOccurs="0"/>
                  <element name="3GPPAAAServerName" minOccurs="0" />
                  <element name="3GPPAAAProxyName" minOccurs="0"/>

<element name="wLANUERemoteIPaddress" minOccurs="0"/>

<element name="statisWLANUERemoteIPAddressList" minOccurs="0"/>

<element name="w-APNBarringTypeList" minOccurs="0"/>

<element name="w-APNChargingDataList" minOccurs="0"/>

<element name="accessDependenceFlag" minOccurs="0"/>

<element name="i-WLANAccessType" minOccurs="0"/>

<element name="wLANIdentifierList" minOccurs="0"/>

<element name="maxNumberAccessesList" minOccurs="0"/>

<element name="maxSubscribedBandwidth" minOccurs="0"/>

<element name="subscribed3GPPWLANQoSProfile" minOccurs="0"/>

<element name="chargingChracteristics" minOccurs="0"/>

<element name="primaryOCSChargingFunctionName” minOccurs="0"/>

<element name="secondaryOCSChargingFunctionName" minOccurs="0"/>

<element name="primaryChargingCollectionFunctionName" minOccurs="0"/>

<element name="secondaryChargingCollectionFunctionName" minOccurs="0"/>

<element name="userStatus" minOccurs="0"/>

</all>
              </complexType>
            </element>
          </sequence>
        </extension>
      </complexContent>
    </complexType>
  </element>

<element name="OptHandover3GPP2Parameters" substitutionGroup="xn: SubNetworkOptionallyContainedNrmClass">
    <complexType>
      <complexContent>
        <extension base="xn:NrmClass">
          <sequence>
            <element name="attributes" minOccurs="0">
              <complexType>
                <all>
                  <element name="rATType" minOccurs="0"/>

</all>
              </complexType>
            </element>
          </sequence>
        </extension>
      </complexContent>
    </complexType>
  </element>

<element name="Non3GPPAccessParameters" substitutionGroup="xn: SubNetworkOptionallyContainedNrmClass">
    <complexType>
      <complexContent>
        <extension base="xn:NrmClass">
          <sequence>
            <element name="attributes" minOccurs="0">
              <complexType>
                <all>
                  <element name="rATType" minOccurs="0"/>

<element name="visitedNetworkIdentifier" minOccurs="0"/>

<element name="mIPSubscriberProfile" minOccurs="0"/>

<element name="permanentUserIdentity" minOccurs="0"/>

</all>
              </complexType>
            </element>
          </sequence>
        </extension>
      </complexContent>
    </complexType>
  </element>

<element name="IMSServiceProfile" substitutionGroup="sn:SuMServiceProfile">
    <complexType>
      <complexContent>
        <extension base="xn:NrmClass">
          <sequence>
            <element name="attributes" minOccurs="0">
              <complexType>
                <all>
                  <element name="theSpecification" minOccurs="0"/>
                  <element name="listofauthorizedvisitednetworkidentifiers" minOccurs="0"/>
                  <element name="registrationStatus" minOccurs="0"/>
                  <element name="sCSCFName" minOccurs="0"/>
                  <element name="diameterClientAddressofSCSCF" minOccurs="0"/>
                  <element name="theServerCapabilities" type="xn:dn" minOccurs="0"/>
                  <element name="subscribedMediaProfileIdentifier" minOccurs="0"/>
                  <element name="initialFilterCriteriaList" minOccurs="0">
		    <complexType>

<sequence>

<element name="initialFilterCriteria" minOccurs="1" maxOccurs="unbounded"/>

</sequence>

</complexType>

</element>
                  <element name="applicationServerInformation" minOccurs="0"/>
                  <element name="serviceIndicationList" minOccurs="0">
		     <complexType>

<sequence>

<element name="serviceIndication" minOccurs="1" maxOccurs="unbounded"/>

</sequence>

</complexType>

</element>
                  <element
                    name="primaryEventChargingFunctionName"
                    minOccurs="0"
                  />
                  <element
                    name="secondaryEventChargingFunctionName"
                    minOccurs="0"
                  />
                  <element
                    name="primaryChargingCollectionFunctionName"
                    minOccurs="0"
                  />
                  <element
                    name="secondaryChargingCollectionFunctionName"
                    minOccurs="0"
                  />
                  <element name="gsmSCFaddressforIMCSI" minOccurs="0"/>
                  <element name="iMSSFaddressforIMCSI" minOccurs="0"/>
                  <element name="oIMCSI" minOccurs="0"/>
                  <element name="vTIMCSI" minOccurs="0"/>
                  <element name="dIMCS" minOccurs="0"/>
                  <element name="gAAServiceType" minOccurs="0"/>
                  <element name="gAAServiceIdentifier" minOccurs="0"/>
                  <element name="gBAUserSecuritySettings" minOccurs="0"/>
                  <element name="userSecuritySetting" minOccurs="0"/>
                  <element name="userPublicIdentity" minOccurs="0"/>
                  <element name="gAAAuthorizationflag" minOccurs="0"/>
                  <element name="keyLifetime" minOccurs="0"/>
                  <element name="uICCSecurityType" minOccurs="0"/>
                  <element name="nAFGroupIdentity" minOccurs="0"/>
				  <element name="thePublicId" type="xn:dnList"/>
                </all>
              </complexType>
            </element>
          </sequence>
        </extension>
      </complexContent>
    </complexType>
  </element>

<complexType name="IMSPublicIdentificationType">

<complexContent>

<extension base="sn:SuMIdentityType">

<all>

<element name="publicUserIdentity" type="string" minOccurs="0"/>

<element name="barringIndication" type="sn:binEnum" minOccurs="0"/>

</all>

</extension>

</complexContent>

</complexType>

<element name="IMSPublicIdentification" type="sn:IMSPublicIdentificationType" substitutionGroup="sn:SuMIdentity"/>

<element name="SuMManagedElement" substitutionGroup="xn:SubNetworkOptionallyContainedNrmClass">
    <complexType>
      <complexContent>
        <extension base="xn:NrmClass">
          <sequence>
            <element name="attributes" minOccurs="0">
              <complexType>
                <all>
                  <element name="theSubscriptionFunction" type="xn:dnList"/>
                  <element name="theServiceProviderFunction" type="xn:dnList"/>
                </all>
              </complexType>
            </element>
          </sequence>
        </extension>
      </complexContent>
    </complexType>
  </element>

<simpleType name="binEnum">

<restriction base="string">

<enumeration value="FALSE"/>

<enumeration value="TRUE"/>

</restriction>

</simpleType>

<simpleType name="multinumberingMSISDNIndicator">

<restriction base="string">

<enumeration value="BASIC"/>

<enumeration value="ALERT"/>

</restriction>

</simpleType>

<complexType name="multinumberingMSISDNList">

<sequence minOccurs="0" maxOccurs="unbounded">

<element name="mSISDN" type="string"/>

<element name="indicator" type="sn:multinumberingMSISDNIndicator"/>

</sequence>

</complexType>

<complexType name="ServerCapabilitiesType">

<complexContent>

<extension base="sn:SuMServiceParameterType">

<all>

<element name="serverCapabilities"/>

</all>

</extension>

</complexContent>

</complexType>

<element name="ServerCapabilities" type="sn:ServerCapabilitiesType" substitutionGroup="sn:SuMServiceParameter"/>

<complexType name="SuMIdentityType">

<complexContent>

<restriction base="xn:NrmClass"/>

</complexContent>

</complexType>

<complexType name="SuMServiceParameterType">

<complexContent>

<restriction base="xn:NrmClass"/>

</complexContent>

</complexType>

<element name="SuMIdentity" type="sn:SuMIdentityType" substitutionGroup="xn:SubNetworkOptionallyContainedNrmClass" abstract="true"/>

<element name="SuMServiceParameter" type="sn:SuMServiceParameterType" substitutionGroup="xn:SubNetworkOptionallyContainedNrmClass" abstract="true"/>

</schema>

End of Modifications