3GPP TSG-SA5 (Telecom Management)	S5 e100038

Meeting SA5#71, 10-14 May 2010, Montreal, Canada	revision of S5e100033

| CR-Form-v9.6 |
| --- |
| CHANGE REQUEST |
| ( | 32.592 | CR | 0001 | ( rev | - | ( Current version: | 9.0.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network | X | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Modify errors in spec references, table number references, and valid value range |
| --- | --- |
| Source to WG: ( | ETRI |
| Source to TSG: ( | SA5 |
| Work item code: ( | OAM10 |  | Date: ( | 14/05/2010 |
| Category: ( | F |  | Release: ( | Rel-10 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) |
| Reason for change: ( | There are errors in spec references, table number references, and valid value range. |
| Summary of change: ( | 1. Correct the wrong spec number references. 2. Change the mismatched valid value range different from TS 36.331. 3. Correct the wrong table number references. |
| Consequences if ( not approved: | There will be errors on the referenced spec numbers, referenced table numbers, and the valid value, which could lead to a wrong implementation. |
| Clauses affected: ( | 6.1.1.7, 6.1.1.10 |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

1st modifications

#### 6.1.1.7	Uplink Power Control

This table contains parameters used for computing UL power.

| Parameter Name | Description | Valid Values | TDD/FDD | Applicable to HNB |
| --- | --- | --- | --- | --- |
| p0NominalPUSCH | Denotes the parameter used to compute the UL UE transmit power for transmission on PUSCH for semi-persistent grants. This parameter corresponds to p0-NominalPUSCH parameter specified in 3GPP TS 36.331 section 6.3.2 and PO_NoMINAL_PUSCH(0) parameter specified in 3GPP TS 36.213 section 5.1.1.1 | int[-126..24] This parameter is settable by the operator. | TDD/FDD | No |
| Alpha | Denotes the parameter used to compute the UL UE transmit power for transmission on PUSCH. aIn corresponds to value of 0.n and aI1 corresponds to value of 1. This parameter corresponds to alpha parameter specified in 3GPP TS 36.331 section 6.3.2 and to α parameter specified in 3GPP TS 36.213 section 5.1.1.1. | Enum {al0, al04, al05, al06, al07, al08, al09, al1} This parameter is settable by the operator. | TDD/FDD | No |
| p0NominalPUCCH | Denotes the parameter used to compute the UL UE transmit power for transmission on PUCCH. This parameter corresponds to p0-NominalPUCCH parameter specified in 3GPP TS 36.331 section 6.3.2 and PO_NoMINAL_PUCCH parameter specified in 3GPP TS 36.213 section 5.1.2.1 | int[-127..-96] This parameter is settable by the operator. | TDD/FDD | No |
| deltaF-PUCCH-Format1 | Each value of deltaF-PUCCH-FormatX corresponds to parameter ΔF_PUCCH(X), where XÎ{1,1b,2,2a,2b}, specified in 36.331 3GPP TS 36.331 section 6.3.2 and in 3GPP TS 36.213 section 5.1.2. Value of deltaFn corresponds to n dB. | Enum{deltaF-2, deltaF0, deltaF2} This parameter is not settable by the operator. | TDD/FDD | No |
| deltaF-PUCCH-Format1b | Each value of deltaF-PUCCH-FormatX corresponds to parameter ΔF_PUCCH(X), where XÎ{1,1b,2,2a,2b}, specified in 36.331 3GPP TS 36.331 section 6.3.2 and in 3GPP TS 36.213 section 5.1.2. Value of deltaFn corresponds to n dB. | Enum{deltaF1, deltaF3, deltaF5} This parameter is not settable by the operator. | TDD/FDD | No |
| deltaF-PUCCH-Format2 | Each value of deltaF-PUCCH-FormatX corresponds to parameter ΔF_PUCCH(X), where XÎ{1,1b,2,2a,2b}, specified in 36.331 3GPP TS 36.331 section 6.3.2 and in 3GPP TS 36.213 section 5.1.2. Value of deltaFn corresponds to n dB. | Enum{deltaF-2, deltaF0, deltaF1, deltaF2} This parameter is not settable by the operator. | TDD/FDD | No |
| deltaF-PUCCH-Format2a | Each value of deltaF-PUCCH-FormatX corresponds to parameter ΔF_PUCCH(X), where XÎ{1,1b,2,2a,2b}, specified in 36.331 3GPP TS 36.331 section 6.3.2 and in 3GPP TS 36.213 section 5.1.2. Value of deltaFn corresponds to n dB. | Enum{deltaF-2, deltaF0, deltaF2} This parameter is not settable by the operator. | TDD/FDD | No |
| deltaF-PUCCH-Format2b | Each value of deltaF-PUCCH-FormatX corresponds to parameter ΔF_PUCCH(X), where XÎ{1,1b,2,2a,2b}, specified in 36.331 3GPP TS 36.331 section 6.3.2 and in 3GPP TS 36.213 section 5.1.2. Value of deltaFn corresponds to n dB. | Enum{deltaF-2, deltaF0, deltaF2} This parameter is not settable by the operator. | TDD/FDD | No |
| deltaPreambleMsg3 | Denotes the parameter used to compute the UL UE transmit power for transmission of random access response grant. This parameter corresponds to deltaPreambleMsg3 parameter specified in 3GPP TS 36.331 section 6.3.2 and to ΔPREAMBLE_Msg3 parameter specified in 3GPP TS 36.213 section 5.1.1.1 | int[-1..6] This parameter is not settable by the operator. | TDD/FDD | No |

Next modifications

#### 6.1.1.10	TDD Frame Structure

This table contains parameters related to configuration of TDD physical layer frame structure.

| Parameter Name | Description | Valid Values | TDD/FDD | Applicable to HNB |
| --- | --- | --- | --- | --- |
| subFrameAssignment | Defines the DL/UL subframe configuration where sa0 corresponds to Configuration 0, sa1 to Configuration 1 and so on. Corresponds to subframAssignment specified in 3GPP TS 36.331 section 6.3.2 and to 3GPP TS 36.211 table 4.2-2. | Enum {sa0, sa1, sa2, sa3, sa4, sa5, sa6} This parameter is settable by operator. | TDD | No |
| specialSubframePatterns | Defines the configuration of the special subframe that contains the guard period between the downlink and uplink transmissions. Corresponds to the specialSubframePatterns specified in 3GPP TS 36.331 section 6.3.2 and to 3GPP TS 36.211 table 4.2-1. | Enum {ssp0, ssp1, ssp2, ssp3, ssp4, ssp5, ssp6, ssp7, ssp8} This parameter is settable by operator. | TDD | No |

End of modifications

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.