3GPP TSG-SA5 (Telecom Management)	S5-101496

Meeting SA5#71, 10-14 May 2010, Montreal, Canada	revision of S5-101205

| CR-Form-v9.6 |
| --- |
| CHANGE REQUEST |
| ( | 32.280 | CR | 0005 | ( rev | - | ( Current version: | 9.1.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | x |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Correction of AoC UNI Protocol Mapping |
| --- | --- |
| Source to WG: ( | Deutsche Telekom |
| Source to TSG: ( | SA5 |
| Work item code: ( | eAoC |  | Date: ( | 14/05/2010 |
| Category: ( | C |  | Release: ( | Rel-10 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) |
| Reason for change: ( | A number of legacy UNI parameters defined in the AoC UNI Protocol Specification (TS 24.647) are currently not supported by the AoC Information Model of TS 32280. Particularly, none of the “Charged Items” values are currently supported. For parameters needed in the future, the mapping guidance in Annex C2 must be enriched to populate these AoC UNI parameters. For Special charging code, Special charging arrangement and Billing Identification, no corresponding Ro information is available. Since these elements are not useful for AoC in IMS, it is proposed to drop them. |
| Summary of change: ( | Add mapping guidance to support missing Charged Items in Annex C2. Delete Special charging code, Special charging arrangement and Billing Identification from Annex C2. Delete Editor’s notes in Annex C2. |
| Consequences if ( not approved: | Wrong or incomplete AoC information mapping to Charging Information Elements.. |
| Clauses affected: ( | Annex C2 |
|  | Y | N |  |  |
| Other specs ( |  | x | Other core specifications ( |  |
| affected: |  | x | Test specifications |  |
|  |  | x | O&M Specifications |  |
| Other comments: ( |  |

1st Modified Section

## C.2	AoC information mapping to Charging Information Elements

Herby is a conceptual mapping advising how to populate the Charging Information Element provided to the UE (as described in TS 24.647 [208]) out of the AoC Information.

| Charging Information Element | Mapping guidance |
| --- | --- |
| Expressing Charging Rates |  |
| Price per time unit | When only one Rate Element with Unit_Type = TIME exists |
| Free of charge | When only one Rate Element with Unit_Type = MONEY and Unit-Value = 0 exists |
| Flat rate | When only one Rate Element with Unit_Type = MONEY and Unit-Value > 0 exists |
| Not available | No Rate Elements provided |
| Charged Items |  |
| Basic communication | When the Rate Element contains Reason-Code = Usage or no Reason Code is available. NOTE: If no other Charged Items are applicable, Basic Communication shall be used as default value. |
| Communication attempt | This parameter may be populated when the Rate Element contains Reason-Code = Communication-Attempt-Charge NOTE: Alternatively, this information may be mapped into “Operation of service” (see below). |
| Communication setup | This parameter may be populated when the Rate Element contains Reason-Code = Set-Up-Charge NOTE: Alternatively, this information may be mapped into “Operation of service” (see below). |
| Operation of service | This parameter may be populated depending on Service- specific Information or when the Rate Element contains Reason-Code <> Usage. NOTE: If this parameter is populated depending on the Reason-Code, Communication Attempt and Communication setup shall not be used. |
| Recorded Charges | Accumulated cost in AoC_Cost_Information |

Note: Other legacy Charging Information Elements (e.g. Special charging code, Special charging arrangement and Billing Identification) are not supported in IMS.

End of modifications

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.