3GPP TSG-SA5 (Telecom Management)	S5-102919

SA5#74-CH, 8 - 10 Nov 2010, Issy-les-Moulineaux, FRANCE	revision of S5-102xxx

| CR-Form-v9.6 |
| --- |
| CHANGE REQUEST |
| ( | 32.260 | CR | 0108 | ( rev | 1 | ( Current version: | 10.1.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Replace the Authorized-QoS AVP name with Authorised-QoS AVP |
| --- | --- |
| Source to WG: ( | ZTE |
| Source to TSG: ( | S5 |
| Work item code: ( | CH10 |  | Date: ( | 10/11/2010 |
| Category: ( | F |  | Release: ( | Rel-10 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) |
| Reason for change: ( | Unify the usage of Authorised-QoS AVP and Authorized-QoS AVP in order to avoid the confusion. |
| Summary of change: ( | Replace the Authorized-QoS AVP name with Authorised-QoS AVP |
| Consequences if ( not approved: | Inconsistent name definition between Authorised-QoS AVP and Authorized-QoS AVP |
| Clauses affected: ( | 6.3.2 |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  | X |  | O&M Specifications | 32.299 |
| Other comments: ( |  |

First change

### 6.3.2	Detailed Message Format for offline charging

The following chapter specifies per Operation Type the charging data that are sent by each of the IMS network elements for:

- IMS session and IMS event (S/I/S/E)

- S-CSCF, E-CSCF, P-CSCF, MGFC, AS, IBCF

- IMS session only (S/I/S)

- MRFC

- IMS event only (E)

- I-CSCF, BGCF

The Operation Types are listed in the following order: S (start)/I (interim)/S (stop)/E (event). Therefore, when all Operation Types are possible it is marked as SISE. If only some Operation Types are allowed for a node, only the appropriate letters are used (i.e. SIS or E) as indicated in the table heading. The omission of an Operation Type for a particular field is marked with "-" (i.e. SI-E). Also, when an entire field is not allowed in a node the entire cell is marked as "-".

Table 6.3.2.1 illustrates the basic structure of the supported fields in the Charging Data Request message for IMS offline charging.

Table 6.3.2.1 : Supported fields in Charging Data Request Message

| Field | Node Type | S-CSCF | E-CSCF | P-CSCF | I-CSCF | MRFC | MGCF | BGCF | AS | IBCF |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Supported Operation Types | S/I/S/E | S/I/S/E | S/I/S/E | E | S/I/S | S/I/S/E | E | S/I/S/E | S/I/S/E |
| Session Identifier | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| Originator Node | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| Originator Domain | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| Destination Domain | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| Operation Type | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| Operation Number | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| Operation Identifier | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| User Name | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| Operation Interval | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| Origination State | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| Origination Timestamp | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| Proxy Information | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| Route Information | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| Operation Token | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| Subscriber Identifier | SISE | SISE | SISE | - | SIS | - | - | SISE | SISE |
| Service Information with PS and IMS Information |
| Event Type | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| Role of Node | SISE | SISE | SISE | E | --- | SISE | E | SISE | SISE |
| Node Functionality | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| User Session Id | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| Outgoing Session ID | - | - | - | - | - | - | - | SISE | - |
| Session Priority | S--E | S--E | S--E | E | S-- | S--E | E | S--E | S--E |
| Calling Party Address | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| Called Party Address | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| Number Portability routing information | S--E | S--E | - | E | - | S--E | E | S--E | - |
| Carrier Select routing information | S--E | S--E | - | E | - | S--E | E | S--E | - |
| Alternate Charged Party Address | - | - | - | - | - | - | - | S--- | - |
| Requested Party Address | S--E | S--E | - | - | S-- | - | - | S--E | S--E |
| Called Asserted Identity | S--E | S--E | - | - | S-- | - | - | S--E | S--E |
| Associated URI (see note 5) | ---E | ---E | ---E | E | - | - | - | - | ---E |
| Time stamps (see note 3) | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| Application server Information (see note 1) | SISE | SISE | - | - | SIS | - | - | - | - |
| Inter Operator Identifiers (see note 1) | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| IMS Charging Identifier | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| Early Media Description (see note 4) | S--E | S--E | S--E | - | S-- | S--E | E | S--E | S--E |
| SDP Session Description | SI-- | SI-- | SI-- | - | SI-- | SI-- | - | SI-- | SI-- |
| SDP Media Component (see note 4) | SI-- | SI-- | SI-- |  | SI-- | SI-- | - | SI-- | SI-- |
| GGSN Address | SI-- | SI-- | SI-- |  | SI-- | SI-- | - | SI-- | - |
| Served Party (see note 1) | - | - | SISE | - | - | - | - | - | - |
| Authorised QoS (see note 1) | - | - | SI-- | - | - | - | - | - | - |
| Server Capabilities (see note 1) | - | - | - | E | - | - | - | - | - |
| Trunk Group ID (see note 1) | - | - | - | - | - | SISE | - | - | - |
| Bearer Service (see note 1) | - | - | - | - | - | SISE | - | - | - |
| Service Id (see note 1) | - | - | - | - | SIS | - | - | - | - |
| Service Specific Info (see note 1) | - | - | - | - | - | - | - | SISE | - |
| Message Bodies (see note 2) | SISE | SISE | SISE |  |  | SISE |  | SISE | SISE |
| Cause Code | --SE | --SE | --SE | E | --S | --SE | E | --SE | --SE |
| Access Network Information | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| IMS Communication Service ID | S--E | S--E | - | - | - | - | - | S--E | S--E |
| Real Time Tariff Information | SISE | - | - | - | - | SISE | - | SISE | SISE |
| NOTE 1: Only present if available in the CTF of the IMS node. NOTE 2: Present only if Messages Bodies is included in the SIP message that triggered the Charging Data Request. NOTE 3: Only present if ACR is triggered on a SIP message (e.g. SIP INVITE, SIP UPDATE). NOTE 4: To be determined for presence in IBCF. NOTE 5: Only present if ACR is triggered on SIP REGISTER 200 OK. |

Table 6.3.2.2 illustrates the basic structure of the supported fields in the Charging Data Response message for IMS offline charging.

Table 6.3.2.2 : Supported fields in Charging Data Response Message

| Field | Node Type | S-CSCF | E-CSCF | P-CSCF | I-CSCF | MRFC | MGCF | BGCF | AS | IBCF |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Supported Operation Types | S/I/S/E | S/I/S/E | S/I/S/E | E | S/I/S | S/I/S/E | E | S/I/S/E | S/I/S/E |
| Session Identifier | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| Originator Node | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| Originator Domain | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| Destination Domain | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| Operation Type | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| Operation Number | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| Operation Identifier | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| User Name | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| Operation Interval | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| Origination State | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| Origination Timestamp | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| Proxy Information | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |
| Route Information | SISE | SISE | SISE | E | SIS | SISE | E | SISE | SISE |

End of changes

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.