3GPP TSG-SA5 (Telecom Management)	S5-103283

SA5#74-OAM , 15 - 19 Nov 2010; Jacksonville, USA	revision of S5-103095

| CR-Form-v9.6 |
| --- |
| CHANGE REQUEST |
| ( | 32.592 | CR | 0005 | ( rev | 1 | ( Current version: | 10.1.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network | X | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Correct errors in spec references, table number references, valid values |
| --- | --- |
| Source to WG: ( | ETRI |
| Source to TSG: ( | S5 |
| Work item code: ( | HNB_eHNB-OAM_Type1 |  | Date: ( | 19/11/2010 |
| Category: ( | A |  | Release: ( | Rel-10 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) |
| Reason for change: ( | There are errors in spec references, table number references, valid values. |
| Summary of change: ( | Correct the wrong spec and table number references in 6.1.1.9. Correct the wrong valid values in 6.1.2.3, 6.1.5.1.7 and 6.1.5.2.1. |
| Consequences if ( not approved: | There will be errors on the referenced spec numbers, referenced table numbers and referenced valid values, which could lead to a wrong implementation. |
| Clauses affected: ( | 6.1.1.9, 6.1.2.3, 6.1.5.1.7, 6.1.5.2.1 |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

First change

#### 6.1.1.9	Positioning reference Signals

This table contains parameters related to Positioning Reference Signals (PRS) configuration.

| Parameter Name | Description | Valid Values | TDD/FDD | Applicable to HNB |
| --- | --- | --- | --- | --- |
| NumPRSResourceBlocks | Defines the number of resource blocks used for PRS. Corresponds to the parameter NRBPRS in 3GPP TS 36.211 section 6.10.4.2 | UnsignedInt This parameter is settable by the operator. | TDD/FDD | No |
| PRSConfigurationIndex | Corresponds to the PRS configuration index defined as parameter IPRS in 3GPP TS 36. 211section 6.10.4.3 and Table 6.10.4.3-1 | int[0..4095] This parameter is settable by the operator. | TDD/FDD | No |
| NumConsecutivePRSSubfames | Defines the number of consecutive positioning subframes. Corresponds to the parameter NPRS in 3GPP TS 36.211 section 6.10.4.3. Value n1 corresponds to number 1 etc. | Enum {n1, n2, n4, n6} This parameter is settable by the operator. | TDD/FDD | No |

Next change

#### 6.1.2.3	Uplink SCH

This table contains parameters related to UL SCH configuration.

| Parameter Name | Description | Valid Values | TDD/FDD | Applicable to HNB |
| --- | --- | --- | --- | --- |
| maxHARQ-Tx | Maximum number of UL HARQ transmissions. Corresponds to parameter maxHARQ-Tx specified in 3GPP TS 36.331 section 6.3.2 and in 3GPP TS 36.321 section 5.4.2.2 | Enum{n1, n2, n3, n4, n5, n6, n7, n8,n10, n12, n16, n20, n24, n28, spare2, spare1} This parameter is not settable by the operator. | TDD/FDD | No |
| periodicBSR-Timer | Timer for Periodic BSR reporting. UE transmits periodic BSR at the expiration of this timer. Corresponds to parameter periodicBSR-Timer specified in 3GPP TS 36.331 section 6.3.2 and in 3GPP TS 36.321 section 5.4.5 Value sfn corresponds to n subframes. | Enum{sf5, sf10, sf16, sf20, sf32, sf40, sf64, sf80, sf128, sf160, sf320, sf640, sf1280, sf2560, infinity, spare1} | TDD/FDD | No |
| retxBSR-Timer | Timer for Regular BSR reporting. UE transmits a Regular BSR at the expiration of this timer if data is available in the buffer. Corresponds to parameter retxBSR-Timer specified in 3GPP TS 36.331 section 6.3.2 and in 3GPP TS 36.321 section 5.4.5 Value sfn corresponds to n subframes. | Enum{sf320, sf640, sf1280, sf2560, sf5120, sf10240, spare2, spare1} This parameter is not settable by the operator. | TDD/FDD | No |
| ttiBundling | Enables/disables TTI bundling. Corresponds to parameter ttiBundling specified in 3GPP TS 36.331 section 6.3.2 and in 3GPP TS 36.321 section 5.4.2.1. | Boolean This parameter is not settable by the operator. | TDD/FDD | No |

##### 6.1.5.1.7	GERAN Frequency Groups

This table contains information about GERAN groups of frequency carriers relevant for inter-RAT cell re-selection from E-UTRA to GERAN.

| Parameter Name | Description | Valid Values | TDD/FDD | Applicable to HNB |
| --- | --- | --- | --- | --- |
| QRxLevMin | Required minimum received RSSI level on this GERAN frequency carrier for re-selection to this UTRA FDD carrier. Actual value in dBm is value * 2 - 115. Corresponds to parameter q-rxLevMin in SIB7 in 3GPP TS 36.331 and to RXLEV_ACCESS_MIN in 3GPP TS 45.008. | int[0..45] This parameter is settable by the operator. | TDD/FDD | No |
| cellReselectionPriority | Absolute priority of this GERAN frequency group, as used by the inter-frequency cell reselection procedure. Corresponds to parameter CellReselectionPriority specified in SIB7 in 3GPP TS 36.331 section 6.3.1 and in 3GPP TS 36.304 section 5.2.4.7. | int[0..7] This parameter is settable by the operator. | TDD/FDD | No |
| ThreshXHigh | Threshold used when reselecting towards a higher priority GERAN frequency group than current serving E-UTRA frequency. Actual value in dB is obtained by multiplying by 2. Corresponds to parameter threshX-High specified in SIB7 in 3GPP TS 36.331 section 6.3.1 and in 3GPP TS 36.304 section 5.2.4.5. | int[0..31] This parameter is settable by the operator. | TDD/FDD | No |
| ThreshXLow | Threshold used when reselecting towards a lower priority GERAN frequency group than current serving E-UTRA frequency. Actual value in dB is obtained by multiplying by 2. Corresponds to parameter threshX-Low specified in SIB7 in 3GPP TS 36.331 section 6.3.1 and in 3GPP TS 36.304 section 5.2.4.5. | int[0..31] This parameter is settable by the operator. | TDD/FDD | No |

##### 6.1.5.2.1	Common Parameters for E-UTRA

This table contains common parameters related to intra-EUTRA connected mode mobility.

| Parameter Name | Description | Valid Values | TDD/FDD | Applicable to HNB |
| --- | --- | --- | --- | --- |
| FilterCoefficientRSRP | Filtering coefficient used for RSRP measurements. Value fc0 corresponds to k = 0, fc1 corresponds to k = 1, and so on. Corresponds to filterCoefficientRSRP parameter specified in QuantityConfigEUTRA IE in 3GPP TS 36.331 section 6.3.5 | Enum{fc0, fc1, fc2, fc3, fc4, fc5, fc6, fc7, fc8, fc9, fc11, fc13, fc15, fc17, fc19, spare1, …} This parameter is settable by the operator. | TDD/FDD | No |
| FilterCoefficientRSRQ | Filtering coefficient used for RSRQ measurements. Value fc0 corresponds to k = 0, fc1 corresponds to k = 1, and so on. Corresponds to filterCoefficientRSRQ parameter specified in QuantityConfigEUTRA IE in 3GPP TS 36.331 section 6.3.5 | Enum{fc0, fc1, fc2, fc3, fc4, fc5, fc6, fc7, fc8, fc9, fc11, fc13, fc15, fc17, fc19, spare1, …} This parameter is settable by the operator. | TDD/FDD | No |
| A1ThresholdRSRP | Threshold to be used in EUTRA measurement report triggering condition for event a1. Valid only if TriggerQuanity is rsrp. Mapping to actual values is specified in 3GPP TS 36.133. Corresponds to parameter a1-Threshold:threshold-RSRP specified in ReportConfigEUTRA IE in 3GPP TS 36.331 section 6.3.5. | int[0..97] This parameter is settable by the operator. | TDD/FDD | No |
| A1ThresholdRSRQ | Threshold to be used in EUTRA measurement report triggering condition for event a1. Valid only if TriggerQuanity is rsrq. Mapping to actual values is specified in 3GPP TS 36.133. Corresponds to parameter a1-Threshold:threshold-RSRQ specified in ReportConfigEUTRA IE in 3GPP TS 36.331 section 6.3.5. | int[0..34] This parameter is settable by the operator. | TDD/FDD | No |
| A2ThresholdRSRP | Threshold to be used in EUTRA measurement report triggering condition for event a2. Valid only if TriggerQuanity is rsrp. Mapping to actual values is specified in 3GPP TS 36.133. Corresponds to parameter a2-Threshold:threshold-RSRP specified in ReportConfigEUTRA IE in 3GPP TS 36.331 section 6.3.5. | int[0..97] This parameter is settable by the operator. | TDD/FDD | No |
| A2ThresholdRSRQ | Threshold to be used in EUTRA measurement report triggering condition for event a2. Valid only if TriggerQuanity is rsrq. Mapping to actual values is specified in 3GPP TS 36.133. Corresponds to parameter a2-Threshold:threshold-RSRQ specified in ReportConfigEUTRA IE in 3GPP TS 36.331 section 6.3.5. | int[0..34] This parameter is settable by the operator. | TDD/FDD | No |
| A3-Offset | Offset to be used in evaluation of EUTRA measurement report triggering condition for event a3. Mapping to actual values is specified in 3GPP TS 36.133. Corresponds to parameter a3-Offset specified in ReportConfigEUTRA IE in 3GPP TS 36.331 section 6.3.5. | in[-30..30] This parameter is settable by the operator. | TDD/FDD | No |
| ReportOnLeave | Indicates whether or not the UE shall initiate the measurement reporting procedure when the leaving condition is met for event a3 for a cell in cellsTriggeredList, as specified in 3GPP TS 36.331 section 5.5.4.1. | Boolean This parameter is settable by the operator. | TDD/FDD | No |
| A4ThresholdRSRP | Threshold to be used in EUTRA measurement report triggering condition for event a4. Valid only if TriggerQuanity is rsrp. Mapping to actual values is specified in 3GPP TS 36.133. Corresponds to parameter a4-Threshold:threshold-RSRP specified in ReportConfigEUTRA IE in 3GPP TS 36.331 section 6.3.5. | int[0..97] This parameter is settable by the operator. | TDD/FDD | No |
| A4ThresholdRSRQ | Threshold to be used in EUTRA measurement report triggering condition for event a4. Valid only if TriggerQuanity is rsrq. Mapping to actual values is specified in 3GPP TS 36.133. Corresponds to parameter a4-Threshold:threshold-RSRQ specified in ReportConfigEUTRA IE in 3GPP TS 36.331 section 6.3.5. | int[0..34] This parameter is settable by the operator. | TDD/FDD | No |
| A5Threshold1RSRP | Threshold1 to be used in EUTRA measurement report triggering condition for event a5. Valid only if TriggerQuanity is rsrp. Mapping to actual values is specified in 3GPP TS 36.133. Corresponds to parameter a5-Threshold1:threshold-RSRP specified in ReportConfigEUTRA IE in 3GPP TS 36.331 section 6.3.5. | int[0..97] This parameter is settable by the operator. | TDD/FDD | No |
| A5Threshold1RSRQ | Threshold1 to be used in EUTRA measurement report triggering condition for event a5. Valid only if TriggerQuanity is rsrq. Mapping to actual values is specified in 3GPP TS 36.133. Corresponds to parameter a5-Threshold1:threshold-RSRQ specified in ReportConfigEUTRA IE in 3GPP TS 36.331 section 6.3.5. | int[0..34] This parameter is settable by the operator. | TDD/FDD | No |
| A5Threshold2RSRP | Threshold2 to be used in EUTRA measurement report triggering condition for event a5. Valid only if TriggerQuanity is rsrp. Mapping to actual values is specified in 3GPP TS 36.133. Corresponds to parameter a5-Threshold2:threshold-RSRP specified in ReportConfigEUTRA IE in 3GPP TS 36.331 section 6.3.5. | int[0..97] This parameter is settable by the operator. | TDD/FDD | No |
| A5Threshold2RSRQ | Threshold2 to be used in EUTRA measurement report triggering condition for event a5. Valid only if TriggerQuanity is rsrq. Mapping to actual values is specified in 3GPP TS 36.133. Corresponds to parameter a5-Threshold2:threshold-RSRQ specified in ReportConfigEUTRA IE in 3GPP TS 36.331 section 6.3.5. | int[0..34] This parameter is settable by the operator. | TDD/FDD | No |
| Hysteresis | Hysteresis applied to entry and leave condition of a report triggering event. Corresponds to parameter hysteresis specified in ReportConfigEUTRA IE in 3GPP TS 36.331 section 6.3.5. | int[0..30] This parameter is settable by the operator. | TDD/FDD | No |
| TimeToTrigger | Time during which measurement report triggering condition needs to be met in order to trigger a measurement report. Corresponds to parameter timeToTrigger specified in ReportConfigEUTRA IE in 3GPP TS 36.331 section 6.3.5. Value ms0 corresponds to 0 miliseconds etc. | Enum{ms0, ms40, ms64, ms80, ms100, ms128, ms160, ms256, ms320, ms480, ms512, ms640, ms1024, ms1280, ms2560, ms5120} This parameter is settable by the operator. | TDD/FDD | No |
| TriggerQuantity | Quantities used to evaluate a measurement report triggering condition. The values rsrp and rsrq correspond to Reference Signal Received Power (RSRP) and Reference Signal Received Quality (RSRQ), respectively. Corresponds to parameter triggerQuantity specified in ReportConfigEUTRA IE in 3GPP TS 36.331 section 6.3.5. | Enum{rsrp, rsrq} This parameter is settable by the operator. | TDD/FDD | No |
| ReportQuantity | Measurement quantities to be included in the measurement report. The value "both" means that both the RSRP and RSRQ quantities are to be included in the measurement report. Corresponds to parameter reportQuantity specified in ReportConfigEUTRA IE in 3GPP TS 36.331 section 6.3.5. | Enum{sameAsTriggerQuantity, both} This parameter is settable by the operator. | TDD/FDD | No |
| MaxReportCells | Maximum number of cells that can be included in a measurement report. Corresponds to parameter maxReportCells specified in ReportConfigEUTRA IE in 3GPP TS 36.331 section 6.3.5. | Int[1..8] This parameter is not settable by the operator. | TDD/FDD | No |
| ReportInterval | Interval between successive measurement reports. Corresponds to parameter reportInterval specified in ReportConfigEUTRA IE in 3GPP TS 36.331 section 6.3.5. | Enum{ms120, ms240, ms480, ms640, ms1024, ms2048, ms5120, ms10240, min1, min6, min12, min30, min60, spare3, spare2, spare1} This parameter is settable by the operator. | TDD/FDD | No |
| ReportAmount | Number of times a measurement report is sent. Corresponds to parameter reportAmount specified in ReportConfigEUTRA IE in 3GPP TS 36.331 section 6.3.5. | {r1, r2, r4, r8, r16, r32, r64, infinity} This parameter is settable by the operator. | TDD/FDD | No |

End of changes

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.