3GPP TSG-SA5 (Telecom Management)	S5e100083

Meeting SA5#74-E, 26 - 28 Oct 2010, Electronic Meeting	revision of S5e10xyzw

| CR-Form-v9.6 |
| --- |
| CHANGE REQUEST |
| ( | 32.376 | CR | 0001 | ( rev | - | ( Current version: | 10.0.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network | X | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Correcting IDL syntax errors |
| --- | --- |
| Source to WG: ( | ZTE |
| Source to TSG: ( | S5 |
| Work item code: ( | OAM10 |  | Date: ( | 28/10/2010 |
| Category: ( | F |  | Release: ( | Rel-10 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) |
| Reason for change: ( | The are two syntax errors in IDL specifications: 1) In SecurityServiceConstDefs.idl, the type of authenticationData is missing, it is an attribute. So it is proposed to add the keyword ‘attribute’ in the definition of authenticationData. 2) In SecurityServiceSystem.idl, a semicolon is missing. |
| Summary of change: ( | 1) Add “attribute” before “Auth_Data authenticationData ;” in the SecurityServiceConstDefs.idl 2) Add “;” at the end of module SecurityServiceSystem in SecurityServiceSystem.idl |
| Consequences if ( not approved: | The IDl specification can not be implemented. |
| Clauses affected: ( | A.4.2;A.4.3 |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

First change

## A.4.2	IDL specification "SecurityServiceConstDefs.idl"

//File: SecurityServiceConstDefs.idl

#ifndef _SECURITYSERVICEConstDefs_idl_

#define _SECURITYSERVICEConstDefs_idl_

// This statement must appear after all include statements

#pragma prefix "3gppsa5.org"

/* ## Module: SecurityServiceConstDefs

This module contains definitions specific for Security Service Request Interceptor Solution.

================================================================

*/

module SecurityServiceConstDefs

{

typedef Any Auth_Data;

/*

Define the credential in Request Interceptor Solution specified in

the Security Service: IS.

*/

interface Credential

{

attribute Auth_Data authenticationData;

};

};

#endif  // _SECURITYSERVICEConstDefs_idl_

Next change

## A.4.3	IDL specification file "SecurityServiceSystem.idl"

//File: SecurityServiceSystem.idl

#ifndef _SECURITYSERVICESYSTEM_idl_

#define _SECURITYSERVICESystem_idl_

#include "SecurityServiceConstDefs.idl"

// This statement must appear after all include statements

#pragma prefix "3gppsa5.org"

/* ## Module: SecurityServiceSystem

This module implements capabilities of IRP Security Service.

================================================================

*/

module SecurityServiceSystem

{

/*

System fails to complete the operation.  System can provide reason

to qualify the exception.  The semantics carried in reason

is outside the scope of this IRP.

*/

exception AuthenticationException { string reason; };

exception AuthorizationException { string reason; };

};

#endif  // _SECURITYSERVICESYSTEM_idl_

End of changes

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.