3GPP TSG-SA5 (Telecom Management)	S5e100142

Meeting SA5#74-E, 26 - 28 Oct 2010, Electronic Meeting	revision of S5e10xyzw

| CR-Form-v9.6 |
| --- |
| CHANGE REQUEST |
| ( | 32.172 | CR | 0025 | ( rev | - | ( Current version: | 10.0.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Correcting errors from release 9.X.0 and undoing error introduced by 32172_CR0022_(Rel-10)_S5-102471 |
| --- | --- |
| Source to WG: ( | Ericsson |
| Source to TSG: ( | S5 |
| Work item code: ( | OAM10-SuM |  | Date: ( | 28/10/2010 |
| Category: ( | F |  | Release: ( | Rel-10 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) |
| Reason for change: ( | Correcting SuM NRM Containment and Association diagram; Missing MobileUserData attribute in SuMSubscriberProfile. |
| Summary of change: ( | Two errors derived from release 9: The relationship between SuMService and SuMSubscribedService should be bi-directional (arrow is unnecessary); The attribute of theMobileUserData is missed in SuMSubscriberProfile. One error introduced by 32172_CR0022_(Rel-10)_S5-102471: The relationship between SuMSusbcriberProfile and SuMSubscribedService should be uni-directional (arrow is missing). |
| Consequences if ( not approved: | The TS is not correct according to agreement and with misalignments might lead to implementation errors. |
| Clauses affected: ( | 6.2.1; 6.3.9 |
|  | Y | N |  |  |
| Other specs ( |  | x | Other core specifications ( |  |
| affected: |  | x | Test specifications |  |
|  | x |  | O&M Specifications | 32.176 |
| Other comments: ( |  |

1st Modified Section

## 6.2	Class diagram

### 6.2.1	Attributes and relationships

This clause depicts the set of IOCs that encapsulate information relevant for this service. This sub-clause provides the overview of all information object classes in UML. Subsequent clauses provide more detailed specification of various aspects of these Information Object Classes (IOCs).

Figure 1a: SuM NRM naming diagram 1

Figure 1b: SuM NRM Containment and Association diagram 1

Next Modified Section

### 6.3.9	SuMSubscriberProfile

#### 6.3.9.1	Definition

This class represents the Subscriber Profile.

This class also contains the reference to its aggregated Subscribed Service as well as the users for a subscriber.

#### 6.3.9.2	Attributes

# Attributes of SuMSubscriberProfile

| Attribute name | Support Qualifier | Read Qualifier | Write Qualifier |
| --- | --- | --- | --- |
| id | M | M | - |
| suMSubscriberProfileInfo | M | M | O |
| theUser | M | M | O |
| theSubscribedService | M | M | O |
| theMobileUserData | M | M | O |

End of Modifications