3GPP TSG-SA5 (Telecom Management)	S5e100147

Meeting SA5#74-E, 26 - 28 Oct 2010, Electronic Meeting	revision of S5e10099

| CR-Form-v9.6 |
| --- |
| CHANGE REQUEST |
| ( | 32.396 | CR | 0001 | ( rev | 1 | ( Current version: | 10.0.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network | X | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Correcting IDL syntax errors |
| --- | --- |
| Source to WG: ( | ZTE |
| Source to TSG: ( | S5 |
| Work item code: ( | OAM8 |  | Date: ( | 28/10/2010 |
| Category: ( | F |  | Release: ( | Rel-10 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) |
| Reason for change: ( | 1) The absence of the 'AlarmIRPConstDefs.idl' leads to the variable `AlarmIRPConstDefs::AlarmInformationSeq', ‘AlarmIRPConstDefs:: AlarmInformationIdSeq' are not defined. 2) The usage of ‘FileTransferIRPConstDefs::FileLocationList’ is inconsistent with the local definition of FileLocationList’. |
| Summary of change: ( | 1) Add '#include <AlarmIRPConstDefs.idl>' 2) Correct 'FileTransferIRPConstDefs::FileLocationList fileList' to 'FileLocationList fileList' |
| Consequences if ( not approved: | The IDL specification can't be implemented |
| Clauses affected: ( | A.3.2 |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

First change

# A.3.2	IDL specification (file name "DeltaSynchronizationConstDefs.idl")

// File: DeltaSynchronizationConstDefs.idl

#ifndef _DELTA_SYNCHRONIZATION_CONST_DEFS_IDL_

#define _DELTA_SYNCHRONIZATION_CONST_DEFS_IDL_

#include <TimeBase.idl>

#include <DeltaSynchronizationConstDefs.idl>

#include <GenericIRPManagementConstDefs.idl>

#include <KernelCmConstDefs.idl>

#include <FileTransferIRPConstDefs.idl>

#include <AlarmIRPConstDefs.idl>

//FileTransferIRPConstDefs::FileLocation value;

// This statement must appear after all include statements

#pragma prefix "3gppsa5.org"

/* ## Module: DeltaSynchronizationConstDefs */

module DeltaSynchronizationConstDefs

{

/*****************************************************************************/

/* definition of types used in several operations for Delta Synchronization: */

/*****************************************************************************/

/* types used in several operations: */

typedef string ManagerReference;

typedef string AgentOrManagerReference;

/*

ManagerReferenceConditional is a type carrying an optional parameter.

The boolean shall be TRUE, if the condition described in TS 32.392 is fulfilled. In this case the value is present. Otherwise the value is be absent.

*/

union ManagerReferenceConditional switch (boolean)

{

case TRUE: ManagerReference value;

};

/*

ManagerReferenceOpt is a type carrying an optional parameter.

The boolean shall be TRUE, if the operation request uses this parameter. In this case the value is present. Otherwise the value is absent.

*/

union ManagerReferenceOpt switch (boolean)

{

case TRUE: ManagerReference value;

};

enum ManageDeltaSynchForXData {ACTIVATE, DEACTIVATE};

/*

ManageDeltaSynchForXDataConditional is a type carrying a conditional parameter.

The boolean shall be TRUE, if the condition described in TS 32.392 is fulfilled. In this case the value is present. Otherwise the value is absent.

*/

union ManageDeltaSynchForXDataConditional switch (boolean)

{

case TRUE: ManageDeltaSynchForXData value;

};

typedef TimeBase::UtcT SynchPoint;

/*

SynchPointConditional is a type carrying a conditional parameter.

The boolean shall be TRUE, if the condition described in TS 32.392 is fulfilled. In this case the value is present. Otherwise the value is absent.

*/

union SynchPointConditional switch (boolean)

{

case TRUE: SynchPoint value;

};

/*

SynchPointOpt is a type carrying an optional parameter.

The boolean shall be TRUE, if the operation request uses this parameter. In this case the value is present. Otherwise the value is absent.

*/

union SynchPointOpt switch (boolean)

{

case TRUE: SynchPoint value;

};

/*

ScopeTypeOpt is a type carrying an optional parameter.

The boolean shall be TRUE, if the operation request uses this parameter. In this case the value is present. Otherwise the value is absent.

*/

union ScopeTypeOpt switch (boolean)

{

case TRUE: KernelCmConstDefs::ScopePara value;

};

/*

BaseMOInstanceOpt is a type carrying an optional parameter.

The boolean shall be TRUE, if the operation request uses this parameter. In this case the value is present. Otherwise the value is absent.

*/

union BaseMOInstanceOpt switch (boolean)

{

case TRUE: GenericIRPManagementConstDefs::DN value;

};

enum Status {SUCCESS, FAILURE};

/********************************************************************/

/* types used in operation manageDeltaSynchronization               */

/********************************************************************/

enum ActivatedStatus {ACTIVATED, DEACTIVATED };

typedef ActivatedStatus ManageDeltaSynchMode;

/********************************************************************/

/* types used in operation getAvailableDeltaSynchPoints             */

/********************************************************************/

typedef boolean SynchPointsRequested;

/*

SynchPointsRequestedConditional is a type carrying a conditional parameter.

The boolean shall be TRUE, if the condition described in TS 32.392 is fulfilled. Otherwise the value may be absent.

*/

union SynchPointsRequestedConditional switch (boolean)

{

case TRUE: SynchPointsRequested value;

};

typedef sequence <SynchPoint> SynchPointList;

/*

SynchPointListConditional is a type carrying an optional parameter.

The boolean shall be TRUE, if the condition described in TS 32.392 is fulfilled. In this case the value is present. Otherwise the value is be absent.

*/

union SynchPointListConditional switch (boolean)

{

case TRUE: SynchPointList value;

};

/********************************************************************/

/* types used in operation triggerDeltaSynchOfCMData and            */

/*            in operation triggerDeltaSynchOfAlarmData             */

/********************************************************************/

/*

AttributeListConditional is a type carrying a conditional parameter.

The boolean shall be TRUE, if the operation’s dnsOnly=FALSE. In this case the value is present.

Otherwise the value is absent.

*/

union AttributeListConditional switch (boolean)

{

case TRUE: GenericIRPManagementConstDefs::MOAttributeSet value;

};

struct ListedInstance

{

GenericIRPManagementConstDefs::DN moInstance;   /* DN is a string; */

AttributeListConditional attributeList;

};

typedef sequence <ListedInstance> ListOfInstances;

struct DeltaListsWithRealLists

{

TimeBase::UtcT startTime;

TimeBase::UtcT endTime;

ListOfInstances listOfCreatedInstances;

ListOfInstances listOfChangedInstances;

ListOfInstances listOfDeletedInstances;

};

struct AlarmDeltaListsWithRealLists

{

TimeBase::UtcT startTime;

TimeBase::UtcT endTime;

AlarmIRPConstDefs::AlarmInformationSeq listOfNewAlarms;

AlarmIRPConstDefs::AlarmInformationSeq listOfChangedAlarms;

AlarmIRPConstDefs::AlarmInformationIdSeq listOfDeletedAlarms;

};

typedef sequence <FileTransferIRPConstDefs::FileLocation> FileLocationList;

struct DeltaListsWithFileReferences

{

TimeBase::UtcT startTime;

TimeBase::UtcT endTime;

FileLocationList fileList;

/* if several files are used, then they shall be processed by the IRPmanager in sequence, i.e. first file first, second file as second, … */

};

enum DeltaListContentChoice {REAL_LISTS, FILE_REFERENCES};

//The CmDeltaList may contain a list of ListOfInstances or a list of filenames

union CmDeltaLists switch (DeltaListContentChoice)

{

case REAL_LISTS: DeltaListsWithRealLists deltaListRealLists;

case FILE_REFERENCES: DeltaListsWithFileReferences deltaListFileReferences;

};

//The AlarmDeltaLists may contain a list of ListOfInstances or a list of filenames

union AlarmDeltaLists switch (DeltaListContentChoice)

{

case REAL_LISTS: AlarmDeltaListsWithRealLists deltaListRealLists;

case FILE_REFERENCES: DeltaListsWithFileReferences deltaListFileReferences;

};

/*

CmDeltaListsConditional is a type carrying a conditional parameter.

The boolean shall be TRUE, if the condition described in TS 32.392 is fulfilled. In this case

the value is present. Otherwise the value is be absent.

*/

union CmDeltaListsConditional switch (boolean)

{

case TRUE: CmDeltaLists value;

};

/*

AlarmDeltaListsConditional is a type carrying a conditional parameter.

The boolean shall be TRUE, if the condition described in TS 32.392 is fulfilled. In this case

the value is present. Otherwise the value is absent.

*/

union AlarmDeltaListsConditional switch (boolean)

{

case TRUE: AlarmDeltaLists value;

};

/********************************************************************/

/* types used in operation triggerDeltaSynchOfAlarmData             */

/********************************************************************/

enum AlarmDataRequested { ALARM_IDS_ONLY, COMPLETE_ALARM_INFORMATION };

/*

AlarmDataRequestedOpt is a type carrying an optional parameter.

The boolean shall be TRUE, if the operation request uses this parameter. In this case the value

is present. Otherwise the value is absent.

*/

union AlarmDataRequestedOpt switch (boolean)

{

case TRUE: AlarmDataRequested value;

};

/********************************************************************/

/* types used in operation triggerDeltaSynchOfCMData                */

/********************************************************************/

enum CMDataRequested { DNS_ONLY, COMPLETE_DATA_SET };

/*

CMDataRequestedOpt is a type carrying an optional parameter.

The boolean shall be TRUE, if the operation request uses this parameter. In this case the value

is present. Otherwise the value is absent.

*/

union CMDataRequestedOpt switch (boolean)

{

case TRUE: CMDataRequested value;

};

/*****************************************************************************/

/* definition of types in notifications for Delta Synchronization            */

/*****************************************************************************/

enum DeltaSynchPointType { DELTA_SYNCH_POINT_FOR_ALARM, DELTA_SYNCH_POINT_FOR_CM_DATA };

typedef ActivatedStatus DeltaSynchStatus;

enum TriggeredBy { IRP_AGENT, IRP_MANAGER };

/*********************************************************************************/

/* Definition of parameters specified in notifications for Delta Synchronization */

/*********************************************************************************/

interface AttributeNameValue

{

const string MANAGER_REFERENCE = "MANAGER_REFERENCE";

const string AGENT_OR_MANAGER_REFERENCE = "AGENT_OR_MANAGER_REFERENCE";

const string DELTA_SYNCH_STATUS_FOR_CMDATA = "DELTA_SYNCH_STATUS_FOR_CMDATA";

const string DELTA_SYNCH_STATUS_FOR_ALARM_DATA = "DELTA_SYNCH_STATUS_FOR_ALARM_DATA";

const string NEW_DELTA_SYNCH_POINT = "NEW_DELTA_SYNCH_POINT";

const string DELTA_SYNCH_POINT_TYPE = "DELTA_SYNCH_POINT_TYPE";

const string REQUESTED_SYNCH_POINT = "REQUESTED_SYNCH_POINT";

const string TRIGGERED_BY_AGENT_OR_MANAGER = "TRIGGERED_BY_AGENT_OR_MANAGER";

};

};

#endif // _DELTA_SYNCHRONIZATION_CONST_DEFS_IDL_

End of changes

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.