3GPP TSG-SA5 (Telecom Management)	S5e100192

Meeting SA5#74-E, 26 - 28 Oct 2010, Electronic Meeting	revision of S5e100117

| CR-Form-v9.6 |
| --- |
| CHANGE REQUEST |
| ( | 32.536 | CR | 0003 | ( rev | 1 | ( Current version: | 10.0.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network | X | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Add NE health check step in automatic software management – Align with 32.532 IS |
| --- | --- |
| Source to WG: ( | Huawei |
| Source to TSG: ( | S5 |
| Work item code: ( | OAM10 |  | Date: ( | 28/10/2010 |
| Category: ( | B |  | Release: ( | Rel-10 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) |
| Reason for change: ( | According to NGMN top 10 requirements, operator would like to have NE health-check function in automatic software management to ensure the correct behaviour and precondition of NE before the software update procedure. |
| Summary of change: ( | Add NE health-check as one of the step of automatic software management. |
| Consequences if ( not approved: | Operator’s NE health-check requirement can’t be fulfilled. |
| Clauses affected: ( | 1, Annex A.3.2, Annex B.3.4 |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

1st Modified Section

# 1	Scope

The present document specifies the Solution Set definitions for the IRP whose semantics are specified in Software Management IRP Information Service (3GPP TS 32.532 [5]).

This Solution Set definitions specification is related to 3GPP TS 32.532 V10.1.X.

Next Modified Section

## A.3.2	IDL specification “SwMIRPConstDefs.idl”

// File: SwMIRPConstDefs.idl

#ifndef _SWM_IRP_CONST_DEFS_IDL_

#define _SWM_IRP_CONST_DEFS_IDL_

#include <NotificationIRPConstDefs.idl>

#include <GenericIRPManagementConstDefs.idl>

// This statement must appear after all include statements

#pragma prefix "3gppsa5.org"

/* ## Module: SwMIRPConstDefs */

module SwMIRPConstDefs

{

/********************************************************************/

/* definition of types used in operations for Software Management : */

/********************************************************************/

/* types used in several operations: */

enum Result { SUCCESS, PARTLY_SUCCESSFUL, FAILURE, NE_INFORMATION_INTERSECTION, STEPNAME_DOES_NOT_MATCH };

enum ResultChangeOrCreateProfileOperation { SUCCESS, FAILURE, NE_INFORMATION_INTERSECTION, NOT_ALLOWED_BECAUSE_OF_ONGOING_ACTIVITY };

enum ResultNaSwmNotification { REQUEST_ACCEPTED, REQUEST_FAILED, NOT_ALLOWED_BECAUSE_OF_ONGOING_SWM_ACTIVITY };

typedef GenericIRPManagementConstDefs::DN Id;

/*

IdOpt is a type carrying an optional parameter.

If the boolean is TRUE, then the value is present.

Otherwise the value is absent.

*/

union IdOpt switch (boolean)

{

case TRUE: GenericIRPManagementConstDefs::DN value;

};

/*

ConflictingProfileIdConditional is a type carrying a conditional parameter.

The boolean shall be TRUE, if the condition described in TS 32.532 or 32.502 is fulfilled.

In this case the value is present. Otherwise the value is absent.

*/

union ConflictingProfileIdConditional switch (boolean)

{

case TRUE: Id value;

};

typedef string NEInformation;

typedef NEInformation MatchingNEInformation;

typedef string AdditionalInformation;

/*

AdditionalInformationOpt is a type carrying a optional parameter.

The boolean shall be TRUE, if the condition described in TS 32.532 is fulfilled.

In this case the value is present. Otherwise the value is absent.

*/

union AdditionalInformationOpt switch (boolean)

{

case TRUE: AdditionalInformation value;

};

typedef GenericIRPManagementConstDefs::DN NEIdentification;

/*

NEIdentificationOpt is a type carrying an optional parameter.

If the boolean is TRUE, then the value is present.

Otherwise the value is absent.

*/

union NEIdentificationOpt switch (boolean)

{

case TRUE: NEIdentification value;

};

enum SwFallbackStatus { FALLBACK_SUCCESSFUL, FALLBACK_UNSUCCESSFUL };

struct NeListEntry

{

SwMIRPConstDefs::NEIdentification nEIdentification;

SwMIRPConstDefs::SwFallbackStatus swFallbackStatus;

};

typedef sequence<NeListEntry> NeList;

typedef string SwVersionToBeInstalled;

/*

SwVersionToBeInstalledConditional is a type carrying a conditional parameter.

The boolean shall be TRUE, if the condition described in TS 32.532 is fulfilled.

In this case the value is present. Otherwise the value may be absent.

*/

union SwVersionToBeInstalledConditional switch (boolean)

{

case TRUE: SwVersionToBeInstalled value;

};

enum NameOfStep

{

NE_HEALTH_CHECK,

SW_DOWNLOAD,

SW_INSTALLATION,

SW_ACTIVATION,

PREPARE_BASIC_CONFIGURATION_AND_OAMLINK,

RETRIEVE_CONFIGURATION_DATA,

SETUP_PRECONFIGURED_SIGNALLING_LINKS,

SET_FINAL_STATE_OF_NE

};

/*

The following values are not used in SWM IRP, but only in inheriting Self-Conf IRP TS 32.502:

PREPARE_BASIC_CONFIGURATION_AND_OAMLINK,

RETRIEVE_CONFIGURATION_DATA,

SETUP_PRECONFIGURED_SIGNALLING_LINKS,

SET_FINAL_STATE_OF_NE

*/

typedef unsigned short SequenceNumberInProcess;

enum StopPointCanBeSetBeforeThisStep { YES, NO };

struct StepsAndOfferedStopPointListEntry

{

SwMIRPConstDefs::NameOfStep nameOfStep;

SwMIRPConstDefs::SequenceNumberInProcess sequenceNumberInProcess;

SwMIRPConstDefs::StopPointCanBeSetBeforeThisStep stopPointCanBeSetBeforeThisStep

;

};

typedef sequence<StepsAndOfferedStopPointListEntry> StepsAndOfferedStopPointList;

enum StopPointSetIndication { STOP_POINT_IS_SET_BEFORE_THIS_STEP, STOP_POINT_IS_NOT_SET };

struct StepAndSelectedStopPointListEntry

{

SwMIRPConstDefs::NameOfStep nameOfStep;

SwMIRPConstDefs::SequenceNumberInProcess sequenceNumberInProcess;

SwMIRPConstDefs::StopPointSetIndication stopPointSetIndication

;

};

typedef sequence<StepAndSelectedStopPointListEntry> StepsAndSelectedStopPointList;

enum StepProgress { NOT_YET_STARTED, RUNNING, COMPLETED, AWAITING_RESUME, FAILURE, TERMINATED };

struct StepInfoListEntry

{

SwMIRPConstDefs::NameOfStep nameOfStep;

SwMIRPConstDefs::SequenceNumberInProcess sequenceNumberInProcess;

SwMIRPConstDefs::StopPointSetIndication stopPointSetIndication;

SwMIRPConstDefs::StepProgress stepProgress;

};

typedef sequence<StepInfoListEntry> StepInfoList;

struct SwMProcessListEntry

{

SwMIRPConstDefs::Id id;

SwMIRPConstDefs::NEIdentification nEIdentification;

SwMIRPConstDefs::StepInfoList stepInfoList;

};

typedef sequence<SwMProcessListEntry> SwMProcessList;

enum FinalAdministrativeStateValue { LOCKED, UNLOCKED, DETERMINED_BY_CONFIGURATION_DATA };

typedef FinalAdministrativeStateValue OfferedFinalAdministrativeStateValue;

typedef sequence<OfferedFinalAdministrativeStateValue> OfferedFinalAdministrativeStateInformation;

typedef FinalAdministrativeStateValue SelectedFinalAdministrativeStateValue;

typedef sequence<SwVersionToBeInstalled> SwVersionToBeInstalledOfferList;

/*

SwVersionToBeInstalledOfferListConditional is a type carrying a conditional parameter.

The boolean shall be TRUE, if the condition described in TS 32.532 is fulfilled.

In this case the value is present. Otherwise the value may be absent.

*/

union SwVersionToBeInstalledOfferListConditional switch (boolean)

{

case TRUE: SwVersionToBeInstalledOfferList value;

};

typedef unsigned short VersionNumber;

struct ProfileId

{

SwMIRPConstDefs::Id id;

SwMIRPConstDefs::VersionNumber versionNumber;

};

struct SwMCapability

{

SwMIRPConstDefs::Id id;

SwMIRPConstDefs::NEInformation nEInformation;

SwMIRPConstDefs::StepsAndOfferedStopPointList stepsAndOfferedStopPointList;

SwMIRPConstDefs::OfferedFinalAdministrativeStateInformation offeredFinalAdministrativeStateInformation;

SwMIRPConstDefs::SwVersionToBeInstalledOfferListConditional swVersionToBeInstalledOfferList;

};

typedef sequence<SwMCapability> SwMCapabilitiesList;

struct SwMProfile

{

SwMIRPConstDefs::Id id;

SwMIRPConstDefs::VersionNumber versionNumber;

SwMIRPConstDefs::NEInformation nEInformation;

SwMIRPConstDefs::StepsAndSelectedStopPointList stepsAndSelectedStopPointList;

SwMIRPConstDefs::SelectedFinalAdministrativeStateValue selectedFinalAdministrativeState;

SwMIRPConstDefs::SwVersionToBeInstalledConditional swVersionToBeInstalled;

};

typedef sequence<SwMProfile> SwMProfilesList;

/******************************************************************/

/* definition of types in notifications for software management : */

/******************************************************************/

typedef string Filter;

typedef string NeAndSWVersion;

enum TriggerForDeletion { IRP_AGENT_TERMINATION, IRP_MANAGER_TERMINATION, AUTOMATED_SWM_SUCCESFULLY_CONCLUDED, SELF_CONFIGURATION_SUCCESFULLY_CONCLUDED };

/*

The following values are not used in SWM IRP, but only in inheriting Self-Conf IRP TS 32.502:

SELF_CONFIGURATION_SUCCESFULLY_CONCLUDED

*/

/********************************************************************

* Definitions for Non-Automated Software Management

********************************************************************/

typedef GenericIRPManagementConstDefs::DN NEIdentifier;

typedef unsigned long RequestID;

typedef string Reason;

typedef string FileLocation;     //The FileLocation may be a directory path or a URL

typedef unsigned long FileSize;  //the unit is byte

typedef string FileCompression;

typedef string FileFormat;

struct SWInfo

{

SwMIRPConstDefs::FileLocation swLocation;

SwMIRPConstDefs::FileSize swFileSize;

SwMIRPConstDefs::FileCompression swFileCompression;

SwMIRPConstDefs::FileFormat swFileFormat;

};

typedef SwMIRPConstDefs::FileLocation SWToBeInstalled;

typedef sequence<SWInfo> SWToBeDownloaded;

typedef string SWVersion;

/******************************************************************

*  Definitions for Non-Automatic Software Management Notifications

******************************************************************/

typedef RequestID DownloadProcessId;

typedef RequestID InstallProcessId;

typedef RequestID ActivateProcessId;

typedef string FailureReason;

typedef sequence<FileLocation> DownloadedNESwInfo;

typedef sequence<FileLocation> InstalledNESwInfo;

struct FailedSwEntry

{

SwMIRPConstDefs::FileLocation failedSw;

SwMIRPConstDefs::FailureReason failureReason;

};

typedef sequence<FailedSwEntry> FailedSwInfo;

typedef SWVersion swVersionActivated;

enum DownloadNESwOperationStatus {NE_SW_DOWNLOAD_SUCCESSFUL, NE_SW_DOWNLOAD_FAILED, NE_SW_DOWNLOAD_PARTIALLY_SUCCESSFUL};

enum InstallOperationStatus {NE_SW_INSTALLATION_SUCCESSFUL, NE_SW_INSTALLATION_FAILED, NE_SW_INSTALLATION_ PARTIALLY_SUCCESSFUL};

enum ActivateOperationStatus {NE_SW_ACTIVATION_SUCCESSFUL, NE_SW_ACTIVATION_FAILED, NE_SWACTIVATION_PARTIALLY_SUCCESSFUL};

interface AttributeNameValue

{

const string ID = "ID";

const string VERSION_NUMBER = "VERSION_NUMBER";

const string NE_INFORMATION = "NE_INFORMATION";

const string SW_VERSION_TO_BE_INSTALLED = "SW_VERSION_TO_BE_INSTALLED";

const string STEPS_AND_SELECTED_STOP_POINT_LIST = "STEPS_AND_SELECTED_STOP_POINT_LIST";

const string SELECTED_FINAL_ADMINISTRATIVE_STATE = "SELECTED_FINAL_ADMINISTRATIVE_STATE";

const string NE_IDENTIFICATION = "NE_IDENTIFICATION";

const string PROFILE_ID = "PROFILE_ID";

const string MATCHING_NE_INFORMATION = "MATCHING_NE_INFORMATION";

const string STEP_INFO_LIST = "STEP_INFO_LIST";

const string NE_AND_SW_VERSION = "NE_AND_SW_VERSION";

const string TRIGGER_FOR_DELETION = "TRIGGER_FOR_DELETION";

const string ADDITIONAL_INFORMATION = "ADDITIONAL_INFORMATION";

const string DOWNLOAD_PROCESS_ID = "DOWNLOAD_PROCESS_ID";

const string DOWNLOAD_OPERATION_STATUS = "DOWNLOAD_OPERATION_STATUS";

const string DOWNLOADED_NESW_INFO = "DOWNLOADED_NESW_INFO";

const string INSTALL_PROCESS_ID = "INSTALL_PROCESS_ID";

const string INSTALL_OPERATION_STATUS = "INSTALL_OPERATION_STATUS";

const string INSTALLED_NESW_INFO = "INSTALLED_NESW_INFO";

const string ACTIVATE_PROCESS_ID = "ACTIVATE_PROCESS_ID";

const string ACTIVATE_OPERATION_STATUS = "ACTIVATE_OPERATION_STATUS";

const string FAILURE_REASON = " FAILURE_REASON";

const string SW_VERSION_ACTIVATED = "SW_VERSION_ACTIVATED";

const string FAILED_SW_INFO = "FAILED_SW_INFO";   };

};

#endif // _SWM_IRP_CONST_DEFS_IDL_

Next Modified Section

## B.3.4	XML Schema “swManagementIRPIOCs.xsd”

<?xml version="1.0" encoding="UTF-8"?>

<schema xmlns="http://www.w3.org/2001/XMLSchema" xmlns:xswmi="http://www.3gpp.org/ftp/specs/archive/32_series/32.536#swManagementIRPIOCs" xmlns:xn="http://www.3gpp.org/ftp/specs/archive/32_series/32.626#genericNrm" targetNamespace="http://www.3gpp.org/ftp/specs/archive/32_series/32.536#swManagementIRPIOCs" elementFormDefault="qualified" attributeFormDefault="unqualified">

<import namespace="http://www.3gpp.org/ftp/specs/archive/32_series/32.626#genericNrm" schemaLocation="genericNrm.xsd"/>

<simpleType name="NEInformation">

<restriction base="string"/>

</simpleType>

<simpleType name="Id">

<restriction base="xn:dn"/>

</simpleType>

<simpleType name="VersionNumber">

<restriction base="unsignedShort"/>

</simpleType>

<complexType name="ProfileId">

<sequence>

<element name="id" type="xswmi:Id"/>

<element name="versionNumber" type="xswmi:VersionNumber"/>

</sequence>

</complexType>

<simpleType name="FinalAdministrativeStateValue">

<restriction base="string">

<enumeration value="LOCKED"/>

<enumeration value="UNLOCKED"/>

<enumeration value="DETERMINED_BY_CONFIGURATION_DATA"/>

</restriction>

</simpleType>

<complexType name="OfferedFinalAdministrativeStateInformation">

<sequence>

<element name="OfferedFinalAdministrativeStateValue" type="xswmi:FinalAdministrativeStateValue" maxOccurs="3"/>

</sequence>

</complexType>

<complexType name="StepsAndOfferedStopPointListEntry">

<sequence>

<element name="nameOfStep" type="xswmi:NameOfStep"/>

<element name="sequenceNumberInProcess" type="xswmi:SequenceNumberInProcess"/>

<element name="stopPointCanBeSetBeforeThisStep" type="xswmi:StopPointCanBeSetBeforeThisStep"/>

</sequence>

</complexType>

<complexType name="StepsAndOfferedStopPointList">

<sequence>

<element name="stepsAndOfferedStopPointListEntry" type="xswmi:StepsAndOfferedStopPointListEntry" maxOccurs="unbounded"/>

</sequence>

</complexType>

<simpleType name="StopPointCanBeSetBeforeThisStep">

<restriction base="boolean"/>

</simpleType>

<complexType name="StepsAndSelectedStopPointListEntry">

<sequence>

<element name="nameOfStep" type="xswmi:NameOfStep"/>

<element name="sequenceNumberInProcess" type="xswmi:SequenceNumberInProcess"/>

<element name="stopPointSetIndication" type="xswmi:StopPointSetIndication"/>

</sequence>

</complexType>

<complexType name="StepsAndSelectedStopPointList">

<sequence>

<element name="stepsAndSelectedStopPointListEntry" type="xswmi:StepsAndSelectedStopPointListEntry" maxOccurs="unbounded"/>

</sequence>

</complexType>

<simpleType name="StopPointSetIndication">

<restriction base="string">

<enumeration value="STOP_POINT_IS_SET_BEFORE_THIS_STEP"/>

<enumeration value="STOP_POINT_IS_NOT_SET"/>

</restriction>

</simpleType>

<simpleType name="SequenceNumberInProcess">

<restriction base="unsignedShort"/>

</simpleType>

<simpleType name="NameOfStep">

<restriction base="string">

<enumeration value="NE_HEALTH_CHECK"/>

<enumeration value="SW_DOWNLOAD"/>

<enumeration value="SW_INSTALLATION"/>

<enumeration value="SW_ACTIVATION"/>

<enumeration value="PREPARE_BASIC_CONFIGURATION_AND_OAMLINK"/>

<enumeration value="RETRIEVE_CONFIGURATION_DATA"/>

<enumeration value="SETUP_PRECONFIGURED_SIGNALLING_LINKS"/>

<enumeration value="SET_FINAL_STATE_OF_NE "/>

</restriction>

</simpleType>

<simpleType name="StepProgress">

<restriction base="string">

<enumeration value="NOT_YET_STARTED"/>

<enumeration value="RUNNING"/>

<enumeration value="COMPLETED"/>

<enumeration value="AWAITING_RESUME"/>

<enumeration value="FAILURE"/>

<enumeration value="TERMINATED"/>

</restriction>

</simpleType>

<complexType name="StepInfoListEntry">

<sequence>

<element name="nameOfStep" type="xswmi:NameOfStep"/>

<element name="sequenceNumberInProcess" type="xswmi:SequenceNumberInProcess"/>

<element name="stopPointSetIndication" type="xswmi:StopPointSetIndication"/>

<element name="stepProgress" type="xswmi:StepProgress"/>

</sequence>

</complexType>

<complexType name="StepInfoList">

<sequence>

<element name="stepInfoListEntry" type="xswmi:StepInfoListEntry" maxOccurs="unbounded"/>

</sequence>

</complexType>

<complexType name="swMCapabilityIOC">

<sequence>

<element name="id" type="xswmi:Id"/>

<element name="neInformation" type="xswmi:NEInformation"/>

<element name="stepsAndOfferedStopPointList" type="xswmi:StepsAndOfferedStopPointList"/>

<element name="offeredFinalAdministrativeStateInformation" type="xswmi:OfferedFinalAdministrativeStateInformation"/>

</sequence>

</complexType>

<complexType name="swMProfileIOC">

<sequence>

<element name="id" type="xswmi:Id"/>

<element name="versionNumber" type="xswmi:VersionNumber"/>

<element name="neInformation" type="xswmi:NEInformation"/>

<element name="stepsAndSelectedStopPointList" type="xswmi:StepsAndSelectedStopPointList"/>

<element name="selectedFinalAdministrativeState" type="xswmi:FinalAdministrativeStateValue"/>

</sequence>

</complexType>

<complexType name="swMProcessIOC">

<sequence>

<element name="id" type="xswmi:Id"/>

<element name="nEIdentification" type="xswmi:NEInformation"/>

<element name="profileId" type="xswmi:ProfileId"/>

<element name="stepInfoList" type="xswmi:StepInfoList"/>

</sequence>

</complexType>

## </schema>

End of Modified Section

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.