3GPP TSG-SA5 (Telecom Management)	S5-110439

SA5#75, 24 - 28 Jan 2011; Sorrento, ITALY	revision of S5-110202

| CR-Form-v9.7 |
| --- |
| CHANGE REQUEST |
| ( | 32.551 | CR | 0001 | ( rev | 1 | ( Current version: | 10.0.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network | X | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Modify the energy saving compensation related use cases |
| --- | --- |
| Source to WG: ( | ZTE |
| Source to TSG: ( | S5 |
| Work item code: ( | OAM-ES |  | Date: ( | 28/01/2011 |
| Category: ( | F |  | Release: ( | Rel-10 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) |
| Reason for change: ( | In the capacity limited scenario, in off-peak traffic situation, some NEs/Cells can be transferred to energySaving state and other related NEs/Cells can be transferred to compensatingforEnergySaving state; when it turns into peak traffic situation, the NEs/Cells in energySaving state shall be transferred to notEnergySaving state, and the related NEs/Cells in compensatingforEnergySaving state shall also be transferred to notEnergySaving state. But in the current use cases of energy saving deactivation, the state of the NEs/Cells in compensatingforEnergySaving state are not transferred. |
| Summary of change: ( | The use cases about evergySaving deactivaton are updated. |
| Consequences if ( not approved: | The use cases do not reflect the real situation. |
| Clauses affected: ( | 6.4.2, 6.4.4 |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

First change

### 6.4.2	Deactivatation of energy saving on selected network elements (Centralized ES on NM layer)

| Use Case Stage | Evolution / Specification | <<Uses>> Related use |
| --- | --- | --- |
| Goal (*) | Deactivating energy saving for a selected part of the network |  |
| Actors and Roles (*) | IRPManager as user |  |
| Telecom resources | Network elements (NEs) and their OSS. |  |
| Assumptions | Centralized ES on NM layer is performed. The network operator has decided to activate energy saving on selected network elements in a part of the network (network elements, e.g., base stations). This requires to activate energy saving on some network elements and to activate energy saving compensation on others. The IRPManager is continuously monitoring load on NEs. An interference control function is available to support the coverage adjustment process among NEs in compensatingForEnergySaving and EnergySaving state. |  |
| Pre conditions | The affected network elements are in ESaving state or in ES-Compensate state. Network elements (base stations) are not in a faulty state. |  |
| Begins when | The IRPManager decides to deactivate energySaving for selected network elements in a part of the network based on network load. |  |
| Step 1 (*) (M) | The IPRManager makes a decision on which NEs should remain in energySaving state or compensatingforEnergySaving state, or enter notEnergySaving state based on network load, geographic positions and maximum coverage of base stations. |  |
| Step 2 (*) (M) | Based on the output of step1, the IRPManager initiates energy saving deactivation and energy saving compensation deactivation on the NEs selected for the respective state transition. |  |
| Step 3 (*) (M) | After the completion of the energy saving deactivation process, the IRPAgent informs the IRPManager on the result of the process. |  |
| Ends when (*) | The selected network elements are in No-ES state. |  |
| Exceptions | FFS. |  |
| Post Conditions | Energy saving deactivation has been performed on the selected NEs. The selected NEs are in notEnergySaving state. The network coverage is maintained. The network capacity accommodates the increased load. |  |
| Traceability (*) | REQ-NCES-FUN-03, REQ-NCES-FUN-04 |  |

Next change

### 6.4.4	Energy saving deactivation on selected network elements (Distributed ES)

| Use Case Stage | Evolution / Specification | <<Uses>> Related use |
| --- | --- | --- |
| Goal (*) | Deactivating energy saving for a selected part of the network |  |
| Actors and Roles (*) | IRPManager as user |  |
| Telecom resources | Network elements (NEs) and their OSS. |  |
| Assumptions | The network operator has enabled the energy saving distributed function on selected network elements in a part of the network, so that the NEs can deactivate energy saving state depending on load conditions. An interference control function is available to support the coverage adjustment process among NEs in compensatingForEnergySaving and energySaving state. |  |
| Pre conditions | The affected network elements are in energySaving state or in compensatingForEnergySaving state. Network elements (e.g. base stations) are not in a faulty state. |  |
| Begins when | The distributed algorithm decides to deactivate energy saving for a selected part of the network based on network load. |  |
| Step 1 (*) (M) | The NE executes the energy saving algorithm that decides which NEs remain in energySaving state or compensatingforEnergySaving state or enter notEnergySaving state. |  |
| Step 2 (*) (M) | Based on the output of step 1, those NEs that in energySaving state or compensatingforEnergySaving state which have been selected to be transferred to notEnergySaving state, initiate energy saving deactivation or energy saving compensation deactivation and inform the IRPManager. |  |
| Ends when (*) | The selected network elements are in No-ES state. |  |
| Exceptions | FFS. |  |
| Post Conditions | Energy saving deactivation has been performed on the selected NEs. The selected NEs are in notEnergySaving state. The network coverage is maintained. The network capacity accommodates the increased load. |  |
| Traceability (*) | FFS |  |

End of changes

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.