3GPP TSG-SA5 (Telecom Management)	S5-110485

SA5#75, 24 - 28 Jan 2011; Sorrento, ITALY	revision of S5-110352

| CR-Form-v9.7 |
| --- |
| CHANGE REQUEST |
| ( | 32.280 | CR | 0020 | ( rev | 2 | ( Current version: | 10.2.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Clarify how 'AoC information' is presented to the UE |
| --- | --- |
| Source to WG: ( | Alcatel-Lucent |
| Source to TSG: ( | S5 |
| Work item code: ( | eAOC |  | Date: ( | 28/01/2011 |
| Category: ( | B |  | Release: ( | Rel-10 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) |
| Reason for change: ( | “AoC information” has been defined for an internal modelling of the overall AoC function behaviour, and only a sub-set of it is used for proceeding on different interfaces. The flows uses this “AoC information” as output for presentation to UE. |
| Summary of change: ( | Replace “AoC information” by “AoC Information XML body” as output for presentation to UE”. |
| Consequences if ( not approved: | How AoC is presented to UE is unclear |
| Clauses affected: ( | 5.3.2 |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

First change

### 5.3.2	Message Flows and Types for Offline Charging

The message flows in this chapter are based on the signalling flows specified in TS 24.647 [208].

The basic IMS session establishment for a user registered to AoC service(s) is depicted in the annex B. This basic call-flow will help describing in the future the message flows for AoC-S, AoC-D, AoC-E and also including cases where information are received from RTTI messages.

NOTE: The detailed AoC call-flows are FFS.

#### 5.3.2.1 	Successful Session Establishment: AoC-S with AoC information in reliable 1xx response (originating side)

Figure 5.3.2.1.1 shows the transactions for the successful delivery of the AoC information in 1xx response to the originating subscriber during session establishment originated by a UE.

# Figure 5.3.2.1.1: Message Sequence Chart for Session Establishment (1xx Response) with AoC-S

- An initial SIP Invite Request is received in the S-CSCF. This request is forwarded to the AoC Function.

- The AoC Function received the AoC Type = [AoC-S] and queries the OCS for Tariff Information.

- The AoC-S information is included in SIP 183 response.

- The UE acknowledges the SIP 183 with PRACK.

- AoC Function responses with SIP 200OK.

- The SIP Invite Request is received in the S-CSCF and forwards this request.

- The S-CSCF receives the SIP 200 OK response and forwards this response.

- The AoC Function queries the OCS and maps the Tariff Information into the AoC Information for further proceeding.

- The ACF inserts the  AoC-S and resulting “AoC information XML body” as defined in TS 24.647[208], in the SIP 200 OK response, and the S-CSCF forwards it towards UE

- The ACF sends a Charging Data Request with AoC service type and AoC Information indicating EVENT_RECORD to the CDF.

- The CDF generates the ACF-CDR to record the AoC service type and AoC Information.

- The CDF acknowledges the reception of the Charging Data Response.

#### 5.3.2.2 	Mid-session procedure: AoC-S with AoC information in an INFO request

Figure 5.3.2.2.1 shows the transactions for the successful delivery of the AoC information to the originating subscriber when a tariff change is detected by AoC Function.

NOTE:	This case is relevant when AoC-S is activated.

# Figure 5.3.2.2.1: Message Sequence Chart for mid-session procedure with AoC-S

- The AoC Function detects that tariff is changed and queries the OCS for Tariff Information.

- SIP INFO request is send with AoC-S and resulting “AoC information XML body” as defined in TS 24.647[208].

- The ACF sends a Charging Data Request with AoC service type and AoC Information indicating EVENT_RECORD to the CDF.

- SIP 200OK is received.

- The CDF acknowledges the reception of the Charging Data Response and generates the ACF-CDR.

#### 5.3.2.3	Session Release: AoC-E – Originating Party Clears

Figure 5.3.2.3.1 shows the transactions for the successful delivery of the AoC information to the originating subscriber when session is released by originating party.

NOTE:	This case is relevant also when AoC-D is activated.

Figure 5.3.2.3.1: Message Sequence Chart for Session Release Originating Party Clears

- A SIP session is released by sending a SIP BYE message. The S-CSCF forwards this message to the ACF and forwards this request.

- The AoC Function received the AoC Type = [AoC-E] and queries the OCS for Tariff Information.

- The S-CSCF receives the 200 OK response and forwards this response.

- The AoC Function maps the Tariff Information into the AoC Information for further proceeding.

- The ACF inserts the  AoC-S and resulting “AoC information XML body” as defined in TS 24.647 [208], in the SIP 200 OK response, and the S-CSCF forwards it towards UE

- The ACF sends a Charging Data Request with AoC service type and AoC Information indicating EVENT_RECORD to the CDF.

- The CDF generates the ACF-CDR to record the AoC service type and AoC Information.

- The CDF acknowledges the reception of the Charging Data Response.

#### 5.3.2.4	Session Release: AoC-E – Terminating party clears

Figure 5.3.2.4.1 shows the transactions for the successful delivery of the AoC information to the originating subscriber when session is released by terminating party.

NOTE:	This case is relevant also when AoC-D is activated.

# Figure 5.3.2.4.1: Message Sequence Chart for Session Release Terminating Party Clears

1)	A SIP session is released by sending a SIP BYE message. The S-CSCF forwards this message to the AoC Function and forwards this request.

2)	The AoC Function queries the OCS and converts the Tariff Information to AoC Information for AoC-E.

3)	The S-CSCF receives the 200 OK response and forwards this response.

4)	The AoC Function maps the Tariff Information into the AoC Information for further proceeding

5)	The ACF inserts the  AoC-E and resulting “AoC information XML body” as defined in TS 24.647[208], in the SIP 200 OK response, and the S-CSCF forwards it towards UE

6)   The ACF sends a Charging Data Request with AoC service type and AoC Information indicating EVENT_RECORD to the CDF.

7)	The CDF generates the ACF-CDR to record the AoC service type and AoC Information.

8)	The CDF acknowledges the reception of the Charging Data Response.

End of changes

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.