## Slide 1: Application Redirection Discussion
What is redirection and is specialized or differentiated charging required?
3GPP TSG SA WG5 (Telecom Management) Meeting #86
12-16 November 2012;New Orleans, USA
S5-123004
Rev of S5-122989

## Slide 2: Overview
TS 23.203 does not go into detail of user plane actions taken for redirection.
This presentation depicts two different types of network access:
  Web site access
  Application X access
PCC and ADC rules are provided to identify the charging available for that type.
For each type, an ADC redirect rule is installed.
Conclusion:
  In both types of redirect, standard PCC rules can be used to capture the redirected traffic with no additional requirements necessary.

## Slide 3: Web Site Access
PCEF
IP
TDF
Web Z.com
IP: z
Web Y.com
IP: y
App IP: x4
App IP: x3
App IP: x2
App X
IP: x1
Opp App X
IP:ox
Oper. Portal
IP:op
ADC Rules
None
PCC Rules
IP=op, RG=2
All other, RG=1
Src IP: UE
Dst IP: y
HTTP GET
Host: Y.com
Src IP: UE
Dst IP: y
HTTP GET
Host: Y.com
Src IP: UE
Dst IP: y
HTTP GET
Host: Y.com
Src IP: y
Dst IP: UE
200 OK
Src IP: y
Dst IP: UE
200 OK
Src IP: y
Dst IP: UE
200 OK

## Slide 4: TDF Web Site Redirect
PCEF
IP
TDF
Web Z.com
IP: z
Web Y.com
IP: y
App IP: x4
App IP: x3
App IP: x2
App X
IP: x1
Opp App X
IP:ox
Oper. Portal
IP:op
ADC Rules
App=X, Redirect to ox
App=Unsubscr. ibed Sites, Redirect to op
PCC Rules
IP=op, RG=2
All other, RG=1
Src IP: UE
Dst IP: y
HTTP GET
Host: Y.com
Src IP: UE
Dst IP: y
HTTP GET
Host: Y.com
Src IP: UE
Dst IP: op
HTTP GET
Host: Y.com
Src IP: op
Dst IP: UE
200 OK
Src IP: op
Dst IP: UE
200 OK
Src IP: op
Dst IP: UE
200 OK

## Slide 5: Application Access
PCEF
IP
TDF
Web Z.com
IP: z
Web Y.com
IP: y
App IP: x4
App IP: x3
App IP: x2
App X
IP: x1
Opp App X
IP:ox
Oper. Portal
IP:op
ADC Rules
App=X, RG=4
PCC Rules
IP=op, RG=2
All other, RG=1
Src IP: UE
Dst IP: x1..x4
App X
Src IP: x1..x4
Dst IP: UE
App X
Src IP: x1..x4
Dst IP: UE
App X
Src IP: x1..x4
Dst IP: UE
App X
Src IP: UE
Dst IP: x1..x4
App X
Src IP: UE
Dst IP: x1..x4
App X

## Slide 6: TDF Application Redirect
PCEF
IP
TDF
Web Z.com
IP: z
Web Y.com
IP: y
App IP: x4
App IP: x3
App IP: x2
App X
IP: x1
Opp App X
IP:ox
Oper. Portal
IP:op
ADC Rules
App=X, redir. To ox
PCC Rules
IP=ox, RG=2
All other, RG=1
Src IP: UE
Dst IP: x1
App X
Src IP: ox
Dst IP: UE
App X
Src IP: ok
Dst IP: UE
App X
Src IP: ox
Dst IP: UE
App X
Src IP: UE
Dst IP: x1
App X
Src IP: UE
Dst IP: ox
App X