## Slide 1: Single arbitrator vs Self-arbitration
Nishant Gupta David Chater-Lea
Samsung Electronics Motorola Solutions

## Slide 2: Release 13 MCPTT
Within the same MCPTT group:
User B is transmitting. The transmitting party is also the floor arbitrator.
User G can pre-empt User B.
If User R and User B are out of range of each other
  User R always starts the transmission, if not aware of another ongoing transmission, regardless of probable interference with reception at User G.
  There is no protocol allowing User G to stop User R from transmitting.
  If User G starts to transmit, both of Users R and B can receive the transmission, and both can request to pre-empt.
  If User R transmits using a different physical/ProSe layer resource from User B, there is no conflict. This situation is not described in Release 13 MCPTT, but user G would be expected to only join one of the two concurrent transmissions.
If User G starts to transmit, both of Users R and B can receive the transmission, and both can request to pre-empt
If User R transmits using a different physical/ProSe layer resource from User B, there is no conflict. This situation is not described in Release 13 MCPTT, but user G would be expected to only join one of the two concurrent transmissions
B
G
R

## Slide 3: Transmission Requests
Problem – As R is not in the range of the transmission arbitrator (P), its requests wont get a response.
Result – R may transmit assuming there is no transmission arbitrator.
Advantage – Information that R want to transmit, is transmitted timely.
Disadvantage – R may cause interference at Xs and G.
Single Arbitrator (P)
Problem – R has at least one transmission arbitrator to make the request to, but whom should R request? B or G?
Result – Non-deterministic. If R asks G, request may be denied. If R asks B, it may be granted.
Advantage – If, the request is sent to G, interference that may have occurred at Xs already receiving 3 transmissions is avoided.
Disadvantage – Non-deterministic results and although the limit is not reached in R’s region, permission may not be granted.
Self-arbitration
*Maximum simultaneous transmissions allowed - 3
O
O
X
X
X
X
R
O
P
O
O
O
O
O
O
G
B
Question:
  Considering R may or may not cause interference at Xs but not at B or Os, should R be allowed to transmit or not?

## Slide 4: Transmission Override
R will send a pre-emptive request to G.
Problem – not possible if R and G are out of range of each other
Result – G will determine priority and may either revoke another transmitter (B) or itself, or deny if needed.
Advantage – Deterministic. Central coordination.
Disadvantage – P may be revoked if P has least priority transmission even though it is not in range of R.
Single Arbitrator (G)
Problem – Whom should R request? B or G?
Result – Non-deterministic.
Advantage – P as not in range of R will never be revoked.
Disadvantage – Non-deterministic user experience.
Self-arbitration
*Maximum simultaneous transmissions allowed - 3
Question:
  Should the behavior be deterministic – every time R tries to override the transmission, while the topology is same, should get the same response?
O
O
X
X
X
X
R
O
P
O
O
O
O
O
O
G
B

## Slide 5: Interference
If R wants to transmit, in either case, single arbitrator or self-arbitration, R will be allowed to transmit media.
Single Arbitrator or self-arbitration
Questions:
  Should the client R be considerate about the probable interference it may cause at G, although user R has no information about such a reception at G?
  Should G be able to inform R about transmissions that it is receiving, even though it is not an arbitrator and not transmitting?
G
R
O
O
O
O
O
O
O
O
O
O
O
P
P
P

## Slide 6: Should self arbitrator consider own transmission only?
This issue relates primarily to the multiple arbitrator option within one group, but could be applied to knowledge of other groups’ resource usage in the single arbitrator case
Should G make arbitration decisions concerning R based on its knowledge of other transmitters B and P?
  Advantage: can minimise interference and contention
  Disadvantage: can lead to unnecessary blocking , as G does not know if B and P are in range of R, and of parties that want to receive R’s transmission (O)
Additional issue: if G grants R transmission rights, how does R choose resources not used by B?
  Implies coupling between layers and information about ProSe usage at application layer
B
G
R
O
P

## Slide 7: Questions
User’s need to transmit vs. probable interference?
Deterministic behavior vs. non-deterministic behavior?
Should the solution take on further complexities:
  Decisions based on reception of other transmissions
  Coupling between layers for resource knowledge