3GPP TSG-SA WG6 Meeting #49-bis-e	S6-221781 rev 3

e-meeting, 22nd June – 1st July 2022	(revision of S6-221700 rev1)

Source:	Convida Wireless LLC

Title:	AC Association-aware solution update with CAAR

Spec:	3GPP TR 23.700-98 v.0.7.0

Agenda item:	9.8

Document for:	Approval

Contact:	Catalina Mladin, mladin.catalina@convidawireless.com

1. Introduction

This proposal is a merge of S6-221699_rev1 and S6-221700_rev1, as discussed at SA6 #49bis conference calls. It uses the text provided in each document to provide in the same clause 7.27 the two options introduced by these tdocs, since they are both technically viable.

In addition, the proposal documents the option where assumption that common EES has been achieved/ pre-provisioned is used, since that simplifying assumption is used by similar solutions.

In S6-221781 higlights have been used differently than before. They are used to bring attention to portions of the updates which are new relative to the text presented in S6-221699_rev1 and S6-221700_rev1, since the other changes have been previously introduced.

July 18 conf call responses to Final phase comments :

[Huawei]

In the EEC context, only association ID is required, and the association ID in the Service session context should also be removed, since the service session context is a part of the EEC context and the EEC context already has the Association ID, no need to duplicated.

[catalina] I made the EEC Context change only for option (ii) – the corresponding changes are highlighted in magenta

Association profile was already used according to the following quotes (i.e. for option ii)

clause 8.8.3.8	 for option (ii) “the receiving EES uses the association ID information to update the information about the AC associations served.”

clause 8.9.1.5	 for option (ii) “When the EES determines that a registered EAS is providing services to an AC which is part of an AC association Profile, the EES updates the corresponding Service Session context with the association ID and updates the information about serviced AC Associations accordingly. “….“T-EES adds it to its own profile”.

why EDN configuration information and EES profile should have the list of AC association profile?

[catalina] As previously discussed:  this is how the information gets from the ECS to EEC in the provisioning response. The EDN configuration is used for option (iii), and EES Profiles for option (ii). Neither is used for option (i) which has been the most aligned with Huawei position.

For the T-EAS discovery procedure only group ID info is required

[catalina] The T-EAS discovery procedure uses the “main” discovery filters. Those are enhanced anyway for the purpose of regular discovery. Why do we need to make an exception here?

For the ACR request message, AC association profile is not required. The S-EES can get the group information during the EAS discovery procedure? During the ACR, when the EEC send the request message contains the UE ID and ACID, then the S-EES can be aware of these UE is related to the group.

[catalina] This comment was already addressed in 1781, where only the ID was retained in the ACR request.

The EEC context does not need to maintain the association information, since during T-EAS discovery procedure, the T-EES can obtain the group info during the EAS discovery

[catalina] That means the T-EES needs to receive a discovery request from EEC in every ACR type. As discussed many times, in 8.8.2.5 this is not the case.

Besides, EEC registration is optional, therefore EEC context is optional, and AC association is optional within that. So again, the EEC Context with this info is an option that does not need to be included with (i)

Another point is that the ECS does not need to maintain the group information, because the EEC or the S-EES will send the group information to the ECS, then the ECS will select the common EES for the group, the ECS does not need to maintain the group information. thus there is no need to add CAAR to maintain the group information.

[catalina] CAAR is added in only one option out of 3, namely (iii).

From another aspect, there is already CBS in the TR, why we need another server to maintain the group information? what is the different between CAAR and CBS?

[catalina] CBS is not Convida proposal, so there is no reason for us to do an analysis of what is different. To summarize what I explained in conference call: CBS is a decision- making entity, CAAR is simply a repository. Information is stored by EES at CAAR and is retrieved by ECS. I believe that in the CBS solution, CBS is the brain of the entire functionality, determining associations and signaling the information as well. Even if the solutions were similar (and they are not) they could be both captured in the TR.

Ericsson:

Besides, some conditions are incorrect: e.g. EDN info impact is not only for option (iii) with CAAR.

[catalina] Are you saying you want it removed for (iii), or that is needed for other options as well?

And the logic for CAAR is not clear, seems it is for option (ii) w/o CAAR

the ECS further compares AC association Profile information in the request (e.g., common EAS characteristics) against the EES profiles from its registered EESs to determine if any of the EES(s) are candidates to service the AC association (e.g., have registered EAS(s) meeting the requirements of the AC association).

[catalina] Let’s discuss this at conf call. Are you saying that if there is no EES currently servicing AA, then ECS cannot determine candidate EESs to provide in the provisioning response? If yes I can delete this from option (iii), but it will make the process of finding common EES more difficult.

2. Reason for Change

Provide further details for solution #27.

3. Proposal

It is proposed to discuss whether the functionality enabled by CAAR in solution #27 is desirable or necessary, and one of the two options in S6-221699, S6-221700, be agreed as update to 3GPP TR 23.700-98.

* * * First Change * * * *

## 7.27	Solution #27: Enabling AC Association Aware services by selecting common EASs

### 7.27.0	General

This solution provides two options for determining a common EES (termed “with CAAR” and “without CAAR”), which is necessary before determining a common EAS. If in the normative phase, viable solutions may be considered with the assumption that the EAS selection information pre-provisions common EES, the solution in this clause may be used to derive three alternatives:

- Determine common EAS based on the assumption that common EES has been achieved/ pre-provisioned (termed “assumed common EES”).

NOTE: [ describe how common EES is achieved for this option. Over the top???]

- Determine common EAS; common EES determined with direct ECS support for maintaining information on AC Association serviced per EES (i.e., “without CAAR”)

- Determine common EAS; common EES determined with CAAR supporting ECS with maintaining information on AC Association serviced per EES (i.e.,” with CAAR”)

## The following descriptions apply to all three alternatives, unless sub-clause titles or clarifying NOTEs specify otherwise.

### 7.27.1	Architecture enhancements

NOTE: The architectural enhancement introduced in this clause is optional. It is necessary if there is no assumption of a common EES having been achieved/ pre-provisioned before the solution is employed. More specifically, it is necessary for the option “with CAAR” (iii) as described in clause 7.27.0.

Figure 7.27.1-1: EDGEAPP architecture enhanced with Central AC Association Repository

The EDGE-X reference point is introduced to support EES interaction with a Central AC Association Repository (CAAR). The EES can store, update and remove information about the AC associations it provides services to via EDGE-X reference point.

The EDGE-Y reference point is introduced to support ECS interaction with CAAR. The ECS can query the AC association information via EDGE-Y reference point.

CAAR can be deployed collocated to the ECS, and it is a single repository for maintaining AC Association information.

NOTE:  It is to be determined in the normative phase whether CAAR and Binding Server from solution 30 can be merged.

### 7.27.2	Solution description

#### 7.27.2.1	General

This solution addresses key issue #17 on discovery of a common EAS in clause 4.17.

The solution describes enhancements to several edge procedures that enable ACs/EECs of different UEs to share AC association information with the EEL. This AC association is formed such that the services for the associated ACs are optimized by selecting a common EAS.

NOTE:	In the following descriptions within this solution, the term "Associated ACs" is used to denote a set of ACs on different UEs for which the association described above has been configured via an AC association Profile. How the AC association Profile is determined is out of scope of the current specification.

#### 7.27.2.2	New Information Elements

The AC association Profile is proposed as a new IE in TS 23.558:

Table 7.27.2.2-1: AC association Profile

| Information element | Status | Description |
| --- | --- | --- |
| Association ID | M | Identity of the Association |
| AC association type | M | Choice of multi-use or multi-session |
| List of associated UEs characteristics | O | Information for determining the UEs with associated ACs |
| > Associated UE group ID | O | Group ID pre-provisioned (i.e. as External Group ID) to the UEs with ACs in the associated group. If this IE is not present, |
| > Associated UEs service area | O | Service area for determining other UEs in the association. The UE location is described in clause 7.3.2. The optional additional EAS selection criteria describe criteria for the EAS selection (e.g., "same latency for all" or "lowest latency for the own UE location"). |
| List of associated ACs characteristics (NOTE 1) | M | Information for determining the ACs on the associated UEs |
| > common ACID | O | If provided, all ACs in the association have the same AC ID as indicated |
| > common ACs Type | O | If provided, all ACs in the association have the same AC Type as indicated |
| > common ACs Schedule | O | If provided, all ACs in the association have the same AC Schedule as indicated |
| List of common EAS characteristics (NOTE 1) | M | Information for determining the common EAS |
| >Common EAS discovery filter (NOTE 2) | O | Describes the characteristics of a common EASs using the EAS discovery filter described in Table 8.5.3.2-2. |
| > Common EAS aggregate Service KPIs | O | Service characteristics provided by the common EAS, detailed in Table 8.2.5-1. The characteristics are described to meet the requirements for the AC association. |
| NOTE 1: Either "List of associated AC characteristics" or "List of common EAS characteristics" shall be present. NOTE 2: Only the "List of EAS characteristics" IE from Table 8.5.3.2-2 is included. The "List of EAS characteristics" IE must include at least one optional IE, if used as an EAS discovery filter. |

Editor's note.	The list of IEs in Table 7.27.2.2-1 and whether AC association information should be provided in a new Profile IE, or via existing ones, is FFS.

Editor's note.	Whether the ACs in an AC association information may have different ACIDs is FFS.

#### 7.27.2.3	Enhancements to existing Information Elements

The enhancements captured (highlighted with bold text) in tables within this clause are proposed to Information Element tables in 3GPP TS 23.558 [2]. Enhancements to requests, responses and notifications are described in following clauses via procedural descriptions

Table 7.27.2.3-1: EAS discovery filters

| Information element | Status | Description |
| --- | --- | --- |
| List of AC characteristics (NOTE 1) | O | Describes the ACs for which a matching EAS is needed. |
| > AC profile (NOTE 2) | M | AC profile containing parameters used to determine matching EAS. AC profiles are further described in Table 8.2.2-1. |
| List of EAS characteristics (NOTE 1, NOTE 3) | O | Describes the characteristic of required EASs. |
| > EASID | O | Identifier of the required EAS. |
| > EAS provider identifier | O | Identifier of the required EAS provider |
| > EAS type | O | The category or type of required EAS (e.g. V2X) |
| > EAS schedule | O | Required availability schedule of the EAS (e.g. time windows) |
| > EAS Geographical Service Area | O | Location(s) (e.g. geographical area, route) where the EAS service should be available. |
| > EAS Topological Service Area | O | Topological area (e.g. cell ID, TAI) for which the EAS service should be available. See possible formats in Table 8.2.7-1. |
| > Service continuity support | O | Indicates if the service continuity support is required or not. |
| > Service permission level | O | Required level of service permissions e.g. trial, gold-class |
| > Service feature(s) | O | Required service features e.g. single vs. multi-player gaming service |
| AC association profile | O | Describes an association between ACs and an association between ACs and a common EAS. |
| NOTE 1: Either "List of AC characteristics", "List of EAS characteristics" or AC association profile shall be present. NOTE 2: "Preferred ECSP list" IE shall not be present. NOTE 3: The "List of EAS characteristics" IE must include at least one optional IE, if used as an EAS discovery filter. |

NOTE 1: The enhancement to EEC Context shown in table 7.27.2.3-2 is necessary for the option “without CAAR” (ii) as described in clause 7.27.0., only.

Table 7.27.2.3-2: EEC Context

| Information element | Status | Description |
| --- | --- | --- |
| EEC ID | M | Unique identifier of the EEC. |
| EEC Context ID | M | Identifier assigned to the EEC Context |
| Source EES Endpoint | M | The endpoint address (e.g., URI, IP address) of the EES that provided EEC context ID. |
| UE Identifier | O | The identifier of the hosting UE (i.e., GPSI or identity token) |
| List of EDGE-1 subscriptions | O | List of subscriptions IDs for capability exposure to the EEC ID (NOTE). |
| UE location | O | Latest UE location of the UE hosting the EEC which was available at the EES. |
| List of AC Profiles | O | Information about the ACs as described in Table 8.2.2-1. |
| List of AC association profiles | O | List of all AC associations applicable to the EEC |
| List of Service Session Contexts | O | List of associated Service Session Context IEs. Each Service Session Context includes information maintained by the EES for the services (involving UE related resources) received from an EAS registered to the EES. |
| > Service Session Context | M | Service Session Context is described in Table 8.2.8-2 |
| NOTE 1: The corresponding EDGE-1 subscription information may include 3GPP CN subscription information such as subscription correlation ID NOTE 2: Whether the Service Session Context IE needs to contain AC Association ID as optional element, is to be determined in the normative phase. |

NOTE 2: The enhancement to EDN configuration information shown in table 7.27.2.3-3 is necessary for the option “with CAAR” (ii) as described in clause 7.27.0., only.

The IE enhancement is used to provide EECs in the service provisioning phase with information about which EESs already service AC associations. This enables the EEC to determine which EES to choose if common EAS association services are needed. Note that the service provisioning response may also be limited by ECS to include only the EDNs/EESs which provide such services. However, that limitation is sub-optimal if the EEC determines that such services are needed after the service provisioning is done.

The information about serviced AC Association is stored by EESs in CAAR and is retrieved by ECS from CAAR.

Table 7.27.2.3-3: EDN configuration information

| Information element | Status | Description |
| --- | --- | --- |
| EDN connection information (NOTE 1) | M | Information required by the UE to establish connection with the EDN. |
| > DNN/APN | M | Data Network Name/Access Point Name |
| > S-NSSAI | O | Network Slice information |
| > EDN Topological Service Area | O | The EDN serves UEs that are connected to the Core Network from one of the cells included in this service area. See possible formats in Table 8.2.7-1. |
| List of EESs | M | List of EESs of the EDN. |
| > EESID | M | The identifier of the EES |
| > EES Endpoint | M | The endpoint address (e.g. URI, IP address) of the EES |
| > EASIDs (NOTE 2) | O | List of EASIDs registered with the EES. |
| > EES Provider identifier | O | The identifier of the EES Provider (such as ECSP) |
| > EES Topological Service Area | O | The EES serves UEs that are connected to the Core Network from one of the cells included in this service area. EECs in UEs that are located outside this area shall not be served. See possible formats in Table 8.2.7-1. |
| > EES Geographical Service Area | O | The area being served by the EES in Geographical values (as specified in clause 7.3.3.3) |
| > List of EES DNAI(s) | O | DNAI(s) associated with the EES/EAS. This IE is used as Potential Locations of Applications in clause 5.6.7 of 3GPP TS 23.501 [2]. |
| > EES Service continuity support | O | Indicates if the EES supports service continuity or not. This IE also indicates which ACR scenarios are supported by the EES. |
| > EEC registration configuration | M | Indicates whether the EEC is required to register on the EES to use edge services or not. |
| >List of association IDs (NOTE 3) | O | List of association IDs of the AC associations the EES is serving |
| Lifetime | O | Time duration for which the EDN configuration information is valid and supposed to be cached in the EEC. |
| NOTE 1: If the UE is provisioned or pre-configured with URSP rules by the HPLMN, the UE handles the precedence between EDN connection info and URSP rules as defined in 3GPP TS 23.503 [12] clause 6.1.2.2.1. EDN connection info is considered to be part of UE Local Configurations. NOTE 2: EAS information is limited to the EEC requested applications. If no AC profiles were present in the service provisioning request, the EAS information is subject to the ECSP policy (e.g. no EAS information or a subset of EAS information related to the EES). NOTE 3: Whether the list needs to contain the entire AC association Profile, or the IDs are sufficient, is to be determined in the normative phase. |

NOTE 3: The enhancement to EES Profile information shown in table 7.27.2.3-3 is necessary for the option “without CAAR” (ii) as described in clause 7.27.0., only.

The IE enhancement is used to provide EECs in the service provisioning phase with information about which EESs already service AC associations. This enables the EEC to determine which EES to choose if common EAS association services are needed. Note that the service provisioning response may also be limited by ECS to include only the EDNs/EESs which provide such services. However, that limitation is sub-optimal if the EEC determines that such services are needed after the service provisioning is done.

The information about serviced AC Association is provided to ECS by EESs directly, via EES registration updates.

Table 7.27.2.3-3: EES Profile

| Information element | Status | Description |
| --- | --- | --- |
| EESID | M | The identifier of the EES |
| EES Endpoint | M | Endpoint information (e.g. URI, FQDN, IP address) used to communicate with the EES. This information is provided to the EEC to connect to the EES. |
| EASIDs | M | List of EASIDs registered with the EES. |
| EEC registration configuration | M | Indicates whether the EEC is required to register on the EES to use edge services or not. |
| EES Provider Identifier | O | The identifier of the ECSP that provides the EES Provider. |
| EES Topological Service Area | O | The EES serves UEs that are connected to the Core Network from one of the cells included in this service area. EECs in UEs that are located outside this area shall not be served. See possible formats in Table 8.2.7-1. |
| EES Geographical Service Area | O | The area being served by the EES in Geographical values (as specified in clause 7.3.3.3) |
| List of EES DNAI(s) | O | DNAI(s) associated with the EES. This IE is used as Potential Locations of Applications in clause 5.6.7 of 3GPP TS 23.501 [2]. It is a subset of the DNAI(s) associated with the EDN, where the EES resides. |
| EES Service continuity support | O | Indicates if the EES supports service continuity or not. This IE also indicates which ACR scenarios are supported by the EES. |
| List of AC association profiles | O | List of AC associations for which the EES is a common EES |

#### 7.27.2.4	Enhancements to Service Provisioning for determining common EES

##### 7.27.2.4.1	Using the “assumed common EES” option (option i)

##### If the “assumed common EES” option is used, procedures for determining common EES are not necessary.

#### 7.27.2.4.2	Determining common EES without CAAR (option ii)

During the service provisioning procedure defined in 3GPP TS 23.558 [2], the AC association Profile is used to indicate that the use of a common EAS is required. The service provisioning response is used to provide information about which EESs may already service which AC association profile. In this option, this information is provided via the EES Profiles in the service provisioning response and is obtained by ECS from EESs via EES registration updates.

Compared to the procedurs specified in 3GPP TS 23.558 [2] clause  8.3.3, the proposed differences are captured below.

Enhancements to 3GPP TS 23.558 clause 8.3.3 Service Provisioning

- The service provisioning request (3GPP TS 23.558 [2] Table 8.3.3.3.2-1) from EEC to ECS is enhanced to include an AC association Profile.

- Upon receiving the request, the ECS uses the AC association Profile information (e.g., association ID) against EES profile(s) the ECS has received from its registered EES(s) to determine whether an EES is already servicing the AC association. If a match is not found, the ECS further compares AC association Profile information in the request (e.g., common EAS characteristics) against the EES profiles to determine if any of the EES(s) are candidates to service the AC association (e.g., have registered EAS(s) meeting the requirements of the AC association).

- If the processing of the request with AC association Profile information was successful, the ECS responds to the EEC with a service provisioning response. The EDN configuration information in the response indicates EESs already be servicing the AC association or candidate EESs to service the AC association.

If the ECS is unable to determine EES(s) to service the AC association, the ECS rejects the service provisioning request and responds with an appropriate failure cause.

If the ECS determines multiple EES(s) to service the AC association, the ECS may provide an EES list to the EEC with parameters used to evaluate the AC association-related service.

NOTE: The full list of service provisioning response parameters is to be finalized in the normative phase. Enhanced functionality may be provided, for example, by indicating the number of ACs in the association which are being served by each EES, etc. Any such parameters are to be provided by the EES in the EES profile.

##### 7.27.2.4.3	Determining common EES with CAAR (option iii)

During the service provisioning procedure defined in 3GPP TS 23.558 [2], the AC association Profile is used to indicate that the use of a common EAS is required. The service provisioning response is used to provide information about which EESs may already service which AC association profile. In this option, this information is provided via the EDN Configuration Information in the service provisioning response and is obtained by ECS via CAAR queries.

Compared to the procedurs specified in 3GPP TS 23.558 [2] clause  8.3.3, the proposed differences are captured below.

Enhancements to 3GPP TS 23.558 clause 8.3.3 Service Provisioning

- The service provisioning request (3GPP TS 23.558 [2] Table 8.3.3.3.2-1) from EEC to ECS enhanced to include an AC association Profile.

- Upon receiving the request, the ECS uses the AC association Profile information (e.g., association ID) to query the (EES ID, association ID list) tuples stored by CAAR to determine whether an EES is already servicing the AC association. The ECS uses the association ID(s) to query the CARR using the procedure in 7.27.2.Z . If a matching EES is not found, the ECS further compares AC association Profile information in the request (e.g., common EAS characteristics) against the EES profiles from its registered EESs to determine if any of the EES(s) are candidates to service the AC association (e.g., have registered EAS(s) meeting the requirements of the AC association).

- If the processing of the request with AC association Profile information was successful, the ECS responds to the EEC with a service provisioning response. The EEC uses the EES(s) obtained from the step 2 CAAR query to update the enhanced EDN configuration information (Table 7.27.2.3-4) with EES(s) already servicing the AC association and send it in the provisioning response.

If the ECS is unable to determine EES(s) to service the AC association, the ECS rejects the service provisioning request and responds with an appropriate failure cause.

If the ECS determines multiple EES(s) to service the AC association, the ECS may provide an EES list to the EEC with parameters used to evaluate the AC association-related service.

NOTE: The full list of service provisioning response parameters is to be finalized in the normative phase. Enhanced functionality may be provided, for example, by indicating the number of ACs in the association which are being served by each EES, etc. Any such parameters are to be provided by the EES to the CAAR.

#### 7.27.2.5	Discovery of common EAS Procedure

In this procedure, the EEC sends an EAS discovery request to an EES including AC association Profile. Based the AC association Profile, the EES determines an EAS discovery result that includes a common EAS for the AC association.

NOTE: The following procedure may be realized in normative phase as an enhancement to the existing EAS discovery procedure. It is captured separately in this specification for the purpose of initial topic discussions.

Pre-conditions:

1.	An AC association Profile has been provided to the EEC.

Figure 7.27.2.5-1: Common EAS discovery with AC association Profile

1.	The EEC sends an EAS discovery request to the EES. The EAS discovery request includes an AC association Profiles. Included in the AC association Profile is information regarding an association between AC(s) on this UE and other ACs indicating that the use of a common EAS is required.

2.	Upon receiving the request, the EES determines whether a common EAS is available to provide services to the associated ACs that meet the criteria specified in the AC association Profile

3.	If the processing of the request was successful, the EES responds to the EEC with an EAS discovery response which includes information about the discovered common EAS able to provide services to the associated ACs.

4.	If the EES is unable to determine a common EAS for the associated ACs, the EES responds with an appropriate failure cause.

#### 7.27.2.6	Enhancements to ACR

During the detection, decision-making and execution phases of the ACR procedures defined in 3GPP TS 23.558 [2], an AC association Profile can be used to identify ACs requiring a common EAS. This information can be used in the ACR procedures to coordinate the transitioning of the associated ACs from a common S-EAS to a common T-EAS.

Compared to the procedures specified in 3GPP TS 23.558 clause  8.8, the proposed differences are captured below.

Enhancements to 3GPP TS 23.558 clause 8.8.3.2	Discover T-EAS procedure

Compared to the procedures specified in 3GPP TS 23.558 [2] clause  8.8.3.2, the proposed differences are captured below:

- The enhanced EAS discovery filter (Table 7.27.2.3-1) within the EAS discovery request from the S-EAS includes AC association Profile information (e.g., common EAS characteristics).

- The S-EES checks if the T-EAS satisfies the AC association Profile (e.g., common EAS characteristics) and can serve as a common EAS for the associated ACs.

- The EAS discovery filter (Table 7.27.2.3-1) within the EAS discovery request issued from the S-EES to the T-EES includes AC association Profile information (e.g., common EAS characteristics).

- The T-EES discovers the T-EAS(s) utilizing the common EAS characteristics of the AC association profit, such that a common EAS able to serve the associated ACs is provided in the response.

Enhancements to 3GPP TS 23.558 clause 8.8.3.3	Retrieve T-EES procedure

NOTE 1: In the “assumed common EES” (i) option, T-EES equals S-EES, so no enhancements are required for 3GPP TS 23.558 clause 8.8.3.3.

Compared to the procedures specified in 3GPP TS 23.558 clause  8.8.3.3, the proposed differences are captured below:

1.	The T-EES retrieve request (3GPP TS 23.558 [2] Table 8.8.4.6-1) from the S-EES to the ECS is enhanced to optionally include includes AC association Profile.

2.	The ECS interacts with the 3GPP core network to retrieve the UE locations.

The ECS determines a common T-EES for the AC association.

NOTE 2: In the option “without CAAR” (ii) the ECS uses AC association Profile, UE location, as well as CAAR query as detailed in clause 7.27.2.Z to make this determination. In the option “with CAAR” (iii) the ECS the AC association Profile, UE location, and EES Profiles provide all the information required to make this determination.

In addition, in options (ii) and (iii) if an “associated group ID” is provided in the AC association Profile, the ECS may interact with the 3GPP core network to determine the number of UEs present in candidate EES(s) service area(s). Alternatively, the ECS uses “Associated UEs service area” in the AC association Profile to determine whether the candidate EES service area meets the needs of the AC association. The ECS uses the associated group ID and UE locations determine whether T-EESs are candidates for servicing the AC association

Enhancements to 3GPP TS 23.558 clause 8.8.3.4	ACR launching procedure

Compared to the procedures specified in 3GPP TS 23.558 [2] clause  8.8.3.4, the proposed differences are captured below:

- The ACR request message (3GPP TS 23.558 [2] Table 8.8.4.4-1) sent to the EES by EEC is enhanced to optionally include an AC association ID.

- If the request in step 1 is for ACR initiation and if the EAS notification indication in ACR initiation data is provided in the step 1 request and the EAS has subscribed to receive such notification, the EES includes the association ID of the AC association in the notification.

The notified EAS uses the association ID during the ACR status update procedure and may store it with the Application context maintained. The content of the application content maintained by EAS is out of scope of the current document.

Enhancements to 3GPP TS 23.558 clause 8.8.3.8	ACR status update procedure

Compared to the procedure specified in 3GPP TS 23.558 [2] clause  8.8.3.8, the proposed differences are captured below:

- The EAS sends the ACR status update request message (3GPP TS 23.558 [2] Table 8.8.4.19-1) to the S-EES that is enhanced to include an association ID of the AC association for which the ACR has been performed.

NOTE 2: S-EAS obtains the association ID via pre-provisioning, from an ACR management event notification or directly from the AC and may store it in the Application Context. T-EAS may obtain the association ID via pre-provisioning or via ACT.

- If ACR is successful, the receiving EES uses the association ID information to update the information about the AC associations served.

NOTE 3: In the “assumed common EES” (i) option, no enhancement to step 2 is required.

In the option “without CAAR” (ii) the EES update is to its EES Profile. The S-EES removes the corresponding AC association profile from the list in its EES Profile. The T-EES uses the corresponding AC association profile from the EEC context it received during ACR and adds it to its own EES Profile. EES Profile updates result in EES registration update.

- In the option “with CAAR” (iii) the EES update is to the information available at CAAR. The S-EES removes its corresponding (association ID, EES ID) tuple from CAAR. The T-EES adds its corresponding (association ID, EES ID) tuple to CAAR.

#### 7.27.2.7	Other procedural enhancements

Enhancements to 3GPP TS 23.558 clause 8.9.1.1	EEC Context handling at EEC registration

Compared to the procedures specified in 3GPP TS 23.558 [2] clause  8.9.1.1, the following differences are captured below:

If the EEC registration request does not include a previously assigned EEC Context ID value, the receiver EES creates an EEC Context. The receiver EES assigns an EEC context ID and set the source EES Endpoint to its own Endpoint. The EEC ID, UE Identifier and List of AC association profiles are set based on the corresponding registration request parameters.

Enhancements to 3GPP TS 23.558 clause 8.9.1.5	Other EEC Context handling

Compared to the procedures specified in 3GPP TS 23.558 clause  8.9.1.5, the following differences are captured below:

When the EES determines that a registered EAS is providing services to an AC which is part of an AC association Profile, the EES updates the corresponding Service Session context with the association ID and updates the information about serviced AC Associations accordingly.

NOTE 4: In the “assumed common EES” (i) option, no enhancement to 3GPP TS 23.558 clause 8.9.1.5 is required.

In the option “without CAAR” (ii) the EES update is to its EES Profile. The S-EES removes the corresponding AC association profile from the list in its EES Profile. The T-EES uses the corresponding AC association profile from the EEC context it received during ACR and adds it to its own EES Profile. EES Profile updates result in EES registration update.

In the option “with CAAR” (iii) the EES update is to the information available at CAAR. The S-EES removes its corresponding (association ID, EES ID) tuple from CAAR. The T-EES adds its corresponding (association ID, EES ID) tuple to CAAR.

#### 7.27.2.8	New procedures

#### 7.27.2.8.1	EES Update of AC Associations with CAAR (option iii)

The EES procedure for updating AC Associatiation information available at CAAR uses an update request in which the following information is provided to the CAAR: EES ID, list of association IDs of the associations being served, registrar ECS information including list of EDNs. This information is updated by EES when any of this information changes or is about to change (e.g. in advance of EES de-registration).

#### 7.27.2.8.2	ECS Query of AC Associations with CAAR (option iii)

The ECS procedure for quering the AC Associatiation information at CAAR uses the association IDs recieived (e.g. in a service provisioning request) and its own ECS information. The response provides a list of its registered EESs which serve the AC Association Profiles IDs being queried for.

NOTE: Whether and how CAAR query may be used to direct EECs to a different ECS for the purpose of receiving services consistent with the AC Association may be addressed in the context of enabling inter-ECSP deployments,

### 7.27.3	Solution evaluation

Editor's note.	Further investigation is required if this solution is feasible.

# Comments

Check again about need for ii

See if we can eliminate by having ECS choose EES.

See if we can stay with just the ID