## Slide 1: Requirements for Common EAS support
Niranth, Yajie
Huawei

## Slide 2: Background
In SA6#50-e, the following technical contributions were discussed on Common EAS topic
  S6-222529 (Huawei)
    Proposed the industry use cases for “multi-player game” and “Smart factory” to be captured in Annex and further proposed requirements for “Enablement of Common EAS discovery” based on use cases.
    Contention is on whether use case is required to be captured in the TR. The use case for “multi-player game” for edge computing usage was not agreed.
  S6-222494 (Qualcomm)
    Proposed requirements for “Common EAS” covering static and dynamic group.
    Contention is on dynamic group requirements.
Observation: Dynamic group related use case (especially the multi-player game) and related requirements needs further discussion.

## Slide 3: Use case for multi-player game deployed on Cloud
It is required to achieve a common understanding on the Gaming architecture for multi-player game.
A typical architecture of multi-player game consists of a Login server which is deployed centrally and Game servers may be deployed in the same cloud. The Game servers information is available to the Login server.
Typical operations
  User initiated a Game request to the Login server
  Login server performs authorization check and also does resource allocation to the users. Login server provides a game response with game server information.
  UEs connect to the game servers provided by login server.
UE1
UE2
User1
User2
3GPP network system
Login server
Centralized System (Cloud)
Game server#1
Game server#2
Sharing similar application criteria (e.g. geo area, gaming service)
1
Game request
2
Game response with Game server information
Gaming servers are known to Login server
3
UEs connect to the game servers

## Slide 4: Use case for multi-player game deployed on edge infrastructure
The architecture of multi-player game is now considered to utilize edge infrastructure.
The Login server continues to be deployed centrally and Game servers now are deployed in the EDNs. A new actor called Edge platform is introduced. The main responsibility is to support the Login server with game servers information in the EDNs.
Typical operations
  User initiated a Game request to the Login server
  Login server performs authorization check and also does resource allocation to the users. Login server retrieves game server information which can serve the users.
  Login server provides a game response with game server information.
  UEs connect to the game servers provided by login server.
UE1
UE2
User1
User2
3GPP network system
Login server
Centralized System (Cloud)
Game server#1
Game server#2
EDN-1
EDN-2
Sharing similar application criteria (e.g. geo area, gaming service)
1
Game request
3
Game response with Game server information
4
UEs connect to the game servers
Edge Platform(s)
2
Get Game server information

## Slide 5: Potential requirement (based on use case)
Requirement to support Common EAS.
  The Edge enabler layer shall provide a mechanism to discover EASs in EDNs to support common EAS selection for dynamic group.

## Slide 6
Thank You