## Slide 1: Common EAS – Discussion & Way Forward for Rel-18
Basavaraj (Basu) Pattan
Samsung

## Slide 2: Minimum Basic Requirements
Enable a group of application clients (ACs) to discover a common EAS i.e., same EASID, EAS endpoint and EDN
  Group formation is pre-established and for later use (=static group?)
  Group formation is instant and usually for immediate use (=dynamic group?)
Handling of common EAS due to group modification
Enable a group of ACs to be relocated to a different common EAS i.e. due to EAS unavailability or relocation of all UEs to a new EDN due to mobility

## Slide 3: Architecture decisions to be made on:
How/When is a pre-established group formed?
How/When is a instant group formed?
How does group members know about group information?
Who/How is a common EAS selected for a group?
How does the group members know about the selected common EAS?
What are the impacts to selected common EAS due to group membership update?
How is the group relocated from one common EAS to another?

## Slide 4: How/When is a pre-established group formed?
Pre-established group
  group creator knows whom to include in the group
  members are included in the group before the group is used
  group members can be added/removed to/from the group
  Group id is assigned
  Role of EEL
  None
    group formation happens at application layer and prior to usage of the group

## Slide 5: How/When is a instant group formed?
Instant group
  group is formed based on certain criteria
  all members are not necessarily included in the group before the group is used
  group members can be stationed or moving
  group members move in/out of the group, upon criteria
  Group id is assigned
  Role of EEL
  group formation can happen at both
    application layer e.g. location based group and
    EEL e.g. implicitly formed based on similar interests expressed by ACs

## Slide 6: How does group members know about group information?
Pre-established group:
  Sharing of group information through
    application layer e.g. configuration, notification
  Group members can be added/removed to/from the group, however that may not be reflected to any ongoing group session
  Role of EEL
    None - group information sharing including modification and participant information is at application layer
Instant group:
  Sharing of group information through
    application layer e.g. notification
  group members move in/out of the group, upon criteria, which is reflected to any ongoing group session
  Role of EEL
    None - group information sharing including modification and participant information is at application layer

## Slide 7: Who/How is a common EAS selected for a group?
Pre-established group:
  Common EAS to be used can be pre-determined and configured (at application layer)
  During Discover EAS procedure and common EAS selected by EEC
  During Discover EAS procedure and common EAS selected by EES
  Role of EEL
    is present for Solution option 2 and 3
Instant group:
  During Discover EAS procedure and common EAS selected by EEC
  During Discover EAS procedure and common EAS selected by EES
  Role of EEL
    is present for both options 1 and 2

## Slide 8: How does the group members know about selected common EAS?
Pre-established group:
  Application layer selected common EAS is known to group members via application layer
  EEL selected common EAS is known to group members via application layer
  EEL selected common EAS is known to group members via EEL
  Role of EEL
    is present for Solution option 3
Instant group:
  EEL selected common EAS (always) is known to group members via EEL
    Service provisioning
    EAS discovery response with the support of cloud server
    EAS discovery response without the support of cloud server
  Role of EEL
    is present for all options

## Slide 9: What are the impacts to selected common EAS due to group membership update?
Pre-established group:
  No impacts, continue same common EAS and the session, if any
  Group membership update is effective from next session and in such case follow Slide#7 for selecting a common EAS
Instant group:
  No impacts, continue same common EAS and session
  Group membership update is effective immediately but the already selected common EAS can be continued (in Rel-18)

## Slide 10: How is the group relocated from one common EAS to another?
New common EAS selection in case of EAS unavailability or all UEs move to new EDN
Pre-established group:
  Determine T-EAS and perform ACT (Rel-17)
  Slide#8 to let group members know about new common EAS selected
Instant group:
  Determine T-EAS and perform ACT (Rel-17)
  Slide#8 to let group members know about new common EAS selected

## Slide 11: Conclusion
TBD