## Slide 1: external TR (exTR) – Contributions on Alignment
3GPP
Samar Shailendra (Intel)

## Slide 2: External TR (exTR) Scope*
Alignment and Deployment Aspects of EDGEAPP with ETSI MEC and GSMA OP
  Alignment will include
    EAS profile (EDGEAPP) and AppInfo (ETSI MEC)
    Alignment of EDGE-3 and Mp1 reference points
    Alignment of EDGE-9 and Mp3 (Mp3 specs do not exist, so no alignment is required!)
    Usage of CAPIF between the two architectures
    Aspects related to Federation & Roaming
    Any Other??
  Deployment Options
    End to End deployment options
    Co-existence of two architectures
      Coexistence of EES and MEC Platforms
      Federation and LCM
* Based upon WID (S6-221496)

## Slide 3: Contributions for exTR
Inviting contributions to external TR
Contributions to exTR based upon agreed contributions from Normative discussions
  Technical aspects needs agreement during normative discussions
Contributions to exTR based upon the Technical Studies
  Deployment aspects and other informative content – Avoid duplication between TS and exTR.

## Slide 4: Deployment Options
1. Collocated Platforms
There are seen as two different Afs on a single Physical Infrastructure.
2. Converged Architecture
MEP + EES is able to satisfy all functionalities of MEP and EES.
Uniform APIs are defined for EAS and MEC App i.e. EDGE-3 and Mp1 are unified into one interface and will consume the same APIs from the MEP+EES.
EDGE-9 and Mp3 are unified as one interface. No alignment required because Mp3 specs do not exist.
3. Non-Collocated Platforms
EES and MEP are not collocated and reside in two different MNOs i.e. EES is deployed in MNO-1 and MEP is deployed in MNO-2

## Slide 5: End-to-end Deployment (1/2)
Deployment with EDGEAPP and ETSI MEC
5GC
UE
RAN
N3
AC
UPF
…
PCF
NEF
SMF
AMF
UPF
Edge Data Network
Application Data Traffic
N9
PLMN domain
ECSP domain
N6
Edge Application (API invoker)
EAS
MEC Application
Edge Platform
EES
MEC Platform
CAPIF Core Function

## Slide 6: End-to-end Deployment (2/2)
To be checked with SA5 !

## Slide 7: End-to-end Deployment with Federation
To be checked with SA5 !
Alignment (if any) of MEF and ECS-ER or a new entity corresponding to MEF is in scope of SA5, is to be discussed.!

## Slide 8: Recommendations
Capture the deployment options in exTR.
Capture the end-to-end deployment scenario in exTR.
  Avoid duplication of content between TS and exTR
  Deployment options are informative content
Alignment aspects of interfaces etc. to be captured based upon the normative discussions !!