3GPP TSG-SA WG6 Meeting #56	S6-xxxxxx

# Gothenburg, Sweden 21st – 25th August 2023                                    revision of S6-232196

# Source:	ZTE Corporation

# Title:	SID on application layer support for Factories of the Future; Phase2

# Document for:	Approval

Agenda Item:	10

3GPP™ Work Item Description

For guidance, see 3GPP Working Procedures, article 39; and 3GPP TR 21.900.
Comprehensive instructions can be found at http://www.3gpp.org/Work-Items

# Title: 	Study on application layer support for Factories of the Future; Phase 2

## Acronym: FS_FFAPP2

## Unique identifier: 	{A number to be provided by MCC at the plenary}

## Potential target Release:	Rel-19

## 1	Impacts

| Affects: | UICC apps | ME | AN | CN | Others (specify) |
| --- | --- | --- | --- | --- | --- |
| Yes |  | X |  | X |  |
| No |  |  | X |  | X |
| Don't know | X |  |  |  |  |

## 2	Classification of the Work Item and linked work items

### 2.1	Primary classification

This work item is a

|  | Feature |
| --- | --- |
|  | Building Block |
|  | Work Task |
| X | Study Item |

### 2.2	Parent and child Work Items

| Parent and child Work Items |
| --- |
| Unique ID | Title | Nature of relationship |
|  |  | {mandatory text: "parent WID" or "child WID"} |

### 2.3	Other related Work Items and dependencies

| Other related Work Items (if any) |
| --- |
| Unique ID | Title | Nature of relationship |
| 820025 | Study on application layer support for Factories of the Future in 5G network | Release 17 study for FF application layer support aspects |
| 930015 | Application layer support for Factories of the Future (FF) | Release 18 stage 2 work on FF application layer support |

## 3	Justification

In Release 17, 3GPP SA6 has studied the application layer support for Factories of the Future in 5G network in TR 23.745.

In Release 18, 3GPP SA6 has specified application layer support for Factories of the Future (FF), mostly solutions are specified in TS 23.434 Service Enabler Architecture Layer for Verticals (SEAL), and currently no normative solution in TS 23.545 and only informative guideline of usage for other service enablers.

SA1 has specified in TS 22.261 to support industry 4.o and factory automation by requirements and services listed in Non-public networks, 5G LAN-type service, positioning services, communication services for cyber-physical control applications, Artificial Intelligence (AI)/Machine Learning (ML) operations, tactile and multi-modal communication service.

There are a lot of factory related use cases such as cooperative carrying, digital twin, mobile robots using edge cloud, AGV detection and tracking in factories, AMR collision avoidance in smart factories, integrated sensing and positioning in factory hall, remote control robot, local AI/ML model split on factory robots in TS 22.104, TR 22.837, TR 22.847 and TR 22.876.

Hence it’s needed to study how to support the above services and use cases for FF application enablers.

## 4	Objective

The objectives of the study include:

1.	Analyze SA1 stage 1 requirements for Factories of the Future which have impact on the enabler layer services and deterministic communication requirements of industrial networking technologies;2. 	Develop key issues and solution recommendations to enable the application layer support for the advanced FF services over 3GPP systems (5GS), including:

a)	Support for FLC-to-network topology management;

b)  Dynamic interface selection and configuration (both PC5 and Uu) in mobile scenarios；

c)	Dynamic field device grouping in AGV/mobile robot use cases;

d)	Support for exposing digital twin capabilities.

NOTE: Enhancements to existing SA6 defined enablers (e.g. SEAL, FFAPP) may be required.

## 5	Expected Output and Time scale

| New specifications {One line per specification. Create/delete lines as needed} |
| --- |
| Type | Series | Title | For info at TSG# | For approval at TSG# | Remarks |
| Internal TR | 23.xxx | Study on application layer support for Factories of the Future (FF) ; Phase 2 | SA#104 (Jun 2024) | SA#105 (Sep 2024) |  |

## 6	Work item Rapporteur(s)

Shao Weixiang, ZTE Corporation, shao.weixiang@zte.com.cn

## 7	Work item leadership

SA6

## 8	Aspects that involve other WGs

SA1 on service aspects, SA2 on aspects related to 3GPP system, SA3 on aspects related to security, SA4 on aspects related to media handling, SA5 on aspects related to charging.

## 9	Supporting Individual Members

Supporting IM name

ZTE Corporation

Convida Wireless LLC

China Mobile

CALTTA

CATT

China Telecom

VIVO