3GPP TSG SA6 Meeting #23	S6-180706

Newport Beach, US, 16th – 20th April 2018	revision of S6-180679, S6-170607

| CR-Form-v11.2 |
| --- |
| CHANGE REQUEST |
|  | 23.282 | CR | 0110 | rev | 3 | Current version: | 15.3.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME | X | Radio Access Network |  | Core Network | x |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Modify MCData download data response |
| --- | --- |
| Source to WG: | Hytera Communications Corp, Sepura plc |
| Source to TSG: | S6 |
| Work item code: | eMCData |  | Date: | 2018-04-19 |
| Category: | F |  | Release: | Rel-15 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | “MCData download data response” information flow is not aligned with Stage 3 and does not handle the situation when the corresponding request is not approved. |
| Summary of change: | “Result” field is added as an optional IE into the “MCData download data response” information flow to be used in the case of failure to approve the download. |
| Consequences if not approved: | Stage 3 misalignment, and “MCData download data request” flow does not formally handle the situation when the request is refused |
| Clauses affected: | 7.5.2.1.4 |
|  | Y | N |  |  |
| Other specs |  | x | Other core specifications | TS/TR ... CR ... |
| affected: |  | x | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | x | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

* * * First change * * * *

##### 7.5.2.1.4	MCData download data response

Table 7.5.2.1.4-1 describes the information flow for the MCData download data response sent from the MCData server to the MCData client.

Table 7.5.2.1.4-1: MCData download data response

| Information element | Status | Description |
| --- | --- | --- |
| MCData ID | M | The identity of the MCData user requesting to download data |
| Content (see NOTE) | O | Requested content to download |
| Result | M | Indicates success or failure of MCData download data request |
| NOTE: Content shall be present when the result of the MCData download data request indicates success. |

* * * End change * * * *